## Slide 1
JUAS 2023
February 2023
Muon Collider
D. Schulte
for the International Muon Collider Collaboration

## Slide 2: Motivation and Goal
2
Previous studies in US (now very strong interest again), experimental programme in UK and alternatives studies by INFN
New strong interest in high-energy, high-luminosity lepton collider
Combines precision physics and discovery reach
Muon collider promises sustainable approach to the energy frontier
limited power consumption, cost and land use
Technology and design advances in past years
review did not find any showstoppers
Goal is
10+ TeV collider
potential initial energy stage (e.g. 3 TeV)
higher energies to be explored later

## Slide 3: Physics Goals
3
Energy for discovery reach
10-14 TeV lepton collisions comparable to 100-200 TeV proton collisions
Leptons make the full energy available for particle production, protons only a fraction
Theorists defined goals:
Yields constant number of events in the s-channel
Luminosity must increase as Ecm2 as production cross sections decrease

## Slide 4
A new Interest in Muon Colliders
A. Wulzer, F. Maltoni, P. Meade et al.
O(150) authors, 15 editors, 100 papers
Strong US involvement starting with Muon Smasher’s Guide
and in Muon Collider Forum

## Slide 5: High-energy Colliders
Electron-positron rings are multi-pass colliders limited by synchrotron radiation due to small electron mass of 0.511MeV: LEP, FCC-ee, CEPC
Hence proton rings are energy frontier: LHC, FCC-hh, SppC
Electron-positron linear colliders avoid synchrotron radiation, but single pass: SLC, ILC, CLIC
Typically cost proportional to energy and power proportional to luminosity,
Novel approach: muon collider (the first of its kind)
Large mass of 105.7 MeV suppresses synchrotron radiation => multi-pass
Fundamental particle requires less energy than protons
But lifetime at rest only 2.2 μs
Proportional to energy γ x 2.2 μs => accelerate rapidly collider in small ring
N
S
N
S
accelerating cavities

## Slide 6: Muon Collider Overview
6
Short, intense proton bunch
Ionisation cooling of muon in matter
Acceleration to collision energy
Collision
Would be easy if the muons did not decay
Lifetime is τ = γ x 2.2 μs
Protons produce pions which decay into muons
muons are captured

## Slide 7: Cost and Sustainability
7
CLIC is highest energy proposal with CDR
No obvious way to further improve linear colliders (decades of R&D)
Cost 18 GCHF, power approx. 500 MW
Rough rule of thumb:
cost proportional to energy
power proportional to luminosity
Muon Collider goals (10 TeV), challenging but reasonable:
Much more luminosity than CLIC at 3 TeV (L=20x1034, CLIC: L=2x1034/6x1034)
Lower power consumption than CLIC at 3 TeV (Pbeam,MC=0.5Pbeam,CLIC)
Lower cost
Staging is possible
Synergies exist (neutrino/higgs)
Unique opportunity for a high-energy, high-luminosity lepton collider

## Slide 8: Accelerator R&D Roadmap
8
On CERN Council request Laboratory Directors Group developed Accelerator R&D Roadmap
global community participated, a global roadmap
No insurmountable obstacle found for the muon collider
but important need for R&D
developed two funding scenarios
Full scenario deliverables by next ESPPU/other processes
Project Evaluation Report
R&D Plan that describes a path towards the collider;
Allows to make informed decisions
Council asked for implementation plan
do not yet have the resources of the reduced scenario
Scenario | FTEy | M MCHF
Full scenario | 445.9 | 11.9
Reduced scenario | 193 | 2.45
http://arxiv.org/abs/2201.07895

## Slide 9: Muon Collider Community
Formed collaboration to implement and R&D Roadmap for CERN Council
50+ partner institutions
30+ already signed formal agreement
US Snowmass has strong support
to contribute to R&D
as a collider in the US
Now waiting for P5
EU Design Study approved this summer, 32 partners, O(3+4 MEUR)
(EU+Switzerland+UK and partners)
Plan to apply in 2024 for HORIZON-INFRA-2024-TECH Goal: prepare experimental programme, e.g. demonstrator, prototypes, …

## Slide 10: Technically Limited Timeline
10
Muon collider important in the long term
Prudently explore if MuC can be option as next project
e.g. in Europe if higgs factory built elsewhere
sufficient funding required now
very strong ramp-up required after 2026
might require compromises on initial scope and performance
  3 TeV
Evaluation+decision
To be reviewed considering progress, funding and decisions
Evaluation+decision

## Slide 11: Initial Target Parameters
11
Parameter | Unit | 3 TeV | 10 TeV | 14 TeV
L | 1034 cm-2s-1 | 1.8 | 20 | 40
N | 1012 | 2.2 | 1.8 | 1.8
fr | Hz | 5 | 5 | 5
Pbeam | MW | 5.3 | 14.4 | 20
C | km | 4.5 | 10 | 14
<B> | T | 7 | 10.5 | 10.5
εL | MeV m | 7.5 | 7.5 | 7.5
σE / E | % | 0.1 | 0.1 | 0.1
σz | mm | 5 | 1.5 | 1.07
β | mm | 5 | 1.5 | 1.07
ε | μm | 25 | 25 | 25
σx,y | μm | 3.0 | 0.9 | 0.63
Target integrated luminosities
Note: currently focus on 10 TeV, also explore 3 TeV
Tentative parameters based on MAP study, might add margins
Achieve goal in 5 years
FCC-hh to operate for 25 years
Aim to have two detectors
CLIC at 3 TeV
28
2 (6)

## Slide 12: Key Challenges
12
3) Cost and power consumption limit energy reach
e.g. 35 km accelerator for 10 TeV, 10 km collider ring
Also impacts beam quality
4) Drives the beam quality
MAP put much effort in design
optimise as much as possible
1) Dense neutrino flux
mitigated by mover system and site selection
2) Beam-induced background
0) Physics case

## Slide 13: Key Technology Challenges
13
Proton complex
- Compressing protons to few bunches
Cooling channel
- Channel design
- Superconducting solenoids
- Normal-conducting RF in magnetic field
- Absorbers and windows
- Integration
RCS
- Beam dynamics
- Ramping magnets
- Power converter
- Superconducting RF system
Collider ring
- Optics
- Superconducting magnets
- Neutrino flux
- Detector background
Target
- High-power Target
- Superconducting solenoid

## Slide 14: Muon Decay
14
Muons decay produces neutrinos, electrons and positrons
Electrons/positrons carry on average 1/3 of the muon energy
They will be lost in the machine
Need to protect machine and detector
Muon decays per bunch passage decreases with energy
235,000 m-1 at 3 TeV
58,000 m-1 at 10 TeV

## Slide 15: Muon Decay and Detector Background
15

## Slide 16: Neutrino Flux
16
~2 x 600 m

## Slide 17: Neutrino Flux Mitigation
17
Goal: similar to LHC: limit neutrino flux to have negligible impact, “fully optimised” (10% of MAP goal)
Verify performance of concept to be good for 14 TeV
Mover and support system
F. Bertinelli et al. (CERN, Riga)
G. Lerner, D. Calzolari, A. Lechner, C. Ahdida
FLUKA dose studies
G. Lacerda, Y. Robert, N. Guilhaudin (CERN)
Mitigation:
Site choice tool
Flux direction map / lattice design / mover impact on beam
C. Carli, K. Skoufaris (CERN)
C. Ahdida, P. Vojtyla, M. Widorski, H. Vincke
Conformity Verification Scheme

## Slide 18: Proton Complex and Target Area
Large aperture superconducting solenoid to guide pions/muons
2 MW Proton beam power is no issue
some challenges in H- source and accumulator and combiner complex
Thick shielding of superconducting solenoid

## Slide 19: Target Design
CNGS
CNGS target
3.5 x 1013 protons/pulse, 400 GeV (2.2 MJ), 1/6 Hz
5 x 1014 protons/pulse, 5 GeV (0.4 MJ), 5 Hz
graphite rod with 15 mm radius
or liquid lead
or fluidised tungsten
Thick shielding around target to protect solenoid from radiation and neutrons

## Slide 20: Capture Solenoid
Solenoid can guide positive and negative pions
Goal: Capture field at target: 20 T, 150 mm aperture
Two approaches:
15 T Nb3Sn with resistive insert
  similar to ITER central solenoid
20 T HTS
  Relevant for advanced fusion reactors
Challenge: shielding of debris of 2 MW proton beam
thick tungsten layer required
1-2 m large aperture of superconducting solenoid
Two limitations:
radiation dose
displacement of atoms due to neutrons
ITER Central Solenoid Model Coil
13 T in 1.7 m (LTS)
MIT/CFS SPARC TF Coil prototype
20 T at 20 K (HTS)

## Slide 21: Final Cooling Principle
Energy loss = cooling
Multiple scattering = heating
High field solenoids minimise beta-function and impact of multiple scattering

## Slide 22: MICE: Cooling Demonstration
22
Principle of ionisation cooling has been demonstrated
Use of data for benchmarking is still ongoing
Nature vol. 578, p. 53-59 (2020)
More particles at smaller amplitude after absorber is put in place
More complete experiment with higher statistics, more than one stage required
Integration of magnets, RF, absorbers, vacuum is engineering challenge

## Slide 23: Cooling: The System Chain
Y
Transverse Emittance (microns)
Longitudinal Emittance (mm)
bunch merge
For acceleration to multi-TeV collider
Final
Cooling
post-merge 6D cooling
For acceleration to NuMAX (325MHz injector acceptance 3mm,24mm)
Target
Phase
Rotator
Front End



pre-merge 6D Cooling
Exit Front End
(15mm,45mm)
Specification
MAP collaboration

## Slide 24: Equilibrium Emittance, Material and Energy
Material property
best is hydrogen
Lithium hydride is good solid material
best at low energies
but rapidly increasing energy spread
use for final cooling
Most of cooling is done here
Hard stochastic losses
Strong solenoid field helps

## Slide 25: Solenoid Fields
HTS insert of NHMFL all SC 32 T
32 T in 40 mm (15 T LTS + 17 T HTS)
NHMFL HTS Little Big Coil
45.5 T in 14 mm (14.5 T HTS + 31 T resistive)
LNCMI/CEA Nougat
HTS insert
32.5 T in 50 mm
(12. 5 T HTS + 20 T resistive)
Sunam NI one-body
HTS magnet
26.4 T in 35 mm
Solenoids with >30 T and aperture of 50 mm exist for high magnetic field science
The limit is the stress in the HTS
Even 60 T might be possible
but important R&D required to see how far we can push
Luca Bottura

## Slide 26: 6D Cooling Cell Design
Initial 6D cooling
MuCool: >50 MV/m in 5 T
Two solutions
H2-filled copper cavities
Cavities with Be end caps
2.2 T
High-gradient cavities in high magnetic field
Tight integration of solenoids, RF, absorbers, instrumentation, cooling, vacuum, alignment, …
Slight bending separates energies and allows longitudinal cooling

## Slide 27: RF Cavity Challenge
Magnetic field concentrates electron emitted from surface
Solution 1:
Beryllium cavity
Experiment (MUCOOL):
Cavity in 3 T: 50 MV/m with 30 μs RF pulse
Solution 2:
Hydrogen-filled cavity
Experiment (MUCOOL):
Cavity in 3 T:
65 MV/m ,5 g/l H2
Sorry, could not find better figure
Density
Gradient

## Slide 28: Acceleration Complex
EMMA proof of FFA principle
Nature Physics 8, 243–247 (2012)
FNAL 300 T/s HTS magnet
F. Boattini et al.
Important cost and power consumption
Started
Integrated design of RCS
  lattice with realistic hardware specifications
  collective effects
Concept of key components
  Fast-ramping normal magnets
  HTS alternative
  Efficient power converters
  RF with transient beam loading
Alternative FFA
H. Damerell, F. Batsch, U. van Rienen, A. Grudiev et al. (Rostock, Milano, CERN)
L. Bottura et al. (LNCMI, Darmstadt, Bologna, Twente)
A. Chance et al. (CEA)
Core of baseline is sequence of pulsed synchrotron (0.4-11 ms)
S. Machida et al. (RAL)
E. Metral et al. (CERN)

## Slide 29: Collider Ring
29
MAP developed 4.5 km ring for 3 TeV with Nb3Sn
magnet specifications in the HL-LHC range
A. Lechner
D. Calzolari (CERN)
Shielding
Coil
500 W/m due to muon decay
Need thick shielding
150 mm aperture
stress managed magnets
Working on 10 km ring for 10 TeV collider ring
around 16 T Nb3Sn or HTS dipoles
final focus based on HTS
C. Carli, K. Skoufaris (CERN)
High field = small circumference = high luminosity

## Slide 30: Collider Ring: Final Focus
Beta-function should be small
Divergence of beam is large
=> challenging optics and magnet design
Beam divergence (angles) is the same at all energies
more difficult to make optics
becomes long
and difficult to correct chromatic effects

## Slide 31: CDR Phase
31
Evaluation+decision
To be reviewed considering progress, funding and decisions
Evaluation+decision
Will contain component prototypes, beam tests and facilities with beam
a muon production and cooling demonstrator is important components
targets
hybrid RCS
…
Can be distributed world-wide

## Slide 32: Test Facility Dimensions
Target
+ horn (1st phase) /
+ superconducting solenoid (2nd phase)
Momentum selection chicane, 10 m
Collimation and upstream diagnostics area, 10 m
Cooling area, 50 m
Downstream diagnostics area, 5 m
C. Rogers
Look for an existing proton beam with significant power
Different sites are being considered
CERN, FNAL, ESS are being discussed
J-PARC also interesting as option

## Slide 33: Possible CERN Locations
M. Calviani
Consider nTOF-like beam from PS for cooling experiment:
1 pulse of 1013 p at 20 GeV per 1.2 s, i.e. 27 kW
maybe O(100kW) possible
If SPL were, installed could use its beam, e.g. 5 GeV, 4 MW

## Slide 34: Staging
Ideally would like full energy right away, but
staging could lead to faster implementation
Substantially less cost for a first stage
Can make technical compromises
  e.g. 8 T NbTi magnets would increase collider ring from 4.5 to 6 km and reduce luminosity by 25%
Timeline might be more consistent with human lifespan
Upgrade adds one more accelerator and new collider ring
only first collider ring is not being reused

## Slide 35: Conclusion
35
Muon collider is unique opportunity for high-energy, high-luminosity lepton collider
  Less mature than other options
  But promises compactness, cost and power efficiency
  Mainly technological challenges
Currently two different options considered
  Goal of 10+ TeV, potential 3 TeV intermediate stage explored
  Deliverables for next strategies: Project Evaluation Report and R&D Plan
Addressing key challenges
  Very motivated team
  Synergy with applications for society, e.g. HTS solenoids
  More funding required for full results by next strategy processes
http://muoncollider.web.cern.ch
To join contact
muon.collider.secretariat@cern.ch

## Slide 36: Reserve

## Slide 37: Muon Collider Luminosity Scaling
Fundamental limitation
Requires emittance preservation and advanced lattice design
Applies to MAP scheme
Luminosity per power increases with energy
Provided technologies can be made available
Constant current for required luminosity scaling
High field in collider ring
Dense beam
High energy
High beam power
Large energy acceptance

## Slide 38: Alternatives: The LEMMA Scheme
LEMMA scheme (INFN) P. Raimondi et al.
45 GeV positrons to produce muon pairs
Accumulate muons from several passages
Excellent idea, but nature is cruel
Detailed estimates of fundamental limits show that we require a very large positron bunch charge to reach the same luminosity as the proton-based scheme
Need same game changing invention
Note: New proposal by C. Curatolo and L. Serafini needs to be looked at
Uses Bethe-Heitler production with electrons

## Slide 39: Acceleration
J. Scott Berg, et al.
Sequence of
linac
two recirculating linacs
two to four rings
  baseline: pulsed synchrotron (RCS)
  alternative: FFA
Hybrid RCS combine static superconducting magnets and fast-ramping normal-conducting magnets

## Slide 40: Magnet Powering
Parameter | unit | RCS 1 | RCS 2 | RCS 3
E1 | GeV | 60 | 300 | 1500
E2 | GeV | 300 | 1500 | 5000
<G> | MV/m | 2 | 2 | 1
Nin | 1012 | 2.82 | 2.48 | 2.18
Nout | 1012 | 2.48 | 2.18 | 1.8
Lstatic | km | 0.47 | 2.35 | 8.5
Lramp | km | 1.26 | 6.28 | 18.3
LRF | km | 0.28 | 1.38 | 1.9
C | km | 2.8 | 13.8 | 38
beam turns |  | 44 | 44 | 92
Tramp | ms | 0.4 | 2 | 11.67
dB/dt | kT/s | 10 | 2 | 0.34
Eramp | MJ | 16 | 80 | 234
Pramp | GW | 64 | 64 | 32
Beam loss | W/m | 20 | 17.8 | 31.4
Move energy into magnets before beam
Take energy out
Put it back in with other sign
Take it out again after beam is gone
So total of 3.3 GJ go into the magnets each second
Need recovery on the 98% level

## Slide 41: Power Converter
Laser Mega Joule (France) 480 x CapacitorBankModule ≈ 400MJ
One CBM: 860kJ @ 24kV; 360us wide 240kA current pulse;
5.76 GW peak power
1 pulse every 25min; 2500 kg; total lifetime  200’000 pulses (12h of the MC)
estimated price 70kCHF
Cost ≈ 0.09 CHF/Joule
POPS (CERN) 6 x CapacitorContainers ≈ 20MJ
One CC: 3.2MJ @ 5kV; 2ms wide 2kA current pulse;
10 MW peak power
1 pulse every 1.2s; 25000 kg;
total lifetime 120’000’000 pulses (1 year of the MC)
estimated price 500kCHF
Cost ≈ 0.15 CHF/Joule
Total stored energy in MC: O(200 MJ), demonstrated
Peak power (all rings combined) 150 GW, demonstrated
But lifetime and average power is demanding (109 pulses)
Also switch the voltage in the capacitors

## Slide 42: First Design
Initial design with two frequencies and active filter for linearisation
Cost of power converter is important
mainly active filters due to linear ramp
need iteration with beam dynamics
then will see for capacitors
Need to estimate power losses
Need optimisation in loop with magnet design, beam dynamics, RF, …
Power converter as project drivers
Synergy power grid applications

## Slide 43: Final Focus Magnet Challenge
At 3 TeV:
Up to 12 T in aperture 150 mm
Similar to HL-LHC final focus magnets
Close to state of the art with Nb3Sn
At 10+ TeV:
Aperture of 200+ mm
20 T field in aperture
Stress is significantly higher
Will need HTS
Parameter | Q1 | Q1 | Q3 | Q4
Aperture (mm) | 90 | 110 | 130 | 150
Gradients (T/m) | 267 | 218 | -154 | -133.5
Peak field (T) | 12 | 12 | 10+ | 10+
Dipole field (T) | 0 | 0 | 2.00 | 2.00
3 TeV FFS Design (MAP)
HTS magnet development is essential for 10 TeV

## Slide 44: Neutrino Flux Mitigation
15 cm
~2 x 600 m
t1
t2
s1
neutrinos
Use mover system to reduce neutrino flux and limit impact on environnement to lvel similar to LHC
time
angle
Active mover system to reduce flux density
Large stroke mover system with precision
High reliability
Alignment system with reference to the surface
Mechanical forces on tilted girders
Connections, e.g. cryogenics (helium)

## Slide 45: Neutrino Flux
45
Expand idea of Mokhov, Ginneken to move beam in aperture: move collider ring components, e.g. vertical bending with 1% of main field
14 TeV, in 200 m deep tunnel comparable to LHC case with +/- 1 mradian
scales with luminosity toward higher E
Need to study mover system, magnet, connections and impact on beam
~2 x 600 m
Dense neutrino flux cone can impact environment Challenge scales with E x L
Goal is to reduce to negligible level, similar to LHC
3 TeV, 200 m deep tunnel is about OK
Working on different approaches for experimental insertion
Other optimisations are possible (magnetic field, emittance etc.)

## Slide 46: Organisation
International Collaboration Board represents the partners
International Advisory Committee
Coordination Committee
executes the study
(only Study Leader in MoC)
Steering Board oversees study and links to regional supervision (addition to MoC)

## Slide 47: Thanks
47
Community conveners: Radio-Frequency (RF): Alexej Grudiev (CERN), Jean-Pierre Delahaye (CERN retiree), Derun Li (LBNL), Akira Yamamoto (KEK). Magnets: Lionel Quettier (CEA), Toru Ogitsu (KEK)‎, Soren Prestemon (LBNL), Sasha Zlobin (FNAL), Emanuela Barzi (FNAL). High-Energy Complex (HEC): Antoine Chance (CEA), J. Scott Berg (BNL), Alex Bogacz (JLAB), Christian Carli (CERN), Angeles Faus-Golfe (IJCLab), Eliana Gianfelice-Wendt (FNAL), Shinji Machida (RAL). Muon Production and Cooling (MPC): Chris Rogers (RAL), Marco Calviani (CERN), Chris Densham (RAL), Diktys Stratakis (FNAL), Akira Sato (Osaka University), Katsuya Yonehara (FNAL). Proton Complex (PC): Simone Gilardoni (CERN), Hannes Bartosik (CERN), Frank Gerigk (CERN), Natalia Milas (ESS). Beam Dynamics (BD): Elias Metral (CERN), Tor Raubenheimer (SLAC and Stanford University), Rob Ryne (LBNL). Radiation Protection (RP): Claudia Ahdida (CERN). Parameters, Power and Cost (PPC): Daniel Schulte (CERN), Mark Palmer (BNL), Jean-Pierre Delahaye (CERN retiree), Philippe Lebrun (CERN retiree and ESI), Mike Seidel (PSI), Vladimir Shiltsev (FNAL), Jingyu Tang (IHEP), Akira Yamamoto (KEK). Machine Detector Interface (MDI): Donatella Lucchesi (University of Padova), Christian Carli (CERN), Anton Lechner (CERN), Nicolai Mokhov (FNAL), Nadia Pastrone (INFN), Sergo R Jindariani (FNAL). Synergy: Kenneth Long (Imperial College), Roger Ruber (Uppsala University), Koichiro Shimomura (KEK). Test Facility (TF): Roberto Losito (CERN), Alan Bross (FNAL), Tord Ekelof (ESS,Uppsala University).
Muon Beam Panel: Daniel Schulte (CERN, chair), Mark Palmer (BNL, co-chair), Tabea Arndt (KIT), Antoine Chance (CEA/IRFU) Jean-Pierre Delahaye (retired), Angeles Faus-Golfe (IN2P3/IJClab), Simone Gilardoni (CERN), Philippe Lebrun (European Scientific Institute), Ken Long (Imperial College London), Elias Metral (CERN), Nadia Pastrone (INFN-Torino), Lionel Quettier (CEA/IRFU), Magnet Panel link, Tor Raubenheimer (SLAC), Chris Rogers (STFC-RAL), Mike Seidel (EPFL and PSI), Diktys Stratakis (FNAL), Akira Yamamoto (KEK and CERN) Contributors: Alexej Grudiev (CERN), Roberto Losito (CERN), Donatella Lucchesi (INFN)
And the participants to the community meetings and the study

## Slide 48: Roadmap
48
In aspirational scenario can make informed decisions:
Three main deliverables are foreseen:
a Project Evaluation Report for the next ESPPU will contain an assessment of whether the 10 TeV muon collider is a promising option and identify the required compromises to realise a 3 TeV option by 2045. In particular the questions below would be addressed.
  What is a realistic luminosity target?
  What are the background conditions in the detector?
  Can one consider implementing such a collider at CERN or other sites, and can it have one or two detectors?
  What are the key performance specifications of the components and what is the maturity of the technologies?
  What are the cost drivers and what is the cost scale of such a collider?
  What are the power drivers and what is the power consumption scale of the collider?
  What are the key risks of the project?
an R&D Plan that describes an R&D path towards the collider;
an Interim Report by the end of 2023 that documents progress and allows the wider community to update their view of the concept and to give feedback to the collaboration.

## Slide 49: R&D Plan
The R&D plan will describe the R&D path toward the collider, in particular during the CDR phase, and will comprise the elements below.
An integrated concept of a muon cooling cell that will allow construction and testing of this key novel component.
A concept of the facility to provide the muon beam to test the cells.
An evaluation of whether this facility can be installed at CERN or another site.
A description of other R&D efforts required during the CDR phase including other demonstrators.
This R&D plan will allow the community to understand the technically limited timeline for the muoncollider development after the next ESPPU.

## Slide 50: Minimal Scenario
Will allow partially informed decisions
No conceptual design of neutrino flux and alignment system
No alternative superconducting fast-ramping magnet system
Several collider systems would (almost) not be covered, in particular
  the linacs
  the target complex
  the proton complex
  engineering considerations of the muon cooling cells
  alternative designs for the final cooling system, acceleration, collider ring
No RF test stand would be constructed for the muon cooling accelerating cavities
No conceptual design of a muon cooling cell for the test programme
No conceptual design of a muon cooling demonstrator facility
No concept of RF power sources
No tests/models to develop solenoid technology.

## Slide 51: Schedule
51
2023
Interim Report to gauge progress
Initial baseline defined
2025
Assessment Report
2025-2027
R&D plan will be refined

## Slide 52: Coordination Committee Members
Physics | Andrea Wulzer
Detector and MDI | Donatella Lucchesi
Protons | Natalia Milas
Muon production and cooling | Chris Rogers
Muon acceleration | Antoine Chance
Collider | Christian Carli
Magnets | Luca Bottura
RF | Alexej Grudiev, Claude Marchand
Beam-matter int. target systems | Anton Lechner
Collective effects | Elias Metral
US (detector) | Sergo Jindariani
US (accelerator) | Mark Palmer
Asia (China) | Jingyu Tang
Asia (Japan) | tbd
Cooling cell design | Lucio Rossi
Demonstrator | Roberto Losito
A strengthening on the physics and detector side is planned

## Slide 53: Key Technologies
Magnets
Superconducting solenoids for target and cooling profit from developments for society
  target solenoid comparable to ITER central solenoid fusion
  6D cooling solenoids similar and wind power generators, motors
  final cooling solenoids synergetic with high-field research, NMR
Collider ring magnets
  profit from developments for other colliders FCC-hh, stress-managed magnets
Fast-ramping normal-conducting magnet system
  HTS alternative, power converter
RF systems
superconducting RF, normal-conducting RF, efficient klystrons
Target, cooling absorbers, windows, shielding
Neutrino mitigation mover system, cooling cell integration, …
Detector

## Slide 54: Key Technologies, cont.
RF systems
Normal-conducting cooling cavities in magnetic field
  profit from CLIC work
Superconducting accelerator RF
  profit from ILC, …
Efficient power sources
  profit from CLIC work
Beam-matter interaction
Proton target
Cooling absorbers
Shielding (accelerator and detector)
Mechanical system
Neutrino flux mitigation system
Muon cooling cell integration

## Slide 55: Collaboration Vision
IMCC is an international collaboration and aims to
Enlarge the collaboration
  Physics interest in all regions, strong US contribution to the muon collider physics and detector, interest in Japan
  First US university have joined collaboration, try to see how to move forward, also with labs
Combine the R&D efforts for the design and its technologies
  Critical contributions in all relevant fields the US
Consider several sites for the collider
  CERN would be one, FNAL and others should also be considered
  A proposal with alternative sites is stronger for a single site
Consider several sites for the demonstrators
  E.g. Muon production and cooling demonstrator at CERN, FNAL, ESS, JPARC
  e.g. RCS at ESRF or elsewhere
  Target tests
  …

## Slide 56: Collaboration Organisation
Collaboration Board (ICB)
  Chair: Nadia Pastrone
Steering Board (ISB)
  Chair Steinar Stapnes
  Reports to LDG but could add DOE
Advisory Committee (IAC)
  To be defined
Coordination committee (CC)
  Study Leader Daniel Schulte
  Deputies: Andrea Wulzer, Donatella Lucchesi, Chris Rogers
  Sergo Jindariani, Mark Palmer as US links
  Will strengthen physics and detectors

## Slide 57: Muon Decay and Detector Background
57
Muons decay produces electrons and positrons
Loss per unit length almost independent of energy
Tools mostly ready to generate background
tentative beamline and mask, FLUKA
tentative beam-beam for muons (GUINEA-PIG)
Studies at 1.5 <and 3 TeV with concept based on CLIC detector
Radiation level in tracking detector similar to HL-LHC
Studies with beam-induced background in progress
some channels are not affected by background
some improvement required for other channels
Concept for 10 TeV in progress
Detector team
O(69) authors, O(150 signatories)

## Slide 58: Note: Liquid Metal Target
Tested with
30x1012 protons with 24 GeV yield 9x1012 muons
Almost enough (loose 90%)
Safety concerns prevent this in Europe
Other metals or dust stream are options

## Slide 59: Cooling Cell Technology
59
Will develop example cooling cell integration
tight constraints
additional technologies (absorbers, instrumentation,…)
early preparation of demonstrator facility
RF cavities in magnetic field
MAP demonstrated higher than goal gradient
Improve design based on theoretical understanding
Preparation of new test stand, but needs funding
Test stand at CEA (700 MHz, need funding)
Test at other frequencies in the UK considered
Use of CLIC breakdown experiment considered
C. Marchand, Alexej Grudiev et al. (CEA, Milano, CERN, Tartu)
Assessment of realistic goal for highest field solenoids
MAP demonstrated 30 T
now magnets aim for 40+ T
even more can be possible
synergy with high-field research
L. Rossi et al. (INFN, Milano, STFC, CERN),
J. Ferreira Somoza et al.
MuCool demonstrated >50 MV/m in 5 T
H2-filled copper
Be end caps
L. Bottura et al.
INFN (Task Leader), CEA, CERN, LNCMI, PSI, SOTON, UNIGE and TWENTE, in collaboration with KEK and US-MDP

## Slide 60: RF Cavity Challenge
Gradient of normal-conducting RF cavities is typically limited by breakdown
Model:
electrons start at one emitter site
electrons are accelerated by cavity field and hit other side
In solenoid field:
electrons spiral around magnetic field line
they all hit one spot on the other site
this can heat spot above plastic deformation stress
and lead to breakdown
in any case electrons bounce back and forth between sites

## Slide 61: RF Cavities: Approach 1
Reduce the time in which we have losses in the wall
shorter pulses
but requires to fill energy into the cavity more quickly
requires higher peak power from klystrons
this is more costly
Reduce the energy lost by the electrons in the cavity walls
e.g. replace copper with beryllium
  lower density, smaller Z
Experimental result (MUCOOL):
Beryllium cavity in 3 T: 50 MV/m with 30 μs RF pulse
To be studied: gradient in higher field

## Slide 62: RF Cavities: Approach 2
Use high-pressure hydrogen gas inside of the cavity
the electrons will collide with the hydrogen and lose energy
condition: The mean free path of the electron must not allow it to gain more than O(15 eV), the ionisation energy of hydrogen
Obviously different design of cooling system
cavities also serve as absorbers
Experimental results (MUCOOL):
Molybdenum cavity in 3 T: 65 MV/m
limited by gas density (gradient is proportional to density)
Some material dependence
Sorry, I can only find this poor quality figure