## Slide 1: An introduction to CERN Beams Controls Software & Services
Chris Roderick
04-04-2023

## Slide 2: CERN Beams Controls Software & Services
“Provides Control & Monitoring solutions for all CERN particle accelerators, transfer lines, associated experimental areas & various supporting technical infrastructure services.”
∙LINAC3/4 ∙PS ∙PSB ∙SPS ∙LHC ∙LEIR ∙ISOLDE ∙AD/ELENA
12 in 1
12 in 1
Key aims:
As simple as possible
High usability, stability, availability
Common approach

## Slide 3: CERN Beams Controls Software & Services
Configure & Set states & reference values (aka settings) in active elements Generate initial values, automate sequences, feedback loops, etc.
The Control System's job is to provide physicists and operators with a means to remotely:
Monitor elements (instruments & actuators) Time-tagged acquisitions with post-processing for quick detection of abnormal situations
Long-term memory of Settings & Acquisitions Years of data with performant data extraction & analysis tools
Health & Diagnostics monitoring for the multitude of sub-systems Online failure detection, remote interventions (e.g. power cycle), failure prediction (Machine Learning) etc.
Ensure machine protection & operational availability High-level fast-reaction interlocks & role-based access to prevent wrong actions
& much more…

## Slide 4: High-Level Software Architecture
Front-end Tier
Real-time control and acquisition
Limited, local scope
Fast reaction possible (interrupts)
Limited computing power (compared to other tiers)
Equipment processing to provide a high-level view of hardware
Real-time (RT) applications rely on frameworks, which capture recurring aspects (react to events, publish new data, etc.)
Based on technologies close to HW (C for drivers, C++ for RT, etc.)
Operating System
(Linux)
Device Drivers *
(e.g. Timing receiver kernel module)
RT Frameworks
(e.g. FESA)
RT Application
(e.g. Kicker system control)
Notes: FESA (Front-End Software Architecture): CERN’s real-time application fram ework.

## Slide 5: High-Level Software Architecture
Server Tier
General purpose services & Specific business logic
Broader scope; able to coordinate across entire accelerator
Powerful computers
Less reactive (network) and at a higher-level of abstraction
Based on technologies suited for higher-level logic (e.g. Java)
Settings Management
(InCA/LSA)
Long-term Logging
(NXCALS)
Automation
(Sequencer, SIS)
Etc.
Notes: Today the services are deployed “bare metal” but as Remi explains we’re looking at containers and container orchestration
LSA (LHC Software Archeticture): CERN’s settings management system.
NXCALS (CERN Accelerator Logging System): CERN’s long-term storage for acquisitions and, soon, settings.
SIS (Software Interlock System): CERN’s non-real-time interlock system based on software decision trees.

## Slide 6: High-Level Software Architecture
Controls Middleware
Client Tier
Graphical applications
Different technologies in use
Java Swing, Java FX
PyQt
Web ecosystem (Angular)
Communication
Accelerator-specific protocols for the lower layers
  Controls Middleware (CMW)
More generic technologies for the higher layers
  RMI/JMS
  REST
  gRPC
  …
Controls Middleware & more generic solutions
Notes: Presentation layer (see Hermann 14) - In its own slide cite != techno Java, Python, Web and show a few pictures from Hermann

## Slide 7: High-Level Hardware Architecture
Resource Tier
Electronics close to the accelerator
Server Tier
Central computing infrastructure
Client Tier
e.g. Control Room infrastructure
Notes: HW – 3 tiers but going for a physical 4 tier w/ the DIOT

## Slide 8: Examples – Accelerator Control
Timing System
New value = x
Server
Database
x
GUI
x, a, b, c
x  a, b, c
RT Application
RT Application
RT Application
Hardware
Hardware
Hardware
a
b
c
Control now!
0x61
0x62
0x63
FESA Class
VMEBus board
General Machine Timing (GMT)
Oracle Database
InCA/LSA Server
Notes: HW – 3 tiers but going for a physical 4 tier w/ the DIOT

## Slide 9: Examples – Equipment Monitoring
Timing System
Here are a, b, c, and Everything is OK
UCAP* Server
a’, b’, c’ @ ti
GUI
RT Application
RT Application
RT Application
Hardware
Hardware
Hardware
a @ ti
b @ ti
c @ ti
Read now!
(time = ti)
0x61
0x62
0x63
Measure now!
FESA Class
VMEBus board
General Machine Timing (GMT)
*UCAP: Unified Controls Acquisition & Processing framework
Notes: HW – 3 tiers but going for a physical 4 tier w/ the DIOT

## Slide 10: Examples – Timeseries Data Logging
Timing System
Values on the 06/06/2021 ?
NXCALS
Hadoop
a, b, c @ 06-06-21
SWAN Notebook
a, b, c @
06-06-21
RT Application
RT Application
RT Application
Hardware
Hardware
Hardware
a @ ti
b @ ti
c @ ti
Read now!
(time = ti)
0x61
0x62
0x63
Measure now!
a, b, c @ ti
FESA Class
VMEBus board
General Machine Timing (GMT)
*SWAN: Service for Web based ANalysis
Notes: HW – 3 tiers but going for a physical 4 tier w/ the DIOT

## Slide 11: Questions?
“Provides Control & Monitoring solutions for all CERN particle accelerators, transfer lines, associated experimental areas & various supporting technical infrastructure services.”
∙LINAC3/4 ∙PS ∙PSB ∙SPS ∙LHC ∙LEIR ∙ISOLDE ∙AD/ELENA
12 in 1
12 in 1
Key aims:
As simple as possible
High usability, stability, availability
Common approach

## Slide 12: Additional Slides
Notes: HW – 3 tiers but going for a physical 4 tier w/ the DIOT

## Slide 13: WRAP
Notes: HW – 3 tiers but going for a physical 4 tier w/ the DIOT

## Slide 14: Sequencer
Notes: HW – 3 tiers but going for a physical 4 tier w/ the DIOT

## Slide 15: UCAP
Find more at: JACoW-ICALEPCS2021-MOPV039_Poster
JACoW-ICALEPCS2021-MOPV039_Paper
Notes: HW – 3 tiers but going for a physical 4 tier w/ the DIOT

## Slide 16: Fault Tracking & Availability
Notes: HW – 3 tiers but going for a physical 4 tier w/ the DIOT

## Slide 17: NXCALS – Data Logging System
Data Extraction
Data Storage
Data Sources
SWAN (Jupyter)
NXCALS
Data Access
API
Configuration via CCDE
Settings, PM, etc
CERN Specific
API
MetaData
API
Extensive Set of APIs & Tools
Spark Bundle
“pip install nxcals”
TIMBER - GUI
Heterogenous Inputs
WinCC OA Datasources
CMW Datasources
TIM & REMUS Datasources
cluster
API
ETL
ETL
ETL
ETL
ETL
ETL
ETL
ETL
Notes: HW – 3 tiers but going for a physical 4 tier w/ the DIOT

## Slide 18: Machine Learning Platform (MLP)
Machine Learning Platform (MLP) is the new central platform for storing, versioning and deploying ML models in the CERN Control Centre
Find more at: JACoW-ICALEPCS2021-MOBL03
https://indico.cern.ch/event/1175862/
create, update and deploy models with minimal effort
automate seamless model updates as machines characteristics evolve
focus on domain & ML by abstracting the infrastructure
Controls application
Accelerators
Training environment
Physicist
VCS, CI
Model registry
Metadata DB
Object Storage DB
model = client.create_model(
model_type = BeamLineModel,
model_parameters = “ion_beam“,
params_version = AUTO
)
result = model.predict(input)
model.fit(training_data)
client.publish_parameters_version(
model,
name = “ion_beam”, version = AUTO # generated )
$ git tag v2.0.0
Serving cluster (TN)
ATS-IT Collaboration!