## Slide 1: Introduction to the activities of WP4.1 Common modelling and simulation tools for HFM magnets and conductors Model-Based Systems Engineering (MBSE) and Product Cycle Engineering Merging simulations, test and magnetic measurements of accelerator magnets
Stephan Russenschuck
18.04.2023

## Slide 2: Overview
What we can(not) calculate
What we can(not) measure
Generalized field descriptions
Model-based system engineering (MBSE)
Product cycle engineering
Software and database frameworks interfaces
M. Bonora: Advances on an open software environment, hosting psMBSE

## Slide 3: Conclusions
HFM magnets require multiphysics calculations in the early design phase.
Multiphysics simulations must be validated with measurements.
Validation requires proper design of experiments.
Design of experiments require collaborative efforts
Collaborative efforts must consider
ownership (being a co-author on a paper is not enough)
accessibly (sending files and software exec is not enough)
sustainability (a ppt presentation or paper is not enough)
Product generation engineering
Model-based systems engineering

## Slide 4: Quench Simulation (Multi-Physics, Multi-Scale)
19
Quench Simulation
Multi physics
  Thermo (hydraulic)
  Mechanic
  Electric (circuit)
  Magnetic
Multi rate
  Fast effects on long time scales
Multi scale
  Filaments 6 μm
  Strands 1 mm
  Cable 0.1 m
  Magnet 10 m
  String 3.2 km
Notes: quench simulation requires coupling of different models
paper reference
adiabatic !?

## Slide 5: Material Parameters
5
Thermal conductivity
Electrical resistivity
Volumetric heat capacity
Empirical parameters:
- RRR
- Ra/Rc
- IFCC effective res.
- heat conductivity
- heat capacity
Measured quantities to be reproduced with all material- and model-parameters within their range of uncertainty.

## Slide 6: SM18 Test Station for SC Magnets

## Slide 7
Instrumentation
Quench antenna
U1
U2
U1
U2
Quench localization
VI Measurements
Trim powering
Cold-Testing of Superconducting Magnets

## Slide 8: Combined Function Magnets (CERN PS)
4 pole face windings
affecting B1 to B5
Figure-of-eight loop
to control B2
Strongly coupled
excitation circuits
No 10-4 predictive model
Remanent field  0.2%
FMR field
marker
Fluxmeter
for gradient
measurements

## Slide 9
  CNGS
  CNGS
  CNGS
PS Beam Stability Test at Injection
Specific powering cycles (CNGS) lead to reproducible radial positioning errors
from relative field changes on the order of 10-5

## Slide 10: 311 Magnetic Measurement Laboratory for NC magnets

## Slide 11: Rotating Coil Magnetometers
380 mm
Rotating Coil Magnetometers

## Slide 12: Local Field Distribution (Fourier-Bessel Series)
Problems arising: You can’t unscramble the egg

## Slide 13: The Leading Term is NOT the Measured One
Deconvolution of the Measured Transversal Harmonics

## Slide 14: The Avatar and Twin (classical black-box measurement)
Raw signal
(voltages)
Processed data (fluxes)
Physical object (magnet)
Capture noise
(random, systematic)
Read-out noise
(electronics, maiinly random=
AD-conversion
Digital integration,
Drift correction
Magnetic flux density in the magnet bore
Field Transducer
Modelling,
Calibration,
Approximation errors
Bringing together Simulations and Magnetic Measurements

## Slide 15: The Avatar and Twin (tracing of manufacturing tolerances and errors)
Raw signal
(voltages)
Processed data (fluxes)
Physical object (magnet)
Num. magnet model (design)
Modeling errors
Discretization errors
Approximation errors
Numerical errors
Manufacturing tolerances/errors
Capture noise
Read-out noise
AD-conversion
Digital integration,
Drift correction
Prediction
Magnetic flux density in the magnet bore
Num. magnet model (as built)
Magnetic flux
density in W
Solver
Observation function
Post-processor
Field
Transducer
QA
Simulated ????? Measured
Bringing together Simulations and Magnetic Measurements

## Slide 16: The Avatar and Twin (generalized field description with updated model)
Raw signal
(voltages)
Processed data
Physical object (magnet)
Observation function
Prediction
Comparable quantity
Magnetic flux density in the magnet bore
Weighted least-squares
Quantity of interest
Expected voltages in transducer, including uncertainty
Physical state variables
Boundary Sources (Single and Double-layer Potentials, or Harmonic coefficients on trivial domains)
Magnetic flux density in
trivial domain W
Field
Transducer
Avatar
Inverse field problem
Bringing together Simulations and Magnetic Measurements

## Slide 17: Example: 3D Multipole Fields in Magnet Ends
Magnetic flux density parameterized by pseudo-multipoles at the surface of cylinder
Raw signal
(voltages)
Flux increments
Physical object (magnet)
Rotating coil
Flux linked with the coil area
Observation function
Magnetic vector potential for particle tracking
Prediction
Comparable quantity
Magnetic flux density in the magnet bore
Weighted least squares
3D Field inversion
Quantity of interest
Bringing together Simulations and Magnetic Measurements

## Slide 18
Model-Based Systems Engineering
Magnets & Devices
Model
Prototype
Series
Instrumentation & Transducers
Design
Calibration
Uncertainty analysis
Design & analysis software
ROXIE
Ansys
Opera
P-spice
LEDET
ProteCCT
Design & numerical modelling
Material data
Input files (models)
Input files(as built)
Notebooks &
Snapshots
DAQ & analysis software
Carpenter (Test follow-up and visualization)
FFMM
(Magnetic measuremts)
Offline
Post-processing
Test & magnetic measurements
Raw data
Protocols
Validation
Avatars
FIDEL
Asset management, E-Traveler, Databases, Version control (Gitlab)
Model-based systems engineering
Product cycle engineering
PROEJCT AND TEST ENGINEERS
DESIGNERS AND CODE SUPERUSERS
SOFTWARE DEVELOPERS

## Slide 19: Simulation Framework Interface
Simulation
software
Software
application
Expert
user
Developer
Designer
F1
F2
F3
Simulation
software
Software
application
Expert
user
Designer
F1
F2
F3
Simulation
software
Software
application
Expert
user
Developer
Designer
F1
F2
F3
Roxie
Ansys
Opera
Comsol
Steam
Glue Logic (Interface Software)
CHART MagNum
Oracle
Infor
EDMS
Gitlab
NXCALS
Cable
data
BH
data
Design
files
Mag.
measure
Quench
data
Data manager
Data manager
Data manager
Data
manager
CERN services
Sustainability
Accessibility
Ownership
Ownership
Releases
Releases

## Slide 20: Ecosystem Extension
Opening up Design Software

## Slide 21: ROXIE Python API
Structured Access To Roxie data files
  Modify blocks, flags, plots, etc
  Combine files
Structured Output
  XML output of run information, results and plots
  Associated parser for data access
Interface to execute Roxie from code
  On local machine
  Via Docker

## Slide 22: CCT module (python API)
Script based modelling of CCT magnets.
Features:
  Straight and curved magnets
  Accurate computation of curvature parameters by automatic differentiation  basis for strip theory (HTS)
  Field quality optimization based on analytic field solutions in straight and curved domains
  Tapered magnets  Stress accumulation
  Faded pitch  peak field reduction
  Multiprocessing
  Interfaces:
    paraview (vtk)
    gmsh (msh)
    Opera3D (cond)
    Catia (step)
Figure 1: Conductor peak fields in curved CCT magnets. Left: constant pitch. Right: Pitch faded in the magnet ends.
Figure 2: Winding frames (a) the Darboux frame, (b) the Frenet Frame (c) a ruled surface developed from the Darboux vector (HTS)

## Slide 23: Iron Meshing
Internal Roxie Meshing extended
  Curved extrusion
Load Arbitrary 3D mesh
  Produce 3D Mesh in Hypermesh
  Translate into Roxie mesh file format (Python script)
  Run Roxie as usual

## Slide 24: Eddy current solver
Biot-Savart (coil)
Source file
.src
edytrans
Parameters
Initialization file
.ini
Geometry (iron)
Mesh file
.hmo
Python script
Edyson files
.cor
.ele
.inp
.bdr
edy_son
Result files
.dyn
.lop
.out
Evaluation locations
Eval loc file
.loc
processing
Python
Features:
Eddy current computation in yoke and endplates (2D and 3D)
Skin effect in conductors in 2D
Skin effect in pancake coils in 3D
Post processing
Visualization
  Python (2D)
  Vtk (3D)

## Slide 25: Linking everything together - pyMBSE
So far: Small modules, packages and projects on top of ROXIE
  R&D of features and extensions
  Missing Concept of Integration
 pyMBSE
  Started in PSI for the CHART/MagNum project
  Introduce the concept of models, interfaces and model based system engineering to magnet design
  Define Magnet Models, dependencies, inputs, outputs, Dependency graph
  Link with Measurements
  Integrated Environment
    Software
    Tools
    Packages

## Slide 26: Linking everything together
Use MBSE concept, but extend Interface
  Load from Databases (e.g Measurement data)
  Load from other Repositories
  Load from other Groups
Define a commonly understood format for data exchange
  Interface to Query Available data for an object
  Documented and curated types of data
    What is included, how it is interpreted
    Version, status, terms of use
  Still in Idea phase
User
Requester
Owner
Provider