## Slide 1: µTCA for physicists? A project of PH-ESE group to evaluate platforms for uTCA based systems at CERN and in the HEP community M. Joos, CERN on behalf of PH/ESE group
Background
  Raising interest and first projects in xTCA (and especially µTCA) in the HEP community
  CERN has followed this new technology as an observer for the last 2 years
  µTCA is perceived to be less complex than ATCA (but many of the concepts are the same)
Motivation
  As the xTCA standards offer many optional features interoperability is an issue
  PH-ESE group recently has started to develop its first AMC (the GLIB card)
    Some µTCA equipment has been purchased for the GLIB project and “first lessons” have been learned which may be relevant for other µTCA projects
  Other xTCA projects are currently under development in ATLAS, CMS and LHCb

## Slide 2: µTCA and MTCA.4
µTCA
Standardized in 2006
Many optional features
Rapidly growing base of suppliers and products
MTCA.4
Reduced set of features (e.g. less communication protocols)
Additional rear transition modules (RTMs)
Standard not yet ratified
First commercial products available
Interoperability MTCA.4 <-> µTCA
Most components (e.g. MCH) should work in both environments
Some areas of potential incompatibility. E.g.:
  Clock distribution
  RTMs
  Backplane topology
  MMC F/W

## Slide 3: Project scope
Phase A:
  Carry out technical evaluations of systems built to both the basic uTCA standard and the MTCA.4 sub-standard. System features that will be covered by the evaluation include:
    Mechanics
    Power supplies
    Cooling
    Backplane properties
    MCH control
    Redundancy
    Scalability to large systems
  Assess the respective advantages and disadvantages of the two alternatives
  Objectives:
    Understand and discuss with the community the issues related to this new technology. The discussion forum will be this Interest Group on xTCA systems
    Design (at least) two AMC boards as tools for the evaluation phase:
      An AMC load board with RTM
      An evaluation AMC for the MMC designed by J.P. Cachemiche (Marseille).

## Slide 4: Project scope - 2
Phase B:
  Carry out informal market surveys and user surveys
Phase C:
  Eventually the support of a selected set of components of uTCA systems, if consensus is reached, could become part of the PH-ESE service activities.
The results of all phases will be available to the community
Additional information (e.g. list of items purchased so far)
  https://twiki.cern.ch/twiki/bin/view/XTCA/PHESExTCAEvaluationProject