## Slide 1: xTCA projects (HW and SW) related to ATLAS LAr
xTCA interest group - CERN
07/03/2011
Nicolas Letendre – Laurent Fournier - LAPP

## Slide 2: ATLAS LAr Context
Analog Pipeline (SCA)
ADC 5MHz 16x12-bits
Σ
Calibration
FRONT END
ELECTRONIC
FEB
128 cells/FEB
L1 Trigger
100kHz max
BACK END ELECTRONIC
ROD
ROS
Optical Link
1.6 Gbit/s
800 Optical
Links
ADC 40MHz 128x18-bits
Mux / Serializer
Calibration
FRONT END
ELECTRONIC
FEB
128 cells/FEB
L1 Trigger
BACK END ELECTRONIC
ROD
ROS
Optical Link
100 Gbit/s
?? Optical
Links
> 100kHz
x1600
x1600
x192
8 ROD/FEB
14 ROD/FEB ?
1
12@10Gbits ??
Upgrade
Today

## Slide 3: BNL & Univ. of Arizona contribution
BNL
  Readout Driver Board in ATCA plateform
    Receive 12x6.25Gbps parallel optical link
    Process data in a Xilinx Virtex 5 FXT FPGA
  Design of a Readout Driver Processing Unit in AMC plateform
    Receive four 12x10Gbps parallel optical links (from Avago receiver)
    Process data in a Xilinx FPGA
University of Arizona
  Readout Driver Injector in ATCA plateform
    Transmit data through 12x6.25Gbps parallel optical link
    Based on a Altera Stratix IIGx FPGA
  Developpement of an AMC PU Injector
    Transmit data through four 12x6.5Gbps parallel optical link (from ReflexPhotonics)
    Based on Altera FPGA

## Slide 4: LAPP contribution
ROD Evaluator
  ATCA Board size
  High speed and high density links to read data from FEB
  High processing power
ATCA Test Board
  ATCA Board size
  Validate ATCA IPM Controller with the ATCA Controller Mezzanine
  Validate ATCA Board management with the ATCA Controller Mezzanine
  Validate ROD Evaluator parts (Power Supplies, DDR3 interface, DSP computing in FPGA)
ATCA Controller Mezzanine
  FMC (FPGA Mezzanine Card) format
  ATCA IPM Controller
  User defined ATCA Board management (board configuration etc..)

## Slide 5: ROD Evaluator
- Links to ATCA backplane (to send data to a ROS? )
- ATCA Controller Mezzanine to configure and manage the board
Rx 12
Tx 12
Rx 12
Tx 12
Rx 12
Tx 12
Rx 12
Tx 12
Flash
CPLD
DDR3
PS
JTAG
Ethernet
ATCA Controller Mezzanine
(IPMI & Config)
IPMB : from Shelf manager
Fabric channels
L1 Sum
12
12
12
12
12
12
12
12
4
2
4
2
Energy
L1 Sum
Energy
4
8
I2C,SPI : to CPLDs
CPLD :
=>Boot FLASH-FPGA
=>T°, power supply FPGA monitoring
FPGA 1
ALTERA STRATIX-IV
48 transceivers
@8.5Gbps
2 FEBs
Flash
CPLD
DDR3
PS
Flash
CPLD
DDR3
PS
FPGA 1 Config
FPGA 2 Config
FPGA1 Config
FPGA2 Config
Update
channels
FPGA 3 Config
FPGA3 Config
FPGA communication :
=> High speed serial links
FPGA 2
ALTERA STRATIX-IV
48 transceivers @8.5Gbps
2 FEBs
FPGA 3
ALTERA STRATIX-IV
48 transceivers @8.5Gbps
12x10Gbps Optic Fibers:
To ATCA backplane:
=> High speed serial links
Power supplies
FPGA BLOCK
J2
J1
ATCA Board
Base Interface
- 48 optical Rx links @8.5Gbit/s
- 48 optical RTx links @8.5Gbit/s
- High DSP computation BW for Energies and L1 Trigger computation

## Slide 6: ATCA Test Board
ATCA Test board
Insertion Switch
Power
Supplies
Zone 1
Zone 2
Ethernet
Sensors
FPGA ARRIA IIGx
CPLD
Flash
DDR3
POL
Supplies
ROD demonstrator tests
  Check Board configuration with the ATCA Controller Mezzanine (Firmware upgrade, Configuration upload etc..)
  Test ATCA compliant power supplies
  Check FPGA Design (communications with DDR3, Flash, configuration with Flash)
ATCA Controller Mezzanine tests
  IO connections (JTAG boundary scan tests)
  IPMI management with the Shelf manager
  Ethernet communication through ATCA Base Interface
ATCA Controller Mezzanine
(IPMC & Config)
IPMBus
Ethernet
ATCA blue led
ATCA led 1 & 2
Update Channel
Base
Interface

## Slide 7
Emerson ATC250
DC-DC converter
ATCA Controller Mezzanine
CPLD
Flash
DDR3
J1
Power &
IPMBus
J2
Fabric Interface
Base Interface
J2 Update Channel
PCB already ordered
The board will be available end of March
ArriaIIGx

## Slide 8: ATCA Controller Mezzanine
IPM Controller
  Communication with Shelf manager through IPMBus A & B
  Hot Swap, Power management etc..
ATCA board management
  Communication via Ethernet (front panel or ATCA Base Interface)
  User functions
    Firmware Upgrade
    ATCA board monitoring & configuration
    Users stuffs….
FMC (FPGA Mezzanine Card) compliant
  up to 160 customizable links( including 74 differential links)
  Low cost
Features:
  ARM cortex M3 processor
  Xilinx Spartan 6 for highly configurable user IO
  Ethernet / USB / JTAG interfaces
69mm
76.5mm
Ethernet
FPGA Spartan 6
µC LM3S9B92
bus
FMC
Mezzanine
Power Supplies
connector
EEPROM
IO
USB
JTAG
JTAG
JTAG
I2C IPMBus
A&B
µC
FPGA
IO
=> We will receive the board this week

## Slide 9: Tests with commercial board
Hardware setup (Adlink 6900 + Vadatech AM210): OS: Scientific Linux CERN SLC release 5.4 (Boron) 64bits KERNEL: 2.6.18-194.3.1 CPU: Intel Xeon L5408 (Quad Core) NETWORK BENCHMARKING TOOL: netperf version 2.4.5
Communication 10GbE between two blades
  Front (i.e. via AMC) : done
    TCP=5.4 Gb/s (message 1 GB)
    UDP=5.6 Gb/s (message 64 KB)
  Zone 3 (RTM) : to be done...
  Zone 2 (fabric interface): done
    TCP=8 Gb/s (message 1GB)
    UDP=6.8 Gb/s (message 64 KB)
Lossless data compression algorithms: to be done

## Slide 10: ATCA Controller Mezzanine Software
Specification compliant
  PICMG 3.0 R3.0 – AdvancedTCA base specification
  IPMI v1.5 and relevant subset of IPMI v2.0
control of the board :
  program the FPGAs
  monitor of the working conditions
  remotely driven

## Slide 11
IP stack
library
IPM Controller
JTAG Controller
board configuration and monitoring
hardware library
IPMC
module
LM3S9B92 (texas Instruments)
+ FPGA (Xilinx)
programmer (Texas Instruments)
debugger (gdb) + OpenOCD
ARM cross compiler
Development tools
web interface
User environment
client interface
file server
(boot and board control)
JTag/USB
I2C (IPMI protocol)
Ethernet
ATCA Controller Mezzanine Software
JTAG module

## Slide 12: ATCA Controller Mezzanine Software
Development tools (operational)
  OS : Linux
  Compiler GNU GCC for ARM Cortex-M3
  Specific drivers (TI Luminary LM3S9B92)
  Debugger GNU GDB + OpenOCD
IPM (Intelligent Platform Management) Controller software
  Implementation of IPMI 2.0 specification
    Library ported and hardware dependent interface written and compiled
    Test foreseen as soon as we have the hardware

## Slide 13: ATCA Controller Mezzanine Software
JTAG control
  allows for initial programming of the FPGAs on main board
  xsvf interpreter tested in simulation
  JTAG connector on front of the board allows for control of the whole JTAG chain or for microcontroller debugging
  the JTAG chain can be controlled either by the microcontroller or by an external device
Board control and monitoring (via Ethernet interface) (in development)
  FPGA firmware upgrade
  Board configuration (e.g. coefficient for physics algorithms)
  Board monitoring (temperature, voltage …)