## Slide 2: UNICOS-CPC Engineering workflow

## Slide 3: UNICOS-CPC
UNICOS Continuous Process Control (UNICOS-CPC) is a package of UNICOS to create PLC based process control applications.
Support for Siemens and Schneider PLCs only.
UNICOS
JCOP Framework
WinCC OA
UCPC package
PLCs CPC
Cooling and Ventilation
Process Control applications
Collimators Interlocks
Gas
Cryogenics

## Slide 4: UNICOS-CPC provides
Libraries at the control and supervision layers
Well defined standard device objects that model most of the devices used in a controls system
A high performance PLC-SCADA communication mechanism (TSPP)
A formalised way to:
  Model control units of a process (based on ISA-88 and IEC 61512)
  Create system specifications
  Develop specific process logic
  Generate process control applications
  Operate a plant

## Slide 5: UNICOS-CPC technology
Supervision Layer: WinCC OA SCADA
Control Layer
    Siemens S7-300, S7-400, S7-1500.
    Schneider Premium, Quantum, M580, M340.
Local operation
    Simatic HMI (WinCC flexible, TIA portal)
    Schneider Magelis
Industrial communications: Profibus, Profinet, Ethernet/IP, Modbus TCP, OPC UA…

## Slide 6: UNICOS-CPC engineering workflow
Process
Modelling
Specification
Specs
Logic templates
Deployment
Generation
(UAB)
P&ID
Process decomposition
Functional Units
Functional Analysis:
System requirements
Instrumentation
Electrical diagrams
UNICOS-CPC specs
Logic Templates
Expert templates (grafcets)
PLC Instances
PLC logic
HMI tags
WinCC OA object instances
Comm resources
SCADA set-up (synoptics)
UAB CPC wizard

## Slide 7: Generation with UAB
CPC
Spec file
User logic Files
HMI generator
PLC: Instance and Logic Gennerator
SCADA generator
CPC Wizard
UAB
Device Instantiation Templates
Process Logic
Templates
Baselines
SCADA
Touch Panel
PLC
Device Types
Analog
Alarm
PID
PLC sources:
Object instances
User logic
Comm
HMI configuration file
WinCC OA configuration file (Import file)
Reverse engineering

## Slide 8: UAB CPC plugins
Siemens S7-300/400:
  S7 Instance Generator, S7 Logic Generator, S7 Project Generator
Siemens S7-1500:
  TIA Instance Generator, TIA Logic Generator, TIA Project Generator
Schneider:
  Unity Instance Generator, Unity Logic Generator, Unity Project Generator
SCADA: WinCC OA Generator
HMI: Touch Panel Generator
General Purpose: Expert User Generator

## Slide 9: UAB CPC wizard

## Slide 10: UAB CPC wizard

## Slide 11: UAB CPC wizard

## Slide 12: UAB CPC wizard

## Slide 13: UAB CPC wizard

## Slide 14: UAB CPC wizard

## Slide 15: UAB CPC wizard