## Slide 1: FASER test beam
FASER is a new experiment at the LHC, targeting TeV energy collider neutrinos
Emulsion/tungsten-based detector, we want to test
  EM shower calibration
  Momentum calibration
FASER
Emulsion/tungsten neutrino target
candidate from 2022 run

## Slide 2: Beam request
50, 100, 200, 400 GeV charged particles (muon or hadrons)
  10^3-104 particles per spill
  Large beam size
50, 100, 200 GeV electrons (electron-rich beam)
  Low intensity, ~10 particles per spill
  Large beam size

## Slide 3: Setup (for NA65, will be shared)
Beam monitor
Target mover
Scintillation counter
Emulsion detector
Movable table
NA65 target mover
~200 kg
Vacuum pipe
XDWC
Counter
Detector
XWDC
Target mover
Emul-sion
2021 NA65 setup
Requirements for infrastructure is the same as NA65

## Slide 4: backup

## Slide 5: Module for momentum measurement test
Mom reconstruction by multiple Coulomb scattering
Emulsion / tungsten x 100 layers x 1 module
  Film size 12.5 cm x 10 cm
Different beams in different angular space
50-400 GeV
Mu+ or Hadron+
50 GeV
100 GeV
200 GeV
400 GeV
50 mrad

## Slide 6: Module for electromagnetic shower
Emulsion / tungsten x 60 layers x 3 modules
  Size 12.5 cm x 10 cm
Different beam in modules
  50, 100, 200 GeV
50-200 GeV
17

## Slide 7: Particle momentum measurement by multiple Coulomb scattering (MCS)
Sub-micron precision alignment thanks to muons.
  Our experience = 0.4 (in DsTau)
This allow to measure particle momenta by the MCS, even above 1 TeV.
Performance with position resolution of 0.4 , in 100 tungsten plates (MC)
Measurable energy vs position resolution
Backup slides for LHCC 2019 Sep

## Slide 8: Example of MCS and fit
position resolution = 0.4
Trajectory in X
smeared with position resolution
Trajectory in Y
RMS of scattering as a function of cell length
Fitting result
track in 100 layers of tungsten x 1 mm
Backup slides for LHCC 2019 Sep