## Slide 1: The NA65/DsTau experiment at the CERN SPS
Study of ντ production for future tau neutrino experiments.
  Measurement of double differential production cross section
  Reduce uncertainty of flux from >50% to 10%  Fundamental input for future ντ experiment: SHiP, and indirectly FASER
Forward charm physics, charm/gluon PDF
Principle of the experiment
  Detection of “double-kink + charm decay” topology within 10 mm.
  protons, proton interactions in target, charm pairs, detected events.
D+
Ds
τ
ντ
400 GeV
proton
ντ
X
X'
~5 mm
Small kink at Ds → τ
DONuT
flux estimation
Re-evaluation of cross-section (2020)
Precise cross-section.
New physics searches in neutrino scattering
oscillation experiments
Astrophysical observations
-2008
2027?-
2022-
Ds
Tau
flux constraint through the study of charm production

## Slide 2: Beam requirement
Beam: 400 GeV proton
Beam size/shape: 2 cm x 2 cm.
  Gaussian-like shape is better than square-like profile.
  A sigma of distribution ~10 mm (not RMS)
  2022 beam shape at H4 is good, 2021 H2 was better
  No beam divergence = No Q-magnet working nearer than 100 m
Beam intensity: a few x 105/spill
Spill time structure: flatter is better

## Slide 3: Requirements for infrastructure
Movable table (Nikhef table or equivalent)
Beam profile monitor
XDWC in front of NA65 detector (longer cable is needed)
Vacuum pipe to transport proton beam
Storage of the target mover (1m x 2 m + some carton boxes)
Movable table
DsTau target mover
~200 kg
Vacuum pipe
XDWC
Counter
Detector
XWDC
Target mover
Emul-sion
2021 setup