## Slide 1
Combining Cherenkov Angle and Timing Measurements in One Detector
E. Nappi
on behalf of INFN-BARI/CERN/UNAM teams

## Slide 2
TOF DETECTORS BASED ON CHERENKOV LIGHT
Y.Enari NIM A547 (2005) 490
K.Inami NIM A560 (2006) 303
Why Cherenkov light for TOF devices?
  Produced promptly
  Almost no time jitter (directionality)
  Single photoelectron statistics
Conventional TOF with scintillators
  Long decay time O(ns) in photon emission
  Time jitter due to photon paths
RD51 Picosec Micromegas Collaboration
Time resolution of a 100-channel
prototype (10x10 cm2)
M. Lisowska et al.
NIM A1046 (2023) 167687

## Slide 3
Proximity focusing RICH detector with TOF capabilities
P. Krizan et al.,
Nuclear Physics B (Proc. Suppl.) 172 (2007) 227–230
Belle II Technical Design Report
2 GeV/c pions and protons
Vacuum Photon Detectors (MCPs, LAPPDs)
Main limitation:
Sensitivity to B (no gain at all for a barrel geometry
PID system embedded in a solenoidal magnetic field)
Gaseous Photon detectors (i.e. PICOSEC MM)
Main Limitation:
Unable to detect visible photons
(cannot be used aerogel as Cherenkov radiator)
Both gaseous and vacuum photon detectors
are bulky (large X0)
SiPMs

## Slide 4
TOF Measurements by SiPMs
Material | Refractive Index at 400 nm |  | [MeV/] | Max c [degree] | Np.e. at saturat. [mm-1]
NaF | 1.33 | 0.75 | 159 | 41.3 | 13
MgF2 | 1.40 | 0.71 | 142 | 44.3 | 14
SiO2 | 1.47 | 0.68 | 129 | 47.9 | 16
Silicone resin | 1.50 | 0.66 | 124 | 48.2 | 16
Epoxy resin | 1.55 | 0.64 | 117 | 49.8 | 17
High-n Corning | 1.84 | 0.54 | 90 | 57.1 | 21
Material | Refractive Index at 400 nm |  |  |  | Np.e. at saturat. [mm-1]
NaF | 1.33 | 0.75 | 159 | 41.3 | 13
MgF2 | 1.40 | 0.71 | 142 | 44.3 | 14
SiO2 | 1.47 | 0.68 | 129 | 47.9 | 16
Silicone resin | 1.50 | 0.66 | 124 | 48.2 | 16
Epoxy resin | 1.55 | 0.64 | 117 | 49.8 | 17
High-n Corning | 1.84 | 0.54 | 90 | 57.1 | 21
Fresnel reflection between
  Window and resin/epoxy
  Resin/epoxy and silicon
  Window and gas
Window chromatic dispersion
SiPM Fill Factor 90%, SPTR=50 ps
Dark count rate ~ 50 kHz/mm2
@ room temperature
SiPMs
Window
Gas
Cluster
Reflection
Reflection
a
Charged track
Resin/Epoxy
Window: 2 mm SiO2
1 GeV/c pion

## Slide 5
Bianca Sabiu, Alice Upgrade Week, 05/2023
FBK NUV-HD-RH SiPM (1x1 mm2, 20 μm SPADs, 72% Fill Factor)
More on TOF Resolution Simulation
Protection Layers:
SR1 – 1 mm silicone resin (n=1.5)
SR15 – 1.5 mm silicone resin (n=1.5)
ER1 – 1 mm epoxy resin (n=1.53)
WR – without protection layer
F. Carnesecchi, et al., Understanding the direct detection of charged particles with SiPMs
https://dx.doi.org/10.1088/1748-0221/17/06/P06007 https://doi.org/10.48550/arXiv.2210.13244
Talk by P. Antonioli tomorrow
Simulation for 5 GeV/c pions

## Slide 6
8 HPK S13552 SiPM arrays for detecting Cherenkov light from aerogel
8x8 HPK S13361 SiPM matrix 3x3 mm2 pixel with a NaF radiatior , 3 mm thick (n = 1.3319 @ 400 nm), for charged particles
Ref. M.N. Mazziotta et al “A light tracker based on scintillating fibers with SiPM readout”, NIMA 1039 (2022) 167040
https://doi.org/10.1016/j.nima.2022.167040
Front-End: Four PETIROC 2A ASICs
2022 Beam Test Campaign @ PS T10

## Slide 7
Measured mean number of clustered SiPMs :
Measured single SiPM time resolution:
Extrapolated mean cluster time resolution:
Test Beam Results on Time Resolution
Planned 2023 beam test:
• R/O Board synchronization
• External tracking detector:
Two X-Y upstream/downstream fiber trackers
Two ALPIDE pixel modules
• Photon yield and timing studies with 1 mm
SiO2 radiator glued on the SiPM matrix

## Slide 8
Barrel RICH: proximity focusing configuration with an aerogel radiator (2 cm, n=1.03),
20 cm expansion gap and SiPM array as photodetector (magnetic field up to 2 T and
strong Rayleigh scattering from aerogel below 300 nm)
Forward RICHs: same configuration, but aerogel with a lower n
Total Photon Sensitive surface ~ 30 m2
The TOF/RICH approach, if successful, would bring a remarkable cost saving
ALICE 3 LOI LAYOUT
Baseline scheme: no TOF

## Slide 9
Yuguo Tao at al. doi: 10.1038/s41598-022-18280-y
SiPM Anti Reflective Coating
R&D TOPICS FOR THE TOF/RICH DETECTOR
Textured Si surface: upright random nano‐micro pyramids made by anisotropic etching
Direct and indirect optical crosstalk is a severe drawback
Secondary photons detected by surrounding SiPMs increase
the rate of accidentals
R&D studies:
• Conventional single-layer antireflection coating (ARC)
• (Multi-layer) ARC: double-layer ARC and triple-layer ARC
• Textured Si surface with upright random nano/micro pyramids
formed by anisotropic etching.
Additional benefits:
• The PDE increase allows operation at lower VOV hence smaller DCR
ALICE 3 RICH Photon Detector hit map

## Slide 10
R&D Project
SiPM-based TOF/RICH detector
Fields of Interest
CMOS SPAD development
Textured anti-reflective coating (increase PDE, operate at lower Vov and decrease DCR)
SiPM Module integration
  System design incorporating cooling/annealing
  Power, clock and control signal distribution
  Local Intelligence
Involvement in DRD4