## Slide 1: ALICE TOF (and AIDAinnova)
Despina Hatzifotiadou
INFN Bologna
On behalf of ALICE-TOF
and AIDAinnova (WP7: Gaseous Detectors; Task 7.2.1. MRPCs for fast timing)
East Area T9/T10 Users Meeting Monday 20 March 2023

## Slide 2: ALICE Time of Flight
resistive
plate
cathode
anode
HV
HV
Readout pads
Multigap Resistive Plate Chamber
It measures the time of flight (from the point of generation to the point of detection) of charged particles with a precision of 60 ps
Time and trajectory length (known from tracking detectors) give the particle velocity
From the tracking detectors we find the trajectory, thus the curvature of the track and therefore the momentum
Momentum and velocity give us the mass, which identifies a particle uniquely
Glass plates :
400 microns thick
Gap width :
250 microns
Gas mixture:
93% C2F4H2(R134a) 7% SF6

## Slide 3: Beam Requirements @ PS (East Hall)
Beam Line: T10 |  |  |  |  | 
Particle type | Polarity | Momentum | Intensity | Beam Size | Target
hadrons | negative | maximum | maximum | focus 2cmx2cm | hadron
The goal
Tests of the performance of few new MRPCs with different configurations in the number and thickness of the gas gaps
(small prototypes of about 20 cmx20 cm and a weight of about 2.5 kg each) with 2 different gas mixtures:
the standard mixture: 93% C2F4H2 (R134a) and 7% SF6 as baseline
ecological gas: R1234ze ( Eco-Freon in a mixture with the SF6)
 in both cases, optimal flow: 5l/h (minimum flow: 2l/h)
Requirement @ T10:
movable table (DESY table) to hold up to 3 chambers to center the beam spot more easily and to scan in different points of the chamber.