## Slide 1: Status of opto R&D at SMU
Jingbo Ye
Dept. of Physics
SMU
For the opto WG workshop at CERN, March 8th, 2011

## Slide 2: Outline
The team and facility at SMU.
Past project and present M&O.
Present R&D projects.
Plan for the near future.
Summary

## Slide 3: The team and facility at SMU
This is a university based opto-electronics lab in the Dept. of Physics at SMU.
Capability: opto-electronics system level design, ASIC design, component evaluation in radiation environment, reliability studies, … .
Equipment: 20 GHz realtime scope, 12.5 Gbps BERT, ProbeStation with RF probes, wire bonder… .
The team: 4 FTEs (1 mostly ASIC, 1 mostly system, 1 ASIC and system, 1 ET supporting), all supported by research grants, meaning … (sigh).

## Slide 4: Past project and present M&O
Coordinator in the team that delivered the optical link system (G-Link based, 1.6 Gbps, 1524 fiber channels) for ATLAS LAr.
Current responsible for the system’s M&O. Participating in the investigations of the VCSEL reliability issue. Proposed a dual-OTx solution for a possible fix to the problem. Decision awaiting for running condition of 2011.
Lessons learned: redundancy is a must for systems that require high reliability but have very limited access for maintenance and repair.
Requires 1 FTE in the past few years for tasks in M&O. Fast turn-around measurements requested in those testing jobs require continuous knowledge and undisrupted test setups.

## Slide 5: Present R&D projects
Five directions:
  The LOC ASIC development for ATLAS LAr readout upgrade.
  The Versatile Link project.
  System level studies for ATLAS LAr readout upgrade.
  Data links inside LAr for LBNE.
  ASIC technology evaluation.

## Slide 6: Present R&D projects
The LOC ASIC development for ATLAS LAr readout upgrade (1 FTE):
  Succeeded in the 5 Gbps LOCs1 serializer and the 5 GHz LCPLL prototyping, see reports in TWEPP 2010 for details.
  Successful proton irradiation on LOCs1 to verify its property in radiation environment. TID, SEU are not of concern with 200 MeV protons.
  No funds for tests with higher LET. Collaboration welcome.
  There are interests in designing a low(er) power 16:1 serializer from 2.5 to 5 Gbps based on the LOCs1 design, but no funds for this work. Collaboration welcome.
  Are designing LOCs2, a 2-lane, shared PLL, serializer array.
  With the current GC process, the speed may reach 8 Gbps.
  Will migrate to the PC process in 2012. Simulation show a 15% speed increase and 50% area reduction.
  Will follow the Peregrine/IBM announcement of 180 nm technology and make use of it whenever possible.
  Need help (collaboration) on packaging with 10 Gbps signals.

## Slide 7: Present R&D projects
The LOCs2 status (1 FTE while we really need 2 FTEs):
PFD
CP
CML 1/2
1/2
1/2
LVDS to CMOS
CMOS 2:1 MUX
CMOS 2:1 MUX
CML 2:1 MUX
CML 2:1 MUX
CML Driver
16 LVDS
16
8
4
2
1
1 CML
10.24 Gbps
LVDS to CMOS
CMOS 2:1 MUX
CMOS 2:1 MUX
CML 2:1 MUX
CML 2:1 MUX
CML Driver
16
16
8
4
2
1
1
Buffer
LC VCO
Buffer
Clk, 640 MHz
5.12 GHz
2.56 GHz
1.28 GHz
640 MHz

## Slide 8: Present R&D projects
The LOCs2 status
  Speed: we aim for a final 10 Gbps with ±10% tuning range. For the GC propose, we aim at 8 Gbps.
  Simulation results on fast components:
CML 2/1
CML 2:1 MUX
CML Driver
Buffer
Above 4.6 GHz, 200 mV swing, post layout and worst case (ss, 85C)
Above 4.3 GHz, schematics with extra trace capacitance, also ss + 85C.
Eye diagram of 7-bit PRBS at 8 Gbps, with inductance peaking (7.4 nH), ss and 85C
Our next step
LC VOC
Successfully prototyped at 5 GHz

## Slide 9: Present R&D projects
The Versatile Project (1 FTE):
  Responsible for system level spec and evaluation procedures.
  Collaborate with Oxford on fiber tests.
  Collaborate with FNAL on link back-end studies.
  By-product: the VBERT, used in proton tests. Have plans to upgrade it to 10 Gbps. It serves as a reference link for the ASIC development.
  Leads to the US-ATLAS/CMS joint proposal in answering DOE’s recent call for generic detector R&D.

## Slide 10: Present R&D projects
System level studies for ATLAS LAr readout upgrade.
  SMU is active in the system level specification for the FEB2.
Data links inside LAr for LBNE (1 FTE).
  SMU is pursuing a program to develop data links (electrical and optical) inside LAr. The immediate application is the LAr20 for LBNE.
  The issue here is mostly system reliability: the hot carrier effect, and the requirement of 15 yrs operation lifetime without access, much more stringent than that in detector front-end for colliders.
ASIC technology evaluation.
  Continuous efforts in ASIC technology evaluations for HEP. Current support: DOE/ADR. Collaborators: Vanderbilt, Duke and Yale.

## Slide 11: Plan for the near future
ASIC development: LOCs2 to LOCsx (x=4 or 6), packaging option studies.
COTS evaluation: on serializers and LDDs.
Versatile Link: continue and benefits for other R&D projects.
Generic Optical Link R&D in US, especially the 10 Gbps optical transmitter in array format. That is, if the proposal is funded.
Specific systems: ATLAS LAr upgrade, LBNE/LAr20.
Follow developments in industry: SerDes embedded FPGA, optical module packaging, ASIC technologies.

## Slide 12: Summary
The optoelectronics group in the Dept. of Physics SMU is responsible for ATLAS/LAr optical link M&O, and is active in many R&D projects, some for collider physics, some for neutrino physics.
There are R&D projects at component (ASIC and COTS) level and at system level, presenting a “full spectrum” for data links.
With a group of 4 technical FTEs, plus faculty and students, this group has reached a critical mass for synergy. We welcome any kind of constructive collaboration. We especially need help in ASIC development and packaging.