## Slide 1: Analysis, simulations and measurements for the operation of accelerator magnets Agnieszka Chmielińska
PE Section Meeting
09.11.2023

## Slide 2: Career history
Oct. 2010 – Feb. 2014
B.Sc. in Applied Physics AGH-UST & TE-VSC Trainee Student
Simulations and tests of the ion pump controller electronic system
Mar. 2014 – Apr. 2016
Aug. 2016 – Dec. 2019
Ph.D. in Physics EPFL & TE-ABT Doctoral Student
Development of a novel beam screen for kicker magnets, involving EM simulations, electric-circuit simulations and RF measurements
Sept. 2020 – Aug. 2023
M.Sc. in Applied Physics AGH-UST & TE-VSC Technical Student
Secondary-electron yield measurements at cryogenic temperatures
Analysis of surface conditioning to better understand the electron-cloud effect
Senior Fellow CERN, TE-MSC
EM simulations of superconducting magnets and design of experiments
Software design and implementation for data-processing in automated workflows
Magnetic field prediction for operation

## Slide 3: Doctoral Student in TE-ABT-PPE (2016-2019)
Optimization of the beam screen for the FCC injection kicker magnets, Ph.D. at EPFL (2019)
Contribution to the upgrade and commissioning of the LHC Injection Kicker Magnet (LHC MKI)
Development of the novel concept of a helical beam screen
  Improved high-voltage performance
  Reduced beam-coupling impedance
Conceptual design
RF measurements (LHC MKI) and signal processing
Prototype validation
Electric-circuit simulations (Cadence PSpice)
EM simulations (CST Studio Suite, Opera-2D)

## Slide 4: Beam screen for the kicker magnets

## Slide 5: Introduction
What do we mean by injection?
A particle beam must be injected into a circular accelerator or accumulator at the right time while:
placing the newly injected particles onto the correct trajectory,
minimizing beam loss.
CERN accelerator complex:
Technological challenges:
fast, high voltage pulse generators,
special types of magnets (kickers and septa).
Machine protection related issues:
high beam energy (up to 2.4 MJ for each LHC injection and twice more for FCC-hh).

## Slide 6: Injection kicker magnet (I)
Single-turn injection:
C-core ferrite:
Ni-Zn ferrite yoke is always used for fast applications (e.g. 8C11, CMD5005)
Kicker magnet is a pulsed dipole magnet with very fast rise and/or fall time (from tens to hundreds of nanoseconds)
It “sees” the circulating beam!

## Slide 7: Injection kicker magnet (II)
Transmission line topology:
Complicated design
Field rise time depends on pulse propagation time through the magnet:
Fast: field rise times
Magnetic flux:
Field rise time:
rise time of the voltage pulse
Field rise time:
Transmission line ferrite-loaded kicker magnet is the best option to achieve fast field rise and fall times with low pulse ripple.

## Slide 8
Example: LHC injection kicker magnet (MKI)
Major problem: beam-induced heating due to the real component of the longitudinal beam-coupling impedance a beam screen is placed in the aperture of each LHC MKI.

## Slide 9
Longitudinal wake function:
Longitudinal beam coupling impedance:
().
source
witness
The wake field generated by the source particle affects the witness particle.
The net force acting on the witness charge:
What happens to the energy lost by the source?
Partially dissipates in the walls or HOM absorbers: Heat load
Partially transferred to the following particles Beam instabilities
.
Beam coupling impedance
Reference system:

## Slide 10
Beam-induced heating
– number of bunches, – bunch intensity, – revolution frequency, – beam spectrum.
Power loss (multipole pass):
25 ns bunch spacing 40 MHz beam harmonics
Beam spectrum
For high-intensity beams, heating of the ferrite yoke can result in: local vacuum degradation loss of the magnetic properties (Curie point exceeded)
Impedance spectrum
Shift the peaks towards higher frequencies!
Consequences:

## Slide 11: Beam screening: Conventional design (I)
LHC MKI post-LS1 beam screen:
General features:
24 (NiCr) straight screen conductors reduced beam coupling impedance
Capacitive coupling to the beam pipe at the upstream end and connection to the beam pipe at the downstream end fast magnetic field rise time
Overlap length determines resonances in the longitudinal impedance spectrum possibility to shift resonant modes to higher frequencies:
Ferrite rings at both ends of the beam screen power loss reduction in the ferrite yoke
More than 15 years of development…
Upstream end

## Slide 12: Beam screening: Conventional design (II)
Magnet voltage and voltage of screen conductor:
Maximum conductor and inter-conductor voltages (for 60 kV PFN voltage):
Induced voltage:
During magnetic field rise and fall, a significant voltage is induced on the screen conductors.
Possibility of HV breakdowns

## Slide 13
Design of a beam screen for FCC-hh
Analysis of the LHC MKI beam screen (not discussed here)
Design of the conventional beam screen for FCC-hh (not discussed here)
Development of a novel helical beam screen for FCC-hh (next slides)

## Slide 14
Design of a kicker magnet module for FCC-hh
Specification of baseline parameters
PSpice model
Analysis of field rise time and field flat-top quality
Injecton energy [TeV]
Angle [mrad]
Pulse duration [µs]
Current [kA]
Voltage [kV]
System impedance [Ω]
System length [m]
Field rise time [µs]
Aperture dimensions [mm]
Magnet fill time [µs]
Good field region (h/v) [mm]
Flat-top tolerance [%]
3.3
0.18
2
2.4
15
6.25
40
0.43
48/48
0.355
8/8
±0.5
Normalized magnetic flux [%]
Baseline parameters:
Analysed kicker waveform:
New PSpice model and CST model
CST model
18 magnets per injection system
14

## Slide 15
Power deposition estimates
15
32 x 32
48 x 48
227.1
353.9
Aperture
dimensions
[mm x mm]
228.1
355.4
P [W/m]
Ideal beam spectrum
P [W/m]
Nominal beam spectrum
/L [W/m]
Freq. [MHz]
Unshielded kicker magnet:
Power loss is at unacceptable level.
LHC MKI limit: 160 W/m.
Induced voltage:
Kicker magnet with the conventional beam screen:
Freq. [GHz]
2.8 MHz, 462
903 MHz, 128
1590 MHz, 94
100
200
300
400
[]
Worst case scenario: 30.2 W/33.4 W/29.3 W
significant reduction in comparison with unshielded kicker (P355 W/m),
lower than for the upgraded LHC MKI8D.

## Slide 16: New concept of a helical beam screen
Induced voltage:
Significantly improved HV performance
the same induced voltage on each conductor
this is one-half of the worst-case voltage induced on a straight conductor.
For an integer number of turns:
Photograph of the alumina tube with 21 screen conductors applied using Ag paint
Each screen conductor has a form of a helix:

## Slide 17: Beam coupling impedance simulations
Beam coupling impedance modelling (CST Studio Suite) to optimize:
  Beam-induced heating
  Power distribution
  Impact on beam stability
Longitudinal impedance optimization
Power deposition distribution
No heating issues are expected for the FCC-hh kicker magnets for nominal beam parameters.

## Slide 18: Characterization of EM properties of ferrites
Novel measurements of EM properties of ferrites as a function of frequency and temperature (short-circuit line method): new input for beam impedance simulations.
Chmielińska, A. et al. "Measurements of electromagnetic properties of ferrites as a function of frequency and temperature", In Journal of Physics: Conference Series, vol. 1067. No. 8, p. 082018. IOP Publishing.
Measured temperature dependence complex permeability for CMD5005.

## Slide 19: Field response of the kicker magnet simulations
Field response modelling (coupling Opera-2D with Cadence PSpice) to achieve required:
  Field rise time
  Field flat-top quality
Central cell inductance vs. frequency (Opera-2D)
Selected baseline: Cu or Ag,
30 µm x 1.3 mm
Impact of a beam screen upon kicker waveform (PSpice)
Proposed beam screen design satisfies the field rise time and the field flat-top quality requirements

## Slide 20: Experimental benchmark
  Coaxial-wire measurements performed on the LHC MKI to validate numerical models (classical and resonant method)
LHC MKI with a helical beam screen
Longitudinal impedance
First demonstrated feasibility of this concept
Chmielińska, A. and Barnes, M. J. "Helical beam screen for the Future Circular Collider for hadrons injection kicker magnets." Physical Review Accelerators and Beams 23.4 (2020): 041002.
Experimental setup

## Slide 21: Measurements of beam coupling impedance
  Coaxial-wire measurements performed on the LHC MKI to validate numerical models (classical and resonant method)
LHC MKI with a helical beam screen
Longitudinal impedance
First demonstrated feasibility of this concept
Chmielińska, A. and Barnes, M. J. "Helical beam screen for the Future Circular Collider for hadrons injection kicker magnets." Physical Review Accelerators and Beams 23.4 (2020): 041002.
Experimental setup
Complete picture of the optimization of the beam screen design.
Consistent results in theoretical, numerical and experimental studies.

## Slide 22: Fellow in TE-MSC-TM (2020-2023)
https://gitlab.cern.ch/te-msc-mm/pymaganalysis
Integration of numerical models with magnetic measurement data to model and characterize the magnetic field of superconducting magnets
Design of experiments (test plan, specification of cycles)
Data-driven updates of numerical models
Magnetic-field prediction for machine operation (FiDeL)
  Semi-empirical model decomposition
Software design and implementation for data-analysis
Operational cycle of MCBC (vdM scans)
Rotating-coil measurements in SM18
Cross-talk simulations in ROXIE
PyMagAnalysis

## Slide 23: Analysis of simulations and measurements to predict the magnetic field for the operation of superconducting magnets

## Slide 24: FiDeL model for machine operation (I)
The Field Description of the LHC (FiDeL) is the magnetic field prediction system that provides a model of the transfer function of magnetic circuits installed in the machine in order to retrieve the current level given the required field:
→ indispensable for LHC operation
  → uses parametric equations to fit magnetic measurements
  → based on physical decomposition of effects that contribute to the total ﬁeld in the aperture of the magnet
  → uses several levels of approximations, starting from a linear dependance on the current and adding correction terms (depending on the magnet type and function).

## Slide 25: FiDeL model for machine operation (II)
2. Magnetization:
1. Geometric:
3. Saturation:
where
  The fitting parameters are implemented in the LHC control system.

## Slide 26: PyMagAnalysis
Plotter
Data input
Analyzer
FiDeL Fit
Multipole inputs:
- ROXIE input,
- Measurement input,
- FiDeL input.
Advanced analysis:
- current vs. time,
- multipole vs. time,
- multipole vs. current,
- linear fit,
- residuals vs. current,
- and many more…
Modelling fit
Presenting results:
- custom labels,
- zoom,
- plot types,
- and many more…
Filtering:
- Time,
- Current,
- Ramp-rate.
Magnetic Measurement DB
ROXIE files
FiDeL reports (EDMS)
https://gitlab.cern.ch/te-msc-mm/pymaganalysis

## Slide 27: Analysis of nonlinear effects during luminosity calibration (I)
MCBC/MCBY magnets are used to provide beam separation during van der Meer (vdM) scans.
MCBY
MCBC
Nonlinearities and lack of repeatability during vdM scans triggered the necessity to review the hysteretic behaviour of MCBC/MCBY magnets.
Operational cycles

## Slide 28: Measurements in SM18
Extensive program of standard and operational test cycles launched to characterize the magnetic field and its reproducibility from scan to scan using the rotating-coil technique.
vdM scans: 1,2,4,5
other scans: 3,6,7

## Slide 29: Analysis of measurements and simulations (I)
Analysis of nonlinear effects due to persistent currents
FiDeL Model & beyond
+ impact on the beam
Update of the ROXIE models
FiDeL model + beyond
Developed numerical model to account for transitions between major magnetization branches

## Slide 30: Benchmark of the proposed model
Comparison of the measured magnetization-branch transitions (markers) and the proposed extended FiDeL model for the MCBC magnet (dashed lines).
Predicted and measured impact of magnetic hysteresis on the transverse displacement
Chmielińska, A., et al. "Magnetization in superconducting corrector magnets and impact on luminosity–calibration scans in the Large Hadron Collider." Eur. Phys. J. Plus (2023) 138: 796.
Courtesy of M. Hostettler

## Slide 31: Magnetic model for the MCBXF (I)
MCBXF
Powering cycles
  Inner coil provides vertical field (main field B1, normal)
  Outer coil provides horizontal field (main field A1, skew).

## Slide 32: Identifying the problem
  The development of FiDeL model is particularly challenging due to angular dependence of saturation (and persistent current magnetization).

## Slide 33
,
,
- inner current
- outer current
where: , – multipole, – fitting parameters.
Original definition:
where is a function of inner and outer current (determined experimentally).
Proposal:
Proposed model (I)

## Slide 34
Proposed model (II)

## Slide 35: Modelling error
New model with angular dependence of saturation
Baseline for HL-LHC
The error is within required specification (±30 units for B1/A1)

## Slide 36: Modelling error
New model with angular dependence of saturation
Baseline for HL-LHC
The error is within required specification (±30 units for B1/A1)
With PyMagAnalysis framework we brought the best available knowledge from simulations and measurements to understand the magnet behavior itself and to provide precise field predictions for operation.

## Slide 37
Thank you for your attention!