RF parameters for the 10 TeV collider
  - Target parameters for the collider: σz = 1.5 mm and σδ=0.1 %
  - The 10 TeV collider is a quasi-isochronous ring
    - Momentum compaction factor ɑp=-2.0e-6 (lattice design)
    - With ɣ=47323, the (first order) slippage factor is η0 = ɑp – 1/ɣ2 ≈ ɑp

---
  - Study made by K. Y. Ng on the RF buckets behavior for a 2+2 TeV muon collider
    - “The Quasi-isochronous Buckets of the Muon Collider”, Report FN-648
    - Effects of high-order momentum compaction/slippage factor are investigated in the paper: bucket distortion with η1, correction of high-order momentum compaction...

---
  - Using the derivation from Ng report, derived possible RF parameters for the 10 TeV collider
  - They are summarized in a short preliminary note: https://www.overleaf.com/read/fjxcgcmmvdqp
Total RF voltage depends on harmonic number and slippage factor

---
  - RF bucket and matched bunch obtained with PyHEADTAIL (Gaussian cut at +- 2 sigma).
  - Inputs:
    - fRF = 1.3GHz
    - VRF = 1.63 GV
    - εz = 0.314 eVs

---
  - RF bucket and matched bunch obtained with PyHEADTAIL (Gaussian cut at +- 2 sigma).
  - Inputs:
    - fRF = 1.0GHz
    - VRF = 2.12 GV
    - εz = 0.314 eVs