## Slide 1
Shielding of FCC CLD fringe field: a few initial thoughts
M. Buzio, M. Pentella TE-MSC

## Slide 2
Fringe field of CLD solenoid at booster beam line
x
x
z
y
Ø50 mm
1.3 m
8.0 m
A few questions:
Definition of Br (modulus of component transverse to booster beam line ?)
Must we cancel out Br on average, or everywhere ? Down to what level ?
Must we shield also Bz ?
Length of booster beam line to shield ?
Qualitative Biot-Savart model
20 m

## Slide 3
Mitigation of fringe field effects – an aide-memoire
Increase size of source magnet iron yoke (very costly ! And probably it is already optimized….)
Passive ferromagnetic shields: see next slides
- massive shield between magnet and beam line - thin shell around beam line
Passive superconducting shields (SuShi-style): complexity, cost …
Active shielding:
- counter solenoids (like in MRI magnets): best results, costly, require full redesign - distributed compensation coils at beam line see next slides
Classic correction with lumped magnetic elements
MNPA25-04 SPS corrector 200 mTm @ 600 A

## Slide 4
Supermendur Co50Fe48Ni1 r  71
(tape 180 USD/kg on Alibaba)
ARMCO pure iron r  57
(sheet 4 CHF/kg in CERN stores)
Choice of ferromagnetic shielding material for B=35 mT, H=28 kA/m
28 kA/m
Extrapolated values (current RT test limit 24 kA/m)

## Slide 5
10 mm of Permendur → attenuation factor ≈ 15
Multi-layer shields (external shells with higher permability) commonly used
Thin, single-layer cylindrical ferromagnetic shield – transverse field attenuation
t
Ø

## Slide 6
A
B
x
z
A
B
x
z
0.5 m ARMCO steel
Some field distortion to be expected end regions (even with iron yoke)
Example 2D calculation: yokeless solenoid B0=1.16 T
Unshielded fringe field along booster beam line (A-B) 2637 mT
0.5 m thick solid ARMCO shield, µr=50
Shielded field 1320 mT, mean attenuation factor ≈ 2.8
Massive iron shield between CDS solenoid and booster beam line
A
B

## Slide 7
Active shielding – compensation coils
Longitudinal component Bz = 20 mT Solenoidal winding →
(e.g. 8 mm2 of air-cooled Cu/longitudinal mm)
Transverse component Br=35 mT:
If local shielding needed in each half beam pipe →
(e.g. 440 mm2 of water-cooled Cu on either side) (Possible alternatives: SC windings, permanent magnets)
+I
+I
-I
-I
+I

## Slide 8
Preliminary conclusions
Shielding a 35 mT stray field is not entirely trivial ….
Passive shielding at source generally much more costly/impactful than shielding at target
Passive shielding with ferromagnetic material around beam pipe: looks feasible, available clearance should be checked
Passive shielding with bulk superconductor (SuShi style): absolutely best performance, at a cost …
Active local compensation also seems feasible
Classic integral lumped correction: probably the simplest solution
Requirements and mechanical constraints to be detailed, for a reasonable choice to be made