## Slide 1: Initial Evaluations of the Cooling Solenoids for the Rectilinear 6D Cooling Channel
Siara Fabbri, Jonathan Pavan

## Slide 2
DISCLAIMER:
These are tentative results based on the geometries and parameters from the US MAP original design [1]
[1] Stratakis, Diktys, and Robert B. Palmer. "Rectilinear six-dimensional ionization cooling channel for a muon collider: A theoretical and numerical study." Physical Review Special Topics-Accelerators and Beams 18.3 (2015): 031003.

## Slide 3: Outline
Goal: simulate and characterize the cooling solenoid magnets based on geometries and initial parameters from the US MAP study.
Overview
Simulation study
  Approach and validation
  COMSOL setup
  Analytic formulas
Results
  Characterization of all coil types
  Case Study: Stage A1
  Characterization of all stages
Summary & Next Steps

## Slide 4: Outline
Goal: simulate and characterize the cooling solenoid magnets based on geometries and initial parameters from the US MAP study.
Overview
Simulation study
  Approach and Validation
  COMSOL Setup
  Analytic formulas
Results
  Characterization of all coil types
  Case Study: Stage A1
  Characterization of all stages
Summary & Next Steps

## Slide 5: Overview: Cooling for a Muon Collider 1/2
Rectilinear 6D cooling scheme to reduce emittance of muon beam by several orders of magnitude
12 unique stages:
  4 cooling stages before bunch recombination (A1-A4)
  8 cooling stages after bunch recombination (B1-B8)
Each stage has a repeating series of a cell type
Figure from MAP study, ref [1]

## Slide 6: Overview: Cooling for a Muon Collider 2/2
High field, very compact solenoids
Each cell has symmetric solenoids of opposite polarity
Dipole component separated out!
Some stats:
Fields on axis: 2 to 14 T
Cell Lengths: 0.8 to 2.7 m
Total length of all Stages: ~ 1 km
Total number of solenoids: 2432
Images taken from ref [1] Stratakis, Diktys and corresponding presentations
Cell in Stage A1
…
Cell in Stage B8

## Slide 7: Overview: Input Parameters and Geometry 1/2
 |  |  | A1 | A2 | A3 | A4
 |  |  | 01 | 01 | 01 | 01
Input Parameters | Bore Radius | mm | 450 | 410 | 270 | 220
 | Magnet Thickness | mm | 100 | 130 | 110 | 140
Geometry | Magnet Length | mm | 210 | 260 | 110 | 90
 | Current Density |  | 63.25 | 126.6 | 165 | 195
 | Cell Length | m | 2 | 1.32 | 1 | 0.8
 |  |  | A1 | A2 | A3 | A4
 |  |  | 01 | 01 | 01 | 01
Input Parameters | Bore Radius | mm | 450 | 410 | 270 | 220
 | Magnet Thickness | mm | 100 | 130 | 110 | 140
Geometry | Magnet Length | mm | 210 | 260 | 110 | 90
 | Current Density |  | 63.25 | 126.6 | 165 | 195
 | Cell Length | m | 2 | 1.32 | 1 | 0.8
Changing Polarity!
66 130 107 88
z [mm]
Notes: A1 has 66 repeating cells, A2 130

## Slide 8: Overview: Input Parameters and Geometry 2/2
 |  |  | B1 | B2 | B3 | B4 |  | B5 |  | B6 |  | B7 |  | B8 |  | 
 |  |  | 01 | 01 | 01 | 01 | 02 | 01 | 02 | 01 | 02 | 01 | 02 | 01 | 02 | 03
Input Parameters | Bore Radius | mm | 770 | 500 | 410 | 175 | 410 | 113 | 217 | 84 | 215 | 50 | 210 | 45 | 140 | 250
 | Magnet Thickness | mm | 150 | 150 | 150 | 200 | 240 | 88 | 165 | 92 | 160 | 74 | 145 | 65 | 80 | 120
Geometry | Magnet Length | mm | 500 | 360 | 370 | 92 | 320 | 100 | 196 | 100 | 177 | 100 | 170 | 120 | 80 | 100
 | Current Density |  | 69.8 | 90 | 123 | 94 | 70.3 | 157 | 168 | 185 | 155.1 | 198 | 155 | 220 | 135 | 153
 | Cell Length | m | 2.75 | 2 | 1.5 | 1.27 |  | 0.806 |  | 0.806 |  | 0.806 |  | 0.806 |  | 
 |  |  | B1 | B2 | B3 | B4 |  | B5 |  | B6 |  | B7 |  | B8 |  | 
 |  |  | 01 | 01 | 01 | 01 | 02 | 01 | 02 | 01 | 02 | 01 | 02 | 01 | 02 | 03
Input Parameters | Bore Radius | mm | 770 | 500 | 410 | 175 | 410 | 113 | 217 | 84 | 215 | 50 | 210 | 45 | 140 | 250
 | Magnet Thickness | mm | 150 | 150 | 150 | 200 | 240 | 88 | 165 | 92 | 160 | 74 | 145 | 65 | 80 | 120
Geometry | Magnet Length | mm | 500 | 360 | 370 | 92 | 320 | 100 | 196 | 100 | 177 | 100 | 170 | 120 | 80 | 100
 | Current Density |  | 69.8 | 90 | 123 | 94 | 70.3 | 157 | 168 | 185 | 155.1 | 198 | 155 | 220 | 135 | 153
 | Cell Length | m | 2.75 | 2 | 1.5 | 1.27 |  | 0.806 |  | 0.806 |  | 0.806 |  | 0.806 |  | 
Large bore!
B4 to B8 tight packed coils at different radii!
Notes: Reminder there are a bunch of cells for each stage
B1 has 20

## Slide 9: Overview: On-Axis Magnetic Field () in A1 to A4

## Slide 10: Overview: On-Axis Magnetic Field () in B1 to B8

## Slide 11: Overview: On-Axis Magnetic Field () in B1 to B8
z [m]

## Slide 12: Outline
Goal: simulate and characterize the cooling solenoid magnets based on geometries and initial parameters from the US MAP study.
Overview
Simulation study
  Approach and Validation
  COMSOL Setup
  Analytic formulas
Results
  Characterization of all coil types
  Case Study: Stage A1
  Characterization of all stages
Summary & Next Steps

## Slide 13: Simulation Study: Our Focus
Magnetic Properties
Mechanical Properties
in coils
and
Stray fields
Stresses
Peak stress
Force densities
Coil parameters
We present results for:
  All coil types
  A detailed case study (A1)
  All stages (primarily a cell in a lattice, with some comparisons to the single cell)

## Slide 14: Simulation Study: Approach
COMSOL
Analytic Formulas
Simulations done in COMSOL but continuously validated against analytical formulas and supplied G4beamline fieldmaps.

## Slide 15: Simulation Study: COMSOL Setup
2D Axisymmetric stationary
Physics modules
  Magnetic
  Solid Mechanics
Very fine mesh (Fig. 1)
  Max element size in air region: 5 mm
  Max element size in coil region: 1 mm
Relative tolerance: < 1e-5
Use of infinite domain for cell and periodic cells:
  Magnetic insulation at boundaries:
Use of periodic boundary condition for cell-cell interface:
  Periodicity on vector potential:
Mechanics interface
  Linear elastic materials
  Lorentz force on coil:
  Rollers on specific faces
  Homogeneous copper: (
Fig. 1
axis

## Slide 16: Simulation Study: Analytic Formulas for a Single Coil
Parameter | Parameter | Equation | References /comments
1 | Self Inductance |  | [1]
2 | Radial Stress | = | [2] and [3]
3 |  | = | [2] and [3]
5 | Peak field at of a single ideal coil |  | [3]
6 | Peak field at inner radius of a single ideal coil |  | [3]
7 | Mutual Inductance |  | [1] Eqs. 1, 29 and 33
Parameter | Parameter | Equation | References /comments
1 |  |  | [1]
2 |  |  | [2] and [3]
3 |  |  | [2] and [3]
5 |  |  | [3]
6 | Peak field at inner radius of a single ideal coil |  | [3]
7 | Mutual Inductance |  | [1] Eqs. 1, 29 and 33
[1] Rosa, Edward Bennett, and Frederick Warren Grover. Formulas and tables for the calculation of mutual and self-inductance. No. 169. US Government Printing Office, 1948.
[2] Wilson, Martin N. "Superconducting magnets." (1983).
[3] Iwasa, Yukikazu. Case studies in superconducting magnets: design and operational issues. Springer science & business media, 2009.

## Slide 17: Simulation Study: Analytic Formulas Coil Calculator
Calculates basics parameters for a given single coil geometry, current density, and tape size.

## Slide 18: Simulation Study: Geometry and Definitions
Cell B8
Stresses
Hoop:
Radial:
Longitudinal:
Repeating cells…

## Slide 19: Simulation Study: Example of Evaluation Locations of Magnetic Fields
Field on axis
Field on conductors
Field radially in Coil 1 midplane
Field radially in Coil 2 midplane

## Slide 20: Simulation Study: Mechanics Calculations
A single coil is split exploiting the symmetry of the system. In the middle of the coil a roller boundary (shown in purple) is placed.
1. Single Coil
2. Single Cell / Periodic Lattice
The stresses are evaluated on just 2 of the 4 coils in the shown cell, exploiting symmetry. Rollers are placed such that they oppose the net axial force on a coil.

## Slide 21: Outline
Goal: simulate and characterize the cooling solenoid magnets based on geometries and initial parameters from the US MAP study.
Overview
Simulation study
  Approach and Validation
  COMSOL Setup
  Analytic formulas
Results
  Characterization of all coil types
  Case Study: Stage A1
  Characterization of all stages
Summary & Next Steps

## Slide 22: Results Part 1: Characterization of all Coil Types 1/4 Coil Properties
18 unique coil types
2 to 6 coils per cell
Inner bore diameter from 90 mm to 1540 mm
Lengths from 80 mm to 210 mm
Current densities from 63 to 220
Notes: Explain here the meaning of coil name notation

## Slide 23: Results Part 1: Characterization of all Coil Types 2/4 Magnetic Properties

## Slide 24: Results Part 1: Characterization of all Coil Types 3/4 Mechanical Properties
(-) Compression
(-) Compression
(+) Tension

## Slide 25: Results Part 1: Characterization of all Coil Types 4/4 Stray Fields
1 mT
100 mT
200 mT
Example
*Turbopumps can operate at 5 to 10 mT

## Slide 26: Outline
Goal: simulate and characterize the cooling solenoid magnets based on geometries and initial parameters from the US MAP study.
Overview
Simulation Study
  Approach and Validation
  COMSOL Setup
  Analytic formulas
Results
  Characterization of all coil types
  Case Study: Stage A1
  Characterization of all stages
Summary & Next Steps

## Slide 27: Results Part 2: Case Study - Stage A1
1. Single Cell
2. Periodic Lattice

## Slide 28: Results Part 2: Case Study - Stage A1

## Slide 29: Results Part 2: Case Study - Stage A1

## Slide 30: Results Part 2: Case Study - Stage A1
1. Single Cell
2. Periodic Lattice
Coil 2 | [MN]
 | -3.80
Coil 2 | [MN]
 | -3.80
Coil 1 | [MN]
 | 3.80
Coil 1 | [MN]
 | 3.80
Coil 2 | [MN]
 | -4.23
Coil 2 | [MN]
 | -4.23
Coil 1 | [MN]
 | 2.91
Coil 1 | [MN]
 | 2.91

## Slide 31: Results Part 2: Case Study - Stage A1
axis
1. Single Cell
2. Periodic Lattice
axis

## Slide 32: Results Part 2: Case Study - Stage A1
1. Single Cell
2. Periodic Lattice
axis
axis

## Slide 33: Results Part 2: Case Study - Stage A1
1. Single Cell
2. Periodic Lattice
axis
axis

## Slide 34: Results Part 2: Comparison to B7

## Slide 35: Outline
Goal: simulate and characterize the cooling solenoid magnets based on geometries and initial parameters from the US MAP study.
Overview
Simulation study
  Approach and Validation
  COMSOL Setup
  Analytic formulas
Results
  Characterization of all coil types
  Case Study: Stage A1
  Characterization of all stages
Summary & Next Steps

## Slide 36: Results Part 3: Characterization of all Stages, 1/4 Magnetic Properties – Cells and Lattices
For comparison purposes an LHC dipole stores ~7 MJ
Above 17 T (B5 to B8), highest performance required & difficult for

## Slide 37: Results Part 3: Characterization of all Stages, 2/4 Mechanical Calculations in Lattices
Maximum and minimum values of hoop stress
Coils with >150MPa will probably require reinforcement
Multi-radius-coil cells (B4-1, B5-1, B6-1, B7-1, B8-1, B8-2): the hoop stress decreases monotonically radially
For all other coils (A1 to B3, B4-2, B5-2, B6-2, B7-2, B8-3): there is a local minimum in hoop stress

## Slide 38: Results Part 3: Characterization of all Stages, 2/4 Mechanical Calculations in Lattices
Maximum and minimum values of radial stress
Multi-radius-coil cells (B4-1, B5-1, B6-1, B7-1, B8-1, B8-2): tensile saddle-like profile on inner coil. To go towards a compressive stress profile these coils would need to be wound in independent layers!
For all other coils (A1 to B3, B4-2, B5-2, B6-2, B7-2, B8-3): compressive ‘parabolic-like’ profile, with a minimum stress in the center

## Slide 39: Results Part 3: Characterization of all Stages, 2/4 Mechanical Calculations in Lattices – Longitudinal Stress
Maximum and minimum values of longitudinal stress
As expected, the stresses are all compressive based on the roller positioning

## Slide 40: Results Part 3: Characterization of all Stages, 2/4 Mechanical Calculations in Lattices - Forces
A support structure for a 37 MN axial force (3700 tons) will be a design challenge

## Slide 41: Results Part 3: Characterization of all Stages 4/4 Stray Fields
200 mT
100 mT
1 mT
*Turbopumps can operate at 5 to 10 mT
Cell
Lattice

## Slide 42: Outline
Goal: simulate and characterize the cooling solenoid magnets based on geometries and initial parameters from the US MAP study.
Overview
Simulation study
  Approach and Validation
  COMSOL Setup
  Analytic formulas
Results
  Characterization of all coil types
  Case Study: Stage A1
  Characterization of all stages
Summary & Next Steps

## Slide 43: Summary of Initial Evaluations
Some key notes:
  Potentially large self inductance and large stored magnetic energy
  Hoop stresses > 150 MPa
  Tensile radial stresses
  Longitudinal forces () on coils up to 37 MN
  Large stray fields
What this study did not include:
  A more complete mechanical structure
  Matching sections between stages
  Deeper engineering considerations
      Iron
      Realistic space requirements (e.g. B8 is super tight)
      …
  Dipole magnets
This study has presented a first look at the cooling stages and their solenoids based on input parameters from the US MAP study. From these results, it is obvious that the magnet parameters will need to be optimised from an energy/cost and engineering perspective
Questions going forward / some next steps:
  Beam dynamics vs. field quality and magnet alignment (as the magnet configurations are iterated on)
  Options to change towards optimized magnet configurations: higher current density (practical limits), number of magnets, magnet size (radius), etc.

## Slide 44: Understanding the Magnetic Field Requirements
Present physics approach focuses on fields along the axis – a sinusoidal wave with defined harmonics. Beam physicists care about just the first ‘few’ harmonics.
How do we define field quality based on the on-axis field?
How do the beam dynamics depend on the ratios of the first few harmonics?
How accurately can we achieve a certain field profile?
What happens to the field off-axis, especially when introducing errors?

## Slide 45: Study on a Single Cell Field
Approach: use a numerical simulation code based on semi-analytic equations for approximating the field inside of a solenoid (validated against COMSOL).
Goals
  Establish different solenoid geometries: evaluate the change in the harmonics on and off axis for changes in solenoid geometries.
  Error analysis: evaluate the change in the field for introduced ‘errors’ to the solenoid geometries/setup.

## Slide 46: Cell B1 – Our Initial Focus for this Study
  on axis: 3.7 T
  at conductor: 7.5 T
Inductance (REBCO 12x0.11 mm) > 6000 H
Stored Magnetic Energy per Coil = 27.2 MJ
Input Parameters | Bore Radius | mm | 770
 | Magnet Thickness | mm | 150
Geometry | Magnet Length | mm | 500
 | Current Density |  | 69.8
 | Cell Length | m | 2.75
Input Parameters | Bore Radius | mm | 770
 | Magnet Thickness | mm | 150
Geometry | Magnet Length | mm | 500
 | Current Density |  | 69.8
 | Cell Length | m | 2.75

## Slide 47: Field and Error Analysis of Cell B1 (ongoing..)
Error Analysis
Introduce change
Small error
New geometry (Ex. different inner bore radius)
Harmonic Analysis
FFT
Inner Bore Radius Variation
Second Harmonic Amplitude Ratio

## Slide 48
Thank you for listening!
Questions?

## Slide 49
Additional Slides

## Slide 50: Results Part 1: Characterization of all Coil Types 1/4 Tape Properties
18 unique coil types
2 to 6 coils per cell
Inner bore diameter from 90 mm to 1540 mm
Lengths from 80 mm to 210 mm
Current densities from 63 to 220
Assuming ReBCO 12 mm mm!

## Slide 51: Results Part 1: Characterization of all Coil Types 2/4 Magnetic Properties
Assuming ReBCO 12 mm mm!

## Slide 52: Results Part 2: Case Study - Stage A1

## Slide 53: Results Part 2: Case Study - Stage A1