## Slide 1
Optical readout Micromegas for neutron and beta imaging
11th Symposium on Large TPCs for low-energy rare event detection
Antoine Cools - 13/12/2023
E. Ferrer-Ribas, T. Papaevangelou, E. C. Pollacco, A. Corsi, K. Aivazelis
(Université Paris-Saclay, CEA, IRFU)
F.M. Brunbauer, L. Ropelewski, E. Oliveri (CERN)
F. Beau, L. Devel, C. Malgorn (Université Paris-Saclay, CEA, Institut Joliot)
F.J. Iguaz-Gutierrez (Soleil Synchrotron)
I. Katsioulas, O. Sidiropoulou (ESS, Lund)
A. Sari (Université Paris-Saclay, CEA, List)
1

## Slide 2
2
Micromegas characterization
    Description
    X-ray characterization and R&D
    Beta imaging
    Setup
    Imaging and activity counting
Neutron imaging
Setup
    Single event study
    Imaging
Conclusion and perspectives

## Slide 3: Optical readout micromegas detector
3
Use of camera (high granularity, large number of pixels, use of lens for large field of view)
Easy handling of the data (light intensity matrix)
Real-time imaging thanks to very low data processing and light integration approach
F. Brunbauer et al. NIM A 955 (2020) 163320
Camera

## Slide 4: Optical readout micromegas detector
4
Glass Micromegas
Produced at MPGD IRFU workshop
8 cm
Gas: Ar/10%CF4
Camera: CMOS Orca-Quest

## Slide 5: X-ray characterization
5
2D light intensity profile
Radiography of a bat
Pixel size : 50x50 µm2
Pixels
Pixels

## Slide 6: X-ray characterization : Soleil synchrotron
6
X-ray beam - 6keV - 50x50 µm² - Ar/10%CF4
Measurement of Point Spread Function (PSF)
Spreading origins : diffusion and optics
1D projection
1 mm
2D light intensity profile
50 x 50 µm² beam (Va=36 kV/cm, Vd= 350V/cm)
σ = 130 µm
Pixels
Pixels
0.5 mm
Light intensity profile of a 50 x 50 µm² over a pillar
A. Cools et al 2023 JINST 18 C06019

## Slide 7: X-ray characterization
7
MTF (10%) : 800 µm
Deconvolution
Pixels
Pixels
10 mm
PSF from experimental data (σ = 280 µm)
Deconvolution
MTF (10%) : 281 µm

## Slide 8: X-ray characterization
8
History of imaging with MPGDs
Glass Micromegas, Optical readout, deconvolution

## Slide 9: Beta imaging
9
Tumor heterogeneity as an effect on drug targeting
Develop more efficient drugs
Requires better detection sensibilities
Pharmaceutical needs at the cell level for drug development:
  Assess the drug distribution among cells
  Quantification of 3H concentration in single cell samples
Tumoural cells collection – Tritium tracking
Tritiated cells deposit on the cathode
Tritium activity counting with Micromegas detector

## Slide 10: Beta imaging
10
First deposit : tritiated glucose
3H concentration ↔ sample activity (Bq)
Activity measurement limits and dynamic range → Activities: 0.1 Bq, 1 Bq and 10 Bq
β
Cathode
Mesh
ITO
Glass
Light cover
Camera
VIS light
e-
Beta imager set-up scheme
A. cools 167910 (2023)

## Slide 11: Beta imaging
11
All drops positions are well assessed
0.1 Bq drops are close to the background noise
Light intensity profile over time - 20% of CF4
Reference | 0.09 | 1.055 | 9.8
Average | 0.086 | 0.84 | 11.74
σ | 0.026 | 0.18 | 1.28
Deviation | 5% | 20% | 17%
Activity measurement (Bq) – 5.2σ INTEGRATION
Pixels
Pixels

## Slide 12: Beta imaging
12

## Slide 13: Beta imaging
13
200 ms frame with single beta events
Single event reconstruction

## Slide 14: Beta imaging
14
Clustering method :
Reference | 0.09 | 1.055 | 9.8
Measurement | 0.108 | 0.85 | 5.13
σ | 0.014 | 0.088 | 0.38
Deviation | 17% | 20% | 48%
Activity measurement (Bq) CLUSTERING
Clusters centroid histogram - 20% of CF4
Pixels
Pixels

## Slide 15: Neutron imaging
15
Cathode : 10B4C neutron-to-charge converter
  Thermal neutrons absorbed by 2 µm thin 10B4C layer
  Conversion efficiency: 5%
  (α or Li) fragments cause strong ionisation
  Limitation: fragments long range in the gas (5 mm)
A. Cools 07009 (2023)

## Slide 16: Setup
16
Acquisition modes:
  Event-by-event: track reconstruction:
  Potentially higher resolution and ɣ-to-n suppression
  Integrated: real-time radiography:
  Almost no data processing
8 cm

## Slide 17: Single event study
17
Drift field affects the electron diffusion
Diffusion spreads the light
50 V/cm drift field
800 V/cm drift field
2000 V/cm drift field
50 V/cm
800 V/cm
2000 V/cm
Rate : 3 events/s
Pixels
Pixels
Am-Be source – Ar/10%CF4

## Slide 18
18
250 µm drift gap
A. Corsi
Simulated dE/dX - maxboltz
Spatial resolution measurement
Simulation

## Slide 19
19
Al cathode with 10B4C pattern deposition
3.4 meV Neutron beam – 10 MHz – PSI Zurich – 09/12/2023
Spatial resolution measurement
Eamp = 25 kV/cm, Edrift = 22 kV/cm, 100 s
Neutron imager with visible cathode
Preliminary

## Slide 20
20
Spatial resolution measurement
Light intensity profile with single amplification
Eamp = 38 kV/cm, Edrift = 500 V/cm, 100 s
Light intensity profile with double amplification
Eamp = 20 kV/cm, Edrift = 24 kV/cm, 100 s
Preliminary

## Slide 21
21
Spatial resolution measurement
Light intensity profile with double amplification
Eamp = 20 kV/cm, Edrift = 24 kV/cm, 100 s
Preliminary

## Slide 22: Conclusion and perspectives
22
  Detector characterization with X-rays showed a PSF of 130 µm
  Sub-bequerel tritium activity measurement has been proven with
  optical MM Readout.
  Single cell and simultaneous 14C and 3H measurement are envisioned
  Higher spatial resolution is expected and is observed with a thin drift gap
  configuration for neutron imaging

## Slide 23
23
Thank you

## Slide 24: Backup
24

## Slide 25: Optical readout micromegas detector
25

## Slide 26
26

## Slide 27: Imaging: Line spread function measurement
27
10B4C cathode with copper tape
Am-Be source
Copper tape

## Slide 28: Imaging
28
Integration mode
6 mm drift gap
Simulated dE/dX - Garfield
A. Corsi
Light intensity
Pixels
Pixels
1 cm
mm
mm
Am-Be source
Ar-10%CF4

## Slide 29: Imaging
29
Single event mode
800 V/cm drift field, 3 events/s
5 mm
α track light intensity profile
Bragg curve
1 cm
2D histogram of neutron positions reconstruction
Pixels
Pixels
Pixels
Pixels
Am-Be source
Ar-10%CF4

## Slide 30: Imaging
30
Single event mode : reduced drift gap
2D histogram of neutron positions reconstruction
1 cm
Am-Be source
Ar-10%CF4
Pixels
Pixels
1 cm
Pixels
Pixels
25 kV/cm drift field, 3 events/s
250 µm drift gap

## Slide 31
Hamamatsu CMOS camera
Readout noise
Photon number resolving
Dark current
Cooling Sensor temperature Dark current
Air - 20 °C 0.016 e- /pixels/s
Pixels
Number Size
4096 x 2304 4.6 µm x 4.6 µm
Minimum exposure time
Mode Rate
Standard 1 µs/frame
Ultra quiet 100 ms/frame

## Slide 32: Light production mechanisms
Light yield : amount of light determines the signal to noise ratio. It depends on electric field, pressure and gas mixture.
Scintillation : excited atoms or molecules emit photons during de-excitation.
Scintillation
f Fluorescence
Prompt emission of photon after absorption of incident radiation.
(1 ns to 1 µs)
Phosphorescence
: Delayed emission of photons after absorption.
(1 ms to 100 s)
Primary scintillation
From the creation of primary electron coming from the excitation of gaz due to incident particles.
Secondary scintillation
From the creation of secondary electrons taking place during avalanche amplification.
Electroluminescence
Electrons with energy lower than ionization threshold just excite atoms or molecules.
Notes: 32

## Slide 34
PRELIMINARY RESULTS WITH TRITIUM SAMPLES
β particle range in Ar-Isobutane gas mixture

## Slide 37
37
Production
Production at CEA Bulk Lab
Gain uniformity check
Planarity check : Laser diffraction measurement
T. Benoit
M. Vandenbroucke
Light intensity
Vertical scale x1000

## Slide 38
DETECTOR CHARACTERIZATION WITH X-RAYS
X-ray radiography
MTF measurement
60 sec exposure time lead target radiography with simple background suppression.

## Slide 39: Beta spectrum : CF4 Overall activity : 76 Bq