## Slide 1: Muon tomography using Micromegas technology
David Attié
Celebrating Ioannis, October 5th, 2023

## Slide 2: Preambule
My contribution to Resistive Micromegas
1

## Slide 3: My contribution to Resistive Micromegas
  After a PhD in Space γ-ray Astrophysics (INTEGRAL/SPI)
    HPGe detectors
X
2006
2007
2008
2010
2009
2011
2012
2013
2014
  Courtesy visit in Astrophysics Department in December 2005  Eric Delagnes  Paul Colas
X

## Slide 4: My contribution to Resistive Micromegas
  Postdoc position on digital TPC:
    Gas detector novice
    Systematic study of gas mixtures
    First small digital TPC using TimePix + Micromegas
2006
2007
2008
2010
2009
2011
2012
2013
2014
  Permanent position at CEA:
X
X
    First large digital TPC (TimePix/Ingrid)
X
X
X
X

## Slide 5: My contribution to Resistive Micromegas
  My first close interaction with Ioannis!
    Micromegas copper grid on TimePix without resitive layer for spark protection
    My first gas box
    But need to borrow a CAEN power supply to Ioannis lab for the first test
2006
2007
2008
2010
2009
2011
2012
2013
2014
X
  Conclusion:
  So we must find an « Ioannis’ proof » solution to improve people trust
  in Micromegas detector!
   Resitive detectors?!
X

## Slide 6: My contribution to Resistive Micromegas
  Resistive Micromegas solution for ILC-TPC
    Tests of several resistive coating with one module
    Beam tests in a large prototype TPC
2006
2007
2008
2010
2009
2011
2012
2013
2014
X
X
X
X
    Unprotected integrated electronics with 7 modules
  MAMMA collaboration
  HARPO
  Clas 12
  T2K
  PiggyBack…

## Slide 7: Micromegas Technology
  First introduced by Dixit et al. NIM A518(2004)721 to improve spatial resolution
  Use material properties (resistivity) and geometry (insulator thickness) to spread charge over several pads
    Resistive ink
    Carbon Loaded Kapton (CLK)
    Diamond Like Carbon (DLC)
  Choice of resistivity: from 100 kΩ/□ to 10 MΩ/□
  Specific Pad Response Function (PRF) needed
  Advantages for resistive readout:
Standard Model of Particle Physics
Resistive foil
Insulated layer
Pads
PCB
Micromegas mesh
left
middle
right
Anode with strips
Plane anode
 | Resistive Anode | 
Properties | Strips | Plane
Charge dispersion |  | 
Spark protection |  | 
Multiplexing readout |  | 
2D readout |  | 
Readout segmentation | Strips | Strips/Pixels
t≈ shaping time
RC from resistive layer

## Slide 8: Muon Tomography
Imaging from muon flux
2

## Slide 9: Muon tomography – Principle
  Enable a non-invasive but penetrating imaging of density contrast using natural charged particles
  Muon tomography can be done using one of the three methods:
Deviation
Transmission
Absorption
Transmission
    Deviation
    Transmission
    Absorption
~1 m
~10-100 m
~1 m
~10-100 m
(M-Cube)
(WatTo, Scanpyramids, G2G3, INB72, EDF, D3DT)
(IZEN)

## Slide 10: Muon tomography – Timeline
  Started with the R&D of resistive multiplexed Micromegas
  Used for hodoscope in cosmic test bench
    Reduce channel number
  WatTo (Water Tower)
  Cosmic bench for Clas12 detectors validation
X
2012
2013
2014
2016
2015
  M-Cube:
  demonstrator for homeland security
X
X
1st muography HD online
2017
X
  M-Cube :
  U detected in less than 4 minutes
  ScanPyramids
X
    Large area with accurate tracking

## Slide 11: Muon tomography – Timeline
2018
X
2017
2019
2021
2020
X
  Maison de l’Imagerie Muonique Ouverte aux applications Sociétales et Académiques
X
X
  G2G3
X
  Common lab
2022
X
INB72
IZEN
X
X
1st muography of a military NR
  G3 nuclear reactor (NR)
Nuclear dismantling projects
Industrialization

## Slide 12: MultiGen detector – Basic element of a telescope
(X1,Y1,Z1 )
X
  MultiGen detector
    Resistive strip bulk Micromegas
    2D readout (X & Y) genetic multiplexing
    PCB size: 546×546 mm²
    Active area: 500×500 mm²
    Can be used in mosaic
  Evolution since 2014: from prototype to serial
  Since 2021 working on replacement of Pyralux by Vacrel
MultiGen Version | Multiplexing Family | Strip number | Strip pitch (μm) | Year | Produced Detector | Improvement
v1 | 17* | 1024 | 488 | 2014 | 7 | (*) one family incomplete: 13 strips missing
v2 | 17 | 1037 | 482 | 2015 | 42 | Complete families; grounding plane added
v3 | 17 | 1037 | 482 | 2017 | 50 | Connectors moved to sides; HV filters on PCB
v4 | 12 | 732 | 683 | 2019 | 52 | Number of family reduced to 12; resistivity increased
INB72 | 5 | 305 | 560 | 2022 | 8 | Smaller detector (200×200 mm²) for specific application
MultiGen v3-v4
MultiGen v2

## Slide 13: MultiGen detector – Illustration with 5 families
INB72 detector
5 multiplexing families
305 (5x61) strips
Pitch: 560 µm

## Slide 14: Telescopes based on MultiGen
  Evolution of the CEA/Irfu telescope: towards compactness and transportability
  CEA/Irfu’s electronis cards
    Front-End Unit (FEU) card developed for Clas12
    High Voltage Power Supply (HVPS) card dedicated to muon
    2015: WatTo, ~200 kg
    2016: ScanPyramids (outside), ~130 kg
    2018: ScanPyramids (inside) cube, ~45 kg
    2019: G2G3, EDF, …, optimized cube, ~45 kg
2015
2016
2018
2019-today
6U Rack
HVPS
DC-DC
FEU
8 ASICs Dream

## Slide 15: Benches of Muon Tomography
  Benches built for specific applications
    M-Cube: smuggled "Special nuclear material" (SNM)
    ENTRANCE: EfficieNT Risk-bAsed iNspection of freight Crossing bordErs without disrupting business
    IZEN: waste package inspection
2014-2017
2020-2023

## Slide 16: Resistive strip and detector production
  Resistive strip with high resistivity strip requested
    R&D made over two years
    CEA/Irfu the only producer by screen printing left
    Target resistivity between 1&5 MΩ/□
  Detector manufacturing transfer to Elvia-PCB
    Started in 2014
    Succeed after many years until obsolescence of Pyralux  Vacrel

## Slide 17: Conclusions
  Micromegas detectors made a late start in the very active field of muon tomography thanks to
    Resistive strip readout
    2D multiplexing technique
    Amplitude feedback to compensate for environmental changes (P, T)
    PCB factory production (more than 150 detectors produced since 2015)
    Gas tightness, recirculation and filtration
  Over a decade, the competition has been caught up, or even surpassed
    First online HD muography (WatTo)
    First nuclear reactor tomography with muons
    ScanPyramids mission results (Big Void, North Face Corridor)
  Muon tomography telescope based on Micromegas technology is a success
    The first telescope will be sale by Iris-Instruments this year
    Probably helped by the research process to make them “Ioannis’ proof” put in place

## Slide 18: Thank you!

## Slide 20: Muon particle
What is it?
1

## Slide 21: Cosmic-rays muons
  Cosmic muons are charged particles produced by cascade of reactions induced by cosmic rays in the upper atmosphere coming from violent phenomena in the Universe (compact objects, supernovae, etc.)
    Natural, free and harmless radiation
    Flux: ~150/m²/s cos²θ (maximum in zenith direction θ=0)
    Mean energy: 4 GeV
    Mµ ~ 200×Me= 105,7 MeV/c²
    Life time ~ 2.2
  Muon production processes:
    𝜋± → 𝜇±𝜈𝜇 branching ratio of 99.99%
    𝐾± → 𝜇±𝜈𝜇 branching ratio of 63.56%
  Muon processes:
    Decay: 𝜇± → e±𝜈𝜇𝜈e
    Capture: 𝜇-+p+ → n+𝜈𝜇
Simulated air shower created by 1 TeV proton

## Slide 22: Muon interation with matter
  Muon trajectories are straights in mean
  Muons interact with matter and can be
    Absorbed/stopped (decay)
    Scattered
  Interaction processes with matter
    Energy loss given by Bethe-Bloch ionization stopping power
    Standard deviation of the scattering angle describe by Molière theory
      Radiation length is given with good approximation by:
Material | Thickness |  (°) | Pabsorption
Air | 100 m | 0.094 | 0.78%
Lead | 10 cm | 1.01 | 2.9%
Water | 1 m | 0.35 | 4.2%
Ground | 100 m |  | 99%
p~4 GeV