## Slide 1: What I hope will come out of this workshop - Thierry
Low Z interesting, but not only C (BN, SiC, NT)
NT as building block, their properties interesting in the context of hierarchical materials (eg density, length, diameter)
Most applications (Bi wires, screens, BID, Isolde targets ) interested in same range properties (low dE/dX, high lambda, tensile strength, mode of rupture)
Most applications need to procure for limited series  can afford higher prices, but likely won’t find the right fit from the available supply
Need to get range of products (eg fibers) where parameters can be selected and “verified” (Eg purity, diameter, etc) and compared to performance in “quick” selection tests (HiRadMat final test, need another “quick and dirty test”;
Simulation are important but mode of failure not fully predicted (lack of data, sometimes did not focus on right mode of failure (work function vs sublimation)
Since material properties of fibers are still orders of magnitude lower than individual CNT, need to see if VdW and fiber quality could be used as selection criteria (and see if curing, removal of impurities, etc can improve the result: probably nanolab + MME could play a role there)