## Slide 1: WP5 progress report
Tuesday 18th April 2022
ITS3
WP5 collaboration

## Slide 2
Detector layout: tolerances
Next wind-tunnel tests

## Slide 3: Detector layout: tolerances at equatorial gap
R nominal
18
24
30
16.5
1
1.5
EM2:
Blank silicon h-layers
Equatorial plane
-0.5 mm
Kapton tape, larger
Within 0.5mm, if Kapton tape cut is improved

## Slide 4: Detector layout: Kapton tape
Improvement of the cut of the Kapton tape: NEXT, Pieter
Target: fine cut +- 0.1 mm accuracy over 270 mm length, reasonable?
Target: Distance from the Silicon as small as possible according to the above target
  Define procedure
  Improvement:
    Alignment (mandrel and cutter)
    Fine cut
      Surgery knife ? (Diamond knives for eyes surgery)
      Laser cut? (FS laser , other ..)
      Any suggestions?
EM2 , L1 during Kapton cut

## Slide 5: Next wind-tunnel tests
First vibration campaign conclude
NEXT:
Reverse flow direction
Thermal test (similar to previous one).
Vibrational tests
Upgrade of the prototype (target in 2 weeks)
Thermal test and vibrational tests both air flow direction
Improvement of the test set-up
Blowing air
BP with window for the displacement sensor,
For vibration measuring of layer0
BP with integrated heater for additional thermal test considering heat coming from BP
Resistive wire
3D printing parts:
Production on going in Grenoble