## Slide 1: Results from FASER
Dave Casper
University of California, Irvine
(for the FASER collaboration)
Dark photon search CONF note on CERN Document Server
Collider neutrino direct detection paper (submitted to PRL)

## Slide 2: FASER collaboration
87 members from 24 institutes in 10 countries
International laboratory covered by a cooperation agreement with CERN

## Slide 3: Outline
Physics motivation and goals
The FASER detector
2022 operations and results
Forward physics facility for HL-LHC

## Slide 4: Motivation: search for long-lived
Dark photon coupling to Standard Model fermions:
Assuming , and give thermal relic density in range expected for dark matter
Dark photon sources at LHC:
  Neutral pion decay:
  Eta meson decay:
  Dark bremsstrahlung:
For , is of branching ratio
Long decay length for boosted , assuming :
Feng, Galon, Kling and Trojanowski, Phys. Rev. D 97 (2018) no. 3, 035001

## Slide 5: Motivation: ALP’s and other searches
Re-casts of dark photon searches:
  gauge boson
  “Proto-phobic” gauge boson
Axion-like particles
  Photon coupling (see Feng, Galon, Kling and Trojanowski)
  W coupling (see Kling and Trojanowski)
  Gluon coupling (see Aloni, Soreq and Williams)
  Typically decay to
    Sensitive to decays in decay volume and spectrometer (~4 meters)
Will not discuss these further today
FASER's Physics Reach for Long-Lived Particles: PRD 99 090511 (2019)

## Slide 6: Motivation: collider neutrinos
“Detecting and Studying High-Energy Collider Neutrinos with FASER at the LHC,” EPJC 80, 61 (2020)
Expect ~1300 interactions in 150/fb
Expect ~20,000 interactions in 150/fb
Expect ~20 interactions in 150/fb

## Slide 7: Looking forward in FASER
production
arXiv:1901.04468
decay probability in decay volume @
Fraction of FASER decays with
Signal expected assuming 50% selection efficiency
Detector subtends of solid angle from ATLAS; rely on collimation from boost
Generator level studies

## Slide 8: signature
Veto entering charged particles
Reconstruct two energetic charged tracks
Confirm particle ID and energy with large shower in EM Calorimeter

## Slide 9: FASER Detector (arXiv:2207.11427)
4 LHCb Outer ECAL modules
Three stations of three layers 72 ATLAS SCT silicon strip modules
24 SCT modules
Halbach dipoles inner radius
4
Tungsten/Graphite/Scintillator stack
thick dual PMT readout ()
thick area
thick area
tungsten/emulsion layers (8 interaction lengths)

## Slide 10: FASER Installation
Calorimeter
Preshower
Tracking spectrometer
Decay volume
Veto
To ATLAS
FASERnu
IFT
2017: Feng, et al. idea paper, Big Bang Theory cameo 2018-19: Proposal, funding and approval 2019-20: Construction and testing on surface 2020-21: Installation underground 2021-22: Commissioning with cosmics 2021: Test beam 2022: Collision data from LHC Run 3
Slide credit: C. Gwilliam
In 2018…

## Slide 11: Magnets
Three permanent magnets with “Halbach” design produce very uniform dipole field of 0.57 T
The most expensive part of the experiment!
Jackson

## Slide 12: Tracker
Extremely precise position resolution in one direction
  Use two sensors with stereo angle to get 3D space point
Reconstruct charged particle trajectories
Measure momenta using bending in field
Silicon microstrip detector modules (SCT) gifted by ATLAS
  1 plane = 8 modules (two-sided)
  1 station = 3 planes
  Full detector = 4 stations
“The tracking detector of the FASER experiment,” NIM 166825 (2022)

## Slide 13: Tracker alignment
Preliminary alignment of three downstream tracker stations used in dark photon and neutrino searches

## Slide 14: Scintillators
Scintillators used to veto charged particles, trigger and measure timing
Veto scintillators:
  Upstream and downstream of FASER
  20 mm thick, single PMT readout
Timing scintillators
  Between decay volume and first spectrometer tracking station
  10 mm thick, dual PMT readout ()
Preshower scintillators
  In front of calorimeter
  20 mm thick, single PMT readout
CAEN digitizer records waveform for all 15 PMT channels (including calorimeter)

## Slide 15: Scintillator performance
All veto scintillator inefficiencies measured to be

## Slide 16: Calorimeter
4 LHCb outer ECAL modules loaned to us
  “Shashlik” design with fibers readout by PMT
  67 layers of scintillator alternating with 66 layers of tungsten
  Total depth: 25 radiation lengths

## Slide 17: Calorimeter: energy resolution
Calorimeter response measured in dedicated 2021 test-beam campaign
  Results close to performance quoted by LHCb
Resolution ~1% or better at energies of interest in dark photon search
Test-beam paper in preparation!

## Slide 18: FASER
730 layers of 1.1 mm thick Tungsten plates interleaved with emulsion films
30 cm height, 25 cm width
Total mass 1.1 tons
Sub-micron spatial resolution
Replaced over course of each year’s run to limit track density
Development and scanning of films from 2022 underway
Simulated charged-current interaction, and decay, in FASER
“Technical Proposal of FASERν neutrino detector,” arXiv:2001.03073

## Slide 19: Trigger and Data acquisition
Based on open-source DAQling framework
Automated, continuous data-taking
  No control room or dedicated shift-takers
Trigger rates up to 1.3 kHz
  Inputs from scintillators and calorimeter (CAEN digitizer)
DAQ deadtime in 2022 run: 1.3%
Event size: 21.5 kB, dominated by PMT waveform data
“The trigger and data acquisition system of the FASER experiment,” JINST 16 P12028 (2021)

## Slide 20: Offline software
Adapted open-source Gaudi/Athena framework to FASER
  “Calypso”
  No time/person-power to build our own from scratch
Use native ATLAS/LHCb geometry descriptions for SCT/Calorimeter modules, respectively
ACTS track reconstruction in production before ATLAS…
FASER tracker frame, as constructed and rendered in Calypso/Athena

## Slide 21: A muon traversing FASER

## Slide 22: Operations and data set
Detector performed almost flawlessly in 2022
  Recorded 96.1% of delivered luminosity
  Over 350M single muon events
Calorimeter gain optimized for TeV energies after second emulsion exchange (green arrow)
  27.1/fb used for dark photon search

## Slide 23: Simulated
Simulated A’ (m = 25 MeV, ε = 3e-5) signal with E(calo) = 645.2 GeV

## Slide 24: selection
Events with no veto activity and blinded until selection finalized.
Simple selection optimized for discovery:
  Collision event with good data quality
  No signal (> 40 pC) in any veto
  Timing and preshower consistent with minimum ionizing tracks
  Exactly two good fiducial tracks:
    and
    Extrapolate to at vetos
  in EM calorimeter
Selection efficiency over region of sensitivity

## Slide 25: cut flow: calorimeter energy

## Slide 26: Dark photon backgrounds
Veto inefficiency
  Negligible
Muon-induced neutral hadrons
  Estimated from three-track sample, ignoring muon and removing photon conversions
Geometric muon background
  Negligible
Neutrino interactions in detector material
  Estimated from GENIE sample, corrected for material missing in simulation
  Small, but dominant background
Non-collision (cosmic or beam) background
  Negligible
Process | Background Estimate
Veto inefficiency | Negligible
Neutral hadron & geometric muon background | 
Neutrino interactions | 
Non-collision background | Negligible
Total background | 
Process | Background Estimate
Veto inefficiency | Negligible
Neutral hadron & geometric muon background | 
Neutrino interactions | 
Non-collision background | Negligible
Total background | 
See https://cds.cern.ch/record/2853210/files/CERN-FASER-CONF-2023-001.pdf for more details and validation studies

## Slide 27: result
95% CL excluded region based on 0 events passing selection
  0 events with even 1 fiducial track
Source | Systematic Uncertainty | Typical Effect on Signal Yield
Theory, Statistics and Luminosity |  | 
cross section |  | 15-45%
Luminosity | 2.2% | 2.2%
MC statistics |  | 1-2%
Tracking |  | 
Momentum scale | 5% | < 0.5%
Momentum resolution | 5% | < 0.5%
1-track efficiency | 3% | 3%
2-track efficiency | 15% | 15%
Calorimetry |  | 
Energy scale | 6% | < 1%
Source | Systematic Uncertainty | Typical Effect on Signal Yield
Theory, Statistics and Luminosity |  | 
 |  | 15-45%
Luminosity | 2.2% | 2.2%
MC statistics |  | 1-2%
Tracking |  | 
Momentum scale | 5% | < 0.5%
Momentum resolution | 5% | < 0.5%
1-track efficiency | 3% | 3%
2-track efficiency | 15% | 15%
Calorimetry |  | 
Energy scale | 6% | < 1%

## Slide 28: Collider Neutrinos: Pilot search
Copious meson production makes the LHC an intense source of the world’s highest energy man-made neutrinos
  De Rujula and Ruckl (1984)
First search using 29 kg emulsion detector in 2018
  12.2/fb at 13 TeV CMS energy
  2.7 excess of neutrino-like neutral vertices
FASER emulsion detector will study in detail with Run-3 data
“First neutrino interaction candidates at the LHC,” PRD 104 L091101 (2021)

## Slide 29: Collider neutrino search
Active electronic detector can find and CC interaction signal above background:
  Long, high-momentum fiducial track
  No activity in forward veto station
  Blinded analysis (35.4/fb Run-3 luminosity used for neutrino search)

## Slide 30: Expected backgrounds
Veto inefficiency
  Measured using singles rate in forward veto (only one of two layers fire)
  Negligible
Muon-induced neutral hadrons
  estimated from simulation
  Conservative; ignores likely veto signal from parent muon
Geometric muons (leakage around veto)
  extrapolated from side-band
Please see https://arxiv.org/pdf/2303.14185.pdf for details

## Slide 31: Collider neutrinos: results
neutrino-like events observed over backgrounds
“No signal” hypothesis excluded at
No attempt to measure cross section, but luminosity-normalized prediction agrees well with data.

## Slide 32: Collider neutrinos: extrapolation
Extrapolate candidate charged tracks to front veto position
  Uniform distribution not expected due to tighter cuts downstream
No evidence of entering contamination near edges

## Slide 33: Collider neutrinos:
Clear evidence of both and interactions with
Luminosity-normalized prediction from GENIE and F. Kling fluxes

## Slide 34: Teaser: candidate in FASER
FASER analysis in progress
This event very -like
  Single track for
  Shower max at
  from beam
Beam view
Side view

## Slide 35: FASER Summary
FASER had a very successful start to Run-3
exclusion in interesting thermal relic region
First direct detection of 153 collider neutrino interactions
High-resolution neutrino studies with FASER underway
Much more data to come!

## Slide 36: Forward Physics Facility for HL-LHC
FPF Whitepaper: arXiv: 2203:05090
April 12 P5 report by Jonathan Feng
FPF slide credits:
FPF Website

## Slide 37: Forward Physics Facility for HL-LHC

## Slide 38: FASER2 working design
Looking for additional U.S. groups interested in FASER2!
6th Forward Physics Facility Meeting: CERN, June 8-9

## Slide 39: Acknowledgements
Financial support for FASER comes from:
We also thank:
  LHC for successful 2022 run
  ATLAS for accurate luminosity data
  ATLAS SCT for donated tracker modules
  ATLAS for Athena software framework
  LHCb for donated ECAL modules
  CERN FLUKA team for simulations
  CERN PBC and technical infrastructure teams for excellent support during design, construction and installation

## Slide 40: FASER publications
The FASER Detector: arXiv:2207.11427
The FASER W-Si High Precision Preshower Technical Proposal: CERN Document Server
The tracking detector of the FASER experiment: NIM 166825 (2022)
The trigger and data acquisition system of the FASER experiment: JINST 16 P12028 (2021)
First neutrino interaction candidates at the LHC: PRD 104 L091101 (2021)
Technical Proposal of FASERν neutrino detector: arXiv:2001.03073
Detecting and Studying High-Energy Collider Neutrinos with FASER at the LHC: EPJC 80, 61 (2020)
Input to the European Strategy for Particle Physics Update: arXiv:1901.04468
FASER's Physics Reach for Long-Lived Particles: PRD 99 090511 (2019)
Letter of Intent: arXiv:1812.09139
Technical Proposal: arXiv:1811.10243

## Slide 41: Backup
Supplemental material

## Slide 42: FASER and NA-62 result from Moriond