Collider absorber materials and cryogenics
  - Short informal meetings on the absorber, cryogenics, and vacuum options
    - https://indico.cern.ch/category/16209/
  - Copper coating of tungsten appears feasible → what is the impact on beam stability?
    - Assume a 100 μm copper coating on tungsten (with infinite thickness)
    - Skin depth is ~400 μm for revolution frequency
  - Focus on 300 K case

---
Impedance models at 300 K
  - Visible effect of coating thickness on transverse impedance → with thicker copper coating (green) the impedance approaches pure copper for a larger frequency range

---
Minimum chamber radius achievable with different materials
Simulations with muon decay included
Lifetime at 5 TeV: 104 ms → 3100 turns in the 10 km ring
Copper coatings perform as well as pure copper
Minimum chamber radius below 20 mm for all damper settings
Simulations with even thinner coatings (1μm and 100nm) running to find the limit in coating thickness

---
Stability simulation parameters
	Unit	Value
Synchrotron tune Qs		0.00233
Synchrotron period	turns	429
Bunch length 1σ	mm	1.5
Bunch intensity	Particles per bunch	1.8e12 (at start)
εx / εy	μm rad	25
# of macropaticles		10000
Machine parameters
	Unit	Value
Circumference	m	10000
Beam momentum	GeV/c	5000
Rev. frequency	kHz	30
RF frequency	MHz	1300
Harmonic number		43478
RF voltage	MV	2e3
αp		-2.0e-6
Avg. beta x/y	m	85 / 51
Chromaticity Q’x/Q’y		0/ 0
Detuning from octupoles x/y	m-1	0 / 0
Scanned parameters
	Unit	Value
Chamber radius	mm	10 to 40
Transverse damper		2 to 500 turns/No damper

---
Impedance simulations parameters: materials
Infinite thickness for all the chambers simulated
Copper at 300 K
Tungsten at 300 K
	Unit	Value
Magnetic field	T	7
Temperature	K	300
RRR		70
DC resistivity	nOhm m	17.9
	Unit	Value
Temperature	K	300
DC resistivity	nOhm m	55.6