## Slide 1
  Integration news
  Topics:
  FCC-ee Underground Structure Overview
  FCC-ee Machine tunnel Layout
F. Valchkova-Georgieva
05.06.2023 / FCC Week

## Slide 2
Only schematic, and not to scale.
Courtesy A. Navascues Cornago
  FCC-ee Underground Structure Overview
F. Valchkova-Georgieva
05.06.2023 / FCC Week

## Slide 3
  Integration of FCC-ee machine elements (regular arc)
Main cross section as for FCC-hh
Main ring below of booster ring
Main ring and booster ring 1.3 m distant
Collider Center
Machine tunnel 5.5m in diameter
F. Valchkova-Georgieva
05.06.2023 / FCC Week
Smoke/He extraction
Cable trays:
Fibre optic
LV distribution
Control cables
Demineralized water DN600
Leaky feed
Warm He recovery DN200
Demineralized water felling DN65
Drain
Fresh air duct
Fresh air diffused
Alignment space occupation
Compressed air DN80
Firefighting/Row water DN400
Chilled water DN150
Cable tray:
MV distribution
Electrical HV
power transmission
Collider ring
Booster ring
He DN50