## Slide 1: EuCARD-WP7-HFM meeting 22 March 2011
Baseline conceptual design: the magnet we will build
Attilio Milanese
Acknowledgements:
MPWG members, S. Caspi, P. Ferracin, ESAC reviewers

## Slide 2: Magnetic cross section
SMC
no bore, O.D. 540 mm
4412 mm2 of cable, Lshell = 0.5 m
≈ 13 T coil field at s.s.
FRESCA2
100 mm bore, O.D. 1030 mm
30199 mm2 of cable, Lshell = 1.6 m
13 T nominal field in the bore

## Slide 3: Coil and field in the cross section
156 turns per pole
(2 x 36 + 2 x 42)
Bcenter = 13.0 T
I13T = 10.7 kA
Bpeak = 13.2 T
E = 3.6 MJ/m
L = 47 mH/m

## Slide 4: Load line and margins
13 T imply 83% @ 4.2 K, 76% @ 1.9 K along the load line
[15 T correspond to 88% along the load line @ 1.9 K]

## Slide 5: Field homogeneity in the cross section
Bcenter = 10 T
b3 = 49.2
b5 = −35.1
b7 = 4.4
Bcenter = 11 T
b3 = 58.3
b5 = −37.5
b7 = 5.1
Bcenter = 12 T
b3 = 66.0
b5 = −36.2
b7 = 4.7
Bcenter = 13 T
b3 = 72.8
b5 = −35.1
b7 = 4.4

## Slide 6: Field homogeneity along the axis in 3d
limit of the straight section

## Slide 7: Field on the coil in 3D
The peak field is in the straight section.
yoke extruded all the way
vertical pad extruded over
the straight section
top central post all in iron
Flared ends
aramp = 17°
Rmin, HW = 700 mm
Rmin, EW = 44.7 mm

## Slide 8: Lorentz forces in 2D and 3D, at 13 T
In 2D:
SFx = 7.5 MN/m
SFy = −3.9 MN/m
(per quadrant)
In 3D:
SFx = 4.95 MN
SFy = −1.97 MN
SFz = 0.52 MN
(per octant)

## Slide 9: Structure
Same bladders and keys principle of previous meeting.
The geometry has been slightly modified:
no central tube
central posts
outer radius of yoke
thickness of shell
See Pierre’s (Françoise’s) presentation next for engineering details and last version.

## Slide 10: Stresses on the coil, 13 T
warm
cold
13 T
The coil does not go above 150 MPa, the Nb3Sn “comfort zone”
The high field and high stress regions do not overlap
2d plane stress analysis confirmed by 3d one in the straight parts
sx

## Slide 11: Conclusion
The conceptual design can be considered finished.
We are now in a new phase, where the magnetic and mechanical modeling is there to support the engineering design for “details”, like end plate geometry, tie rods, wedge, proper prestress of easy way part, field in the splice region, …
Consequently:
MPWG: Magnet Predesign Working Group
MDWG: Magnet Design Working Group

## Slide 12
Thank you.