## Slide 1
Overall status of the HL-LHC project
O. Brüning
CERN, Geneva, Switzerland

## Slide 2
LHC in the Geneva Basin and its Experiments
LHC ring:
27 km circumference
CMS
ALICE
LHCb
ATLAS
Super-Conducting Dipole
Magnets along the 8 symmetric
Arcs [22km]
Features proton-proton and Lead-Lead and Lead-proton collisions!
Notes: Specialized and Multi-Purpose

## Slide 3
Over 160 fb-1 at 13 TeV during Run1 & Run2
Higgs Discovery in 2012!
ca. 70 fb-1 / year at hand!!!
 over 400 fb-1 by the end of LHC Run3 by end 2025!!!
So Why do we need an Upgrade?
Higgs discovery in 2012!  But many questions remain and the search continues!!!
Higgs properties [coupling]
More than one Higgs?
BSM Physics? Dark Matter & Dark Energy?
Need for more Data and Statistics!!
Doubling the accuracy for the experiments implies 4 times the data volume!!!
 over 20 Years of operation with current peak performance after end of Run 3 (after 2025)!
HL-LHC Goals in a nutshell:
Extend the LHC lifetime by 15+ years
Prepare the machine for producing in that period
10 times more data as compared to the nominal LHC operation period
Need to overcome several technological challenges! [not just in the machine but also in the detectors!]
HL-LHC is a technology driver in many areas

## Slide 4
Organized into 19 Technical Work Packages
Impossible to be exhaustive in this presentation!
More information under:
HL-LHC News: https://hilumilhc.web.cern.ch/news
HL-LHC Newsletter: https://hlcb-newsletter.web.cern.ch

## Slide 5
Run3 operation
Approval of
HL-LHC Project
EU funded HiLumi
Design Study
Series production is well underway - or ready to be launched - for all components!
Over Half Way!
7 years since project approval
Less than 6 years until start Run4
HL-LHC Operation
We are here
Ca. 1.1BCHF
Ca. 75% committed
Notes: 5

## Slide 6
Q2
27 MGy
MCBX3 20 MGy
Cold bore insulation
≈ 35 MGy
6
HL-LHC Technical Challenge 1: Triplet Magnets
ATLAS
CMS
Epoxy and most insulation materials
will become brittle at these radiation levels and loose their mechanical integrity!!!
– essential for the coil production of
superconducting magnets! –
Operation beyond 2025:
Requires replacement of LHC Triplet magnets
10 x the luminosity  Requires new, more radiation resistant triplet magnets

## Slide 7: HL-LHC technical Challenge: Radiation Hard Triplet Magnets
Need to replace existing triplet magnets with radiation hard system such that the new magnet coils receive a similar radiation dose @ 10 times higher integrated luminosity!!!!!  Shielding!
Requires larger aperture!
LHC: 70mm  HL-LHC: 150mm diameter
Tungsten blocks
Capillaries
US-LARP MQXF magnet design
Based on Nb3Sn
technology
Incompatible with Nb-Ti
 New, brittle superconductor!
 New magnet technology!
8T peak field at coils
Nb3Sn technology
@ 140 T/m
 12T field at coils!!!
@ 210 T/m
G. Apollinari - MOPL040
A. Milanese - WEPM060
[at the limit of Nb-Ti technology]
Longer magnets
Notes: 10

## Slide 8: New HL-LHC Triplet Lay-out:
CMS
ATLAS
Longer Triplet assembly implies longer distance over which the 2 LHC beams share the same path!
ca. 40 unwanted [parasitic] collision points
Crossing angle & Crab Cavities

## Slide 9: HL-LHC Technical Challenge 2: Crab Cavities
Geometric Luminosity Reduction Factor:
Challenging space constraints – 194mm separation between the 2 beams
 requires compact cavity design
Crab Cavities:
effective cross section
Full Crossing angle:
285mrad LHC TDR
329mrad in LHC op
500mrad HL TDR
DQW
RF-Dipole

## Slide 10: HL-LHC Challenge 3: Machine Efficiency
UA57
US57
UR55
UL57
UPR57
PC IT
PCs IT Trims
DFX
DSHX
DFHX
CDBs
PIC,BIS
QDS
CLIQ
Warm Diodes
DCM
Q1
Q2A
Q2B
Q3
CP
D1
OC PCs
D1 PC
Cold Diodes
OC EE
DSHM
D2 PC
D2 OC EE
Cold box
CDBs
DFM
DFHM
DQHDS
D2
Q4
Q5
Q6
Valve box
D2 OC PCs
Crab
Cavities
RF Powering
UW57
TAXN
Cooling and Ventilation
 Low radiation areas for electronics
Accessibility of equipment!
But up to 100m between PC and magnets!

## Slide 11: HL-LHC Technical Challenge 4: Superconducting Link based on HT MgB2 Superconductor
D2
DSHM
DFHM
Q1
Q2A
Q2B
Q3
CP
D1
DCM
DFM
DFX
DSHX
DFHX
Diam ca. 90mm
> 100kA @ 25K

## Slide 12: HL-LHC is a truly International Collaboration
Q1
Q2a
Q2b
Q3
D1
DFX
DFM
Connection to LHC (UL)
Service gallery (UR)
TAXS
Crab cavities
UA Gallery
Q4
TAXN
Service cavern
SC Links
D2
Collimators
CP
DFHX
DFHM
Notes: 17

## Slide 13: IR1 & IR5 Underground Civil Engineering: completed in 2022!
Most of the work was conducted during LS2  vibration impact
Transition to LHC tunnel
13
Work started at End Run1 during 2018
Construction Finished End 2022
Notes: 18

## Slide 14: Completion of the Surface Buildings in 2023
SF17
SHM17
SD17
SE17
SU17
Example Point 1
20th January 2023
Celebration Ceremony: Point 5
Work Ended Spring 2023

## Slide 15: Status of the HL-LHC Triplet Magnets
IPAC 2023, Venice May 9th 2023 Oliver Brüning
Notes: Centre piece

## Slide 16
Cryostated Assembly LMQXFA-01
Magnet Pair Alignment
Heat Exchanger Installation
Shell Longitudinal Seam Welding
Cryostated Assembly @ FNAL
  First AUP horizontal test: LQXFA01 reached nominal +300A @1.9K & @4.5K last weekend!
   tests are ongoing
Update on MQXFA – Q1 & Q3: Cryo-Module Assembly in the USA
May 2022: Endurance Test on MQXFA05: 50 quenches, 5 TC  magnet remains @ nominal! ✓
7 magnets constructed and validated  Started Coldmass construction [2 / Coldmass]! ✓
G. Apollinari - MOPL040

## Slide 17
Update on MQXFB – Q2: Cryo-Module Assembly at CERN
  MQXFBP3 test at CERN  nominal +300A @ 1.9K and TC ✓
  MQXFB02 test at CERN  nominal +300A @ 1.9K and TC ✓
P3 and MQXFB02 satisfy the CERN acceptance criteria ✓
Limitation @ 4.5K, but Temperature margins compatible with ultimate operation energy:
P3 & 02 reached nominal +300A @ 1.9K,
P3 and 02 went through
3 TC
without degradation!
On Track for Series Production of Nb3Sn
HL-LHC Triplet Quadrupole Magnets!
[Both tests conducted in temporary cryostat]
A. Milanese - WEPM060

## Slide 18: Status of the Superconducting Link
D2
DSHM
DFHM
Q1
Q2A
Q2B
Q3
CP
D1
DCM
DFM
DFX
DSHX
DFHX
Successfully Demonstrated
Concept between 2020 / 22
with > 120kA @ 30K
Cable production complete
Assembly of the first complete
system incl. flexible cryostats
is ongoing
International Collaboration for the Feedboxes: with UK Southampton and Sweden Uppsala University
Demo-3 in SM18
Diam ca. 90mm
> 100kA @ 25K

## Slide 19: Status Crab Cavities
DQW Crab Cavity Prototype Cryostat in the SPS
DQW Cavity – RI pre-series
Beam measurement in the SPS of the bunch deflection
RF-Dipole
2-Cavity
String
assembly
and
Cryostat
assembly
RF-Dipole Cavity – US & Canada

## Slide 20
HL-LHC IT STRING a reproduction of HL-LHC P5L
P5
P5L
P5R
SPS
HL-LHC
P1
P2
P3
P4
P5
P6
P7
P8

Notes: 23

## Slide 21: HL-LHC IT STRING in a surface building @ SM18
STRING area
Magnet test cryostats
Cryogenic infrastructure
RF test zone
Horizontal benches for cryomagnets
SC link system test bench

## Slide 22
On top of the empty metallic structure
IT-String Status in pictures
Under the metallic structure
PC and Energy Extraction racks installed on the metallic structure
Cryo Distribution
June 2024
Sept 2024
Aug 2025
Jan 2026

## Slide 23
MQXFB02
D1
proto
Repaired
MB Dipole
CP
MQXFBP3
Summary:
Nb3Sn Technology validated
Superconducting Link demonstrated
Crab Cavity Operation and Production demonstrated
Civil Engineering Work Completed
1st Part of Collimation Upgrade completed
The project is on Track for installation
during LS3 starting in 2026
Stay Tuned for completion of the IT-String installation in 2023/24 and operation in 2025!
Some HL-LHC related contributions at this conference:
Project management: WEPM124; TUPA154; TUPA155
Configuration: MOPL001; MOPL034; WEPL102; WEPA091
Triplet Magnets: MOPL040; WEPM057; WEPM060;
Crab Cavities & RF: WEPA149; WEPL119; TUPA160;
Collimation, Beam Dump and Machine Protection:
MOPL017; MOPL036; MOPA126; MOPL022; MOPA101; MOPL023; MOPA100; MOPL036; WEPM058; WEPM109; WEPA022; WEPA148; TUPM122
All magnet productions on good track!


## Slide 24: Status Collimation
New Dispersion Suppressor Collimators for Pb+82 operation installed @ ALICE
The ALICE HL-LHC running period started in Run3 – thanks to the LIU upgrade
HL-LHC will almost double the proton current [ca. 1A] – thanks to the LIU upgrade
HL-LHC features new, low impedance collimators  ca ½ already installed for Run3!
HL-LHC features new, physics debris collimators next to the experiments
 In preparation for installation during LS3
HL-LHC features crystal collimators for Pb ion beam cleaning; ready for Run3!
S. Redaelli - MOPL017
LIU: M. Meddahi - MOXD1

## Slide 25: Thank you for your attention

## Slide 26
Significant Progress on many fronts!

## Slide 27: Summary
IPAC 2023, Venice May 9th 2023 Oliver Brüning
Nb3Sn Technology validated
Superconducting Link demonstrated
Crab Cavity Operation and Production demonstrated
Civil Engineering Work Completed
1st Part of Collimation Upgrade completed
The project is on Track for installation
during LS3 starting in 2026
Stay Tuned for completion of the IT-String installation in 2023/24 and operation in 2025!
Some HL-LHC related contributions at this conference:
Project management: WEPM124; TUPA154; TUPA155
Configuration: MOPL001; MOPL034; WEPL102; WEPA091
Triplet Magnets: MOPL040; WEPM057; WEPM060;
Crab Cavities & RF: WEPA149; WEPL119; TUPA160;
Collimation, Beam Dump and Machine Protection:
MOPL017; MOPL036; MOPA126; MOPL022; MOPA101; MOPL023; MOPA100; MOPL036; WEPM058; WEPM109; WEPA022; WEPA148; TUPM122
All magnet production on good track!

## Slide 28
Technology
Landmarks
Separation / Recombination
dipole magnets: D1 & D2
Non-Linear Corrector magnets
Hollow Electron Lens installation delayed until after LS3  no longer part of the HL-LHC baseline

## Slide 29
LHC (Large Hadron Collider): Magnet Technology
A 27 km circumference collider…
The LHC dipole magnets mark the
culmination of 30 years of superconducting
NbTi magnet technology development!
29
 Requiring 1.9K [-271 degrees Celsius] operating temperature
1983 1991 2000 2010

## Slide 30: SC Magnet Technology
source:
D. C. Larbalestier @ Researchgate
30
Nb3Sn
HL-LHC with 11-12T
16 T for HEP?
Almost a commodity!
  15-20 t per year for MRI
  ITER needs 500 t
ca 5 times cost of LHC Nb-Ti
Brittle material
HTS (needed  20 T)
 on going R&D!
Bi-2212: cost today 2-5 x Nb3Sn
YBCO: cost today 10 x Nb3Sn
More SC
for the
same field
 Cost!

## Slide 31
Luminosity optimization:
Luminosity Levelling at the luminosity frontier:
To cope with the total number of events per time interval and the
event pileup in the detector
 Design for highest possible virtual luminosity, but keep the luminosity artificially lower during operation!!
Lifetime proportional to total particles:
 Maximize the number of particles in the storage ring and the number of bunches!
 Stored Beam Power in the LHC!
All levelling methods have been successfully demonstrated in
Machine Studies in the LHC!!!
31
 Injector Complex Upgrade - LIU

## Slide 32: The LHC is NOT a Standalone Machine
The LHC performance fully relies on the performance of its injector complex
By itself one of the largest accelerator facility in the world with its own diverse and, for many aspects, unique physics program
LHC : 2x(0.45 – 7) TeV
SPS : 26 – 450 GeV
PS : 2 - 26 GeV
PSB : 0.16 -2 GeV
Linac 4: 0-160 MeV H-
LHC : 2x(0.45 – 7) TeV
SPS : 26 – 450 GeV
PS : 1.4 - 26 GeV
PSB : 0.05 -1.4 GeV
Linac 2: 0-50 MeV
LHC Injector Upgrade Project
Installation finished in LS2
 Now being commissioned!
Notes: Maybe skip?

## Slide 33: Machine Efficiency
Chart: LHC Cycle
| 0 | 10 | 20 | 37 | 40 | 50 | 60 | 70
Energy | 6500 | 6500 | 50 | 50 | 450 | 450 | 6500 | 6500
Minimum of 2h between end of one, and start of the next fill
Average LHC Turnaround time of 4-5h!!!!
Average LHC fill length of 8h  65% of scheduled physics time!!!
ca. 50% in LHC operation including faults at best conditions!
33
This becomes more challenging with increased Collider size and Requires even more powerful injector complex!!!!

## Slide 34
10 GJoule  flying 700 km/h
Energy management challenges: Example LHC
Energy stored in the LHC magnet system [8.3T]: 10 GJoule
Energy stored in the two beams: 720 MJ [ 6 1014 protons (1 ng of H+) at 7 TeV ]
700 MJ melt one ton of copper
700 MJoule dissipated in 88 ms
 8 TW
Installed World Electrical Capacity:
3.8 TW
560 tons
10 GJoule  55 km/h
88’000 tons
Beam Dump robustness [core and windows]
Kicker reliability  many kicker elements
 Failure likelihood & reliability
Sectorization!!
Tracking
[ppm]!!!
1 electron volt = 1,602× 10-19 joule
Worry about beam losses:
Failure Scenarios  Local beam Impact
 Equipment damage
Lifetime & Loss Spikes  Distributed losses
 Magnet Quench & QPS
 Machine efficiency
e.g. Cryo Sectors: 95% availability requires 99% with 8 sectors
8 Sectors  [12 Sectors  20 Sectors]
Notes: 34
Aircraft carrier

## Slide 35
Nb3Sn quadrupole: Transition from Prototype to Series production
Second short (1.5 m) under preparation for test at CERN
Insertion of coil package inside mechanical structure of the first IT quad prototypes (4.2 m long) in LBNL-USA
35

## Slide 36: Crossing Angle & Parasitic Collisions
Parasitic bunch encounters:
non-linear fields from long-range beam-beam interaction:
 Operation requires crossing angle
efficient operation requires large beam separation at unwanted collision points  Separation of 10 -12 s  large triplet apertures for HL-LHC!!
Insertion Layout:
ca.130m  150m
ca.50m
Operation with ca. 2800 bunches @ 25ns spacing  approximately 50 unwanted collision per
Interaction Region (IR).

## Slide 37: HL-LHC cavity designs
RF Dipole: Waveguide or
waveguide-coax couplers
Double ¼-wave: Coaxial couplers with
hook-type antenna
2 Designs with
Different Coupler concepts and
Deflection planes
Present baseline: 4 cavities / IP / side  16 total
DQW crab-cavity
Cryomodule for
SPS tests

## Slide 38
Crab cavity cryo-module for installation in the SPS
38