## Slide 1
RFQ2 Update
L. Millar, A. Grudiev
CERN, SY-RF-MKS Section
26/05/2023

## Slide 2: Recap
Q factor of the first RFQ was 6772, The Q factor of the new RFQ (RFQ2) seems to be ~5200.
Last time we agreed to:
Look inside the cavity with a borescope.
Measure Q0 vs tuner position (simulate and compare with measurement).
Investigate how individual tuners affect Q while forming the matrix which will be used for tuning (in progress) .

## Slide 3: 1: Borescope Investigation

## Slide 4: Borescope Investigation
Inspection performed on 25/05/2023, photos and videos not included in this presentation. To summarise, no obvious problems were visible.

## Slide 5: 2: Q0 vs Tuner Position (with simulation results)

## Slide 6: A Reminder..
Two quadrupole modes measured:
Mode 1 (operating mode)
Mode 2

## Slide 7: Mode 2
CST
Measurement
Note: Absolute values shown in simulation, simulation setup is not entirely identical to the measurement setup.

## Slide 8: Mode 2
Absolute Q0 values are different.
Reasonable tracking of normalised Q and frequency.

## Slide 9: Mode 1
CST
Measurement
Note: Absolute values shown in simulation, simulation setup is not entirely identical to the measurement setup.

## Slide 10: Mode 1
Relative losses higher at full insertion (when field is concentrated around central module).

## Slide 11: Mode 1
More lossy when field is concentrated in central module.

## Slide 12: 3: Effect of Individual Tuners

## Slide 13: Effect of Individual Tuners
Idea is to measure how individual tuners affect Q0:
Field and surface current change as tuners are moved. By measuring Q0 we can “localise” losses to an extent.
Can use this data to form the matrix we need for tuning. This needs to be done anyway, no time lost!