## Slide 1: Update on Task 3.2 Concept of a SC solenoid
Michal Duda (PSI)
1/06/2023

## Slide 2
Experimental setup
HTS solenoid assembly
Warm wide bore through tube
Vacuum chamber
Thermal shielding
Cryo coolers
Electrical and thermal Leads
Thermal lead buffers
Support structure
Ground support frame
Backbone frame for vacuum chamber
HTS solenoid for P3 experiment
Lead shield and gate valve
Mineral girder
DN63CF wide bore flange
DN160CF bellow

## Slide 3: Specification Requirements
DN40CF gate valve
Lead shield
DN40CF bellow
Shielding
Chamber
Needs of fine adjustment
of vacuum chamber
144 mm

## Slide 4: Support Structures
Weight of chamber assembly ~ 1 Ton
Force between NC and SC solenoids 30 kN
Welded frames from ▢80 / D6 and ▢100 / D8 stainless steel tubes
Solenoid support directly in contact with backbone plate
Earthquake and deviation analysis
Girder brackets (D10)
Sub mm adjustment
Vertical / horizontal
Tilt
1200 mm
Remachined support plates for precise repositioning
Crane hooks

## Slide 5: P3 Main Assembly
Air side cabling and leads
Water cooler with 50W heater
A = 3 * 300mm2 J = 1.3A/mm2 @ I = 1.17kA
G10 separator
Thermal shielding case EN AW-1050 and 3 x 10 layer MLI
7 G10 support pillars
Supports only Al shield D2 and MLI (7kg)
Remachined vacuum chamber
Cryo cooler 1
Leads
Thermal shield
Thermal lead buffers
Warm wide bore through pipe
Cryo cooler 2
Coil assembly
Right buffer

## Slide 6: Vacuum Chamber Remachined
Two DN63CF
Ports for
vacuum
gauges
DN160ISO-K ports for
cryo cooler 2
Remachined vacuum chamber
D25 welded stainless steel chamber
Front rim remachined after welding
O-ring sealed
24x M6 holes
for coil support pillars
with alignment pockets
7x M8 holes
for thermal Al
Shield mount
DN160ISO-K ports for
cryo cooler 1
Spare
DN63CF port
DN100CF port
for leads
DN100CF port
for electrical
feedthrough
instrumentation
DN100CF port
for vacuum
pumps
Spare
DN100CF port
DN160CF upstream port
4 benchmarks
for metrology

## Slide 7: Solenoid Access Bore
DN160CF
Bellow
one side rotatable
W target insertion
upstream side
DN63CF-R
wide bore
upstream
flange
O-ring sealed
retention groove
DN40CF-R
wide bore
downstream
flange

## Slide 8: Thermal Lead Buffers: Casting
Melting Pb (119kg) directly in SS cage
Support structure for Cu braids (allow for some excess length)
Cu braids with solder stop
Submerge Cu braids
Pits (H25) around braids for better flexibility
To cryo cooler cold head
To coil pack terminal
Right thermal lead buffer
Left thermal lead buffer
4 integrated crane hooks

## Slide 9: Assembly
Assembly of
Coil pack supports
Shield supports
Thermal shield (with MLI, not shown)
Coil pack
in horizontal position.
Assembly of
Cryo coolers
Flex cables, HTS leads
Supports for lead buffers
Coil pack
in vertical position.