## Slide 1: FCC-ee Machine detector interface Alignment STUDIES
Léonard WATRELOT
PhD student, CERN BE-GM-HPA section, SMI, CNAM (Conservatoire National des Arts et Métiers)
Mark JONES (CERN), Mateusz SOSIN (CERN) and Stéphane DURAND (GeF, CNAM)
Many thanks to :
Manuela Boscolo, Francesco Fransesini, Michael Koratzinos, Hélène Mainaud Durand, Mika Masuzawa, Luigi Pellegrino and Vivien Rude
02/06/2023, BE-Seminar
Notes: Sources :

## Slide 2: Table of content
1
Léonard WATRELOT, PhD student, BE-GM-HPA
The FCC-ee MDI design
Challenges to face
Alignment strategy proposition
External alignment system
Internal alignment system
Full system implementation
Prototype testing
Discussion
02/06/2023, BE-Seminar
Image: CERN
Notes: Sources :

## Slide 3
2
Léonard WATRELOT, PhD student, BE-GM-HPA
The FCC-ee Machine Detector Interface (MDI) design
Crab waist configuration (big crossing angle and small L*) => accelerator components inside the detector
Still a extremely early design which continues evolving
Compensation solenoid
Screening solenoid
Skeleton
LumiCal
Beam pipe
QC1R1e
QC1R1p
QC1R2e
QC1R2p
QC1R3e
QC1R3p
IP
Compensation solenoid support
Screening solenoid support
02/06/2023, BE-Seminar
Design by M. Koratzinos
Design similar to :

## Slide 4
3
Léonard WATRELOT, PhD student, BE-GM-HPA
“Status and plans for optics corrections and emittance performance”,Tessa Charles, Bernhard Holzer, Katsunobu Oide, Frank Zimermann
and the FCC-ee optics team, FCC-week 2021
Why do we need a precise alignment in the FCC-ee interaction region ?
Maximise performance in terms of integrated luminosity
Maintain the related background at a tolerable level for the experiments (includes minimizing synchrotron radiation)
Minimize emittance blow-up
02/06/2022, FCC-week 2022
FCC-ee layout, FCC-ee CDR

## Slide 5
4
Léonard WATRELOT, PhD student, BE-GM-HPA
FCC-ee CDR
Continuous alignment
Continuous alignment
Why does it need to be more precise than in the rest of the machine ?
Maintain the related background at a tolerable level for the experiments (includes minimizing synchrotron radiation)
“Hole” in the machine => “hole” in the alignment -> align both side precisely so they collide
“Antennas” in which the alignment depends only on measurements along the line
No stable point or reference at the extremity
02/06/2023, BE-Seminar

## Slide 6
Maintain the related background at a tolerable level for the experiments (includes minimizing synchrotron radiation)
“Hole” in the machine => “hole” in the alignment -> align both side precisely so they collide
Minimal beam size in the entire ring + collide as precisely as possible near the center of the experiment
5
Léonard WATRELOT, PhD student, BE-GM-HPA
Z
WW
ZH
tt
FCC-ee CDR
FCC-ee CDR
Why does it need to be more precise than in the rest of the machine ?
02/06/2023, BE-Seminar

## Slide 7: Why is this alignment difficult to do ?
6
Léonard WATRELOT, PhD student, BE-GM-HPA
Design (lot of components to measure, layered design, very little space, design not definitive)
Design by M. Koratzinos
FCC-ee QC1
02/06/2023, BE-Seminar

## Slide 8: Why is this alignment difficult to do ?
7
Léonard WATRELOT, PhD student, BE-GM-HPA
Design (lot of components to measure, layered design, very little space, design not definitive)
Conditions (cryogenic temperature, radiations, magnetic fields)
FCC-ee QC1
“Superconducting magnet system for SuperKEKB Interaction region”, Norihito Ohuchi, FCC workshop, 24/01/2017
Design by M. Koratzinos
02/06/2023, BE-Seminar

## Slide 9: Why is this alignment difficult to do ?
8
Léonard WATRELOT, PhD student, BE-GM-HPA
Design (lot of components to measure, layered design, very little space, design not definitive)
Conditions (cryogenic temperature, radiations, magnetic fields)
Requirements (very tight alignment requirement, especially on Final Focusing Quadrupoles, BPM, Screening and Compensation solenoids, and LumiCal)
Misalignment tolerances include all possible error sources such as: manufacturing errors, assembly errors, deformation both during/after installation and during operation, magnetic field measurements, metrology measurement, reference network and alignment measurement, anticipated degradation in the alignment over time as a function of ground motion and other effects.
Experience from previous accelerator projects indicates that a reasonable assumption for the relative radial alignment precision can be derived by applying a factor 1/3.
Alignment tolerance at 30 µm => alignment precision required <10 µm
FFQ : Alignment tolerance at 30 µm + Monitoring
Screening solenoid : Alignment tolerance at ~100 µm + Monitoring
Compensation solenoid : Alignment tolerance at ~100 µm + Monitoring
LumiCal
Alignment tolerance at 50 µm
w.r.t. the IP (longitudinal)
+ Monitoring
02/06/2023, BE-Seminar

## Slide 10
9
Léonard WATRELOT, PhD student, BE-GM-HPA
Hasn’t it been done in the past ? Is there any similar MDI ?
s
SuperKEKB/Belle II MDI
N. Ohuchi, “Final-Focus Superconducting Magnets for SuperKEKB”, IPAC 18, 01/05/2018
L. PELLEGRINO, MDI mechanical design, integration and assembly at DAFNE/KLOE with the crab-waist configuration, 3rd FCC-ee MDI workshop, 9-20 September 2019, CERN.
DAFNE/KLOE MDI
CLIC Machine Detector Interface, MDI mini workshop, HKUST IAS, Philip Burrows on behalf of Lau Gatignon, 2020
Marcel Stanitzki, The SiD Detector – Machine Backgrounds, 01/2020, Hong Kong
CLIC
ILC
02/06/2023, BE-Seminar

## Slide 11
10
Léonard WATRELOT, PhD student, BE-GM-HPA
Can existing sensors do the job ?
HIE-ISOLDE alignment and system, technical design and project status, J.-C. Gayde, 2012.
BCAM, Open Source Instrument
Hydrostatic Leveling System (HLS)
Wire Positioning Sensor (WPS)
Gayde, J-Ch, and Kamugasa, S., "Evaluation of Frequency Scanning Interferometer Performances for Surveying, Alignment and Monitoring of Physics Instrumentation." (2018): WEPAF069.
M. Sosin, A. Herty, J. Rutkowski on behalf of GM-HPA Team
WP15.4 Sensor review, 2021.07.06
02/06/2023, BE-Seminar

## Slide 12
10
Léonard WATRELOT, PhD student, BE-GM-HPA
Can existing sensors do the job ?
HIE-ISOLDE alignment and system, technical design and project status, J.-C. Gayde, 2012.
BCAM, Open Source Instrument
Hydrostatic Leveling System (HLS)
Wire Positioning Sensor (WPS)
Gayde, J-Ch, and Kamugasa, S., "Evaluation of Frequency Scanning Interferometer Performances for Surveying, Alignment and Monitoring of Physics Instrumentation." (2018): WEPAF069.
M. Sosin, A. Herty, J. Rutkowski on behalf of GM-HPA Team
WP15.4 Sensor review, 2021.07.06
Radiations
02/06/2023, BE-Seminar

## Slide 13
10
Léonard WATRELOT, PhD student, BE-GM-HPA
Can existing sensors do the job ?
HIE-ISOLDE alignment and system, technical design and project status, J.-C. Gayde, 2012.
BCAM, Open Source Instrument
Hydrostatic Leveling System (HLS)
Wire Positioning Sensor (WPS)
Gayde, J-Ch, and Kamugasa, S., "Evaluation of Frequency Scanning Interferometer Performances for Surveying, Alignment and Monitoring of Physics Instrumentation." (2018): WEPAF069.
M. Sosin, A. Herty, J. Rutkowski on behalf of GM-HPA Team
WP15.4 Sensor review, 2021.07.06
Radiations
Infrastructure required
02/06/2023, BE-Seminar

## Slide 14
10
Léonard WATRELOT, PhD student, BE-GM-HPA
Can existing sensors do the job ?
HIE-ISOLDE alignment and system, technical design and project status, J.-C. Gayde, 2012.
BCAM, Open Source Instrument
Hydrostatic Leveling System (HLS)
Wire Positioning Sensor (WPS)
Gayde, J-Ch, and Kamugasa, S., "Evaluation of Frequency Scanning Interferometer Performances for Surveying, Alignment and Monitoring of Physics Instrumentation." (2018): WEPAF069.
M. Sosin, A. Herty, J. Rutkowski on behalf of GM-HPA Team
WP15.4 Sensor review, 2021.07.06
Infrastructure required
Radiations
Early design
02/06/2023, BE-Seminar

## Slide 15
10
Léonard WATRELOT, PhD student, BE-GM-HPA
Can existing sensors do the job ?
HIE-ISOLDE alignment and system, technical design and project status, J.-C. Gayde, 2012.
BCAM, Open Source Instrument
Hydrostatic Leveling System (HLS)
Wire Positioning Sensor (WPS)
Gayde, J-Ch, and Kamugasa, S., "Evaluation of Frequency Scanning Interferometer Performances for Surveying, Alignment and Monitoring of Physics Instrumentation." (2018): WEPAF069.
M. Sosin, A. Herty, J. Rutkowski on behalf of GM-HPA Team
WP15.4 Sensor review, 2021.07.06
Infrastructure required
Radiations
Early design
Other sensor technology share the same limitations (inductive, ultrasonic …)
Underlined by the absence of solutions from the CLIC and ILC projects
02/06/2023, BE-Seminar

## Slide 16
11
Léonard WATRELOT, PhD student, BE-GM-HPA
Proposition of a strategy for the alignment and monitoring of the MDI
Goals :
Monitor an interface at the end of QC1 to retrieve the position of internal component (monitored thanks to the internal monitoring system).
Monitor the alignment between QC1 and QC2.
Monitor the alignment between the inner components and the experiment solenoid.
Monitor the alignment between the two sides of the experiment.
Alignment and monitoring system composed of :
  External alignment system
  Internal alignment system
QC1L
QC1R
QC2L
QC2R
FCC-ee QC1
Design by M. Koratzinos
02/06/2023, BE-Seminar

## Slide 17
12
Léonard WATRELOT, PhD student, BE-GM-HPA
Optimal network : too much measurements, some (plenty) wont be possible.
Any update on the design would be much welcomed.
External alignment and monitoring system
Permanent network of interferometric distance measurements based on Frequency Scanning Interferometry (FSI).
Goals :
Monitoring of the interface at the end of QC1
Monitor the alignment between QC1 and QC2.
Monitor the alignment between the inner components and the experiment solenoid.
Monitor the alignment between the two sides of the experiment.
02/06/2023, BE-Seminar

## Slide 18
13
Léonard WATRELOT, PhD student, BE-GM-HPA
Goal : monitor the deformation extremely precisely over the length of the assembly
Create a network of points accurate enough so another system can measure from it onto the inner components
Seems not possible to cross or put a hole here for the monitoring system (and numerous holes would be required)
Internal alignment system
Interface
02/06/2023, BE-Seminar

## Slide 19
13
Léonard WATRELOT, PhD student, BE-GM-HPA
Goal : monitor the deformation extremely precisely over the length of the assembly
Create a network of points accurate enough so another system can measure from it onto the inner components
Seems not possible to cross or put a hole here for the monitoring system (and numerous holes would be required)
So we need to take the long way from the extremity and create a stable reference
Internal alignment system
Interface
02/06/2023, BE-Seminar

## Slide 20
13
Léonard WATRELOT, PhD student, BE-GM-HPA
Goal : monitor the deformation extremely precisely over the length of the assembly
Create a network of points accurate enough so another system can measure from it onto the inner components
Seems not possible to cross or put a hole here for the monitoring system (and numerous holes would be required)
Once we have a well monitored network, we can measure the objects inside
So we need to take the long way from the extremity and create a stable reference
Internal alignment system
Interface
02/06/2023, BE-Seminar

## Slide 21
14
Léonard WATRELOT, PhD student, BE-GM-HPA
Internal alignment system
Design by M. Koratzinos
  Deformation models
Cylinder of which the deformation is well known and from which we will measure the inner components
Measurement on the inner components
Goal : monitor the deformation extremely precisely ove the length of the assembly
Create a network of points accurate enough so another system can measure from it onto the inner components
Deformation monitoring system + distance measurement system
Measurement system waiting for design update.
02/06/2023, BE-Seminar

## Slide 22
15
Léonard WATRELOT, PhD student, BE-GM-HPA
Deformation monitoring
Optical fiber placed in a helix shape, separated in portion by semi-reflective mirrors, which can be simultaneously and independently measured
Helixes defined by their length, radius, step, number and position of portions
Two technology available for such measurements :
  SOFO (Surveillance d’Ouvrage par Fibre Optique) (locked at a prototype state)
  In-line multiplexed and distributed FSI measurement (in development at CERN)
https://iopscience.iop.org/article/10.1088/1361-6501/acc6e3
02/06/2023, BE-Seminar

## Slide 23
16
Léonard WATRELOT, PhD student, BE-GM-HPA
Deformation monitoring
https://iopscience.iop.org/article/10.1088/1361-6501/acc6e3
Ø
Ø
02/06/2023, BE-Seminar

## Slide 24
17
Léonard WATRELOT, PhD student, BE-GM-HPA
Deformation monitoring
https://iopscience.iop.org/article/10.1088/1361-6501/acc6e3
Ø
Ø
02/06/2023, BE-Seminar

## Slide 25
18
Léonard WATRELOT, PhD student, BE-GM-HPA
+ equation of portion length as function of the deformation polynomials
Least square adjustment
Helixes observations
(= 3D lengths of portions)
Cylinder deformations
Deformation monitoring
https://iopscience.iop.org/article/10.1088/1361-6501/acc6e3
Simulations shown micrometric accuracy
To be confirmed by a prototype
02/06/2023, BE-Seminar

## Slide 26
19
Léonard WATRELOT, PhD student, BE-GM-HPA
Full alignment and monitoring system
Simulations shown micrometric accuracy for the alignment between final focusing quadrupoles on both sides.
To be refined with upcoming updates of the detector design.
02/06/2023, BE-Seminar

## Slide 27
C
B
A
D
20
Léonard WATRELOT, PhD student, BE-GM-HPA
Prototype testing
A
B
C
02/06/2023, BE-Seminar
Deformation test

## Slide 28
21
Léonard WATRELOT, PhD student, BE-GM-HPA
Alignment strategy proposal
- Layout of the alignment system in one muon spectrometer endcap.
- Use of optical alignment systems.
- Relative alignment of the detector parts up to bellow 100µm
Aefsky, S., et al. "The optical alignment system of the ATLAS muon spectrometer endcaps." Journal of Instrumentation 3.11 (2008): P11005.
- Layout of the alignment system in the silicon detector modules in the ATLAS SemiConductor Tracker.
- Use of Frequency Scanning Interferometry.
- Relative alignment of the detector parts up to bellow 50µm
Gibson, S. M., et al. "Monitoring the heart of ATLAS using Frequency Scanning Interferometry." Proceedings of the Eighth International Workshop on Accelerator Alignment, CERN, Geneva. 2004.
Thanks to the detectors it is possible to measure the position of the IP and/or the position of the beam (relatively accurately with respect to the detector part)
This could be linked with the alignment system installed on the accelerator, allowing to link the position of the IP, the LumiCals and the FFQ.
Would be a win-win to link with relative measurement the machine and the detector (especially for the dense FCC-ee MDI).
The MDI alignment system could be seen as a standalone backbone, on which sub-system alignment systems could connect.
02/06/2023, BE-Seminar

## Slide 29
22
Léonard WATRELOT, PhD student, BE-GM-HPA
Re-adjustment system
Interest of having a system able to move one or multiple element without requiring to disassemble the entire QC1 ?
Not necessary to be accurate at 10 μm, a system able to correct major displacements ~0.2 mm to 1mm (due to transport, gravity deformation, movement during cool down, intense magnetic fields …) would be already extremely convenient.
Not necessary to work at cryogenic temperatures only at room temperature would be already extremely convenient.
Not necessary to be able to work during the run of the machine, during shut downs would be already extremely convenient.
Universal Alignment Platform Tests, Kacper Widuch, Vivien Rude BE-GM-HPA 2021-03-11
A lot of possibilities are open, from the system working only at warm temperature allowing a re-adjustment to the 0,1mm level of major components at the end of shut downs, to the system able to realign in real time and during the run of the machine the cold components to the micrometer level.
Systems to work in these conditions exist, the difficulty is to quantify their advantage compared to a loss of luminosity due to any misquantified misalignment value or to the need to dismount, disassemble, realign, reassemble and remount the assembly.
Larchevêque, C., et al. "The Euclid VIS read-out shutter unit: a low disturbance mechanism at cryogenic temperature." arXiv preprint arXiv:1801.07496 (2018).
The EUCLID VIS Read-out Shutter Unit, which will operate in space (very similar to conditions inside the MDI)
02/06/2023, BE-Seminar

## Slide 30
23
Léonard WATRELOT, PhD student, BE-GM-HPA
Conclusion
Listing of the challenges in the FCC-ee MDI
Study of existing systems in similar MDI
Study of existing sensors
Proposition for a new system
  External alignment system
  Internal alignment system
Simulations
Prototype testing
Discussion
02/06/2023, BE-Seminar

## Slide 31: Thank you for your attention
Léonard WATRELOT, PhD student, BE-GM-HPA
24
02/06/2023, BE-Seminar
Notes: Sources :

## Slide 32: Spares
Léonard WATRELOT, PhD student, BE-GM-HPA
25
02/06/2023, BE-Seminar
Notes: Sources :

## Slide 33
26
Léonard WATRELOT, PhD student, BE-GM-HPA
Coordinate system definition
Deformations are defined in the (O, 𝑂𝑥, 𝑂𝑦, 𝑂𝑧) Euclidean system linked to the interface plate, shown in Figure 11. The origin of this system is the centre of the plate, the 𝑂𝑥 is perpendicular to the plate (and ideally is the bisector of the crossing angle between the two beams), 𝑂𝑦 is the intersection of the plane of the plate and the plane formed by the incoming and outgoing beams and 𝑂𝑧 is the last vector in order to form an oriented orthogonal system.
x
y
z
02/06/2023, BE-Seminar

## Slide 34
27
Léonard WATRELOT, PhD student, BE-GM-HPA
Deformation model
Polynomial (classic model, easy to manipulate)
6 polynomial of degree 4
  Elongation
  Radial deformation (horizontal)
  Radial deformation (vertical)
  Torsion
  Radius deformation (horizontal)
  Radius deformation (vertical)
02/06/2023, BE-Seminar

## Slide 35
Léonard WATRELOT, PhD student, BE-GM-HPA
Advantages :
- Usual distance measurement
- Rather simple equations
Disadvantages :
- Takes a lot a space in the cryostat
Rather difficult to implement
Lot of R&D required
Gayde, J-Ch, and Kamugasa, S., "Evaluation of Frequency Scanning Interferometer Performances for Surveying, Alignment and Monitoring of Physics Instrumentation." (2018): WEPAF069.
Deformation monitoring : distance measurements
It has been put aside for now as it is less realistic than the other system and easier to come back on if needed (simpler equations)
28
02/06/2023, BE-Seminar

## Slide 36
29
Léonard WATRELOT, PhD student, BE-GM-HPA
Additional implementation : multiple helixes and realistic intersection
X
Automatic position determination of the retroreflectors along the fibers, in order to have different lengths and a homogeneous coverage along the cylinder length.
Automatic intersection computation and automatic modification of the radius for helixes going above another one.
02/06/2023, BE-Seminar

## Slide 37
30
Léonard WATRELOT, PhD student, BE-GM-HPA
Known precision requirements for the inner components
Drawing by Mike Koratzinos
“Internal misalignment should be better than 30µm”
“Final Focusing quads misalignment (QC1_1-QC1_3 and QC2_1-QC2_2) (if not respected, beams do not collide):
  Geodesy : transverse shift of FF quads with sigma xy= 25µm
  vibrations : transverse shift of FF quads with sigma xy= 0.1µm
IR BPM misalignment (if not respected, beams do not collide) :
  geodesy : transverse shift of BPM with sigma xy= 25µm
  vibrations : errors of BPM reading with sigma xy= 0.1µm”
“Measurement of the component's position inside the detector is needed”
“ The distance between the two calorimeters has to be measured to 110 µm”
“Distance LumiCal/ nominal IP to be controlled/ measured to ~50µm level”
“Alignment accuracy of SC magnets = 100µm”
“For a 1mrad tilt of the detector solenoid (wrt the rest of the system – beam, screening and compensation solenoid) the corresponding uncorrected distortion is unacceptably large.”
“IR quadrupoles and sextupoles (75µm in radial and longitudinal, 100µrad roll), BPM (40µm in radial and 100µrad for the roll relative to quadrupole placement).”
02/06/2023, BE-Seminar

## Slide 38: DAΦNE/KLOE MDI
31
Léonard WATRELOT, PhD student, BE-GM-HPA
Alignment (strongly summarized)
1. Alignment of the elements on the girder (part of the cylinder) thanks to a laser tracker.
2. Installation of the cylinder inside the experiment, and re-alignment of the articulated cylinder thanks to laser tracker target supports and screws.
3. Occasional partial check, can’t be regular because of obstacles on the lines of sight of the laser tracker targets (cables, pipes …)
Luigi Pellegrino and Giancarlo Sensolini
L. PELLEGRINO, MDI mechanical design, integration and assembly at DAFNE/KLOE with the crab-waist configuration, 3rd FCC-ee MDI workshop, 9-20 September 2019, CERN.
L* = 0.3 m
= 50 mrad
Beam size :
= 250 µm
= 3.1 µm
= 15 mm
Alignment aim :
~ 100 µm
03/02/2020, Technology for Nanobeam Workshop

## Slide 39: SuperKEKB/Belle II MDI
L* = 0.76 m LER
= 83 mrad
Beam size :
= 10.1 µm
= 0.048 µm
= 5 mm
Alignment aim :
~ 100 µm
32
Léonard WATRELOT, PhD student, BE-GM-HPA
Alignment (strongly summarized)
Many thanks to Mika Masuzawa for all the information on SuperKEKB alignment.
Pre-alignment of the components before installing them in the cryostat, fiducialization.
Alignment of the cryostat (QCS) with respect to the beam line.
3. Installation of the cryostats inside the experiment.
4. Check of the position of the inner magnets thanks to the Single Stretched Wire (SSW) method coupled with capacitive measurement between the cryostat and the experiment before the run of the machine.
L* = 1.22 m HER
= 83 mrad
Beam size :
= 10.7µm
= 0.062 µm
= 6 mm
Alignment aim :
~ 100 µm
Final correction on the beam thanks to corrector magnets.
Arimoto, Yasushi, et al. "Magnetic measurement with single stretched wire method on SuperKEKB final focus quadrupoles." IPAC'19, Melbourne, Australia, 19-24 May 2019
Arimoto, Yasushi, et al. "Magnetic measurement with single stretched wire method on SuperKEKB final focus quadrupoles." IPAC'19, Melbourne, Australia, 19-24 May 2019
N. Ohuchi, “Final-Focus Superconducting Magnets for SuperKEKB”, IPAC 18, 01/05/2018
03/02/2020, Technology for Nanobeam Workshop

## Slide 40: LHC/ATLAS MDI
33
Léonard WATRELOT, PhD student, BE-GM-HPA
03/02/2020, Technology for Nanobeam Workshop
L* = 23 m
< 200 µrad
Beam size :
= 16.6 µm
= 16.6 µm
= 7.5 cm
Alignment (strongly summarized)
Hydrostatic Leveling System (HLS)
Wire Positioning Sensor (WPS)
Distance Offset Measurement Sensor (DOMS)
Remotely Controlable Actuators
L* = 23 m
= 285 µrad
Beam size :
= 16.7 µm
= 16.7 µm
= 75 mm
Alignment aim :
~ 100 µm
Summary of MDI challenges

## Slide 41: CLIC MDI
No solution found yet.
The problem has evolved throughout the years :
- Only one detector
- QD0 have been removed from the experiment
2 µm pre-alignment over 500m (L*=3,5m)
=> 10 µm pre-alignment over 500m (L*=3,5m)
=> 10 µm pre-alignment over 500m (L*=6,5m)
34
Léonard WATRELOT, PhD student, BE-GM-HPA
03/02/2020, Technology for Nanobeam Workshop
CLIC Machine Detector Interface, MDI mini workshop, HKUST IAS, Philip Burrows on behalf of Lau Gatignon, 2020
Proposed solution
QD0 sticks far in the detector and requires :
- stable support
- Power, cooling
- Antisolenoid
- Vacuum elements
- Access, connection disconnection
Attempt :
Monitoring QD0 thank to zerodur rods and optical alignment system inside the detector. But it was not shown to work.
L* = 3.5 m 500 GeV
= 20 mrad
Beam size :
= 0.202 µm
= 0.0023 µm
= 0.072 mm
Alignment aim :
~ 10 µm
L* = 3.5 m 3TeV
= 20 mrad
Beam size :
= 0.040 µm
= 0.001 µm
= 0.044 mm
Alignment aim :
~ 10 µm
Notes: Sources :

## Slide 42: ILC MDI
35
Léonard WATRELOT, PhD student, BE-GM-HPA
03/02/2020, Technology for Nanobeam Workshop
Introduction
Similar to the CLIC MDI :
- 2 detectors in push-pull configuration,
- 2 different L*, both < detector size
(And it is still the case)
- Alignment precision of 20 µm as requirement for QD0 prealignment system
L* = 3.5 m 250 GeV
= 14 mrad
Beam size :
= 0.516 µm
= 0.0077 µm
= 0.300 mm
Alignment aim :
~ 20 µm
L* = 3.5 m 500 GeV
= 14 mrad
Beam size :
= 0.474 µm
= 0.0059 µm
= 0.300 mm
Alignment aim :
~ 20 µm
Marcel Stanitzki, The SiD Detector – Machine Backgrounds, 01/2020, Hong Kong
Marcel Stanitzki, The SiD Detector – Machine Backgrounds, 01/2020, Hong Kong
Roman Poschl, (Selected) MDI Issues of ILD, MDI Workshop at IAS Conference, 01/2020, Hong Kong
Notes: Sources :
Beam size, crossing angle : Aihara, Hiroaki, et al. "the international linear collider. A global project." arXiv preprint arXiv:1901.09829 (2019).
L* : ILC TDR vol.4
Alignment : Mark Jones, Alignment in the MDI area : CLIC, ILC and HL-LHC solutions as case studies for FCC-ee, FCC-ee MDI workshop 13/09/2019

## Slide 43
36
Léonard WATRELOT, PhD student, BE-GM-HPA
Additional implementation
Helix installation error models
Punctual step error, but catches with theoretical position
Punctual step error implying a offset for the rest of the helix length
Variable step helixes
Ex : Smaller step as it goes forward inside the detector
Model implemented and working
Additional tests to be done (comparison between full variable step network, hybrid variable and fix step network, full fixed step network)
Easily seen in the least square adjustment residues (lot of redundancy)
Allow to choose where to have more dense or more precise measurements
14/06/2022, 2nd year CST presentation

## Slide 44
37
Léonard WATRELOT, PhD student, BE-GM-HPA
A prototype of the “in-fiber” FSI have been build and a testing bench assembled to test it.
First tests have been done and additional ones are ongoing.
Gluing
Soldering
Ready to measure
First testing
FSI “in-fiber” prototype and first tests
14/06/2022, 2nd year CST presentation

## Slide 45
38
Léonard WATRELOT, PhD student, BE-GM-HPA
C
B
A
D
FSI “in-fiber” prototype and first tests
A bench has been assembled
3 independent measuring portions + “regular” in-air measurement at the end
Verification thanks to regular FSI measurements
“Stability bench” made by gluing a fiber to an aluminium plate
14/06/2022, 2nd year CST presentation

## Slide 46
C
B
A
D
39
Léonard WATRELOT, PhD student, BE-GM-HPA
FSI “in-fiber” prototype and first tests
A
B
C
14/06/2022, 2nd year CST presentation

## Slide 47
C
B
A
D
40
Léonard WATRELOT, PhD student, BE-GM-HPA
FSI “in-fiber” prototype and first tests
A
B
C
Sag
14/06/2022, 2nd year CST presentation

## Slide 48
C
B
A
D
41
Léonard WATRELOT, PhD student, BE-GM-HPA
FSI “in-fiber” prototype and first tests
A
B
C
Difference of refraction index between air and glass
14/06/2022, 2nd year CST presentation

## Slide 49
C
B
A
D
42
Léonard WATRELOT, PhD student, BE-GM-HPA
FSI “in-fiber” prototype and first tests
A
B
C
Hyp. : fiber sliding in the protecting sleeve
14/06/2022, 2nd year CST presentation