## Slide 1: EP-DT Group Meeting
June 16, 2022
Burkhard Schmidt
Welcome/Bienvenue!

## Slide 2: EP-DT Barbeque
Many thanks to all who contributed!

## Slide 4: Outline
Overview of the EP-DT group composition
Some of the main activities of the group
on Projects to which we contribute
  Details can be fond in the EP-DT Annual Report
  to be released soon…
Things coming up
  News about building 140+
  Two-factor authentication
Concluding remarks

## Slide 5
Organigram EP-DT Group
http://ep-dep-dt.web.cern.ch
Many thanks to Giovanna for having led and contributed
to the DT-DI section so well over the past 7 years !
Many thanks to Leszek for having led and contributed
to the GDD and RD51 so well over the past 15 years !

## Slide 6: EP-DT Composition and Structure
Personnel | FTE 2023 (2022)
Staff | 84 (87)
Fellows / TTE | 31 (35)
PJAS/COAS | 3 (5)
Doct. Students | 20 (16)
Tech. Students | 11 (10)
Trainees | 9 (3)
FSU PH-02: FSU PH-40: | 16 (16) 16 (13)
Contributing Retirees | 6 (5)
Total | 196 (190)
Comments:
The number of Staff members is reduced slightly, but two more staff will be hired still this year
  1 Staff members (included in the counting) is on long term sick-leave
Many Fellows, DOCT and TECH are affiliated to DT, but are only partially on DT quota.
The Field Support Units PH-02 and PH-40 are crucial to fulfil our mission (~15% of workforce).
Section | Persons
Technology &Physics (TP) SL: Thierry Gys | MPE: 13 MPA etc. 5
Detector Development (DD) SL: Petra Riedler | MPE: 18 MPA etc. 10
Fluidic Systems (FS) SL: Paolo Petagna | MPE: 28 MPA etc. 16
Detector Interface (DI) SL: Xavier Pons | MPE: 10 MPA etc. 6
Engineering Facilities (EF) SL: Hans Danielsson | MPE: 12 MPA etc. 1
Engineering Office (EO) SL: Andrea Catinaccio | MPE: 15 MPA etc. 4
Construction & Operations (CO) SL: Antti Onnela | MPE: 19 MPA etc. 2

## Slide 7: EP-DT Summer Students 2023
Maria
RAMOS
12.06. to 01.09.
SV: G. RIGOLETTI
Welcome to EP-DT! We wish a very profitable time at CERN!
We have scheduled three sessions during the summer, in which you will have an opportunity to present your work: July 25, August 8 and August 22 (always AM)
  The aim is to have each time 4 presentations
Elias
St ONGE ARNQVIST
05.06. to 25.08
SV: Moritz WIEHE
Zachary
ZAWISZA
12.06 to 11.08.
SV: M. KRAWCZYK
Diego
VASQUEZ LEVANO
05.06 to 28.07.
SV: F. RAVOTTI
Juha William
NUMMI
01.06 to 31.08.
SV Fl. Brunbauer
Chiara
VOLPATO
12.06 to 08.09.
SV: F BRUNBAUER
Uzay Tan
ISLEK
12.06. to 08.09.
SV: G. RIGOLETTI
Magnus
THOGERSEN
26.06. to 01.09
SV: Justus BRAACH
August Rumle
GERSHOLM BRASK
26.06. to 01.09
SV: K. FLOETHNER
Jenan
AMER
19.06. to 11.08.
SV: LEENA DIEHL
Marianna
GLAZEWSKA
03.07. to 04.09.
SV: Eraldo OLIVERI
Mohammed
NECHIRAWAN
03.07 to 25.08
SV: A. ADEB ABUD

## Slide 8: Activities of Staff and Fellows in EP-DT
Chart: DT Fellows 2021 (302 months)
Funding Source of Fellows (w/o TTE)
Involvement of Staff and Fellows
In Projects
Involvement in projects related to the upgrade of the LHC experiments is more than 80%.
The remaining 20% are shared equally between other experiments and project studies.
DT based Fellows (and Students) are mainly on non-DT resources
Very good collaboration with ATLAS, CMS, NA62 and NP for funding Fellows/Students
Fellows represent 50% of the resources for R&D
  Involvement of DT in EP R&D and the ECFA R&D Roadmap will be shown by Eraldo

## Slide 9
FSU Activities in EP-DT
Total of hours for 2022: ~55,000 hours (~30 FTE) for a cost of about 3 MCHF
FSUs are an important resource to respond to urgent needs of the experiments
A renewal of the contracts is needed as they are in place since 12 years
  A new contract, starting on July 1, is in place for the support of the MPT workshop
  The Invitation to Tender for PH-02 & PH-04 is still under preparation;
    The plan is to start with the new contract in January or April 2024

## Slide 10: DT Staff involvement in Services
Chart: DT-Staff (FTE) in Services
| Mech.WS & Comp.Lab | Engineering Office | Thin Film & Glas lab | Bondlab, QARTlab, DSF | Irradiation Facilities | Exp. Magnet Support | DAQ and DCS support | Magnet M&O | Cooling Systems | Gas Systems | MPT workhop
2017 | 8.1 | 0.7 | 2.2 | 2.3 | 2.8 | 1.8 | 3 | 3 | 3.9 | 5.7 | 7.3
2022 | 1.7 | 0.2 | 1.5 | 3 | 2.3 | 1.2 | 3.4 | 2.8 | 7.2 | 6.4 | 6.6
The involvement in services has been optimized over the past years (10% reduction).
A minimum of Staff involvement (~2FTE) is needed to keep a service operational.
Some of the services are crucial for the world-wide detector physics community, e.g.
the MPT workshop, the Irradiation Facilities, the magnetic field measurement service etc.
Some services are based on Service Level Agreements with the experiments
About 80% of the Staff involved in Cooling Systems is working on Cooling plants for the
ATLAS and CMS Phase II upgrades.

## Slide 11
CO2 Cooling Systems for Phase II upgrades
Total HW investment ~23 MCHF
EP-DT Responsibility: * Design, procurement and installation of Surface storage, Plants HW and Control cabinets
* Supervision on design and procurement of Main Transfer Lines and Manifolds
* Commissioning and M&O of the whole system
THE “2PACL SYSTEM”:
16 plants (different sizes)
  9 in CMS (includes one spare)
  7 in ATLAS (includes one spare)
14 accumulators (different volumes)
  8 in CMS
  6 in ATLAS
2 large (10 m3) surface storage vessels
  1 for CMS
  1 for ATLAS
Long cold transfer lines
Distribution manifolds
> 1 MW power form electronics
to be removed
  0.8 MW in CMS
  0.5 MW in ATLAS
T ≤ −45 °C at the accumulator

## Slide 12
Demo cooling plant
  Full-scale prototype for Phase-2 systems
  100 kW, − 45°C on Accumulator
  − 53°C at pump inlet
Modular design
  Main plant, 3 pumping heads (largest version)
  Backup plant, 3 pumping heads (smallest version)
  Accumulator (shared, as in final system)
  Transfer lines (coaxial)
  Dummy load
  Primary chiller (first prototype of the new R744 transcritical cycle)
  System switchable from “traditional 2PACL” mode to “2-PACL Flow-Through” mode (and back)
Main plant (3H)
Spare plant (1H)
Control cabinets
Surface storage simulator
Accumulator
R-744 primary
Dummy load
Transfer line
DEMO Cooling Plant
DEMO prototype experience and results:
Component selection
Test of novel approaches
Process and design verification
Consolidation of final design for outsourced production
Functional Analysis and parameter tuning
Results led to approval of combined ATLAS/CMS PRR in April
Fine testing continuing in parallel to procurement process
Activity planned until spring 2024

## Slide 13: ATLAS Phase II Upgrade: ITk Pixel Outer Barrel
DT Leading role in ATLAS ITk Pixel Outer Barrel Mechanics & Modules
  Module construction, Local Supports, on-detector cooling and global support structures
  Detector assembly and integration (DT commitments extend up to the end of LS3)
  Close collaboration EP-ADE, Université de Genève, Bonn, CPPM and EN-MME
In 2022, significant progress in the Longerons and Inclined Half Rings (IHRs)
  Big step forward in pre-production of bare local supports (production starts in Q3-2023)
  Finished design qualification of loaded local supports (pre-production started in Q2 2023)
New IHR Soldering Tool
L2, L3 & L4 Carbon Rings
Longeron & IHR RD53A Demonstrators
Pre-production Functional Longerons
QC Setup for Module Cells
Diego Alvarez

## Slide 14: ATLAS ITk Module Production
X-ray scan ITkPixV1.1 module (top right chip)
Abhishek Sharma
QC studies:
CT scan to examine glue spread between sensor & flex
Module Production Assembly Tooling
CERN is one of the production centers for quad modules for the ITk Outer Barrel (up to 1200 modules) – close collaboration between EP-DT and EP-ADE.
Assembly production line established in DSF cleanroom including test setups, inspection systems and assembly tooling.
Total number of assemblies built in the last 12 months: 62
35 pre-production ITkPixV1.1 Quad modules
27 ITkPixV1.1 Digital Quad Modules for serial powering, flex design validation, readout studies
Strong contributions towards hybridisation vendor qualifications, module QC and flex pre-production
Module assembly and testing steps
ATLAS ITkPixV1.1 Quad modules
Assembly area in DSF cleanroom

## Slide 15
TBPS: High-precision, low-mass structures & cooling for « tilted » detectors pointing towards beam IP. 9 pre-production Rings completed in 2022 – 2023. Ramping up to series production, to be completed in 2025.
CMS Phase 2 Upgrade Tracker
TB2S: Carbon-composite support Wheel (L=2.4m, Ø2.4m) Design completed in 2023. Now in manufacture in industry.
Modules: Quality control of electronic hybrids (10cm x 1cm) Design & production of jigs, for production use Q3 2023 -

## Slide 16: EP-DT – CMS team: main activities for HGCAL
3. Sensors in irradiation holder
3. Per-cell leakage current @ -40°C
after neutron irradiation
20cm ≅ 8”
4. New “Particulars” setup for cold IV+CV+Charge Collection measurements
6. Reconstructed showers in HGCAL endcap
5. Charge Collection Efficiency vs. fluence
⇒ Leakage current scales with delivered fluence and cell area, as expected
⇒ Agreement between results from established DT-SSD setup and new Particulars setup
⇒ Results being used for HGCAL optimisation
⇒ First combination of particle-flow approach & end-to-end ML-based reconstruction
⇒ Promising results for clustering and energy reconstruction w/ and w/o pile up
pre-irradiation value: O(1nA)
200um, 8x1015neq/cm2
120μm
200μm
300μm
8” Sensor Quality Control
Production phase started, with ~28’000
wafers to be delivered in 2023‒2025
Hub for full-sensor testing infrastructure used in 7 CMS HGCAL institutes
8” sensor neutron irradiation studies covering both full and new partial sensors (used in border regions of HGCAL)
Test setup development for radiation hardness (EP R&D funded setup, in collaboration with EP-DT SSD)
Small-sized test structure irradiations: X-ray and neutrons
End-to-end HGCAL event reconstruction using machine-learning algorithms
Region with simulated pileup events
Black = Noise
Colours = showers

## Slide 17
ALICE ITS3
Reliable radiators and support structures based on carbon foam for the next generation of ultralight vertex detectors (MB <0.1%).
IR thermal imaging of the Carbon foam radiator
Overall ΔT sensor < 5 °C
Sensor and air <10 °C
CFD simulation of the air flow in the cooling volume
4m/s< Air speed <8m/s
EP R&D team & ALICE team
3D print gas distributors for flow control integrated with services
Gas cooling
(Air, N2)
Engineering Model Development:
3 silicon layers (40 µm thick)
Layers radius 18, 24, 30 mm
Carbon foam frames/radiators
Cooling performance
Pixel matrix ∼ 0.05 W/cm2
Readout endcap 1 W/cm2
ΔT across sensor < 5 °C
ΔT Sensor and air <10 °C
4m/s< Air speed <8m/sec
Support: Longerons ERG Carbon RVC @Duocel
ρ = 0.06 kg/dm3, k = 0.033 W/m·K
280 mm
Support & cooling: Half ring radiators
Allcom K9 standard density
ρ = 0.2-0.26 kg/dm3, k = >17 W/m·K
ALICE ITS3 upgrade

## Slide 18: Contributions to LHCb
UT was closed in March in time for the start of the LHC run
DT is involved in many subsystems of LHCb, including VELO, RICH, SciFi, Calorimeters, Muon System
Contribution to the Upstream Tracker

## Slide 19: LHCb VELO – Vacuum Incident
Measurement of RF deformation with tomography
Primary vacuum (beam) and secondary vacuum (VELO)
are separated by a thin RF foil
Safety vacuum balance ΔP < 10mbar
Relay failure on January 10, 2023, let to loss of control of protection system
- Safety valve did not open
- Pressure difference went up to ΔP ≈ 200mbar
RF foil deformed towards the beam vacuum
VELO modules and cooling not damaged and operational
VELO will not be fully closed during the 2023 run
VELO will be opened by 16 mm with respect to the nominal fully close position
RF foil will be replaced during the 23/24 YETS
VELO modules and RF Foil

## Slide 20: Two-factor authentication
Computer Security is currently rolling out Two-factor authentication (2FA) protection for the accounts of many members of the Organization.
Two-factor authentication is the silver bullet in protecting computing accounts against any kind of abuse.
In our latest phishing campaign in 2022, 2000+(!) people provided their password to a fake login page. 2FA would have protected their accounts from any evil abuse.
Technically this 2FA protection implies that in order to access CERN web applications protected by CERN's new Single Sign-On (SSO), the new CERN SSO will require your 2nd factor about every 12 hours when staying in the same browser session. As today, separate browser sessions on the same or different devices require additional logins.
Some useful links:
  Instructions to configure and set-up 2FA at CERN: https://cern.service-now.com/service-portal?id=kb_article&n=KB0006587
  Outage TG: https://cern.service-now.com/service-portal?id=outage&n=OTG0071297
  2FA FAQ: https://auth.docs.cern.ch/trouble-shooting/2fa-tips/
  "Log in. Click. Be secure": https://home.cern/news/news/computing/computer-security-log-click-be-secure
  « Authentifiez-vous pour cliquer en toute sécurité »: https://home.cern/news/news/computing/computer-security-log-click-be-secure
The suggestion is to proceed as follows:
We fix the target date to e.g. July 4th (people who did not register by then will not be affected and will be contacted later)
Computer Security will send an email to the whole group.
We collect the number of USB-A and USB-C Yubikeys needed for your/our colleagues. Note that not everyone needs one as the Smartphone app might be enough.

## Slide 21: Building 140 Project: Site analysis
General analysis of this part of the Meyrin site has been carried out.
General circulation flows are taken into account in the development of the Project Requirements.

## Slide 22: Building 140 Status: Project requirements
Update of the space per person in the offices;
All auditoriums gathered in Phase 2;
Different distribution between general common spaces and EP common spaces. Additional space for lactation room and storage;
WC and technical spaces already included in the program;
New cafeteria and entrance hall concept;
Total surface estimated by CERN after adding 30% for all required spaces for the operation of the building and adding 20% for the construction elements.
Total surface estimated by CCHE
Outcome of study done last year:
Total space for EP-DT: Offices: 504m2, Lab- and Workshop space: 1258m2, Storage: 126m2

## Slide 23: DT Bike to Work competition 2023
EP-DT participated with 6 teams (out of 270 CERN wide):
Team led by Soledad
Team led by Joao
Team led by Justus
Team led by Dominik
Team led by Enrico
Team led by Eraldo

## Slide 24: Concluding remarks
We are living in very challenging times, from many viewpoints!
We are committed to support the CERN experiments with the resources available, which are very tight.
The collaboration with the teams of the experiments is very good, which is important, as much work is before us, in particular for the Phase II upgrades of ATLAS and CMS.
It is important to maintain the expertise and facilities of EP-DT and the various services.
The age-profile of persons on ICs is
a concern as 30% of the staff will
retire before the end of the decade.
We have to ensure continuity of the
competencies in the DT group!
Chart: EP-DT age distribuiton in 2021
| 25-30 | 30-35 | 35-40 | 40-45 | 45-50 | 50-55 | 55-60 | 60-65
LD | 2 | 9 | 8 | 3 | 4 | 1 | 0 | 0
IC | 0 | 0 | 4 | 6 | 14 | 11 | 23 | 3