## Slide 1: Improved RPC (iRPC) detector for CMS data taking in HL-LHC
Salvatore Buontempo
(INFN – Napoli)
on behalf of CMS Muon Group
ICHEP2024 – July 20th 2024 - Prague (Czech Republic)

## Slide 2: Outline
The Compact Muon Solenoid (CMS) for the HL-LHC
The improved Resistive Plate Chambers (iRPCs) in CMS
iRPC production and quality control
Time and space resolution
Performance of iRPCs under gamma background
Installation in CMS
Conclusions and Perspectives

## Slide 3
The Compact Muon Solenoid for HL-LHC
CMS is under Run III data taking and in the process of preparation to extend its sensitivity to new physics searches for the High-Luminosity LHC period starting in 2029, anticipated to feature a higher Instantaneous Luminosity to around 3000 fb-1.

## Slide 4
RPC is the only Muon subsystem
that covers the entire CMS:
Barrel and Endcap

## Slide 5
/
TC
International CMS RPC
RC, Operation
& Construction
UC, PCB, FEB
Assembly site, Operation
& Construction
Assembly site, Operation
& Construction
HPL, PM,
RM, EC
TC, RC, DPGC
Operation
& Construction
Cooling,
Construction
GAP, DPGC
TrigC
Back end
TrigC
EC, Link System
Operation
& Construction
PM, RM, DPGC,
EC, TC, Operation
& Construction
Assembly site, PM,
UC, Operation
& Construction

## Slide 6
The Resistive-plate Chambers in CMS
6
Abbrescia et al, 2018
Park, S et al (2012). CMS endcap RPC gas gap production for upgrade. Journal of Instrumentation. 7. P11013. 10.1088/1748-0221/7/11/P11013.
Gas mixture used in CMS/RPC: 95.2 % C2H2F4 + 4.5 % i-C4H10 + 0.3 % SF6
Guiducci, Luigi & Montanari, Alessandro & Odorici, Fabrizio & Rossi, Antonio. (2006). Design and Test of the Off-Detector Electronics for the CMS Barrel Muon Trigger
RPC barrel and end cap efficiency during Run II (2015-2018)
Notes: 95.2 % C2H2F4 (R134a tetrafluoroethane), 4.5 % isobutane (C4H10) and 0.3 % SF6 (Sulphur hexafluoride)

## Slide 7
The Resistive-plate Chambers in CMS
7
Abbrescia et al, 2018
Park, S et al (2012). CMS endcap RPC gas gap production for upgrade. Journal of Instrumentation. 7. P11013. 10.1088/1748-0221/7/11/P11013.
Gas mixture used in CMS/RPC: 95.2 % C2H2F4 + 4.5 % i-C4H10 + 0.3 % SF6
Guiducci, Luigi & Montanari, Alessandro & Odorici, Fabrizio & Rossi, Antonio. (2006). Design and Test of the Off-Detector Electronics for the CMS Barrel Muon Trigger
RPC barrel and end cap efficiency during Run II (2015-2018)
Performance of eco-friendly alternative gas mixture in CMS iRPC detector in HL-LHC environment
Poster by Joao Pinheiro
Latest results of longevity studies on the present
CMS Resistivity Plate Chamber (RPC) system for the HL-LHC phase
Poster by Mapse Barroso Ferreira Filho
Operations and Performance Summary of CMS Muon System for LHC Run 3
Talk by Gabriella Pugliese

## Slide 8
CMS Muon LHC Phase-II Upgrade
8
CERN-LHCC-2015-010
To cope with the high particle rate and high pileup environment due to increased luminosity in HL-LHC, the CMS forward region demands → improved trigger and reconstruction performance !
Interesting Physics in the forward region (CERN-LHCC-2017-012):
  long-lived particles decaying leptonically;
  final states with low pT muons;
  heavy slowly moving charged particles;
  highly boosted di-muons;
Muon System Upgrade for HL-LHC (|η| < 2.8):
  Existing DTs, CSCs and RPCs:
→ Upgrade the Electronics!
  Installation of new detectors in the forward region:
    Gas Electron Multipliers: ME0 and GE21
    Improved Resistive Plate-Chambers (iRPC) : RE31 and RE41
Hottest point
~ 700 Hz/cm2
CERN Document Server courtesy
Notes: Replacement of ageing electronic parts
Increase event reconstruction capabilities particularly in forward region
Extend acceptance, Adding new detectors extending the eta coverage
Repair / replace your aged detectors as well as its electronic components - better timing
Update the trigger hardware and algorithms
Make your readout electronics with deeper buffering and faster processing

## Slide 9
CMS Muon LHC Phase-II Upgrade
9
CERN-LHCC-2015-010
To cope with the high particle rate and high pileup environment due to increased luminosity in HL-LHC, the CMS forward region demands → improved trigger and reconstruction performance !
Interesting Physics in the forward region (CERN-LHCC-2017-012):
  long-lived particles decaying leptonically;
  final states with low pT muons;
  heavy slowly moving charged particles;
  highly boosted di-muons;
Muon System Upgrade for HL-LHC (|η| < 2.8):
  Existing DTs, CSCs and RPCs:
→ Upgrade the Electronics!
  Installation of new detectors in the forward region:
    Gas Electron Multipliers: ME0 and GE21
    Improved Resistive Plate-Chambers (iRPC) : RE31 and RE41
Hottest point
~ 700 Hz/cm2
CERN Document Server courtesy
The CMS Muon System Upgrade for High Luminosity LHC
Talk by Archie Sharma
Notes: Replacement of ageing electronic parts
Increase event reconstruction capabilities particularly in forward region
Extend acceptance, Adding new detectors extending the eta coverage
Repair / replace your aged detectors as well as its electronic components - better timing
Update the trigger hardware and algorithms
Make your readout electronics with deeper buffering and faster processing

## Slide 10
CMS RPC Upgrade Project
Upgrade of Link System to improve timing resolution for existing RPC system (||<1.9)
Replace all off-chamber electronics.
iRPC: Extend the RPC coverage up to ||=2.4
in high eta region in stations 3 and 4

## Slide 11
Upgrade of Link System to improve timing resolution for existing RPC system (||<1.9)
Replace all off-chamber electronics.
Extend the RPC coverage up to ||=2.4
to restore redundancy in high eta region in stations 3 and 4
CMS RPC Upgrade Project

## Slide 12
Upgrade of Link System to improve timing resolution for existing RPC system (||<1.9)
Replace all off-chamber electronics.
Extend the RPC coverage up to ||=2.4
to restore redundancy in high eta region in stations 3 and 4
Focus of present talk
CMS RPC Upgrade Project

## Slide 13
13
 | RPC | iRPC
HPL thickness (mm) | 2 | 1.4
Number of gas gaps | 2 | 2
Gas gap thickness (mm) | 2 | 1.4
Resistivity (Ωcm) | 1 - 6 x 1010 | 0.9 - 3 x 1010
Charge threshold (fC) | 150 | 30 - 40
Space resolution in η (cm) | 20 - 28 | 1.5
Space resolution in φ (cm) | 0.8 - 1.9 | 0.3 - 0.6
Intrinsic timing resolution (ns) | 1.5 | 0.5
iRPC: improved Resistive Plate Chambers
+ 72 chambers in RE3/1 and RE4/1 positions
  20 o coverage in 𝞍 per chamber
  Variable strip width from 0.6 cm to 1.23 cm
  trapezoidal geometry ~1.2 x 1.6(3) m2 for RE 3(4)/1
Double readout in the strips high and low radius
Charge threshold between 30 and 40 fC
FEB positioned external and @ HR (lowest dose region)
Strip PCB allow Return line concept
Notes: The new layout reduces the amount of the avalanche charge produced by the passage of a charged particle through the detector.
This improves the RPC rate capability by reducing the needed time to collect this charge.

## Slide 14
iRPC Front-end electronics (FEB)
14
HR Direct signal
LR Return signal
To Back-end board
Cooling pipe
Fiber readout
Gas supply
FEB
HV connector
2V for left FEB
2V for right FEB
4V for both FEBs
Cooling plate with thermal pads
Front-end Electronics for iRPC
iRPCROC
iRPCROC
iRPCROC
TOP/BOT
TOP/BOT
TOP/BOT
CYCLONE V
CYCLONE V
CYCLONE V
Gas return

## Slide 15
The iRPC back-end electronics
15
Back-end functions include:
Fast/slow control and monitor
Cluster finding and trigger primitive generation
Timing reference adjustment
Data acquisition
At present, microTCA-based with
custom back-end board by IHEP is in use
Serenity
Set up in CMS Underground Service Cavern
FEB TDC data recorded in few BX,
well inside the 20 BX trigger latency
Data transmission delay properly adjusted by Back-end
Notes: The plot shows the number of Time-to-Digital Converter (TDC) data recorded for different readout window markers. X-axis marks the location of readout window position. For each bunch crossing (BX), every 25 ns, a maximum of 3 TDC data can be transmitted by the Front-End Board (FEB). The information from the FEB, and the signal from the trigger arrive at different timestamps. The Back-End Board (BEB) is in charge of making sure the data transmission delay is properly adjusted.

## Slide 16
ohmic region
avalanche region
16
Cosmic stand for gaps validation
Leak test (drop < 0.4 mbar/10 min)
Spacer bonding test
Dark current test (< 2.5 uA)
First QC step performed in the original sites of components manufacturing
Second QC step is again on component level, but in the chamber assembly sites
(CERN and Ghent University) to check component quality & stability after transport
Chamber assembly with validated components:
iRPC production and Quality Control @
62/72 chambers manufactured so far, completion expected by end of August 2024

## Slide 17
17
After TDC channel mapping, the hit position along the strips are obtained by the arrival time between LR and HR signals:
Efficiency of 98% and working point around 7050 V is stable up to 12 BX readout window!
Average noise < 1 Hz/cm2
measured in dedicate random scans
3rd step: Cosmic efficiency with portable FEB v2.3
3 scintillators for coincidence + veto
30 x 40 cm2 coincidence region
iRPC production and Quality Control @
Notes: Noise cut at 5 hz/cm2

## Slide 18
18
Step 4: Final chambers with final FEBs (v2.3)
→ Long stability test: current monitoring @ WP for 1 month
Average cluster size = 2.6!
Cluster size is defined as the number of adjacent strips fired when a muon crosses the detector
The strips pitch in the coincidence region is ~1 cm
→ Final cosmic test with final FEB v2.3 + cooling system
Cluster size in cosmic test with FEB v2.3
cover (not shown in the picture)
iRPC production and Quality Control @
Notes: 2.5 uA @ 7.1 kV

## Slide 19
19
Step 4: Final chambers with final FEBs (v2.3)
→ Long stability test: current monitoring @ WP for 1 month
Average cluster size = 2.6!
Cluster size is defined as the number of adjacent strips fired when a muon crosses the detector
The strips pitch in the coincidence region is ~1 cm
→ Final cosmic test with final FEB v2.3 + cooling system
Cluster size in cosmic test with FEB v2.3
cover (not shown in the picture)
iRPC production and Quality Control @
Production and quality control for CMS iRPC
Poster by Dilson De Jesus Damiao
CMS improved Resistive Plate Chamber (iRPC) upgrade:
Web-based automation for Quality Control
Poster by Ece Asilar

## Slide 20
20
Space resolution
20
Telescope in Lyon University IP2I made up with 4 RPC chambers (2 mm double gap 30 x 50 cm2)
X-axis resolution depends on strip pitch in the telescope region:
  0.8 - 0.9 cm
In y-axis, resolution depends on

## Slide 21
21
Time resolution
21
Timing resolution performed with 2 identical chambers and a muon beam
Absolute timing resolution of the system after alignment by back-end:
u

## Slide 22
22
Performance of iRPC under gamma bkg
iRPC performance validated under background gamma rate within a safety factor of 3!
Performance of a iRPC chamber in Gamma Irradiation Facility (GIF++) at CERN
→ 12 TBq 137Cs gamma source 662 KeV
→ Muon beam ~ 150 Gev/c
@ bkg-rate = 600-1000 Hz/cm2:
→ Efficiency = 96 - 96.7 %
→ Working Point = 7.07 - 7.11 kV
Gamma Irradiation Facility ++
Event display @ GIF++
Efficiency curves
threshold @ ~ 40 fC
12 BX trigger window
Data analysis ongoing with fine-tuned threshold and further optimised FEB configuration modes

## Slide 23
23
Installation in CMS
23
4 demonstrator chambers (RE+4/1/15,16 and RE+3/1/15,16) were installed in CMS in the end of the Long Shutdown 2 (2021-22), 4 FEBs v2.1 and 4 FEBs v2.2:
  Noise < 1Hz/cm2 with final end cap disk grounding
  FEB temperature stable in CMS endcap closed mode with water cooling
  HV currents showing smooth operation during LHC Run III
  Normal operation in 3.8 T magnetic field
2 mass production final chambers with final FEBs installed in CMS last YETS (2023):
  RE-3/1/16 and RE-3/1/18
All services are already installed since LS2 waiting for all 72 chambers
Average noise ~ 0.2 Hz/cm2
Dec 21
Jan 22
Dec 23
All 70 remaining chambers are expected to be installed next YETS 2024-2025 access time

## Slide 24
24
Installation in CMS
24
4 demonstrator chambers (RE+4/1/15,16 and RE+3/1/15,16) were installed in CMS in the end of the Long Shutdown 2 (2021-22), 4 FEBs v2.1 and 4 FEBs v2.2:
  Noise < 1Hz/cm2 with final end cap disk grounding
  FEB temperature stable in CMS endcap closed mode with water cooling
  HV currents showing smooth operation during LHC Run III
  Normal operation in 3.8 T magnetic field
2 mass production final chambers with final FEBs installed in CMS last YETS (2023):
  RE-3/1/16 and RE-3/1/18
All services are already installed since LS2 waiting for all 72 chambers
Average noise ~ 0.2 Hz/cm2
Dec 21
Jan 22
Dec 23
All 70 remaining chambers are expected to be installed next YETS 2024-2025 access time
CMS RPC Detector consolidation and preparation for new
chambers installation for Phase II upgrade programme
Poster by Joao Pinheiro

## Slide 25
25
Conclusions and perspectives
iRPC chamber is an innovative design detector to operate in CMS at High Eta region with HL-LHC
iRPCs production and quality control for installation in CMS are ongoing in 2 assembly sites: 62/72 chambers manufactured and QC (with portable FEB) so far. Completion expected by end of August 2024
iRPC space resolution is ​∆x = 0.4 cm and ∆y = 1.6 cm, improved wrt to present ∆x = 1-2 cm and ∆y = 20-30 cm
iRPC timing resolution is ∆t ~ 0.5 ns, improved wrt to present ∆t ~ 1.5 ns
At 600 Hz/cm2 and with a threshold of ~40 fC, the iRPC chambers have a performance of:
  96.7 % muon efficiency
  Working point ~ 7076 V
(further improvements recorded in last June/July test beam with FEB optimised threshold and configuration modes)
Demonstrators in P5 have already shown less than 1Hz/cm2 of noise and stable operation with CMS yoke grounding, water cooling, 3.8T magnetic field and no interference with nearby subdetectors
First 2 final chambers successfully completed, installed and commissioned last December 2023 in CMS
Chamber construction (with FEB) expected to be completed by the November 2024, installation planned during next YETS access time expected in January 2025

## Slide 26
ICHEP2024 – July 20th 2024 - Prague (Czech Republic)
Thank you for your attention