## Slide 1: Muon tomography with multiplexed Micromegas detectors using compact telecopes for societal applications
David Attié
July 18, 2024

## Slide 2: Overview
  Introduction
    Muon tomography - Principle
    Micromegas technology
    Multiplexed Micromegas detector (MultiGen)
    Muon telescopes using MultiGen
  Societal Applications
    WatTo demonstrator
    ScanPyramid mission
    First muon tomography a nuclear reactor
    Other nuclear applications
  Summary & Conclusions

## Slide 3: Introduction
1

## Slide 4: Muon tomography – Principle
  Use of atmospheric muons for non-invasive and non-destructive probe of internal structure of objects not accessible by usual methods (X-ray radiography, magnetometry, electrical resistivity, etc.)
  Muon tomography can be done using one of the three methods:
MCS
Transmission
Absorption
Transmission
    Multiple Coulomb Scattering
    Transmission
    Absorption
~1 m
~10-100 m
~1 m
~10-100 m
  Safe and free
  Flux: 150 m-²s-1 (in cos²)
  Highly penetrating (<E>4 GeV)
  Ultra-relativist with life time 2 μs
  Straight trajectories in mean
μ

## Slide 5: Micromegas technology
Pillar from bulk Micromegas
  Gaseous detector invented at CEA (1996)
    Defined by two regions:
      Conversion region (few mm to few m): Edrift ~100 V/cm
      Amplification region (~100 μm): Eamplification ~59 kV/cm
    Bulk Micromegas (2005)
      Robust, large area
      Industrialized manufacturing (printed circuit processes)
  Excellent performances for high-energy physics
    Spatial resolution < 100 µm
    Time resolution < 10 ns
    High flux operation
  Successful industrial transfer
    Started in 2012 with Elvia-PCB
    Production of 1250 m² for ATLAS/NSW
    ~ 150 resistive bulk Micromegas of 50×50 cm² for muon tomography

## Slide 6: Multiplixed Micromegas detector
    Resistive strip Bulk Micromegas
    2D readout (X & Y) with genetic multiplexing Each coordonate read out by 61 electronic channels
    PCB: 546×546 mm²
    Active area: 500×500 mm²
    Can be used in mosaic
MultiGen v3-v4
  « MultiGen » detector
MultiGen v2
MultiGen Version | Number of Multiplexing Family | Number of strips (X/Y) | Strip pitch (μm) | Drift length (mm) | Year | Number of detector | Improvements
V1 | 17* | 1024 | 488 | 10 | 2014 | 7 | (*) one family incomplete: 13 strips missing
v2 | 17 | 1037 | 482 | 15 | 2015 | 42 | Complete families; grounding plane added
v3 | 17 | 1037 | 482 | 8-10 | 2017 | 50 | Connectors moved to sides; HV filters on PCB
v4 | 12 | 732 | 683 | 8 | 2019 | 52 | Number of family reduced to 12; resistivity increased
INB72 | 5 | 305 | 557 | 5 | 2022 | 8 | Number of family reduced to 5
  Evolution since 2014: from prototype (CERN) to industrialization (ELVIA-PCB)
[doi.org/10.1016/j.nima.2016.08.006]
[doi.org/10.1016/j.nima.2013.08.071]

## Slide 7: Genetic multiplexing - Example
    5 multiplexing families
    305 (5×61) strips

## Slide 8: Muon Telescopes using MultiGen
1st Gen
(2015)
2nd Gen
(2016)
3rd Gen
(2017)
4th Gen
(2018)
WatTo
ScanPyramids
GBar
Gbar m bkg
  Improvements
    Compactness
    Autonomy
    Stability
  Perfomance today
    Spatial resolution ~250 µm
    Angular resolution ~ 2 mrad
    Time resolution ~10 ns
  Applications
    Fundamental Research
    Archaeology
    Nuclear Domain
    Civil Engineering
    ….
MultiGen evolution

## Slide 9: Societal Applications
2

## Slide 10: Muon tomography timeline at CEA/Irfu
  Started with the R&D of resistive multiplexed Micromegas
  Used for hodoscope in cosmic test bench
    Reduce channel number
    Large area with accurate tracking
  WatTo (Water Tower)
  Cosmic bench for Clas12 detectors validation
X
2012
2013
2014
2016
2015
  M-Cube:
  demonstrator for homeland security
X
X
1st muography HD online
2017
X
  M-Cube :
  U detected in less than 4 minutes
  ScanPyramids
X

## Slide 11: Muon tomography timeline at CEA/Irfu
2018
X
2017
2019
2021
2020
X
  Maison de l’Imagerie Muonique Ouverte aux applications Sociétales et Académiques
X
X
  G2G3 nuclear Reactor (NR)
X
  Common lab
2022
X
IZEN
X
1st muography of a military NR
  G2 NR
Nuclear
Dismantling
projects
Industrialization

## Slide 12: WatTo - Demonstrator
  Static muography (position 1)
    4 weeks
 First muography of a recognizable building
Muons flux in the tank
Water heigh in the tank
  Dynamic muography (position 2)
    4 days
    Scintillator telescope
[ doi.org/10.1016/j.nima.2016.08.002]

## Slide 13: ScanPyramids: Big Void
[doi.org/10.1038/s41467-023-36351-0]

## Slide 14: ScanPyramids: North Face Corridor
Data/Sim wo NFC
Data/Sim with NFC
Raw data
2x2x9 m3
(a)
(b)
(c)
Three telescopes
(a)
(b)
(c)
First "double“ outdoor telescope (100×50 cm2)
Improved gas system (filters & recirculation): total gas flow of 0,5 L/h 20 detectors
High precision simulation (Geant4 + pyramid model) used for analysis
March 2nd, 2023
[doi.org/10.1038/s41467-023-36351-0]

## Slide 15: Nuclear Reactor G2G3 in dismantling
  Main objectives: survey military G2 and G3 reactors, located at CEA–Marcoule, using muon tomography
    Check the validity of existing drawings (1960s)
    Check the internal structure and aging of the reactors
    Identify defects (e.g. cracks) in the concrete body (if possible)
Buildings G2-G3 @ CEA Marcoule
G3 reactor @ 1960s
G2 reactor @ 2018

## Slide 16: G2 – First Measurement
  First analysis: look for disagreements Reality–CAD Model
  Data/Monte Carlo comparison
    Monte Carlo generated with the geometry from the 3D - CAD model
    Any anomaly will imply differences between the model and the real structure
2 Data / MC disagreements
1 : Loading tubes and block
2 : Unloading tubes
Assembling channels
    Detector placed at the centre of the reactor (level – 0)
    Optimal position for a first overall image

## Slide 17: G2 – Multiposition with 4 telescopes
27 positions

## Slide 18: G2 – Multiposition  Tomography 3D
See video at vimeo.com/672377812/1ad9048fa0
  Second analysis: Simultaneous Algebraic Reconstruction Technique (SART) first used for CT scan (1984)
[doi.org/10.1126/sciadv.abq8431]
SART Method
[D] (nv x nm) [𝞺] (nv) = [o] (nm)
nv: Voxels number = 2688000 of 25 cm side
nm: 27 positions with 200 x 200 directions per 2D muography (1 080 000 measurements)
→ [D] has ~ 2,9 1012 elements
[𝞺] represents the (unknown) density in each voxel,
[o] is the opacity vector
[D] is a distance matrix

## Slide 19: IZEN – Container scanning
  Main goal: container verification scope based on Micromegas detectors
    First order density of waste (~water, heavy metals, …)
    Integrity of the blocking concrete
  Muon tomography using absorption method (1 Top Tracker + 1m2 bottom veto)
    More compact setup
    Less bluring
  Veto (1 m²) movable
    3 positions
    Reconstruction artefact to be solved

## Slide 20: Summary & Conclusions
  CEA/Irfu group developed a muon telescope based on Micromegas detectors
    Robust technology
    Good performance (angular and spatial resolution)
  This telescope has been used in the last years in different muography applications
    Archaeology
    Engineering
    Nuclear domain
  Among the different projects related to nuclear domain
    Reactor model verification
    Nuclear waste containers inspection (still in progress)
  New ideas and projects on going

## Slide 21: Thanks! This talk has been possible thanks to the work of: Raphaël Bajou, Théophile Benoit, Héctor Gómez, Mariam Kebbiri, Baptiste Lefèvre, Irakli Mandjavidze, Philippe Mas, Daniel Pomarede and Sébastien Procureur
CEA SACLAY
91191 Gif-sur-Yvette Cedex
France
david.attie@cea.fr
Phone + 33 1 69 08 11 14

## Slide 22: Cosmic test bench at CEA/Irfu
  Technological transfert from cosmic test bench hodoscope initially developed for Clas12 project
  Developed for detector characterization
    Based on bulk Micromegas detectors
    Reduced number of electronic channel  Genetic Multiplexing (patented)
    High performance (~250 μm space resolution)
  Advantages w.r.t. test beam in accelerators
    No booking needed
    Available anytime
    Free
HV module
Trigger Module
Top Scintillator
Bottom Scintillator
Bottom mMs pair
Top mMs pair
Characterized detector
DAQ
LV Module
doi.org/10.1016/j.nima.2013.08.071

## Slide 23: Muon Telescopes using MultiGen
2018
2019-today
2015
2016
  Evolution of the CEA/Irfu’s telescopes: towards compactness, transportability and industrialization
    2015: WatTo, ~200 kg
    2016: ScanPyramids (outside), ~130 kg
    2018: ScanPyramids (inside), cube, ~45 kg
    2019: G2G3, EDF, …, optimized cube, ~45 kg
  CEA/Irfu’s electronics cards: towards compactness, transportability and industrialization
    Front-End Unit (FEU) card developed for Clas12
    High-Voltage Power Supply (HVPS) card dedicated
6U Rack
HVPS
DC-DC
FEU
8 ASICs Dream

## Slide 24: Simulations and data analysis

## Slide 25: Iris-Instruments – Common laboratory
  Supplier of instrumentation for Geophysics reaching an academic clientele
  Lab-Com created in early 2020 with licensing agreement in geoscience, territorial security and industrial control (extension until mid-2025)
  Aim: R&D to develop a demonstrator for sale
  Success:
    Telescope now in catalog
  See website: http://www.iris-instruments.com
*Declaration versus Mass Measurement Comparison