## Slide 1
Accelerator design and R&D efforts for Super Tau-Charm Facility
Jingyu Tang
On behalf of the STCF accelerator team
ICHEP 2024, July 17-24, 2024, Prague

## Slide 2: Topics
Design goals of STCF
Current accelerator design scheme and key parameters
Key challenges in accelerator physics and technologies
Organization of the STCF accelerator study
Summary
Notes: 报告时间：12+3

## Slide 3
1st Generation
Single ring
2nd Generation
Double-ring
More bunches
Low by@IP
3rd Generation
Double-ring
Large Ib and crossing angle
Extremely low by@IP
High-lumi e+/e- circular colliders
Notes: STCF is a national facility of global HEP strategy, an 𝑒+/𝑒− collider, dedicated to precision study of properties of charm-quark, tau-lepton, study of strong interactions, search of BSM physics

## Slide 4: STCF Design Goals
Core design goal:
  CoM energy: 2-7 GeV
  Luminosity: >51034 cm-2s-1 @4GeV
  Upgrading potential: polarized beam, higher luminosity
Accelerator structure
  Double-ring collider: low emittance, high current, large Piwinski angle
  Injector: full-energy linac, e+ damping ring or accumulator, beam transport lines

## Slide 5
Current deign scheme and main parameters
Injector:
  Variable energy: 1-3.5 GeV
  High beam quality (emittance, energy spread)
  Two different CR injection: off-axis and swap-out
  Damping ring or accumulator ring for positrons @1 GeV
  Total length: ~400 m (+100 m beam transp.)

## Slide 6
Collider rings:
  Injection energy: 1-3.5 GeV
  Optimal energy: 2 GeV
  Two injection schemes: off-axis, swap-out
2-fold lattice
1-IP lattice
Parameters | Units | STCF
Optimal beam energy, E | GeV | 2
Circumference, C | m | 871.76
Crossing angle, | mrad | 60
Revolution period, | s | 2.908
Horizontal emittance, / | nm | 6.857/0.034
Coupling, k |  | 0.50%
Beta functions at IP, / | mm | 40/0.6
Beam size at IP, | m | 16.56/0.143
Betatron tune, |  | 32.55/29.57
Momentum compaction factor, | 10-4 | 12.322
Energy spread, | 10-4 | 8.986
Beam current, I | A | 2
Number of bunches, |  | 726
Particles per bunch, | 1010 | 5.00
Single-bunch charge | nC | 8.01
Energy loss per turn, | keV | 406.8
Damping time, / | ms | 28.4/28.6/14.4
RF frequency, | MHz | 499.333
Harmonic number, h |  | 1452
RF voltage, | MV | 1.8
Synchrotron tune, |  | 0.0158
Bunch length, | mm | 9.72
RF bucket height, | % | 1.47
Piwinski angle, | rad | 17.61
Beam-beam parameter, / |  | 0.0027/0.082
Hour-glass factor, |  | 0.87
Luminosity, L | cm-2s-1 | 
Parameters | Units | STCF
Optimal beam energy, E | GeV | 2
Circumference, C | m | 871.76
 | mrad | 60
 |  | 2.908
 | nm | 6.857/0.034
Coupling, k |  | 0.50%
 | mm | 40/0.6
 |  | 16.56/0.143
 |  | 32.55/29.57
 | 10-4 | 12.322
 | 10-4 | 8.986
Beam current, I | A | 2
 |  | 726
 | 1010 | 5.00
Single-bunch charge | nC | 8.01
 | keV | 406.8
 | ms | 28.4/28.6/14.4
 | MHz | 499.333
Harmonic number, h |  | 1452
 | MV | 1.8
 |  | 0.0158
 | mm | 9.72
 | % | 1.47
 | rad | 17.61
 |  | 0.0027/0.082
 |  | 0.87
Luminosity, L | cm-2s-1 | 

## Slide 7: Key challenges in accelerator physics and technologies

## Slide 8: Key challenges on AP and technologies
Collider Ring and IR AP design:
IP beam size (Y) nm scale, Crab-Waist, nonlinear compensation extremely difficult
Injection into CR (small DA): high Ib and low  e+/e- sources
IR Technologies:
SC magnets, MDI
Other key technologies:
Ring RF, beam instrum. and control, beam injection…
Design goal: Super-high lumi., high-quality (high-current, low emittance) e+/e- beams collision (extremely low *), stable operation
Great challenges: IR strong nonlinearity and collective effects; IR superconducting magnets
Big Piwinski angle + Crab Waist

## Slide 9
No | Key design or tech | Prio. | Comments
1 | Collider ring AP design | A+ | Espec. IR, key to realize high-lumi
2 | IR SC magnets | A+ | Complex structure, high-field, tight space, less exp.
3 | Collider ring RF | A+ | High-power, deep-damped HOM, less exp.
4 | Injector AP design | A | Prov. high-qual. beams to CR, 2 injection schemes
5 | MDI | A | Very tight space and complex mech. (acc. and det.)
6 | Collider beam instrum. | A | High-prec. and fast bunch meas., fast feedbacks
7 | Collider ring injection | A | ns-scale kickers for bunch swap-out injection
8 | Positron source | A | Low e- energy to generate e+ beam
9 | Collider ring vacuum | A- | High-current circ. beams, ultra-high vacuum for IR
10 | Electron source | A- | High-bunch charge photocathode e-gun
11 | Linac microwave | A- | Large-aper. S-band acc. struct., less exp, LLRF
12 | Linac power source | A- | High-power solid-state modulator
Key challenges on AP and technologies

## Slide 10
Key challenges (1) – CR AP design
A new-generation e+/e- collider
  How to attain two-order lumi. gain over the last-generation collider (BEPC-II)?
IR physics design
  The key and challenge for STCF accelerator
  New collision scheme: beam param (Ib, x ; nm spot at IP), crossing angle, correlation with the B-B effect [Luminosity need]
Take advantage of a new machine, lessons from SuperKEKB  better design
  Special optics: Final Focus + Crab Waist (Telescope-Mini , dispersion, phase advance) [Complexity]
  Strong nonlinearity: Local CC for extreme-low , fringe-field, crab sextupoles  very small DA and MA [very short beam lifetime]
  Complex MDI: SC magnets, vacuum, cryostat, beam monitors, interface with detector [Iterations]

## Slide 11
Beam-Beam effects
  3rd-Gen colliders pushing to 0.1 or higher (Limiting
  Large Piwinski + Crab-Waist: strong correlation with transverse motion
  Mutual influencing with frequent injections
Collective effects
  Factors: high current, low emittance, high impedance
  Intra-beam scattering: transverse IBS, Touschek (very short lifetime)
  Impedance: multiple strong collective instabilities, in particular the coupling bunch instability
Beam injection
  Touschek lifetime very short (<300 s), frequent injections
  At different beam energies: damping time by damping wigglers
  Injection schemes: off-axis injection easier, emittance blow-up and background; bunch swap-out injection  more powerful injector
Beam collimation
  Very high beam loss rate: background and radiation protection
  Collimation efficiency and impedance: more complex collimation design (e.g. nonlinear collimation)
Other key problems in CR AP design

## Slide 12
Key challenges (2) – Injector AP design
Injector providing e+/e- beams to CR
  Quality: energy spread, bunch charge, emittance, stability
  High frequency injections (~30 Hz)
  Large energy range: 1-3.5 GeV,  <20 nm
  High current: 1.5 nC (off-axis); 8-10 nC (swap)
Better design:
A new machine, utilizing design and technology from FEL and 4G light source linacs.
Off-axis injection
Swap-out injection

## Slide 13: Key challenges (3) – IR SC magnets
IR SC magnets
  Technically very challenging, very few labs have experience
  Very tight space, complex and combined coils
  3rd-Gen e+/e- colliders even more difficult: twin-aperture, higher field gradient (~50 T/m)
  In China: IHEP built the first IR magnet for BEPC-II; some experience in other SC magnets
  STCF R&D: developing prototypes by steps, different technologies under consider. (BEPCII serpentine, CCT, cos2θ/DCT)
IHEP BEPCII-U (Serpentine)
A CCT type prototype just started
(60 mrad, 54 mm separation, 50 T/m)

## Slide 14
Key challenges (4) – Ring RF
RF for Collider rings
  High synchrotron radiation (2 Amperes): RF power and couplers
  HOM deep-damped: instabilities
  Large energy range (1-3.5 GeV): high VRF
  Beam loading: at bunch swap-out injection
  Stability: more powerful LLRF
  Selected for R&D: TM020 RT cavity, 500 MHz; 200 kW coupler
TM020 cavity in prototyping
RF parameters | 
Working mode | TM020
Frequency [MHz] | 499.7
R/Q [Ω] | 84.4
Unloaded quality factor | 62828
 | 1.92
[mA/V] | 2.64
Vcav (inpot: 100 kW) [kV] | 728.2
RF parameters | 
Working mode | TM020
Frequency [MHz] | 499.7
R/Q [Ω] | 84.4
Unloaded quality factor | 62828
 | 1.92
 | 2.64
Vcav (inpot: 100 kW) [kV] | 728.2

## Slide 15
Key challenges (5) – Beam instrumentation
Requirements for beam instrum.
  CR precise bunch meas.: bunch-by-bunch 3D meas., trans. position res. <5 m, long. phase res.<0.2 ps
  CR B-by-B fast feedback: coupled bunch inst.
  IP: orbit feedback
  Injector: bunch length and charge meas.
R&D efforts
  Bunch 3D meas.: probe, signal treat, electronics, S/N, integration
  B-by-B fast feedback: raising bandwidth, avoiding interference to single bunch
  Injector bunch length and charge meas.: cavity-based
  Prototypes: beam tests in different machines
Integrated board for B-by-B 3D meas.
Cavity-based:
bunch length, charge and profile meas.

## Slide 16: Electron-positron beams test platform
Test platform for supporting several injector R&Ds
  Electron source: mainly photocathode (also thermal e-gun)
  High-power solid-state modulator
  Positron target
  Magnetic horn
  Large-aperture S-band acceleration tube
  Beam diagnostic devices
Basic requirements
  Photocathode electron source
  100-MeV e- linac
  Positron target and magnetic horn
  100-MeV e+ linac
  Beam properties measurements, beam dumps

## Slide 17
e- linac: 2* 6-m sections; e+ linac: 3 large-aper. accel. tubes
Located in the accelerator test hall of HALF (Hefei Advanced Light Facility under construction)

## Slide 18: From prelim. study phase to R&D phase
Preliminary study phase (from 2018 to mid 2023)
  Very limited manpower (a dozen, mostly: small-portion part-time, students, retired consultants): preliminary conceptual design on the STCF accelerator
  Lacking experience in colliders
  Supporting the STCF study project
Key R&D phase (since August 2023)
  National Synchrotron Radiation Laboratory (NSRL) fully engaged in, as the co-supporter of the STCF project
  NSRL is focusing on the constr. of HALF (a 4G synchrotron light source, 2023.5 to 2028.9), still limited manpower
  Domestic collaborations: 8 institutions, contributing to half of current manpower
  About 90 persons, half are students, majority without experience in colliders

## Slide 19: Summary
STCF accelerator goal is very challenging
Provincial and national financial resources to support the design and key technological R&Ds, aiming for construction in late 2020
STCF is a national project, attracts domestic institutions in the study
It is very important to collaborate with international labs, in particular, KEK and BINP
Thanks for attention!