## Slide 1: Development of LiCl aqueous solution for neutrino detection for Jinping Neutrino Experiment
Zhe Wang
Tsinghua University
（for the research group）
July 18, 2024

## Slide 2: Contents
Jinping Neutrino Experiment(JNE) in plan Target volume, 500 m3, at Jinping laboratory ---- Solar, Geo, Supernova neutrinos, etc.
Properties and development of LiCl aqueous solution as a neutrino target (organic luminescent material added)
Sensitivity for solar neutrino upturn effect
Prospects for geo and supernova neutrinos

## Slide 3: China Jinping Underground Laboratory (CJPL) ---- An ideal low background experiment site
2400 m overburden
1000 km to reactors

## Slide 4
SST Tank
PMT Truss
Acrylic Sphere
PMT
HV, FEE, Trigger, Clock
Online Data-taking
Shift Station
Pure Water
Calibration Unit
A 500 m3 detector is planned at CJPLII
Target volume: 500 cubic meter

## Slide 5
Goal of the Jinping Neutrino Experiment (JNE)
Solar neutrino B-8 neutrino spectrum, upturn effect (matter-induced survival probability increase)
Geo neutrino crust geo neutrino model study (Qinghai-Tibetan Plateau geoneutrino)
Diffuse supernova neutrino background (DSNB, aka supernova relic neutrinos)
Other new physics

## Slide 6: (Saturated) LiCl aqueous solution for neutrino det.
CC process for ne:
  Measure neutrino energy
High cross-section:
  ne-Li7: 60 times of ne-e elastic
  for solar B8 neutrinos
High natural abundance of Li7: 92%
High solubility: 80 g LiCl in 100 g water
B8 Event rate/100 ton-year solution

## Slide 7
CC-Li7 process for ne:
  Measure neutrino energy
Elastic scatter on e-:
Delayed coincidence for :
with neutron capture on H, Li6, and Cl35
measure energy
Spectrometer for and . Good chance for solar, geo, and supernova neutrinos.
ne CC-Li7, ES, and detection and separation
CC-Li7, ES separated by solar angle

## Slide 8
CC-Li7 vs ES for solar neutrino oscillation study
CC-Li7 process on nuclei is good to measure B-8 neutrino spectrum and any energy-dependent physics
ES process at 4 MeV
Relative difference=6.7%
CC process at 4 MeV
Relative difference=23%

## Slide 9
Solar B8 neutrino extraction simulation
With a solar angle cut, CC-Li7 process signals can be clearly extracted.
JNE can serve as a solar neutrino spectrometer.

## Slide 10: LiCl Water Solution Attenuation Length
LiCl water solution attenuation length improvement
Absorption with powered activated charcoal
Thermal recrystallization

## Slide 11: LiCl Water Solution Attenuation Length
50 m attenuation length
achieved.

## Slide 12
LiCl aqueous solution with carbostyril 124
Adding 1 ppm CS124 to LiCl aqueous solution
Convert short wavelength UV to longer wavelength
Convert short attenuation length UV to long attenuation length visible light
Minor scintillation light yield
CS124 absorption and emission spectra
LiCl solution
LiCl solution + 1 ppm CS124

## Slide 13
Uniform light output from LiCl solution+CS124
Light yield verification with a muon telescope
Cherenkov
Reflection
Cherenkov
Scintillation
3.7 PE detected from isotropic scintillation (uniform)
12.3 PE for Cherenkov (forward)

## Slide 14: Solar Neutrino Upturn effect
Solar neutrino survival probability vs energy
SNO
SK

## Slide 15: Upturn effect sensitivity with LiCl Solution
6400 ton-year, 4 MeV cut
Upturn discovery sensitivity versus exposure
Solar neutrino survival probability-average vs energy
SNO
SK
CC on Li7 has an advantage than n-e ES in measuring solar neutrino upturn effect.
JNE - A compact detector!
5-10 years for 3 sigma

## Slide 16
Light Sterile Neutrino in Solar Neutrino Physics
Dip and wiggle
Light sterile neutrino
Delta mass squared ~ 10-5 eV2
Not the same as reactor neutrino anomaly and LSND results ( ~ 1 eV2)
Structures: need a CC-Li7 detector

## Slide 17: CC-Li7 for Light Sterile Neutrino Rejection
Sensitive to small delta mass squared region of sterile neutrinos, 1e-5 eV2
Sensitivity calculation for JNE.

## Slide 18: Geo Neutrinos at JNE
1000 km radius
Ondrej Sramek et al, 2016
JNE is very sensitive to Qinghai-Tibet plateau crust neutrinos

## Slide 19: Geo Neutrino at JNE
With the prompt-delayed signal detection method in LiCl solution:
Minor reactor BKG at CJPL
Expect tens of geoneutrinos in 5-10 years with the 500-ton detector
(constrain crust model to
10-20%)
Initial result on U/Th ratio
Event rate summary for hundred-ton detector

## Slide 20
Adding CS124 indicates that: a high salt (LiCl) Cherenkov liquid scintillator is possible
Pure
LiCl aqueous solution
fluor
LiCl
aqueous + fluor solution
Direction
Energy
Position
Particle identification
Better than pure water or liquid scintillator

## Slide 21: Cherenkov Liquid Scintillator Reconstruction
Reconstruct both Cherenkov light and scintillation light
Energy; 2. Direction; 3. Position; 4. Particle identification
Guide liquid scintillator development
Scintillation decay time
Scintillation light yield

## Slide 22: Diffuse supernova neutrino background
With Cherenkov-scintillation liquid scintillator:
Have the capability for particle identification to suppress atmospheric neutrino neutral current background
Expect a few golden candidate supernova relic neutrinos in 5-10 years with the 500-ton detector
Expect an improvement better than this figure. Work in progress.
Cherenkov LS

## Slide 23: Summary
LiCl aqueous solution
  Long attenuation length, 50 m at 430 nm
  Fluor can be added, ex. CS-124  Cherenkov liquid scintillator
Compact detector for solar neutrino upturn study
Sizable geo-neutrino signal strength from Qinghai-Tibet plateau
Great signal-to-background ratio in DSNB detection
LiCl aqueous solution -- A new neutrino detection medium candidate

## Slide 24: Thank you. All related publications can be found at http://jinping.hep.tsinghua.edu.cn/Publications.php