## Slide 1
Overview of TRIUMF
HL-LHC collaboration meeting
Oliver Kester
Director, Accelerator Division TRIUMF
Monday, September 25, 2023
Notes: I would like to start with acknowledging the unceded and traditional territories of the Musqueam, Squamish and Tsleil-Waututh Nations, on which the SFU Morris J. Wosk Centre for Dialogue building is located.

## Slide 2
Welcome to B.C.!
Home of TRIUMF
TRIUMF is Canada’s particle accelerator centre. We are a world-class hub of research, education, and innovation that is home to ~600 staff and students
Founded in 1968 by the University of British Columbia, Simon Fraser University, and the University of Victoria, TRIUMF is a cornerstone of BC’s innovation ecosystem, driving impact locally, nationally, and around the world
2

## Slide 3
TRIUMF is located on the traditional, ancestral, and unceded territory of the Musqueam people, who for millennia have passed on their culture, history, and traditions from one generation to the next on this site.
TRIUMF’s home has always been a seat of learning.

## Slide 4
Member Universities:
University of Alberta University of British Columbia University of Calgary Carleton University
University of Guelph University of Manitoba
McGill University McMaster University
Université de Montréal
University of Northern
British Columbia
Discovery, accelerated.
Our multidisciplinary community uses TRIUMF’s world-class accelerator infrastructure to drive leading-edge research that delivers impact in science, medicine, and industry, helping position Canada as a global leader
Queen's University
University of Regina
Saint Mary's University
Université de Sherbrooke Simon Fraser University University of Toronto University of Victoria
University of Waterloo
Western University
University of Winnipeg York University

## Slide 5: TRIUMF accelerator complex
500 MeV Cyclotron and BL1A
ISAC-II
High energy
ISAC-I
Low and
medium
energy
ARIEL
Isotope Cyclotrons
elinac
Primary beam driver (1974):
500 MeV Cyclotron, 300 A, H-
Produces rare isotopes, neutrons and muons
Isotope Separator and Accelerator facility – ISAC (1996)
ISAC-I: Normal conducting-linac
  0.15-1.8 MeV/u (2000)
ISAC-II: Superconducting-linac
  1.5-16.5 MeV/u (2006)
Advanced Rare Isotope Laboratory – ARIEL (in progress)
Superconducting electron linac 30 MeV, 10 mA, cw (2019)
4 (+1) Cyclotrons for medical isotope production – TR30 and TR13 designed by TRIUMF
IAMI

## Slide 6
Constructed in the early 70th of last century
Largest normal conducting Cyclotron in the world: D = 18 m
Magnet weight: 4000 t, Coil current: 18500 A
H- cyclotron (multiple extraction at different energies)
5500 hours of beam delivery per year

## Slide 7: The TRIUMF 500MeV Cyclotron
H- extraction
  Multiple high-power beams by stripping extraction
    Variable energy – simultaneous beam delivery – presently 3 beams extracted
B
v
H- extraction
Carbon Foil
H- Ion
p

## Slide 8: Overview of applications driven by the 520 MeV Cyclotron
STF PIF/NIF
ARIEL symbiotic target
IPF
The 520 MeV cyclotron provides beam for medical isotope production (Nuclear Imaging & research on particle radiation therapy).
Irradiation capabilities with protons and neutrons.
Proton beams are delivered to
  the Solid Targetstation Facility (STF) for Sr production [85Rb(p,4n)82Sr]
  Isotope Production Facility (IPF)
  Proton Irradiation Facility (PIF)
  Neutron Irradiation Facility (NIF)
  And in the future to the ARIEL Proton Target Station West (APTW) with the symbiotic medical target in the beam dump.

## Slide 9: Isotope Separator Accelerator facility - ISAC at TRIUMF
Experiment
Isotope Separation On-line (ISOL) facility for rare isotope beam (RIB) production
High power proton beam (50 kW)
Extracted ions are mass separated and either post-accelerated or delivered to low energy experiments directly.

## Slide 10: ISAC – World’s Highest Power ISOL Target Systems
Containment Box
Shielding
Target assembly mounted in the Target Module containment box
The target containment box is mounted on the bottom end of the target module.
The target module is moved to/from target stations via remote handling crane – target exchange is done in a hot cell
Target assembly
Target station
Target module
500 MeV protons

## Slide 11: RIB-Post Accelerators
Refrigerator
RFQ
Mass Separator
Targets
DTL
ECR charge breeder
SCRF Lab
SC-Linac
6
7
8
World leading flexibility and performance:
Fully variable energy from 0.15 MeV/u to 16.5 MeV/u
Designed and built in house

## Slide 12
ARIEL: ISAC×3
ARIEL is the world’s most powerful isotope separation online complex.
It will triple ISAC's present rare isotope capabilities by adding
  a 50kW proton target station
  a 100kW electron target station
  Unique beam preparation and transport system (CANadian Rare isotope facility with Electron Beam ion source - CANREB)
ARIEL is the only rare isotope facility that will provide three RIB beams simultaneously to experiments.
ARIEL completion is planned for 2027

## Slide 13: ARIEL – superconducting electron-Linac
e-gun
cryo-module 2
10 kW beam dump
cryo-module 1
E-gun delivers max. 10 mA at 300 keV beam
The injector cryomodule (1) accelerates to 5-10 MeV
The accelerator cryomodule (2) is equipped with two cavities and reaches max. 30 MeV.
Elliptical cavities, 1.3 GHz
9 cell, TESLA type
11 MV/m demonstrated

## Slide 14: Early science supported by the ARIEL e-linac (active)
FLASH radiotherapy involves the ultra-fast delivery of radiation treatment at dose rates several orders of magnitude greater than those currently in routine clinical practice. It is enabled by the new ARIEL convertor technology:
Studies comparing response to identical dose deposited at FLASH and conventional rates in mouse, fruit fly and DNA completed
FLASH does rates about 100 Gy/s, conventional 0.1 Gy/s
Future activities are planned
Dark matter search – DARK LIGHT experiment looking for a 5th force (dark photons) in electron scattering
at the ARIEL e-linac Experiment gets additional motivation from recent results from the muon g-2 experiment at Fermilab.

## Slide 15: TRIUMF SRF Infrastructure (I)
TRIUMF hosts two SRF linacs (ISAC-II heavy ion linac and the ARIEL electron linac) and SRF supporting infrastructure.
Activities range from student R&D on test resonators to work for others (prototyping cavities and components) and to full cryomodule assemblies
For student training and R&D we have added
  UHV RF induction oven
  Coaxial test resonators for fundamental studies
  New high parallel field spectrometer for beta-NMR

## Slide 16: TRIUMF SRF Infrastructure (II)
ISAC-II SCRF Area
RF Measurments
Boot-up
17m
Preparation Area
Boot Area
RF Meas
Water Rinse/Clean Area
SCRF Test Clean Area
Test Pit
Clean Assembly Area
Chemical Lab
RF Controls Lab
42m
TRIUMF SRF test and assembly areas
  500m2 of floor space, overhead crane comprising: US cleaning tanks, HPWR area, cryogenics on tap, cryomodule assembly area (clean room for hermetic string assembly), chemical etching lab (BCP), rf testing
  Minor upgrades of clean room performed to meet the HL-LHC requirements.
  Cryomodule test capability in ISAC-II
    LHe – 100ltr/h in falling level, 200W at 4K, 40W at 2K
    LN2 at 1.5 Bar
    Shielded pit, LLRF, controls
  Issues with space for the HL-LHC project (larger CM assembly space in adjacent hall) New clean room for ISAC-II ordered!

## Slide 17
  TRIUMF released the 20-year vision September 2022 as a response to an international peer review.
  The product of an 18 months process engaging a broad research and stakeholder community leading to five core themes.
  The Visions lays out a long-term direction for the laboratory built around five pillars defining how the community sees the laboratory’s future.

## Slide 18: Thank you Merci
Follow us @TRIUMFLab
www.triumf.ca