## Slide 1: RF power system IOTs & challenges
Erci.Montesinos@cern.ch on behalf of all colleagues involved in the topic

## Slide 2: RF system
FPC
HPRF High Power RF station (including power transmission lines)
FPC Fundamental Power Coupler
HOMC High Order Mode Coupler
LLRF Low Level RF
HPRF
Cryomodule
LLRF
Controls
HOMC

## Slide 3: HPRF stations Technical Specification
With a no offset beam, HPRF will have to provide 20 kW
HPRF has been defined such to deliver up to 40 kW, about
1 mm+ offset
In case of a too large offset, HPRF must provide up to 80 kW during almost 1 ms, allowing for a clean beam dump
Courtesy Rama Calaga

## Slide 4: Integration of the HPRF in the galleries
P5 - CMS
P1 - ATLAS
Four different places
with four HPRF stations each
Total 16 HPRF stations

## Slide 5: Integration of the HPRF in the galleries
Point 1
Point 5
Left side
Right side

## Slide 6: Integration of the HPRF in the galleries
Volume L x l x h each HPRF station must be
maximum 2 x 2 x 2 meters all inclusive
In a gallery so no possibility to increase the size

## Slide 7: Integration of the HPRF in the galleries
From HPRF station to cavity
Line 1 65 meters
Line 2 59 meters
Line 3 52 meters
Line 4 45 meters
Almost the same for all four points

## Slide 8: Mismatch
V forward
V reflected
V transmitted
HPRF station
Transmission Lines
Cavity

## Slide 9: Reflection from cavity
0 | when the line is perfectly matched, no reflection
 | when the line is perfectly matched, no reflection
-1 | when the line is short-circuited complete negative reflection
0 | when the line is perfectly matched, no reflection
1 | when the line is open-circuited complete positive reflection
 | when the line is short-circuited complete negative reflection
 | when the line is perfectly matched, no reflection
 | when the line is open-circuited complete positive reflection
Cavity
Zc
Cavity
Z Zc
Cavity
Z
Standing Wave Ration SWR is a measure of impedance matching of the cavity
A wave is partly reflected when a transmission line is terminated with other than a pure resistance equal to its characteristic impedance
The reflection coefficient is defined by
Zc
Vr
Line = Zc
Vf

## Slide 10: Reflection from cavity
At some points along the line the forward and reflected waves are exactly in phase
full reflection
At other points they are 180° out of phase
full reflection
The Voltage Standing Wave Ratio is equal to
DUT
(Device Under Test)
Zc
Cavity
Z
Zc
Vf
Vr
Line = Zc

## Slide 11: Full reflection
In case of full reflection Vmax = 2 Vf
(Pmax equivalent to 4 Pf)
RF power amplifiers based on Klystron and SSPA will not like this reflected wave
If correctly designed, Grid tube and IOT can sustain it
Swift protection if Pr > Prmax, but then the system is NOT operational (not always possible)
Cavity
Pf
Swift protection if Pr > Prmax
Pr

## Slide 12: Circulator
The circulator helps the system to remain operational and to protect our lines and our amplifiers from the reflected power
It is a passive non-reciprocal three-port device
The signal entering any port is transmitted only to the next port in rotation, an RF signal experiences a low loss in the direction of the arrow and high loss in reverse direction while propagating through the Circulator
The best place to insert it is close to the reflection source
If full reflection lines between circulator and cavity, the lines shall sustain Vmax = 2 Vf (Pmax equivalent to 4 Pf)
A load of Pf is needed on port 3 at all time
1
2
3
In case of full reflection
there will be 2 Vf along the line
(4 Pf)
Vr
↓
Load
Vf →
← Vr
Vf →
Cavity
Pf
4 Pf
Pf

## Slide 13: Circulator
The most misunderstood concept of circulators is that of isolation
Circulators do not provide isolation until one of the ports is terminated
Then the isolation between the other two ports (in the direction opposing the direction of circulation) is approximately equal to the return loss due to any mismatch on the terminated port
So, a very good load is needed on port 3 in order to guaranty a good isolation at port 1
VSWR
1
2
3
Reverse power flows from 2 to 3
Load on 3 absorb most of the signal coming from 2
Isolation from 2-1 depends on 3 termination VSWR
Reflected signal from 3 is circulated back to 1

## Slide 14: Coaxial Lines
Characteristic impedance is
with
D = inner dimension of the outer conductor
d = outer dimension of the inner conductor
εr = dielectric characteristic of the medium
Size | Outer conductor |  | Inner conductor | 
 | Outer diameter | Inner diameter | Outer diameter | Inner diameter
7/8" | 22.2 mm | 20 mm | 8.7 mm | 7.4 mm
1 5/8" | 41.3 mm | 38.8 mm | 16.9 mm | 15.0 mm
3 1/8" | 79.4 mm | 76.9 mm | 33.4 mm | 31.3 mm
4 1/2" | 106 mm | 103 mm | 44.8 mm | 42.8 mm
6 1/8" | 155.6 mm | 151.9 mm | 66.0 mm | 64.0 mm
Coaxial cables are often with PTFE foam to keep concentricity
Flexible lines have spacer helicoidally placed all along the line
Rigid lines are made of two rigid tubes maintained concentric with supports

## Slide 15: Coaxial lines Maximum Power handling
Power handling of an air coaxial line is related to breakdown field E
with
E = breakdown strength of air (‘dry air’ E = 3 kV/mm, commonly used value is E = 1 kV/mm for ambient air)
D = inside electrical diameter of outer conductor in mm
d = outside electrical diameter of inner conductor in mm
Zc= characteristic impedance in Ω
εr = relative permittivity of dielectric
f = frequency in MHz
Valid only for straight Lines, in case of elbows, reduce at minimum
by – 30 %
d
D

## Slide 16: Coaxial lines Attenuation
The attenuation of a coaxial line is expressed as
with
α = attenuation constant, dB/m
Zc= characteristic impedance in Ω
f = frequency in MHz
D = inside electrical diameter of outer conductor in mm
d = outside electrical diameter of inner conductor in mm
εr = relative permittivity of dielectric
tan δ = loss factor of dielectric
Material | εr | tan δ | Breakdown MV/m
Air | 1.00006 | 0 | 3
Alumina 99.5% | 9.5 | 0.00033 | 12
PTFE | 2.1 | 0.00028 | 100

## Slide 17: Why 50 Ohms lines ?
Taking all the coaxial line formulas together
A compromise to normalize line construction and instrumentation was chosen at 50 Ω
30 Ω
Best for power
60 Ω
Best for voltage
75 Ω
Best for losses
50 Ω
Best compromise

## Slide 18: Possible damages
Damages to internal conductor of a coaxial line in case of excess of power

## Slide 19: Rectangular waveguides
The main advantage of waveguides is that waveguides support propagation with low loss
Wavelength | 
Cutoff frequency dominant mode | 
Cutoff frequency next higher mode | 
Usable frequency range | 1.3 to 0.9
Wavelength | 
Cutoff frequency dominant mode | 
Cutoff frequency next higher mode | 
Usable frequency range | 
b
a

## Slide 20: Rectangular waveguides
Waveguides are usable over certain frequency ranges
For very lower frequencies the waveguide dimensions become impractically large
For very high frequencies the dimensions become impractically small & the manufacturing tolerance becomes a significant portion of the waveguide size
b
a
Waveguide name |  |  | Recommended frequency band of operation (GHz) | Cutoff frequency of lowest order mode (GHz) | Cutoff frequency of next mode (GHz) | Inner dimensions of waveguide opening (inch) | Inner dimensions of waveguide opening (mm)
EIA | RCSC | IEC |  |  |  |  | 
WR2300 | WG0.0 | R3 | 0.32 — 0.45 | 0.257 | 0.513 | 23.000 × 11.500 | 584.2 x 292.1
WR1150 | WG3 | R8 | 0.63 — 0.97 | 0.513 | 1.026 | 11.500 × 5.750 | 292.1 x 146
WR340 | WG9A | R26 | 2.20 — 3.30 | 1.736 | 3.471 | 3.400 × 1.700 | 86.1 x 43.2
WR75 | WG17 | R120 | 10.00 — 15.00 | 7.869 | 15.737 | 0.750 × 0.375 | 19.05 x 9.52
WR10 | WG27 | R900 | 75.00 — 110.00 | 59.015 | 118.03 | 0.100 × 0.050 | 2.54 x 1.27
WR3 | WG32 | R2600 | 220.00 — 330.00 | 173.571 | 347.143 | 0.0340 × 0.0170 | 0.86 x 0.43

## Slide 21: Rectangular waveguides, Maximum Power handling
with
Ppeak = Peak power in watts
a = width of waveguide in cm
b = height of waveguide in cm
λ = free space wavelength in cm
Emax = breakdown voltage gradient of the dielectric filling the waveguide in Volt/cm (for dry air 30 kV/cm, for ambient air 10 kV/cm)
Chart: Peak Power vs Frequency
| 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000
WR2300 | 526.6212 | 691.9711 | 780.7698 | 836.2189 | 873.7253
WR2100 | 505.359 | 603.6639 | 662.6881 | 701.8693 | 729.5056
WR1800 | 356.7648 | 426.8444 | 470.6129 | 500.5393 | 522.1536
WR1500 | 266.9728 | 302.4189 | 326.8145 | 344.6071 | 358.0966 | 368.6196
WR1150 | 156.0606 | 172.9928 | 185.53 | 195.1925 | 202.852 | 209.0547
WR975 | 107.9109 | 119.5368 | 128.3767 | 135.3407 | 140.9658 | 145.5965
WR2300
WR2100
WR1800
WR1500
WR1150
WR975
Theoretical for straight WG, in in practice consider the limit being 10 % of this value

## Slide 22: Rectangular waveguides, Attenuation
The walls of the waveguides are not perfect conductors, they have finite conductivity resulting in skin depth effect
Due to current in the wall of the waveguides, losses appear following the rule
with
α = attenuation constant, dB/m
a0 = 3 10-7 [dB/m] for copper
a = width of waveguide in m
b = height of waveguide in m
λ = free space wavelength in m
Attenuation factors of waveguides made from different material normalized to a waveguide of same size made of copper | 
Copper | 1.00
Silver | 0.98
Aluminium | 1.30
Brass | 2.05
Chart: Peak Power vs Frequency
| 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000
WR2300 | 0.11918 | 0.08698 | 0.075652 | 0.070332 | 0.067643
WR2100 | 0.11633 | 0.094541 | 0.085004 | 0.080085 | 0.077442
WR1800 | 0.15349 | 0.12459 | 0.11126 | 0.10398 | 0.099747
WR1500 | 0.18508 | 0.15998 | 0.14626 | 0.13794 | 0.13266 | 0.12927
WR1150 | 0.27748 | 0.24602 | 0.22674 | 0.21398 | 0.20516 | 0.19893
WR975 | 0.37177 | 0.33005 | 0.3036 | 0.28555 | 0.27267 | 0.26322
WR2300
WR2100
WR1500
WR1150
WR975

## Slide 23: Rectangular waveguides
Adaptor from WR 1150 to N

## Slide 24: Integration of the HPRF in the galleries
Taking into account the theory of transmission lines, and to be compatible with the integration, we decided to have
6-1/8’’ coaxial lines in the galery (attenuation ~ 0.5 dB)
A circulator to protect the coaxial lines (attenuation ~ 0.3 dB)
WG WR 2300 HH in the core (to match high power and to ease installation) (attenuation ~ 0.1 dB)
Total attenuation ~ 1 dB

## Slide 25: HPRF stations in galery
One HPRF station per cavity, delivering power through 6-1/8’’ coaxial lines

## Slide 26: Circulators
6-1/8’’ coaxial lines connected to a circulator, with its port 2 connected to a WG WR 2300 HH

## Slide 27: Detailed view of circulators
Waveguide WR 2300 HH
50 kW load
Circulator
6-1/8’’ RF coaxial line
Adapter to WG WR 2300 HH
One can notice that the load is vertically oriented to avoid trapped air

## Slide 28: WG in the cores
The waveguide WR 2300 lenght is 10.4 metre
The line is composed of an adpter, 7 straight parts, a tailor made 45°, a 90° elbow and 2 belows
10.4m

## Slide 29: WG connection to FPC
Due to the opening of the cores, we have to design a tailor made 45° waveguide with an inclination of 0.7 degrees
Tailor made 45° waveguide

## Slide 30: Power requirements from HPRF system
10 seconds
10 ms
RF output power [kW]
40 kW → 50 kW
Time
80 kW → 100 kW
Average output power is ~ 50 [kW]
0 kW

## Slide 31: Gain flatness & monotonous
Gain
Output
Power
CW + pulsed
Pulsed
100 W
50 kW
100 kW
4 dB

## Slide 32: Gain flatness & monotonous
Output power
Input Power
CW + pulsed
Pulsed
100 W
Nominal gain
Nominal gain + 2 dB
Nominal gain - 2 dB
50 kW
100 kW
0 dBm

## Slide 33: Phase flatness & monotonous
Output power
CW + pulsed
Pulsed
100 W
30 deg
50 kW
100 kW

## Slide 34: RF power source classification
Vacuum Tubes
Grid Tubes
Triodes
Tetrodes
Pentodes
Diacrodes
Linear Beam Tubes
Klystrons
Travelling Wave Tubes (TWT)
Gyrotrons
Inductive Output Tubes (IOT)
Crossed-field Tubes
Magnetrons
Transistors
Bipolar Junction Transistor (BJT)
Field Effect Transistor (FET)
Junction Gate FET (JFET)
Metal Oxide Semiconductor FET (MOSFET)
power MOSFET
Vertically Diffused Metal Oxide Semiconductor (VDMOS)
Laterally Diffused Metal Oxide Semiconductor (LDMOS)
Silicon Germanium (SiGe)
Gallium Arsenide (GaAs)
Gallium Nitride (GaN)

## Slide 35: Available RF sources at a glance
Chart: Frequency MHz
| 30 | 30 | 30 | 30 | 30 | 30 | 50 | 50 | 60 | 80 | 80 | 110 | 110 | 110 | 120 | 120 | 130 | 200 | 200 | 200 | 200 | 200 | 200 | 210 | 220 | 352 | 352 | 400 | 400 | 450 | 450 | 815 | 500 | 605 | 503 | 805 | 400 | 352 | 402 | 805 | 350 | 352 | 401 | 500 | 500 | 500 | 500 | 700 | 500 | 915 | 470 | 860 | 128 | 200 | 600 | 500 | 860
Tetrode peak | 1000 | 700 | 500 | 1500 | 500 | 4000 | 600 | 1000 | 1000 | 120 | 2500 | 500 | 3000 | 120 | 200 | 30 | 100 | 15 | 200
Tetrode CW | 750 | 700 | 400 | 300 | 150 | 1500 | 2000 | 1500 | 2000 | 100 | 100 | 1700 | 60 | 200 | 60 | 450 | 40 | 20 | 60
Klystron peak | 2800 | 2500 | 5000
Klystron CW | 1100 | 1300 | 300 | 180 | 250 | 310 | 800 | 1000 | 800 | 100
IOT peak | 130 | 110 | 100 | 100
IOT CW | 30 | 90 | 80 | 85 | 60 | 60
SSPA*100 | 60 | 30 | 140 | 144 | 140 | 120 | 45

## Slide 36: Overhead and maximum power
Chart: Grid tubes, Klystrons, SSPA
| 0 | 0.14857142857142858 | 0.29428571428571426 | 0.45 | 0.61428571428571432 | 0.79285714285714282 | 1 | 1.3142857142857143 | 1.8871428571428572 | 3.2142857142857144 | 6.4285714285714288 | 0.54545454545454541 | 0.61818181818181817 | 0.72727272727272729 | 0.83636363636363631 | 0.98181818181818181 | 1 | 1.1272727272727272 | 1.3090909090909091 | 1.509090909090909 | 1.7636363636363637 | 2.0363636363636362 | 2.3636363636363638 | 2.4727272727272727 | 3.676408537275877E-2 | 0.16810482465774959 | 0.30804216967959258 | 0.44534997545593652 | 0.59379996727458195 | 0.75953918166077616 | 0.999381782168974 | 1.2091871815897948
Tetrode, Diacrode & IOT | 0 | 0.16667 | 0.33333 | 0.5 | 0.66667 | 0.83333 | 1 | 1.1667 | 1.3333 | 1.5 | 1.6667
Klystron | 0.593 | 0.67 | 0.763 | 0.876 | 0.979 | 1 | 1.092 | 1.219 | 1.284 | 1.312 | 1.311 | 1.282 | 1.275
SSPA | 0.025333 | 0.16667 | 0.33333 | 0.5 | 0.66667 | 0.83333 | 1 | 1.0833
Possibility of short power excursions only for gridded tubes
(possible for SSPA at a cost of an overdesigned system)

## Slide 37: No klystron at that ‘little power’ available
Klystron of such small power does not exist on the market
The ones that exist provide too much power and are not possible to integrate in our ‘small’ galleries
In addition, for such specific power requirements, as output power reduces if we go over saturation (nominal) point of operation, we would need to operate lower than nominal point of operation
This would induce loss of efficiency, almost doubling the cost (acquisition + operation)
Finally, phase stability is given by construction from HV stability (very expensive)
CERN LHC, 16 x TH 2167 klystrons in LHC UX45 cavern
delivering 330 kW @ 400 MHz, into operation since 2008

## Slide 38: SSPA, an option but at high cost
Transistors are destroyed in case of large overdrive (+ 3 dB = x 2) longer than ~ 100 µs
Hard protection limit are needed, could be built in, but then it is complex to manage for LLRF, so we try to have a good LLRF protection system
To avoid destruction, overhead must be perfectly and correctly defined
Overhead very costly (compare to gridded tubes)
Chart: SSPA
| 0.04 | 0.19 | 0.34 | 0.48 | 0.66 | 0.83 | 1.1000000000000001 | 1.33 | 1.65 | 1.92 | 2.2000000000000002 | 2.21
SSPA | 3.4 | 22.4 | 44.7 | 67 | 89 | 112 | 134 | 145 | 154 | 161 | 165 | 0 | 0
Operating point CW
Operating point pulsed
Spare slides if you wish to better understand the constraints

## Slide 40: SSPA obsolescence
When we started SPS SSPA in 2017, the chosen transistor was the ‘best for new design’ quoted by the transistor supplier
Beginning 2022, we received a ‘Last Buy Order’ email…
(the same with other labs, within 3-5 years, ‘best to use’ transistors turn to be ‘do not use for new design’, and to ‘obsolete’ item…)
The difficulty with Accelerators is that when we buy a new amplifier, it must last 20-25 years
Changing the transistor generation is often linked to changing the operating voltage, this makes that change out of budget
The amplifier architecture should then be designed such that the amplifier will last the 20 years without major upgrade
Spare slides if you wish to better understand the constraints

## Slide 41: IOT, ‘like if designed’ for the Crab
A great advantage of gridded tubes is that they allow overdrive without damage
Tetrodes & Diacrodes are limited in frequency (max ~ 400 MHz)
IOT can operate from low (100 MHz) to high frequencies (1.3 GHz), including 400 MHz
The gain of an IOT is around 23 dB, so to reach 100 kW, an only 500 W driver is needed
Chart: IOT TH795 @ 400 MHz
| 0 | 0.08 | 0.15846153846153846 | 0.24230769230769231 | 0.33076923076923076 | 0.42692307692307691 | 0.53846153846153844 | 0.70769230769230773 | 1.0161538461538462 | 1.7307692307692308 | 3.4615384615384617
Tetrode, Diacrode & IOT | 0 | 12.6 | 25.2 | 37.8 | 50.4 | 63 | 75.6 | 88.2 | 100.8 | 113.4 | 126
Operating point CW
Operating point pulsed

## Slide 42: IOT, Already tested in the SPS
CERN SPS, TH 793 IOT, Trolley (single amplifier), and transmitter (combination of amplifiers)
Two transmitters of four tubes delivering 2 x 160 kW @ 801 MHz, into operation since 2014

## Slide 43: IOT, Already tested in the SPS
CERN SPS, TH 795 IOT upgrade to deliver full power at 801 MHz
The tube is an evolution of the TH793, providing even more reliability than the TH793

## Slide 44: IOT trolley designed by CERN for SPS tests
605
593
788
620
TH18795 800 MHz trolley
TH18795 modified by CERN 400 MHz trolley

## Slide 45: IOT trolley designed by CERN for SPS tests
TH18795 800 MHz trolley and 800 MHz coupling elements
TH18795modified by CERN
400 MHz trolley and
400 MHz coupling elements

## Slide 46: Still difficult linearisation at very low power
Following a careful adjustment of all parameters (Fc, BW, HV, Focus, Heater), correct transfer curve
If some parameters are not correct (Fc, BW, HV, Focus, Heater), step in transfer curve at low power
The difficulty is that this never occurs on a 50 Ω load

## Slide 47: Still difficult linearisation at very low power
During MD, we noticed a problem with a tube that needed a replacement of this tube
After exchange, as retuning all parameters, we were able to remove the nonlinearity
The difficulty is that this phenomena does not appear when the amplifier is connected onto a 50 Ω load
Next MD, we will retune all parameters of the second amplifier
Jun 2023, MD
Jul 2023, MD
Cav 1
Cav 2
Cav 1
Cav 2

## Slide 48: New trolley as a collaboration CERN/Thales
Two output cavities
will become
one single output cavity with a radial coupling element

## Slide 49: New HPRF as a collaboration station CERN/Thales

## Slide 50: IOT HPRF schedule
2022
2023
2024
2025
2026
2027
2028
Pre-series
Integration & commissioning
Series production
2
4
4
4
4
2
As per 2018
2022
2023
2024
2025
2026
2027
2028
Pre-series
Integration & commissioning
Series production
MS
4
4
4
4
2
As per 2023
Contract
Proto at CERN
Proto OK
2029
In line with possible Japanese in-kind
edms 2874821

## Slide 51: HPRF stations, where?, when?
2023
2024
HPRF1
BB3 (FPC processing)
HPRF2
BA6
HPRF3
BA6
Collaboration with Thales
SM18
BA6 + FPC processing
Canada on request

## Slide 52: FPC

## Slide 53: RF Processing

## Slide 54: Clean room preparation of FPC

## Slide 55: Arcing in FPC

## Slide 56: Arcing in FPC

## Slide 57: RF processing to avoid failures

## Slide 58: FPC RF processing

## Slide 59: FPC transport to Canada and UK
Initially, we intended to disassemble the two couplers from their test box, and to transport them individually
However, this would remove all the RF processing work we did, so we now prefer to send them still assembled onto their test box, under vacuum

## Slide 60: Last year at Uppsala

## Slide 61: Couplers Master Schedule
DQW
3 HOMC
RFD
11
12
06
01
02
03
04
05
3 HOMC
09
07
08
2 FPC
2023
2024
2 FPC
10
11
12
11 HOMC
2 FPC
2 FPC
6 Lines
2 FPC
2 FPC
2 FPC
4 FPC
2 PUA + 2 HFHOMC
7 PUA + 7 HFHOMC
5 PUA + 5 HFHOMC
2 Lines
10 HOMC
6 Lines
6 Lines
2 Lines
6 Lines
9 HOMC
2 FPC
2 FPC
01
02
03
2025
2 FPC
06
04
05
09
07
08
10
07
06
08
09
01
02
03
04
05
4 FPC
Delivered Canada
Delivered UK
Delivered CERN

## Slide 62: Conclusion
IOT is really THE solution for Crab
We really hope that in-kind with Japan will happen
Our schedule is in-line with proposals made by our colleagues
Production of FPC (and HOMC and RF lines for cryomodule) is on good way

## Slide 63: They did not know it was impossible, so they did it (Mark Twain) Simplicity is the ultimate sophistication (Leonardo da Vinci, 500 years ago)

## Slide 64: Thanks to all colleagues involved with this HPRF & couplers projects Thanks to all colleagues from Japan for trying to make the in-Kind a reality Thanks to Rama and Ofelia (WP4 leaders), to RF management and to HL-LHC management for supporting us with this very exciting (and very challenging) project We (SY-RF teams and all associated colleagues from many groups) are devoted to provide HL-LHC with reliable RF systems

## Slide 65: SSPA obsolescence spare slides

## Slide 66: Transistor power ratings
Voltage limits |  | 
 | 2002 | Since 2006
900 MHz | 41 V/m | 3 V/m
1800 MHz | 58 V/m | 
2100 MHz | 61 V/m | 
Device | Distance | Power
Phone | 20 km | 2 W
Microcell | 2 km | 10 W
Macrocell | 20 km | 50 W
The tendency is to increase the number of smaller cells in order to keep the phone battery autonomy, increase the data bandwidth, and reduce the exposition of population to too high electromagnetic fields

## Slide 67: Macro cells vs Small cells vs femtocells

## Slide 68: A few numbers to situate RF transistors in accelerators
Chart: Millions of Mobile phones over time (world wide)
| 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
Millions of Mobile phones | 34 | 56 | 91 | 145 | 215 | 318 | 492 | 740 | 962 | 1159 | 1418 | 1765 | 2205 | 2745 | 3368 | 4030 | 4640 | 5290 | 5890 | 6261 | 6661 | 6998 | 7152 | 7481 | 7724 | 7997 | 8292 | 8335 | 8648
Chart: Transistor market Size in Billions USD
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Series 1 | 1.45 | 1.5 | 1.6 | 1.75 | 2.1 | 2.25 | 2.6
Some of the Key Players
Ampleon
Analog Devices
BONN Elecktronik
Broadcom Pte.
Cree
General Dynamics
Infineon
Integra
MACOM
Maxim Integrated
Mitsubishi
NoleTec
NXP Semiconductors
Qorvo
Qualcomm
Skyworks Solutions
STMicroelectronics
Tagore Technology
Thales Alenia Space
Toshiba

## Slide 69: A few numbers to situate RF transistors in accelerators

## Slide 70: A few numbers to situate RF transistors in accelerators
Source: RF Power Semiconductor Market Trends From Yole Développement Patrick Hindle - Editor, Microwave Journal July 11, 2017

## Slide 71: A few numbers to situate RF transistors in accelerators
FCC (400 MHz to 800 MHz) due in ~ 15 years

## Slide 72: Transistor power ratings – personal view of future perspective (CWRF 2016, updated 2022)
Transistor supplier main business will not be higher power per transistor
Conclusion: below a GHz, 1 kW per transistor (LDMOS) seems (to me) a very good goal
8.5 Billions Smartphones in 2021
90 Millions Femtocell stations 2016
7 Millions Macrocell stations 2017
NXP Semiconductors revenue in 2020 was $8’600 Millions
Assumption (with a lot of simplifications)
  Cost of a LDMOS ~ $100
  Total cost of FCC ~ $100 Million
  Over minimum 5 years
  of construction ~ $20 Million per year
RF for accelerators could be 20 / 8600 = 0.2 % of main suppliers' revenue
Machine | # RF stations | Power | # 1 kW LDMOS
FCC | 1’000 | 1 MW | 1’000’000

## Slide 73: Drain voltage
Evolution of the transistors market is quick
This is still a volatile market (as tubes have been a century ago)
Drain voltage is increasing with the development of transistors, and the Drain supply used with a generation of device could not suit the next generation (moving from 12V to 24 V to 30 V to 36 V to 48 V to 50 V to 60 V to 80 V to 100 V)
Changing the transistor will not be the only challenge, either it will be under used as keeping the previous power supply, or power supply voltage will have to be upgraded
Why LDMOS is the best technology for RF energy
Technology
News | June 21, 2018
By Jean-Pierre Joosting
SOLEIL elementary 600 W 300 Vdc / 30 Vdc converter board

## Slide 74: SSPA granularity & redundancy

## Slide 75: Combination
3 dB combiner is very common for RF power combination at these frequencies since the 70’s
If one correctly adjusts the phases and the amplitudes, equations show that
With PA1 = PA2 = PA3 = PA4 = P then
Pout = 4 P
Load A5 = A6 = A7 = 0
In case one amplifier is stopped (PA1 for example), then
Pout = (9/16) 4P = 2,25 P
Load A5 = 0,5 P
Load A7 = 0,25 P

## Slide 76: Cavity Combiner
With our latest combiner, @ 750 MHz, the body is composed of four main pieces
a tube
a bottom plate
a top plat
an output probe housing
The tube has machined holes compatible with N-type solder cups, the bottom plate has an indentation for disc tuning and the output probe housing is compatible with a standard EIA 3-1/8” flange
The return loss of the output port is ≤ -20 dB between over a 1 MHz bandwidth
The transmission between the 96 individual inputs and output is -19.84 ± 0.05 and the cross talk between the inputs is < -35 dB

## Slide 77: Redundancy
In order to ensure 100 % availability, given a Redundancy, the technology of the combining system will define the number of Units
Power per Unit = 1
Pout must be 12 x P
at all time, even with 2 Units ‘off-line’
In order to be 100 % available a 3 dB combiner requires
16 Units
Pout must be 12 x P
at all time, even with 2 Units ‘off-line’
In order to be 100 % available a cavity combiner only requires 14 Units

## Slide 78: Redundancy
In order to ensure 100 % availability, given a Granularity, the technology of the combining system will define the number of Units
Pout must be 8 x P
at all time, even with 1 Unit ‘off-line’
In order to be 100 % available a 3 dB combiner requires 16 Units
1 Module =
4 x Units
Pout must be 8 x P
at all time, even with 1 Unit ‘off-line’
In order to be 100 % available a cavity combiner only requires 12 Units

## Slide 79: Redundancy & Granularity for Crab
Let imagine that we go for a SSPA for Crab
We would have to deliver 50 kW CW and 100 kWp
At 400 MHz, power per LDMOS transistor would (safely) be around 500 W, breaking with 2.2 x the 500 W equivalent drive
Going with single Power Supply per transistor to keep the granularity, and imposing full characteristics even with 10 % Units off, this would mean
With a 3 dB combiner
256 Units
Full power with 230/256 Units = 103 KWp
With a cavity Combiner
220 Units
Full power with 200/220 Units = 100 kWp
Chart: SSPA
| 0.04 | 0.19 | 0.34 | 0.48 | 0.66 | 0.83 | 1.1000000000000001 | 1.33 | 1.65 | 1.92 | 2.2000000000000002 | 2.21
SSPA | 3.4 | 22.4 | 44.7 | 67 | 89 | 112 | 134 | 145 | 154 | 161 | 165 | 0 | 0
Operating point CW
Operating point pulsed

## Slide 80
CERN 2 x 16 x 80 = 2560 modules of 2 kWp each @ 200 MHz solid state amplifiers (2021) in the SPS
delivering 2 x 1.6 MWp (compared to 2 x 2.5 MW possible)