## Slide 1: Status report on alignment on RFD prototype : Crab-cavities (Collaboration : STFC / CERN)
Vivien RUDE
2023-09-27
13th HL-LHC Collaboration Meeting, Vancouver (Canada), 25-28 September 2023
On behalf :
Mateusz SOSIN
Clara CALA FRANCO
Hélène MAINAUD DURAND
Andreas HERTY
Vincent BARBARROUX
Michel NOIR
Roberto FERNANDEZ BAUTISTA
Vancouver, 24 Sept. 2023

## Slide 2: Outline
Alignment objective for HL-LHC internal monitoring
  Internal monitoring
  Crab-cavities configuration
  Alignment requirement
  Alignment simulation for RFD prototype
RFD prototype (Survey tasks : STFC-CERN collaboration)
  Determination of the position of the capacitive plates of the cavities
  Alignment of the 2 cavities before and after connection in clean room
  Thermal contraction anticipation
  Alignment at step 4 : on the trolley
  Alignment at step 6 : cavities suspended from the top plate
  Alignment at step 9 : cavities suspended from the top plate inserted in the cryomodule
  FSI installation
  Diverse information
  Schedule expected after reception of the cryomodule at CERN

## Slide 3: Internal monitoring for “special” components
Vacuum vessel
Cold mass
Crab cavities
Cryomodule
Nominal axis
Vacuum vessel
Axis of the Cold mass
Axis of the Crab cavities
Cryomodule
Q1, Q2a, Q2b, Q3
Crab-Cavities

## Slide 4: Internal monitoring : Configuration
beam
  FSI : Frequency Scanning interferometry
   Absolute distance measuring interferometric technique
FSI target on the flange of
Helium TANK of the cavities
FSI Head (sensor) on the Cryomodule

## Slide 5: Configuration (RFD prototype) : Requirement and Uncertainty
TANK 1 | Accuracy
Tx (mm) Radial | 0.088
Ty (mm) longitudinal | 0.044
Tz (mm) vertical | 0.015
Rx (mrad) | 0.044
Ry (mrad) | 0.215
Rz (mrad) | 0.233
Scale (ppm) | 66
TANK 2 | Accuracy
Tx (mm) Radial | 0.021
Ty (mm) longitudinal | 0.077
Tz (mm) vertical | 0.011
Rx (mrad) | 0.023
Ry (mrad) | 0.180
Rz (mrad) | 0.047
Scale (ppm) | 101
 | Requirement
Tx (mm) Radial | < 0.1
Ty (mm) longitudinal | --
Tz (mm) vertical | < 0.1
Rx (mrad) | <0.3
Ry (mrad) | <1.7
Rz (mrad) | <0.3
Scale (ppm) | --
TANK1
TANK2

## Slide 6: Outline
Alignment objective for internal monitoring
  Internal monitoring
  Configuration
  Alignment requirement
  Simulation for RFD prototype
RFD prototype (Survey tasks)
  Determination of the position of the capacitive plates of the cavity
  Alignment of the 2 cavities before and after connection in the clean room
  Thermal contraction anticipation
  Alignment at step 4 : on the trolley
  Alignment at step 6 : cavities suspended from the top plate
  Alignment at step 9 : cavities suspended from the top plate inserted in the cryomodule
  FSI installation
  Diverse information
  Schedule expected after reception of the cryomodule at CERN

## Slide 7: Determination of the position of the capacitive plate of the cavity
Y
Z
Y
Z
X
A
B
H_HOM
FPC
V_HOM
Pick-up
Plot
tuning
Y
Z
X
A
B
H_HOM
FPC
V_HOM
Rod
tuning
Bare Cavity
Cavity inside the TANK
Side view
(VERTICAL)
A
B
Y
Z
Capacitive
plates
Capacitive
plates
Chart: 
| -95.5 | 95.5
plaque capacitive | 0 | 0
Bride AB | 1.24 | -1.72
Capacitive
plates
Axe AB
(Stainless steel flanges axis)
Flange B
Flange A
Z [mm]
Y [mm]

## Slide 8: Alignment of the 2 cavities before connection in the clean room
Nominal axis (cavity line)
 trajectory of the rails
Coordinate frame :
Primary axis : Nominal axis (cavity line)  trajectory of the rails
Secondary axis : Normal vector to vertical plane of rails
Origin : Beginning of the rail
X
Y
Z
Origin
283 mm
324 mm

## Slide 9: Configuration (DQW-SPS-2018) : Cooling down
X
Y
Z
Take into account of thermal contraction and vacuum

## Slide 10
Position after STEP 4 (June 2023)
Longitudinal | Nominal | After step 4
TANK1 | 809.6 mm | 809.6 mm
TANK2 | 1992.1 mm | 1992.1 mm
Longitudinal . Difference to nominal
Max : 0.1 mm
Chart: Vertical position of the cavities w.r.t. Nominal
| 0 | 3000
nominal BEAM axis | 0 | 0
TANK1 Nominal position | -0.88 | -0.71
TANK2 Nominal position | -0.9 | -0.73
TANK1 (14th June 2023) | -0.931 | -0.793
TANK2 (14th June 2023) | -0.959 | -0.748
Chart: Radial position of the cavities w.r.t. Nominal
| 0 | 3000
NOMINAL BEAM AXIS | 0 | 0
TANK1 Nominal position | -0.99 | -0.79
TANK2 Nominal position | -0.88 | -0.68
TANK 1 (14th June 2023) | -0.951 | -0.768
TANK2 (14th June 2023) | -0.916 | -0.743
Vertical : Difference to nominal
Max : 0.1 mm
Radial : Difference to nominal
Max : 0.1 mm

## Slide 11
Chart: Radial position of the cavities w.r.t. Nominal
| 0 | 3000
NOMINAL BEAM AXIS | 0 | 0
TANK1 Nominal position | -0.99 | -0.79
TANK2 Nominal position | -0.88 | -0.68
TANK1 (after step6) | 5.53 | 4.851
TANK2 (after step6) | 4.404 | 3.025
TOP VIEW
Y
X
Position after STEP 6 (July 2023)
5 mm
5-6 mm

## Slide 12
Position after STEP 6 (August 2023)
Chart: Vertical position of the cavities w.r.t. Nominal
| 0 | 3000
nominal BEAM axis | 0 | 0
TANK1 Nominal position | -0.88 | -0.71
TANK2 Nominal position | -0.9 | -0.73
TANK1 (after step6) | -1.144 | -0.864
TANK2 (after step 6) | -1.105 | -0.878
Chart: Radial position of the cavities w.r.t. Nominal
| 0 | 3000
NOMINAL BEAM AXIS | 0 | 0
TANK1 Nominal position | -0.99 | -0.79
TANK2 Nominal position | -0.88 | -0.68
TANK1 (after step6) | -0.981 | -0.948
TANK2 (after step6) | -0.878 | -0.643
Longitudinal | Nominal | After step 6
TANK1 | 809.6 mm | 813.6 mm
TANK2 | 1992.1 mm | 1995.5 mm
+4.0 mm
+3.4 mm
Difference
to nominal
Vertical : Difference to nominal
Max : 0.2 mm
Radial : Difference to nominal
Max : 0.2 mm

## Slide 13
Position after STEP 9 (September 2023)
Chart: Vertical position of the cavities w.r.t. Nominal
| 0 | 3000
nominal BEAM axis | 0 | 0
TANK1 Nominal position | -0.88 | -0.71
TANK2 Nominal position | -0.9 | -0.73
TANK1 (11 sept 2023) | -1.357 | -1.17
TANK2 (11 sept 2023) | -1.527 | -1.047
Chart: Radial position of the cavities w.r.t. Nominal
| 0 | 3000
NOMINAL BEAM AXIS | 0 | 0
TANK1 Nominal position | -0.99 | -0.79
TANK2 Nominal position | -0.88 | -0.68
TANK1 (11 sept 2023) | -0.703 | -0.805
TANK2 (11 sept 2023) | -0.675 | -0.686
Longitudinal | Nominal | After step 9
TANK1 | 809.6 mm | 813.5 mm
TANK2 | 1992.1 mm | 1995.6 mm
+3.9 mm
+3.5 mm
Difference
to nominal
Vertical : Difference to nominal
Max : 0.6 mm
Radial : Difference to nominal
Max : 0.3 mm
Radial and vertical objectives for the final alignment : < 0.1 mm
(will be done at CERN, before Bunker test)

## Slide 14
FSI installation
targets
Sensors : FSI Heads

## Slide 15
Origin
X
Y
Z
FSI targets (installation done in June 2023)
Objective :  < 2 mm
 | Difference To nominal position |  | 
 | X [mm] | Y [mm] | Z [mm]
1 | -1.1 | 0.4 | 0.8
2 | -0.8 | 0.2 | 1.5
3 | 0.1 | -0.3 | 1.9
4 | 0.1 | -0.2 | 0.6
5 | 0.8 | 0.5 | -2.0
6 | 1.1 | 0.2 | -2.6
7 | 0.6 | -0.4 | -2.1
8 | 0.3 | -0.3 | -1.7
9 | -0.9 | 2.1 | -0.9
10 | -0.5 | 1.8 | 0.0
11 | 0.2 | 2.1 | 0.4
12 | 0.3 | 2.3 | -0.7
13 | 0.3 | -1.1 | -0.2
14 | 0.5 | -1.4 | -0.2
15 | 0.3 | -1.4 | 0.3
16 | 0.6 | -1.2 | 0.2

## Slide 16
FSI heads / installation on top plate and cryomodule

## Slide 17
2 °
1 °
0.5 °
Close
to the
noise
0.5° = 8.7 mrad  8.7 mm at 1 m
FSI heads : Calibration

## Slide 18
Validation of FSI observation (June and September 2023)
+ 3.9 mm
w.r.t. nominal
+ 3.5 mm
w.r.t. nominal
 |  | After step 4 | 
 | Optical sight | WARM Angle (°) [ < 0.5° ] | Estimated COLD Angle (°) [ < 0.5° ]
TANK1 | Head1  Target 1 | 0.36 | 0.42
TANK1 | Head2  Target 2 | 0.23 | 0.33
TANK1 | Head3  Target 3 | 0.05 | 0.12
TANK1 | Head4  Target 4 | 0.20 | 0.05
TANK1 | Head5  Target 5 | 0.17 | 0.22
TANK1 | Head6  Target 6 | 0.32 | 0.24
TANK2 | Head7  Target 11 | 0.33 | 0.27
TANK2 | Head8  Target 12 | 0.17 | 0.09
TANK2 | Head9  Target 9 | 0.40 | 0.42
TANK2 | Head10  Target 10 | 0.11 | 0.18
TANK1 | Head11  Target 7 | 0.27 | 0.24
TANK1 | Head12  Target 8 | 0.25 | 0.37
TANK2 | Head13  Target 13 | 0.13 | 0.19
TANK2 | Head14  Target 14 | 0.26 | 0.31
TANK2 | Head15  Target 15 | 0.23 | 0.24
TANK2 | Head16  Target 16 | 0.26 | 0.26
 < 0.5 °
0.5 ° <  < 1 °
 > 1 °
Acceptable
Objective
Not acceptable
After step 9 | 
WARM Angle (°) [ < 0.5° ] | Estimated COLD Angle (°) [ < 0.5° ]
0.40 | 0.40
0.20 | 0.22
0.42 | 0.29
0.55 | 0.42
0.48 | 0.51
0.56 | 0.53
0.47 | 0.43
0.31 | 0.32
0.64 | 0.60
0.34 | 0.28
0.19 | 0.07
0.18 | 0.26
0.37 | 0.40
0.26 | 0.32
0.20 | 0.27
0.13 | 0.20

## Slide 19
Cryomodule and
top plate measurement

## Slide 20
Top plate installed on the cryomodule
Top plate hanging
1 mm
Difference
Deformation of the top plate between installation on cryomodule and hanging
For the test under vacuum scheduled end of September, a special attention will be given

## Slide 21
Difference up to 1.6 mm
Deformation of the cryomodule with and without the top plate installed on the top
For the test under vacuum scheduled end of September, a special attention will be given

## Slide 22
Next step (at CERN)
Measurement with FSI possible
2 days of installation
and measurement
Test of adjustment system
+ realignment
RFD prototype at CERN
Installation : FSI system, Optical fibers
Laser Tracker : Measurement of FSI Heads
 Position of the cavities inside the cryomodule
Under vacuum
Laser Tracker : Impact of vacuum on the cryomodule
Measurement with FSI possible
 Position of the cavities inside the cryomodule
0.5 days of measurement
Laser Tracker
Cooling down
Laser Tracker : Impact of cooling down on the cryomodule
Measurement with FSI possible
 Position of the cavities inside the cryomodule
0.5 days of measurement
Laser Tracker if possible
Objective : < 0.1 mm w.r.t. nominal

## Slide 23
Conclusion
The RFD prototype is ready to go into the SPS accelerator !
Many thanks to STFC team :
Nik
Ed
Luke
Ryan
Carlos
Andy
…
Many thanks to CERN team :
Teddy
Marco
Kurt
Simon
Raphael
Luca
Nuria
Katarzyna
Rama
Ofelia
Julien
…
Thank you for your attention

## Slide 24
Thank you
for your attention

## Slide 25
SPARE

## Slide 26: Alignment requirements for the cryostat / cryomodule
R = 0.33 mm
Left
Right
Alignment objectives (2023) for FRAS
  Position of the components cryostat along one side of the tunnel : +/- 0.1 mm *
  Position of the components cryostat along one side of the tunnel w.r.t the other side : +/- 0.33 mm *
Q5
Q4
CC2
CC1
D2
TCLX
TCTPH
TCTPV
TAXN
D1
CP
Q3
Q2b
Q2a
Q1
EXP.
UPS gallery
P1
P2
P3
P4
P5
P6
Q1
Q2a
Q2b
Q3
CP
D1
TAXN
TCTPV
TVTPH
TCLX
D2
CC1
CC2
Q4
Q5
Alignment between Q1 and Q5 :
Limits :  (1 sigma) < 0.1 mm
Alignment between Q5-left and Q5-right :
Limits :  (1 sigma) < 0.33 mm
R = 0.1 mm
R = 0.1 mm
* On main components
Inner
Tracker

## Slide 27: Alignment requirements for the cryostat / cryomodule
R = 0.33 mm
Left
Right
Alignment objectives (2023) for FRAS
  Position of the components cryostat along one side of the tunnel : +/- 0.1 mm *
  Position of the components cryostat along one side of the tunnel w.r.t the other side : +/- 0.33 mm *
Q5
Q4
CC2
CC1
D2
TCLX
TCTPH
TCTPV
TAXN
D1
CP
Q3
Q2b
Q2a
Q1
EXP.
UPS gallery
P1
P2
P3
P4
P5
P6
Q1
Q2a
Q2b
Q3
CP
D1
TAXN
TCTPV
TVTPH
TCLX
D2
CC1
CC2
Q4
Q5
R = 0.1 mm
R = 0.1 mm
* On main components
Inner
Tracker

## Slide 28: External monitoring
Remote alignment thanks to alignment sensors and actuators:
FRAS LSS components equipped with reference sensors
  WPS – Wire Position Sensor (Radial, Vertical position)
  HLS – Hydrostatic Reference Sensor (Vertical Leveling, roll)
  Inclinometers – (Roll)
  Long range monitoring from UPS gallery
  Longitudinal monitoring
Each component equipped in motorized adapters – for the remote adjustment of its position
Sensors | Technology | Largest standard uncertainties | Uncertainty on 2023 | 
WPS | Capacitive | Calibration of WPS (if Lcable < 70 m) Calibration of WPS (if 70m < Lcable < 100 m) | 5 µm 15 µm | 50 µm (12 µm for WPS in UPS)
 |  | Shape of wire | 10 µm | 
 |  | Position of WPS in the framework of the vacuum vessel Position of WPS in the framework of the UPS plate | 50 µm 2 µm | 
HLS | Interferometry | Calibration of HLS | 5 µm | 50 µm (70 µm for HLS double)
 |  | Shape of water | 10 µm | 
 |  | Position of HLS in the framework of the vacuum vessel | 50 µm | 
Inclinometer | Capacitive Interferometry | Calibration of inclinometer | 15 µrad | 150 µrad
 |  | Position of the inclinometer in the framework of the vacuum vessel | 150 µrad | 
Long range FSI 14 m | Interferometry | Calibration of the Long range FSI | 20 µm | 50 µm
 |  | Position of the FSI in the framework of the UPS plate | 2 µm | 
 |  | Position of the target in the framework of the vacuum vessel | 50 µm | 
Longitudinal FSI | Interferometry | Calibration of Longitudinal FSI | 10 µm | 300 µm
 |  | Position of Longitudinal FSI in the tunnel framework | 300 µm | 
 |  | Position of the target in the framework of the vacuum vessel | 50 µm | 
Accuracy of each sensor in the framework of cryostat

## Slide 29
Chart: DCUM [m]
| -215 | -207 | -200 | -178 | -171 | -164 | -162 | -157 | -148 | -140 | -136 | -133 | -128 | -120 | -115 | -110 | -80 | -77 | -72 | -63 | -62 | -51 | -41 | -40 | -30 | -30 | -29 | -20.010000000000002 | -20 | -15 | 15 | 20 | 20.010000000000002 | 29 | 30 | 40 | 41 | 51 | 62 | 63 | 72 | 77 | 80 | 90 | 95 | 110 | 128 | 133 | 136 | 140 | 148 | 157 | 162 | 164 | 171 | 178 | 200 | 207 | 215
Realistic accuracy | 0.33929 | 0.32394 | 0.31421 | 0.26721 | 0.25842 | 0.24508 | 0.24128 | 0.23181 | 0.20922 | 0.19994 | 0.19254 | 0.18701 | 0.17787 | 0 | 0 | 0 | 0.088849 | 0.076761 | 0.073643 | 0 | 0.053687 | 0.055835 | 0.010982 | 0.048705 | 0.010764 | 0 | 0.04873 | 0.077473 | 0.077491 | 0 | 0 | 0.07755 | 0.077538 | 0.048749 | 0.010764 | 0.048489 | 0.010981 | 0.055618 | 0.053255 | 0 | 0.073665 | 0.076855 | 0.088698 | 0 | 0 | 0 | 0.17777 | 0.1869 | 0.19242 | 0.19982 | 0.20908 | 0.23166 | 0.24113 | 0.24493 | 0.25825 | 0.26703 | 0.31401 | 0.32372 | 0.33822
Position accuracy (radial) of the mechanical axis of component in R-general
The RADIAL propagation of errors is linear
P1
P2
P3
P4
P5
P6
The uncertainty at Q5 is largely influenced by :
Uncertainty Q3-Q3 (link Left-Right through UPS gallery)
Uncertainty Q1-D1 (slope of the error propagation)
Wire Q1-D1
Wire Q1-D1
Wire Q1-Q5
Wire Q1-Q5

## Slide 30: Precision / Accuracy
Accuracy and precision
  The “absolute” position of CC1 (in general coordinate system) will be known with an accuracy of 0.25 mm (1)
  The “absolute” position of CC2 (in general coordinate system) will be known with an accuracy of 0.25 mm (1)
  The “relative” position of CC1 w.r.t. CC2 will be known with a precision of few microns
  The “relative” movement of CC1 will be known with a precision of few microns
UPS gallery
P1
P2
P3
P4
P5
P6
R = 0.33 mm
Left
Right
R = 0.1 mm
R = 0.1 mm
General coordinate system
Experience
IP
CC2
CC1

## Slide 31: Multi-target Frequency Scanning Interferometry (FSI)
from Mateusz Sosin
RT1
RT3
RT2
α – is a sweep rate of the laser ( - laser frequency change in time );
c – speed of light;
n – refractive index of light transmission medium;
– time of flight of laser to the target