## Slide 1: Full Remote Alignment System (FRAS) Status and plans
Hélène Mainaud Durand, on behalf of WP15.4 members
HL-LHC collaboration board, Vancouver, 27 September 2023

## Slide 2: Outline
A short reminder on Full Remote Alignment System (FRAS)
Single Component Test : status
Inner-Triplet String Test: status and next steps

## Slide 3
Introduction to Full Remote Alignment System (FRAS)
It consists of alignment systems (alignment sensors, motorized adapters, their acquisition and control/command systems, associated software) allowing to determine the position of components and readjust them remotely within a range of ± 2.5 mm.
FRAS will provide:
  An important reduction of the dose taken by surveyors as no access in tunnel will be needed between YETS or LS
  A reduction in the mechanical misalignment, allowing to decrease the required correctors strength and to push the accelerator performance
  A gain in aperture for several components
All components from Q1 to Q5 will be:
  Either equipped with sensors and motorized axes
  Or FRAS compatible: they are static components that can absorb the displacements of their adjacent components.

## Slide 4: Alignment requirements for the components
R = 0.33 mm
Left
Right
Alignment objectives (2023) for FRAS
  Position of the components cryostat along one side of the tunnel : +/- 0.1 mm *
  Position of the components cryostat along one side of the tunnel w.r.t the other side : +/- 0.33 mm *
Q5
Q4
CC2
CC1
D2
TCLX
TCTPH
TCTPV
TAXN
D1
CP
Q3
Q2b
Q2a
Q1
EXP.
UPS gallery
P1
P2
P3
P4
P5
P6
Q1
Q2a
Q2b
Q3
CP
D1
TAXN
TCTPV
TVTPH
TCLX
D2
CC1
CC2
Q4
Q5
Alignment between Q1 and Q5 :
Limits :  (1 sigma) < 0.1 mm
Alignment between Q5-left and Q5-right :
Limits :  (1 sigma) < 0.33 mm
R = 0.1 mm
R = 0.1 mm
* On main components
Inner
Tracker

## Slide 5: Solutions for Full Remote Alignment
  Wire Positioning Sensors (WPS):
    Based on capacitive technology, performing continuous radial and vertical offset measurements w.r.t. a stretched wire, within a submicrometric resolution
    In-house design based on flexible polyimide PCB with electrodes printed on the surface and coated with gold
  Hydrostatic Levelling Sensor (HLS):
    Based on the communicative vessel principle, performing vertical offset w.r.t. a water surface, within a submicrometric resolution
    Frequency Scanning Interferometry (FSI) technology
    Qualification under finalization
  Inclinometers (in-house concept):
    Vertical pendulum measured either via capacitive or FSI technologies
    First tests: repeatability below ±10 µrad
HLS
WPS
WPS
WPS
WPS

## Slide 6: Solutions for Full Remote Alignment
UAP platform permanently equipped with WPS sensors, inclinometers and motor assemblies
UAP platform temporarily equipped with plugged-in motor assemblies
Alignment solutions for a heavy component (> 2 tons)
Alignment solutions for a light component (< 2 tons)

## Slide 7: Full Remote Alignment: control/command & acquisition aspects
In-house designs, with prototypes being qualified on the Single Component Test
Collaboration between 3 groups of the BE department at CERN
68 components
9 sensor systems
1150 sensors
344 motors
Acquisition & control/command chain

## Slide 8: FRAS risk and safety assessment
  FRAS must be operated and maintained without putting the LHC components or the persons intervening in the tunnel at risk.
  Identification of the main failure modes and their consequences, using the Failure Mode And Effect Analysis (FMECA):
    Damage at an interconnection bellow
    Damage of the HL-LHC components
    Risk for personnel less critical as limited exposure time and all safety procedures already in place.
  Development of control measures reducing the risk to an acceptable level:
    Use of standard IEC 61511-3
    Application of protection layers to mitigate the risk of bellow damage during the displacements of 2 adjacent components: use of independent solutions based on different technologies to determine the 3D position of components and bellows
  Corresponding document approved : EDMS 2727128

## Slide 9: FRAS qualification strategy
We are there

## Slide 10: Outline
A short reminder on Full Remote Alignment System (FRAS)
Single Component Test : status
Inner-Triplet String Test: status and next steps

## Slide 11: Single Component Test - Objectives
To perform the individual and combined qualification of sensors, measurements systems, motorized adapters, data acquisition and alignment algorithms
To provide the possibility to qualify the FRAS performance before the IT String Test
To validate the interfaces between the 3 groups CEM, GM and ICS

## Slide 12: Single Component Test - Sensors
8 HLS installed on 1 hydraulic network
8 WPS installed on 2 wires
2 inclinometers
Distance sensors
Environmental sensors
Wire Position Sensor (WPS)
Hydrostatic Levelling Sensor (HLS)
Inclinometer

## Slide 13: Single Component Test – Position determination
Accuracy (absolute position in R-general) :
Radial position of TAP Magnet : 27 μm
Vertical position of TAP Magnet : 17 μm
Roll : 18 μrad
VERY GOOD RESULTS ACHIEVED!  Launch of procurement for IT String Test
Position determination
Alignment systems

## Slide 14
Epicycloid standard reduction for actuation
Hydrostatic actuation based on polyurethane pastille
3 Gear trains for speed reduction and absolute position monitoring
Single Component Test - Adjustment
Resolver implemented in absolute mode – ~350° for full adapter range (+/-2.5mm)
Both types of motor assemblies qualified locally. Final qualification scheduled
in October.
Vertical motor assembly
Radial assembly

## Slide 15: Single Component Test – Acquisition & control/command systems
New in-house solution named SAMbuCa (Sensors Acquisition and Motion Control system) - EDMS 2274146
Low Level controls
FSI acquisition system
24 channels FSI acquisition system developed and qualified.
Software specification prepared and approved: LHC-_-ES-0047
Low Level and High Level software under finalization – final qualification scheduled in November 2023.

## Slide 16: Outline
A short reminder on Full Remote Alignment System (FRAS)
Single Component Test : status
Inner-Triplet String Test: status and next steps

## Slide 17: IT String Test status
Network determined
Cryo installation
Marking performed

## Slide 18: Next steps
SCT: Final qualification of low level and high level software (November 23)
Procurement of mechanical equipment and sensors launched  control at reception, assembly and calibration
IT-String Test:
  Jacks installation & alignment
  Components alignment
  FRAS installation
  FRAS local qualification
  Final smoothing of components using FRAS

## Slide 19: Other items from WP15.4
Standard alignment of the collimator mock-up and final qualification of the Universal Adjustment Platform and sensors supports
Fiducialisation measurements on-going
A lot of work on-going on quality aspects: naming, preparation of databases, etc.
Internal monitoring & assembly measurements of crab cavities :
 See presentation by V. Rude
Internal monitoring of MQXF :
 See presentation by V. Rude.

## Slide 20: Summary
The Single Component Test (SCT) confirms to be a very useful mock-up to qualify the hardware (motor assemblies, sensors) and software for the Full Remote Alignment System (FRAS) in order to be ready for the IT String Test.
All sensors (except longitudinal sensors) have been qualified. Procurement launched for the IT String Test.
All motor assemblies qualified on individual test benches; to be qualified through repositioning cycles on the SCT in October.
Low-level and high-level software under finalization (final qualification expected in November 2023); they will have to be extrapolated to the control of the 6 components of the IT String Test.
Once fully qualified on the SCT, a 1000 channels FSI acquisition system will be developed for the IT String Test.

## Slide 21: Thank you very much!

## Slide 22
3D calculation with :
8 / 8 : WPS
7 / 8 : HLS  Issue with sliding part ?
1 / 2 : inclinometer  issue with one sphere
A priori precision WPS : 20 μm
A priori precision HLS : 20 μm
A priori precision inclino : 150 μrad
FUV : 0.6 [1]
WPS1
WPS2
WPS3
WPS4
WPS5
WPS6
WPS7
WPS8
HLS5
HLS6
HLS7
HLS8
HLS2
HLS3
Accuracy (absolute position in R-general) :
Radial position of TAP Magnet : 27 μm
Vertical position of TAP Magnet : 17 μm
Roll : 18 μrad
3D calculation
X
Y
R-general
Z
HLS4
 | Residual |  | A priori precision | 
WPS1-WPS_rad | 10 | μm | 20 | μm
WPS1-WPS_vert | 2 | μm | 20 | μm
WPS5-WPS_rad | -10 | μm | 20 | μm
WPS5-WPS_vert | -7 | μm | 20 | μm
WPS2-WPS_rad | -12 | μm | 20 | μm
WPS2-WPS_vert | -6 | μm | 20 | μm
WPS3-WPS_rad | -5 | μm | 20 | μm
WPS3-WPS_vert | 13 | μm | 20 | μm
WPS6-WPS_rad | 12 | μm | 20 | μm
WPS6-WPS_vert | 11 | μm | 20 | μm
WPS7-WPS_rad | 5 | μm | 20 | μm
WPS7-WPS_vert | -6 | μm | 20 | μm
WPS4-WPS_rad | 7 | μm | 20 | μm
WPS4-WPS_vert | -8 | μm | 20 | μm
WPS8-WPS_rad | -7 | μm | 20 | μm
WPS8-WPS_vert | 2 | μm | 20 | μm
HLS5-HLS_vert | 24 | μm | 20 | μm
HLS2-HLS_vert | -11 | μm | 20 | μm
HLS3-HLS_vert | 4 | μm | 20 | μm
HLS6-HLS_vert | 6 | μm | 20 | μm
HLS7-HLS_vert | -10 | μm | 20 | μm
HLS4-HLS_vert | -10 | μm | 20 | μm
HLS8-HLS_vert | -3 | μm | 20 | μm
inclino 1 | 63 | μrad | 150 | μrad
Inclino 1