## Slide 1: Optical readout studies of MPGDs with different gases and wavelength shifters
Juha Nummi
Florian Brunbauer
Francisco Garcia

## Slide 2: Outline
Basic principles of Micro Pattern Gaseous Detectors (MPGD)
Motivation of my studies
Measurement setup
Light yield measurements
Scintillation studies
Influence of wavelength shifter on spatial resolution

## Slide 3: Introduction
Gaseous detectors
  A charged particle ionizes a gas atom
  Electron-ion pair is separated by an electric field
  Electron is accelerated
  Can ionize more gas atoms
  One 5.9keV Xray photon (from ⁵⁵Fe) can create 220 e⁻ in argon + gas mixture
-
+
-
+
Ion
Electron
Ionization
Gas atom
Charged particle
Gas volume

## Slide 4: Introduction
Gas density is so low that an amplification is needed
Gaseous Electron Multiplier (GEM)
  Two foils of conductors, separated by a layer of insulator
  Holes are etched to the structure, typically 50-100 per
  Potential difference between the foils
  Electrons are quickly accelerated inside the holes
-
+
Ion
Electron
30-50μm
50-70μm
Copper
Polyimide
Copper

## Slide 5: Introduction
Scintillation
  After an ionization, atoms and molecules remain in excited states in many cases
  Transition to the ground state can lead to an emission of a photon
Photon
Particle

## Slide 6: Motivation
Most common readout format is electronic
  Fast
  Not accurate enough in some cases
Optical readout with commercially available cameras (CCD/CMOS)
  Pixelated readout
  Tunable magnification
  Low framerate
  Photons in visible wavelength range are needed
Many noble gases scintillates in ultraviolet wavelength range
Simulated electron & nuclear recoil
MIGDAL collaboration, RD51 CM, 2020

## Slide 7: Motivation
is used as a scintillation gas
  has a scintillation peak in the visible wavelength range
  Limits: high Global Warming Potential (GWP), expensive
Pure noble gases with a solid wavelength shifter
  Unstable - scintillation photons can cause more ionization or photoelectric effect on metal surfaces
  A quencher is needed
Study of or other gases mixed with argon for optical readout
  Cheap, nonflammable, nontoxic
  Light yield measurements
  Comparison to and argon and other quenchers gas mixture

## Slide 8: Setup
Triple GEM
Electronic signal is read from the bottom of the last GEM
Optical readout with a photomultiplier tube (PMT)
Wavelength shifter can be installed
X-ray source holder
PMT
X-ray source
PMT/Camera
Cathode
GEMs
Wavelength shifter
Electronic readout

## Slide 9: Light yield measurements
⁵⁵Fe x-ray source
Wavelength shifter: TPB (Tetraphenyl butadiene)
Light yield measurements in 4 cases:
Ar/CO₂ 70/30 | Ar/CF₄ 80/20
With TPB | With TPB
Without TPB | Without TPB
Adapted from https://doi.org/10.1016/j.phpro.2012.02.455

## Slide 10: Electronic readout
Effective gain on the GEMs ≈ 1.2E+05
Peaks at 5.9 keV and 3 keV
Ar/CF₄
Ar/CO₂

## Slide 11: Optical readout: Ar/CF₄
Effective gain on the GEMs ≈ 1.2E+05
Gain on the PMT ≈ 1E+05

## Slide 12: Optical readout: Ar/CO₂
Effective gain on the GEMs ≈ 1.2E+05
Gain on the PMT ≈ 1E+06
No clear peak

## Slide 13: Scintillation studies
Setup
Single glass GEM
Current is read at the bottom of the GEM
300mbar pressure
Scintillation spectrum measurements
With both gas mixtures

## Slide 14: Scintillation studies
Ar/CO₂ 70/30
Ar/CF₄ 80/20
Two peaks with Ar/CF₄
No indication of photons with Ar/CO₂
TPB emission
CF₄ scintillation

## Slide 15: Spatial resolution studies
Spatial resolution measurements
With and without TPB
Results only with Ar/CF₄ gas
X-ray tube
Multiplication structure
Camera

## Slide 16: Spatial resolution studies
The position of the TPB affects to the resolution
GEMs
Cathode
TPB
Camera

## Slide 17: Spatial resolution measurements with Ar/CF₄ gas
Resolution is worse with TPB
With TPB
Without TPB

## Slide 18: Outlook
Scintillation studies to confirm the light wavelength range with different gases
Studies on how the position of the TPB affects the spatial resolution

## Slide 19: Backup
Image of a single GEM hole