## Slide 1: Summary slides: FCC-hh and HFM
Soren Prestemon
Lawrence Berkeley National Laboratory

## Slide 2: Review of FCC-hh general parameter ranges
Modifications improve:
  Injection layout
  Magnet fill factor
Gustavo Pérez Segurana

## Slide 3: Infrastructure
High voltage source and transmission system does appear to be compatible with FCC-hh (focus has been on FCCee)
Tunnel size and layout
  Critical decision that needs to accommodate both ee and hh
  Interfacing with magnets and cryogenics critical
Collimation critical – “FCC-hh beams are highly destructive”
Mario PAROD
Roderik Bruce
Laurent Delprat

## Slide 4: Cryogenics for FCC-hh
Fairly understood at 1.9K
Heat loads slightly less clear at 4.5K
Lots of unknowns at 20K
Conclusions:
In 1.9 K & 4.5 K configurations distribution system (vs FCC-ee tunnel) compatible
At 20K, lots of unknowns, ”seems compatible”
Laurent Delprat

## Slide 5: Magnet development
Message: For Nb3Sn magnets, 14+ T
Magnet prototypes therefore need to prove themselves at ~15-15.5T to demonstrate adequate margin for reliable operation
Structure of European HFM is now more clearly focused
  An effective timeline for Nb3Sn magnet development laid out
Ezio Todesco
Bernhard Auchmann

## Slide 6: Roadmap focused on dev. / downselect / scaleup

## Slide 7: Opportunities for HTS solutions
HFM focus is on REBCO
  Primarily on design concepts leveraging conductor anisotropy
Roadmap is challenging:
  Significant R&D needed to “catch up”
Bernhard Auchmann

## Slide 8: Conductor developments and considerations
Challenges:
  Superconductivity applications are a tiny fraction of the Nb market space
  Superconductivity needs pure Nb
For HTS, many challenges and opportunities
  Bi2212 led primarily by HEP
  REBCO driven primarily by Fusion now
Lance Cooley

## Slide 9: Magnet protection
Evolution of the LHC powering and protection strategy
Margins for protection get tighter at higher field
CLIC provides significant flexibility, but has some drawbacks when scaled to FCChh;
  alternative concepts are under development that may address those issues
Modeling has advanced significantly, enabling coupled physics simulations of powering circuit and thermo-mechanical response of magnets during quench
Emanuele Ravaioli

## Slide 10: US MDP and collaboration with HFM
MDP focused on “general” high field magnet development
  “Stress-management” concepts
  “Hybrid” LTS/HTS magnets
  REBCO and Bi2212 HTS magnet technology

## Slide 11
Thanks for coming to San Francisco!