## Slide 1: First test-beam experience with the CALICE tungsten A-HCAL prototype ALCPG Workshop 19.-23. March 2011 Eugene, Oregon
Dominik Dannheim (CERN), Angela Lucaci-Timoce (CERN) on behalf of the CALICE collaboration

## Slide 2: Outline
Tungsten for hadronic calorimetry
W-AHCAL test-beam setup
Calibration and particle identification
Data quality assessment

## Slide 3: Hadronic calorimetry at 3 TeV
Resolution of hadronic calorimetry driven by:
  Intrinsic resolution
  Leakage (number of λi)
To maximize number of λi:
  Increased depth
  Denser absorber
Depth severely constraint by:
  Feasible coil size for large B-field
  Size of tracker needed for good momentum resolution
CALICE investigates dense absorbers for hadronic calorimetry

## Slide 4: Simulation results at 3 TeV
Shorter HCal leads to:
  more leakage
  worse resolution
Flat region reached at smaller depth for tungsten than for steel absorber
For Ejet<50 GeV: resolution constant, dominated by intrinsic resolution
For Ejet>100 GeV: leakage dominates resolution
Aim for HCAL depth of 7.5 λi (+1 λi from ECAL)
Energy resolution for single π, reconstr. with neural network:

## Slide 5: Tungsten as absorber material
Expected benefits of tungsten absorber vs. iron:
  λi(W) = 10 cm; λi (Fe) = 17 cm
  Less leakage for same depth  more showers contained
  Smaller shower diameter  better separation
However: little experience with tungsten for hadronic calorimetry
  So far: tungsten used for EM calorimetry (~1 λi)
  No experience with tungsten in HCALs (4-9 λi)
  Simulation of hadronic showers in tungsten not validated
    No data/MC comparisons
    In particular: no validation with high granularity
    Low-energy spallation neutrons increased, less ionization
       Late component of shower more important, making time stamping more challenging
Goal of CALICE test-beam program with tungsten absorber:
  Validate particle-flow based calorimetry for CLIC conditions
  Help to improve/validate Geant-4 simulation models

## Slide 6: W-AHCAL prototype
Tungsten Absorber:
  30 plates of 10 mm thickness 1 x 1 m2 surface
Active material:
  Scintillator tiles of 3 x 3 cm2 (center) and 6 x 6 cm2 (edges)
Total depth incl. supports: ~3.8 λi
Readout:
  Light collection via WLS fibres, readout with multi-pixel SiPMs
  MICROMEGAS in last readout layer
  T3B high-precision timing meas. behind last readout layer (cf. talk by F. Simon tomorrow)
will concentrate on SiPM readout in the following

## Slide 7: Test beam at CERN-PS
Several weeks of low-intensity μ runs in T7, to obtain MIP calibration
19 days of beam time in T9 area of CERN-PS
  Typically 2-3 spills / 45 s, 24-33 Hz DAQ rate
  28 million events in total: e+-, μ+-,π+-, p+- from 1 to 10 GeV in steps of 1 GeV

## Slide 8: Test beam setup

## Slide 9: Beam instrumentation
Trigger:
  Coincidence of 2 scintillators + PMT in front of W-AHCAL
Tracking:
  3 delay-line wire chambers with x/y planes in front of W-AHCAL
  Resolution of predicted impact point on W-AHCAL surface ~0.5 mm
Particle ID:
  2 Cherenkov counters filled with CO2 at ~0<pabs<3 bar
  PMT+Scintillator+Discriminator  Cherenkov bit: on/off
  Used offline to separate electrons, muons, pions, protons

## Slide 10: Event displays
μ- candidate
Ebeam=8 GeV
π – candidate
Ebeam=8 GeV
Online reconstruction of events using calibration from 2007
(layers 31-38 missing in 2010 setup)

## Slide 11: Calibration procedure
Dead/noisy channels
  Dead/noisy channels monitored during data taking
  Number of problematic channels ~constant
  Flagging for offline analysis handled by new software package
Temperature monitoring/correction
   See following slides
Gain calibration
   See following slides
Intercalibration
  Ratio of readout response between physics+calibration mode
  Probed with LED runs
  Good agreement with previous calibration (FNAL 2008)
MIP calibration
  See following slides

## Slide 12: Temperature monitoring
SiPM properties depend on ambient temperature:
  Gain decreases with 1.7% / K
  Breakdown voltage increases with 65 mV / K
  Response decreases with 3.7% / K
Continuous temperature monitoring with 5 sensors per readout plane
Corrections for gain/response are applied offline during calibration procedure
Calibration offsets for temp. sensors:
Temperature profile during run:
Additional heat sources next to last layers, originating from alternative readout modules  larger spread

## Slide 13: Gain calibration
Gains (ADC counts per pixel) obtained from periodic low-intensity LED-pulser calibration runs during data taking
Efficiency for extracting gain constants is used for data-quality monitoring
Good agreement between gains for FNAL 2008 data (red) and gains for CERN 2010 data (black) (after preliminary temperature correction)
Gain = ADC counts per SiPM pixel (modulo correction for difference between calibration and physics readout mode)
0 pixels
1 pixel
2 pixels
3 pixels
gain value
#entries (normalised)

## Slide 14: MIP calibration
ADC-to-MIP calibration performed with long low-intensity μ runs
Fit ADC distributions per channel with Gauss+Landau
MPV of Landau gives MIP value for corresponding channel (at reference temperature given by the average temperature of the corresponding runs)
Example of MIP fit for one channel:
Comparison old / new MIP calibration:
Energy response for -5 GeV run with pion+muon selection
cell energy [a.u.]

## Slide 15: Particle-ID using Cherenkov counters
Use Cherenkov counters offline to select / veto various types of particles
Becomes difficult at low energy (limited by pmax=3.0 bar)
Efficiency of Cherenkov selection limited by discrimination threshold of PMT readout
Pion purity limited by in-flight pion decays
Optimized pressure settings for each energy point, to allow for selecting exclusive sample of sufficient size
Electron efficiency (tag and probe):

## Slide 16: Response to e, μ, π, p
Use CERN 2007 (Fe) calibration for now, to study global quantities (e.g. total energy sum and resolution)
Obtain particle types per event from Cherenkov counters
μ contamination at all energies, as expected from in-flight π decays and Cherenkov cross-efficiencies
μ separation difficult for low energies, where e, π, p also look like MIPs
However: at low energies combined fits still allow to obtain individual mean and sigmas from the inclusive selections
μ+π peak at -2 GeV:
μ+ peak
e+/π+/p+ peak

## Slide 17: μ and π response at different energies
(negative charge)
Preliminary studies with fits indicate:
  EM resolution slightly worse than for Fe (lower sampling fraction for X0)
  Hadronic resolution similar to Fe
  e/π stable vs. energy

## Slide 18: Summary/Conclusions
Successful first W-AHCAL test beam at CERN PS
28 million events collected: e, μ, π, p from 1 to 10 GeV
Calibration and data-quality studies show satisfactory results
Final calibration and simulation in progress
2 test beam campaigns planned in 2011 at CERN SPS (H8):
  Hadrons, electrons and muons from 9 to 350 GeV
  1st period: will add 8 additional tungsten layers
  2nd period: will add also tail catcher
Outlook

## Slide 19: Backup slides

## Slide 20: Simulation
Geant-4 simulation for AHCAL setup implemented in Mokka framework
Comparison of data with different Geant-4 physics lists ongoing
Expect differences for shower shapes and timing between:
  QGSP_BERT  high neutron content
  QGSP_BERT_HP  in addition: high precision neutron tracking