## Slide 1: RADWG Activities Overview
Rudy Ferraro (BE-CEM-EPR)
RadWG Workshop – 06th July, 2023

## Slide 2: Radiation Test Service
BE-CEM-EPR provides, the service of radiation testing of electronic components supporting the Radiation Working Group (RadWG)
The RadWG supports the accelerator sector equipment groups for the assessment of radiation tolerance of electronic equipment to be installed in radiation exposed areas.
It is as a forum for electronic engineers to discuss
  design practices
  radiation tests
  radiation induced failures in the accelerators.
The RadWG is one of the pillars of the CERN Radiation Hardness Assurance process
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 3: Radiation test service – BE-CEM-EPR
01
02
03
04
05
06
Test planning and structure
Each component/system is analyzed, and all the possible radiation effects are taken into account for planning the test and structure it
Board and instrumentation preparation
For each component a dedicated set of test board is prepared and the associated instrumentation is chosen to face the complexity of the radiation test
Result analysis
The results are analyzed during and after the tests for each component considering the end application and the possible operational issues
Request collection
The requests for radiation testing are collected and processed selecting the most suitable methodology and facilities
Database and Publication
The results are collected, stored and in EDMS and published in the RADWG database to allow an easy research of the best candidates for the new radiation tolerant designs
Testing
The test are carried out at CERN facilities such as CHARM or Co60 and in external facilities. The transport, personnel and instrumentation are selected considering the peculiar aspect of each facility
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 4: 2023 In Number
93 component test request for 2023 (so far)
33 components tested (so far)
5 Radiation campaigns done (3*PSI, 2*CC60, 2*CHARM)
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
Compare to previous year we are in the high range of components tested per month
5 more PSI campaigns are planned, together with regular CHARM tests
We will probably test more components this year than the previous years

## Slide 5: Test Service Status: Requests per type
Total requests: 93 [not only references but also #lots]
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 6: Test Service Status: Requests per group/project
*Cryogenic Systems components are few part references but a lot of different lots
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 7: Test Service Status: Requests per lot type
Distribution of the type of lots:
Quite balanced between new test and production lot qualification
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 8: PSI 2023 Test Status: 24 devices tested so far
March 3-6 (7DUTs)
August 26-27
July 15-16
April 1-2 (9 DUTs)
May 13-14
September 8-10
October 21-22
November 25-26
FCA36N60NF x2 lots (SiC MOS – TE-CRG)
ISO7763FQDWRQ1 (Isolator – TE-CRG)
ISO124U x3 lots (Isolator – TE-CRG)
TCA9406 (I2C Transceiver – TE-CRG)
= Production Lot
= Test Lot
DS2401+ (1-Wire – SY-EPC)
CY62157EV30 (SRAM – BE-CEM)
INA146UA (Opamp – BE-CEM)
SN74LVC16T245DGG (Transceiver – BE-CEM)
PCA9615 (I2C Transceiver – BE-CEM)
( RD3P130SP (MOSFET – SY-EPC ))
CD4066 (Analog Switch BE-CEM)
SM30T12CAY (Thyristor TE-CRG)
SMP75-8 (Thyristor TE-CRG)
SP00800SDT (Thyristor TE-CRG)
SP0080SC (Thyristor TE-CRG)
SM15T12CAY (Thyristor TE-CRG)
LFSPXO018038 (Oscillator BE-CEM)
LFSPXO018041 (Oscillator BE-CEM)
LFSPXO0180xx (Oscillator BE-CEM)
IKW15N120BH6 (IGBT – SY-EPC)
ISO124U x1 lot (Isolator – TE-CRG)
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
We still have available slots for this year so don’t hesitate to make requests

## Slide 9: Recent Results: TSS/TSV Thyristors (TE-CRG)
6 References were tested
8 DUTs per reference tested
Main objective: Measure current leakage around -1 V to 1 V
Test setup made to:
Bias devices during irradiation
Read complete thyristor characteristics
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 10: Recent Results: TSS/TSV Thyristors (TE-CRG)
TVS versus TSS standard characteristics:
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 11: Recent Results: TSS/TSV Thyristors (TE-CRG)
SM15T12CAY
SM30T12CAY
TVS Results
No change of VBR visible
High current leakage increase in SM30T12CAY (up to 10 uA)
Report: EDMS 2913493
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 12: Recent Results: TSS/TSV Thyristors (TE-CRG)
SP00800SDT
TSS Results
SP0080SC
SMP75-8
Slight increase of VBO, VBR and IH (but negligible overall)
Slight increase current leakage but all lower than 1 uA
Report: EDMS 2913493
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 13: Recent Results: HAS-100S Hall Effect sensor (TE-EPC)
Tested at CHARM in position 13 for 3 weeks
Cumulated Radiation Levels:
  TID: 917 Gy DD: 6.91x1012neq.cm², DDEF/TID: 7.5 x109 neq/cm²/Gy
Test Method:
  Fixed current to be measured set at 20 A
  Acquisition of the Ameasured = f(Ainjected) from 0 to 50 A
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 14: Recent Results: HAS-100S Hall Effect sensor (TE-EPC)
Preliminary Analysis:
Small drift of the measured current
  Maximum change: -1.5 A (-7.6%)
Change of calibration curve
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 15: Recent Results: HAS-100S Hall Effect sensor (TE-EPC)
Characteristic Relative change in current / Difference of measured current:
Nonlinear degradation behaviour, one of several rebounds visible
Quite big variability within devices
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 16: Recent Results: HAS-100S Hall Effect sensor (TE-EPC)
Bigger error on lower current measurement
Characteristic Relative change in percentage

## Slide 17: Recent Results: HAS-100S Hall Effect sensor (TE-EPC)
CHARM
PSI
Two devices were tested in the same conditions at PSI
Only two devices were tested due to their size (can be put only one by one in the beam)
As visible the variation was bigger for most of the devices
Can be a lot-to-lot variation but the internal design is made of bipolar devices, so it is most likely due to combined TID-DD effects
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 18: Recent Results: HAS-100S Hall Effect sensor (TE-EPC)
On the calibration the difference is more noticeable
CHARM
Lowest degradation
Biggest degradation
PSI
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 19: Recent Results: LT8610 DCDC
1 V Output
Output Load set to 100 mA
5 DUTs set to 1V output and 5 DUTs set to 5V outputs
1 Power cycle every 12h
SETs
SETs
No significant degradation observed but some quite big SETs were observed with probably a high occurrence since those were captured by the MultiDAQ sampling every 10s

## Slide 20: Recent Results: 1-Wire serial ID (TE-EPC)
Tested at PSI
Test protocol: Continuous reading of the ID and comparison with the one before irradiation
Devices died before target of 500 Gy ( died = returned corrupted ID, CRC etc.. Random data)
Use of reliability Weibull tool to extract Weibull failure distribution parameters
Failure distribution of the device
Weibull(a,b) parameters fit
PSI Failures
Target
Outsider
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 21: Test Request Template:
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
Test Request document: EDMS 2779784
Contains:
  Information about equipment:
    Locations, Deployment plan, lifetime, number of units in operation
  Information about radiation levels in operation: TID, DDEF, HeH, ThN
  Information about DUTs:
    Use in the system (schematic)
    Parameters of interest
    Radiation Design requirements
    Maximum tolerated failure rate (SEEs)
Will help us to track better the request and also to prepare better the tests
To be sent to: EPR-Radiation-Test-Team@cern.ch
All request are then put in the following EDMS folder: [link]

## Slide 22: Test results analysis and reporting
The website https://radwg.web.cern.ch/ embeds an User-Friendly database
  More than 558 reports from the 2011 up to 2023
225 users subscribed to the mailing list lhc-proj-radwg-members
The service produces reports in a common template for all the components tested
  Test reports template ensure a coherent reporting
databases accessible by all the equipment groups
https://radwg.web.cern.ch
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 23: Conclusions
BE-CEM-EPR provides the service of radiation testing of electronic components supporting the Radiation Working Group (RadWG)
High testing activity in 2023
CHARM Tests has restarted
3 PSI campaigns were performed and they are still some spots in the 5 next campaigns for this year
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 24
Thank you for your attention!