## Slide 1: Electromagnetic design optimization
June 2023
Susana Izquierdo Bermudez, Juan Carlos Perez , Lucio Fiscarelli, Ezio Todesco, Emma Lucie Gautheron

## Slide 2: Introduction
∿ 55 mm coil; ∿ 360 A/mm2 Joverall; ∿ 17.5 T Bss
Goal:
  Electromagnetic optimization, understanding better the role of the iron on b3 and Bp/B0
Some constrains:
  Inner support thickness L1 = 4 mm
  Yoke vertical ‘aperture’, 150 mm, to flare the ends
  Yoke OR = 300 mm

## Slide 3: Starting point – v207
 |  | v207
strand diameter | mm | 1.1
Cu/SC | -- | 0.9
# of strands/cable | -- | 44
# turns/quadrant | -- | 50
Eq. coil width | mm | 56
Inom | A | 20120
Joverall | A/mm2 | 325
Jcu | A/mm2 | 1016
Jsc | A/mm2 | 914
Ratio Bp/Bo | -- | 1.05
B0 at Inom | T | 14.00
Bp at Inom | T | 14.76
Bss | T | 18.03

## Slide 4: Iron v4
Chart: I, A
| 40.24 | 2651.8 | 5263.4 | 7875 | 10487 | 13098 | 15710 | 18321 | 20933 | 23544 | 26156
b2 | -0.097986 | -0.94641 | -3.8948 | -7.6323 | -9.1521 | -12.306 | -17.479 | -22.453 | -26.74 | -30.403 | -33.569
b3 | 7.8568 | 4.0987 | -5.2424 | 0.064522 | 3.9327 | 4.548 | 3.7767 | 3.0231 | 2.4824 | 2.0902 | 1.809
b5 | 1.7049 | 2.2293 | 4.6213 | 5.8306 | 6.5791 | 7.053 | 7.3812 | 7.6281 | 7.8205 | 7.9758 | 8.1039
b7 | 1.3129 | 1.3182 | 1.339 | 1.399 | 1.4501 | 1.4948 | 1.534 | 1.5661 | 1.5918 | 1.6128 | 1.6303
Chart: I, A
| 40.24 | 2651.8 | 5263.4 | 7875 | 10487 | 13098 | 15710 | 18321 | 20933 | 23544 | 26156
BIGB | 0.035591 | 2.3308 | 4.426 | 6.2943 | 8.0647 | 9.7521 | 11.371 | 12.964 | 14.55 | 16.131 | 17.709
PEAK | 0.037094 | 2.4317 | 4.6324 | 6.5916 | 8.4506 | 10.233 | 11.955 | 13.652 | 15.343 | 17.029 | 18.712
Bp/B0 | 1.0425 | 1.0435 | 1.0466 | 1.0472 | 1.0479 | 1.0493 | 1.0514 | 1.0531 | 1.0545 | 1.0557 | 1.0566

## Slide 5: Iron v5
Chart: I, A
| 40.24 | 2651.8 | 5263.4 | 7875 | 10487 | 13098 | 15710 | 18321 | 20933 | 23544 | 26156
b2 | -0.0347 | -0.92192 | -3.836 | -7.4496 | -9.2021 | -12.715 | -17.901 | -22.65 | -26.738 | -30.258 | -33.32
b3 | -150.93 | -126.77 | -70.197 | -45.037 | -31.391 | -24.859 | -21.584 | -19.304 | -17.492 | -15.992 | -14.712
b5 | 8.406 | 7.1422 | 7.0686 | 7.5773 | 7.9596 | 8.211 | 8.3923 | 8.5276 | 8.6316 | 8.7147 | 8.7824
b7 | 1.0275 | 1.1005 | 1.2258 | 1.3167 | 1.3839 | 1.4385 | 1.4846 | 1.5214 | 1.5509 | 1.5752 | 1.5954
Chart: I, A
| 40.24 | 2651.8 | 5263.4 | 7875 | 10487 | 13098 | 15710 | 18321 | 20933 | 23544 | 26156
BIGB | 0.041908 | 2.6863 | 4.7262 | 6.5665 | 8.3229 | 9.9995 | 11.612 | 13.204 | 14.789 | 16.37 | 17.948
PEAK | 0.04569 | 2.8992 | 5.0196 | 6.9427 | 8.7845 | 10.555 | 12.268 | 13.964 | 15.653 | 17.339 | 19.022
Bp/B0 | 1.0905 | 1.0796 | 1.0621 | 1.0573 | 1.0555 | 1.0556 | 1.0565 | 1.0576 | 1.0584 | 1.0592 | 1.0598

## Slide 6: Iron v6
Chart: I, A
| 40.24 | 2651.8 | 5263.4 | 7875 | 10487 | 13098 | 15710 | 18321 | 20933 | 23544 | 26156
b2 | -0.13951 | -0.84825 | -3.5319 | -6.8477 | -8.6754 | -12.325 | -17.4 | -21.957 | -25.922 | -29.356 | -32.359
b3 | -995.47 | -506.72 | -310.03 | -224.98 | -177.91 | -149.35 | -130.24 | -115.77 | -104.27 | -94.869 | -87.017
b5 | 46.747 | 68.868 | 48.464 | 39.211 | 33.96 | 30.424 | 27.869 | 25.886 | 24.295 | 22.987 | 21.893
b7 | 34.998 | 0.34178 | -0.20642 | -0.010245 | 0.18208 | 0.35367 | 0.49837 | 0.61871 | 0.71961 | 0.80521 | 0.87862
Chart: I, A
| 40.24 | 2651.8 | 5263.4 | 7875 | 10487 | 13098 | 15710 | 18321 | 20933 | 23544 | 26156
BIGB | 0.069138 | 3.0474 | 5.0557 | 6.8889 | 8.6422 | 10.314 | 11.924 | 13.517 | 15.103 | 16.684 | 18.263
PEAK | 0.10873 | 2.8888 | 4.7836 | 6.6124 | 8.3904 | 10.109 | 11.778 | 13.435 | 15.089 | 16.741 | 18.393
Bp/B0 | 1.5727 | 0.94835 | 0.94671 | 0.96631 | 0.97786 | 0.98526 | 0.99069 | 0.99482 | 0.99907 | 1.0034 | 1.0071

## Slide 7: Iron v7
Chart: I, A
| 40.24 | 2651.8 | 5263.4 | 7875 | 10487 | 13098 | 15710 | 18321 | 20933 | 23544 | 26156
b2 | 6.3593 | 6.0936 | 28.807 | 51.25 | 53.328 | 44.554 | 34.54 | 25.415 | 17.316 | 10.251 | 4.0963
b3 | 5.3742 | 0.87602 | -11.084 | -9.6487 | -7.9711 | -7.4478 | -7.0394 | -6.5835 | -6.1326 | -5.6991 | -5.2957
b5 | 1.7136 | 2.2317 | 4.6135 | 5.8115 | 6.5274 | 7.0074 | 7.3533 | 7.6129 | 7.814 | 7.975 | 8.1071
b7 | 1.3236 | 1.3357 | 1.3667 | 1.436 | 1.4904 | 1.5362 | 1.5722 | 1.6003 | 1.6228 | 1.6411 | 1.6563
Chart: I, A
| 40.24 | 2651.8 | 5263.4 | 7875 | 10487 | 13098 | 15710 | 18321 | 20933 | 23544 | 26156
BIGB | 0.035264 | 2.2983 | 4.3334 | 6.1257 | 7.8302 | 9.4637 | 11.069 | 12.661 | 14.247 | 15.829 | 17.407
PEAK | 0.036789 | 2.401 | 4.5366 | 6.4129 | 8.2065 | 9.938 | 11.644 | 13.339 | 15.028 | 16.713 | 18.396
Bp/B0 | 1.0436 | 1.0452 | 1.0515 | 1.0551 | 1.0566 | 1.0573 | 1.0575 | 1.0577 | 1.0577 | 1.0576 | 1.0576

## Slide 8: Iron v8
Chart: I, A
| 40.24 | 2651.8 | 5263.4 | 7875 | 10487 | 13098 | 15710 | 18321 | 20933 | 23544 | 26156
b2 | -0.32438 | -0.35287 | -1.6744 | -3.9795 | -7.7993 | -13.434 | -18.484 | -22.829 | -26.601 | -29.885 | -32.76
b3 | -1.2578 | -4.0778 | -17.294 | -19.191 | -18.278 | -16.958 | -15.537 | -14.179 | -12.946 | -11.853 | -10.893
b5 | 1.9242 | 2.3157 | 4.5964 | 5.8322 | 6.5544 | 7.0431 | 7.3944 | 7.6565 | 7.8588 | 8.0198 | 8.151
b7 | 1.3664 | 1.3699 | 1.3938 | 1.4741 | 1.5303 | 1.5735 | 1.6059 | 1.6308 | 1.6505 | 1.6664 | 1.6795
Chart: I, A
| 40.24 | 2651.8 | 5263.4 | 7875 | 10487 | 13098 | 15710 | 18321 | 20933 | 23544 | 26156
BIGB | 0.034137 | 2.2407 | 4.2486 | 5.9694 | 7.6266 | 9.2394 | 10.836 | 12.424 | 14.008 | 15.588 | 17.167
PEAK | 0.035724 | 2.3467 | 4.4688 | 6.2982 | 8.0609 | 9.7797 | 11.482 | 13.175 | 14.863 | 16.549 | 18.232
Bp/B0 | 1.0468 | 1.0476 | 1.0519 | 1.0551 | 1.0569 | 1.0585 | 1.0596 | 1.0604 | 1.061 | 1.0616 | 1.062

## Slide 9: Iron v9
Chart: I, A
| 40.24 | 2651.8 | 5263.4 | 7875 | 10487 | 13098 | 15710 | 18321 | 20933 | 23544 | 26156
b2 | -0.27387 | -0.98486 | -3.805 | -7.3913 | -9.2598 | -12.752 | -17.737 | -22.268 | -26.205 | -29.584 | -32.583
b3 | -633.1 | -415.98 | -256.08 | -185.69 | -146.53 | -122.97 | -107.36 | -95.564 | -86.166 | -78.465 | -72.024
b5 | 41.702 | 47.376 | 32.004 | 26.03 | 22.898 | 20.857 | 19.414 | 18.308 | 17.427 | 16.708 | 16.108
b7 | -159.04 | -41.511 | -24.191 | -17.248 | -13.484 | -11.056 | -9.3472 | -8.0513 | -7.0288 | -6.2004 | -5.5148
Chart: I, A
| 40.24 | 2651.8 | 5263.4 | 7875 | 10487 | 13098 | 15710 | 18321 | 20933 | 23544 | 26156
BIGB | 0.069417 | 3.0482 | 5.0571 | 6.8893 | 8.6424 | 10.316 | 11.927 | 13.52 | 15.105 | 16.687 | 18.266
PEAK | 0.11087 | 2.9112 | 4.8104 | 6.6396 | 8.4185 | 10.139 | 11.81 | 13.468 | 15.123 | 16.776 | 18.428
Bp/B0 | 1.5972 | 0.95542 | 0.95165 | 0.96614 | 0.97767 | 0.98507 | 0.99044 | 0.99615 | 1.0012 | 1.0053 | 1.0089
2 mm shims in the aperture

## Slide 10: Load lines

## Slide 11: Let’s better put numbers in a table
I assume a nominal field of 14 T
I assume an increase of energy from injection to collision of 15 (similar to the baseline FCC, 3.3 TeV for 50 TeV collision)
 | I (A) | B0 | Bp | Bss | Bp/B0 | Bp/Bss [%] | Δb2 | Δb3 | Δb5 | Δb7
Coil only | 24664 | 14.00 | 14.93 | 15.68 | 1.067 | 95.3 | 0.0 | 0.0 | 0.0 | 0.0
iron v4 | 20027 | 14.00 | 14.76 | 17.97 | 1.054 | 82.1 | -24.8 | -3.7 | 5.8 | 0.3
iron v5 | 19633 | 14.00 | 14.81 | 17.87 | 1.058 | 82.9 | -24.4 | 124.4 | 0.6 | 0.5
iron v6 | 19116 | 14.00 | 13.94 | 17.90 | 0.996 | 77.9 | -22.8 | 741.4 | -27.8 | -24.3
iron v7 | 20526 | 14.00 | 14.81 | 17.90 | 1.058 | 82.7 |  | -9.8 | 5.9 | 0.3
iron v8 | 20920 | 14.00 | 14.85 | 17.85 | 1.061 | 83.2 | -26.2 | -10.5 | 5.8 | 0.3
iron v9 | 19112 | 14.00 | 13.97 | 17.90 | 0.998 | 78.1 | -23.0 | 477.4 | -25.3 | 117.2

## Slide 12: Peak to bore field ratio
5.4 % enhancement with the ‘good field quality solution’
The insert in the pad is not helping to improve the ratio peak field bore field (v5 has 5.8 % enhancement), and adds 100 units of b3 in saturation
What helps enormously is the iron pole, but is > 700 units of b3 from injection to nominal
 | I (A) | B0 | Bp | Bss | Bp/B0 | Bp/Bss [%] | Δb2 | Δb3 | Δb5 | Δb7
Coil only | 24664 | 14.00 | 14.93 | 15.68 | 1.067 | 95.3 | 0.0 | 0.0 | 0.0 | 0.0
iron v4 | 20027 | 14.00 | 14.76 | 17.97 | 1.054 | 82.1 | -24.8 | -3.7 | 5.8 | 0.3
iron v5 | 19633 | 14.00 | 14.81 | 17.87 | 1.058 | 82.9 | -24.4 | 124.4 | 0.6 | 0.5
iron v6 | 19116 | 14.00 | 13.94 | 17.90 | 0.996 | 77.9 | -22.8 | 741.4 | -27.8 | -24.3
iron v7 | 20526 | 14.00 | 14.81 | 17.90 | 1.058 | 82.7 |  | -9.8 | 5.9 | 0.3
iron v8 | 20920 | 14.00 | 14.85 | 17.85 | 1.061 | 83.2 |  | -10.5 | 5.8 | 0.3
iron v9 | 19112 | 14.00 | 13.97 | 17.90 | 0.998 | 78.1 | -23.0 | 477.4 | -25.3 | 117.2

## Slide 13: Peak to bore field ratio
2 mm thick iron shims in the aperture can fix 260 units out of 740 units, with negligible impact in Bp/B0
  At least two shims per quadrant needed if we don’t want other harmonics to get very high
One could try to further reduce optimizing the shape of the pole
  My feeling is that it would be very hard to get < 200 units of Δb3 saturation. Is it something to explore?
 | I (A) | B0 | Bp | Bss | Bp/B0 | Bp/Bss [%] | Δb2 | Δb3 | Δb5 | Δb7
Coil only | 24664 | 14.00 | 14.93 | 15.68 | 1.067 | 95.3 | 0.0 | 0.0 | 0.0 | 0.0
iron v4 | 20027 | 14.00 | 14.76 | 17.97 | 1.054 | 82.1 | -24.8 | -3.7 | 5.8 | 0.3
iron v5 | 19633 | 14.00 | 14.81 | 17.87 | 1.058 | 82.9 | -24.4 | 124.4 | 0.6 | 0.5
iron v6 | 19116 | 14.00 | 13.94 | 17.90 | 0.996 | 77.9 | -22.8 | 741.4 | -27.8 | -24.3
iron v7 | 20526 | 14.00 | 14.81 | 17.90 | 1.058 | 82.7 |  | -9.8 | 5.9 | 0.3
iron v8 | 20920 | 14.00 | 14.85 | 17.85 | 1.061 | 83.2 |  | -10.5 | 5.8 | 0.3
iron v9 | 19112 | 14.00 | 13.97 | 17.90 | 0.998 | 78.1 | -23.0 | 477.4 | -25.3 | 117.2
v6

## Slide 14: Peak to bore field ratio
If for mechanical reasons, it is a problem to have iron in between apertures, the price to remove is not very expensive:
  We increase the Bp/Bo ratio from 1.054 to 1.058, and we lose 0.6 % of margin in the load line
  +20 units of b2 (cross talk)
 | I (A) | B0 | Bp | Bss | Bp/B0 | Bp/Bss [%] | Δb2 | Δb3 | Δb5 | Δb7
Coil only | 24664 | 14.00 | 14.93 | 15.68 | 1.067 | 95.3 | 0.0 | 0.0 | 0.0 | 0.0
iron v4 | 20027 | 14.00 | 14.76 | 17.97 | 1.054 | 82.1 | -24.8 | -3.7 | 5.8 | 0.3
iron v5 | 19633 | 14.00 | 14.81 | 17.87 | 1.058 | 82.9 | -24.4 | 124.4 | 0.6 | 0.5
iron v6 | 19116 | 14.00 | 13.94 | 17.90 | 0.996 | 77.9 | -22.8 | 741.4 | -27.8 | -24.3
iron v7 | 20526 | 14.00 | 14.81 | 17.90 | 1.058 | 82.7 | -50 | -9.8 | 5.9 | 0.3
iron v8 | 20920 | 14.00 | 14.85 | 17.85 | 1.061 | 83.2 |  | -10.5 | 5.8 | 0.3
iron v9 | 19112 | 14.00 | 13.97 | 17.90 | 0.998 | 78.1 | -23.0 | 477.4 | -25.3 | 117.2

## Slide 15: Peak to bore field ratio
If we also remove the iron form the horizontal pad, we increase a bit more the Bp/B0 ratio, and loose another 0.5 % margin
Also the fringe field will be large (didn’t check)
 | I (A) | B0 | Bp | Bss | Bp/B0 | Bp/Bss [%] | Δb2 | Δb3 | Δb5 | Δb7
Coil only | 24664 | 14.00 | 14.93 | 15.68 | 1.067 | 95.3 | 0.0 | 0.0 | 0.0 | 0.0
iron v4 | 20027 | 14.00 | 14.76 | 17.97 | 1.054 | 82.1 | -24.8 | -3.7 | 5.8 | 0.3
iron v5 | 19633 | 14.00 | 14.81 | 17.87 | 1.058 | 82.9 | -24.4 | 124.4 | 0.6 | 0.5
iron v6 | 19116 | 14.00 | 13.94 | 17.90 | 0.996 | 77.9 | -22.8 | 741.4 | -27.8 | -24.3
iron v7 | 20526 | 14.00 | 14.81 | 17.90 | 1.058 | 82.7 | -50 | -9.8 | 5.9 | 0.3
iron v8 | 20920 | 14.00 | 14.85 | 17.85 | 1.061 | 83.2 |  | -10.5 | 5.8 | 0.3
iron v9 | 19112 | 14.00 | 13.97 | 17.90 | 0.998 | 78.1 | -23.0 | 477.4 | -25.3 | 117.2

## Slide 16: Iron and 2 in 1 contribution
 | I (A) | B0 | Bp | Bss | Bp/B0 | Bp/Bss [%]
Coil only | 24664 | 14.00 | 14.93 | 15.68 | 1.067 | 95.3
iron v4 | 20027 | 14.00 | 14.76 | 17.97 | 1.054 | 82.1
Coil only | 20070 | 11.39 | 12.15 | 15.68 | 1.067 | 77.5
Coil only | 21268 | 12.07 | 12.88 | 15.68 | 1.067 | 82.1
Fr Ezioom:
  +15 % due to iron saturation
  + 5 % from 1in1 to 2in1
What I get:
  With the same current, the single coil produces 19 % field less than the 2in1 magnet with iron, so Ezio is right and accurate 
  To produce the same field, the magnet needs 23 % more current and operates with 13 % less margin in the load line
  If we place ourselves at the same margin of the load line, the current is 6 % higher and the field 14 % lower

## Slide 17: Conclusion
The best is to put as much iron as possible 
It would be interesting to take a look to the magnetic measurements of FRESCA2 and RMM, to see the role of the pole

## Slide 18
 | I (A) | B0 | Bp | Bss | Bp/B0 | Bp/Bss [%] | Δb2 | Δb3 | Δb5 | Δb7
Coil only | 24664 | 14.00 | 14.93 | 15.68 | 1.067 | 95.3 | 0.0 | 0.0 | 0.0 | 0.0
iron v4 | 20027 | 14.00 | 14.76 | 17.97 | 1.054 | 82.1 | -24.8 | -3.7 | 5.8 | 0.3
iron v5 | 19633 | 14.00 | 14.81 | 17.87 | 1.058 | 82.9 | -24.4 | 124.4 | 0.6 | 0.5
iron v6 | 19116 | 14.00 | 13.94 | 17.90 | 0.996 | 77.9 | -22.8 | 741.4 | -27.8 | -24.3
iron v7 | 20526 | 14.00 | 14.81 | 17.90 | 1.058 | 82.7 |  | -9.8 | 5.9 | 0.3
iron v8 | 20920 | 14.00 | 14.85 | 17.85 | 1.061 | 83.2 | -26.2 | -10.5 | 5.8 | 0.3
iron v9 | 19112 | 14.00 | 13.97 | 17.90 | 0.998 | 78.1 | -23.0 | 477.4 | -25.3 | 117.2
v4
v5
v6
v7
v8
v9