## Slide 1
Power Update - Winter 2023
Dr. Emanuele Simili HEPiX Benchmarking Working Group meeting 06 December 2023
Notes: PoW @ HEPiX

## Slide 2
Outline
Update on my benchmarks results: - HEPscore/Watt comparison extended to more machines - Thread-Scan , Frequency Scan , Open issues - What Watt: investigating the best estimate of average power
Me vs. the Energy Plug-in - Testing experience and run strategy - Plug-in validation (comparison with my exporter tools)
Outlook and next steps - Collect / consolidate / streamline - Joining the developers …
…
Notes: outline

## Slide 3
AMD48c / AMD96ht: Single AMD EPYC 7003 48-Core Processor (GIGABYTE) CPU: x86 AMD EPYC 7643 48C/96HT @ 2.3GHz (TDP 225W) RAM: 256GB (16 x 16GB) DDR4 3200MT/s  2.7 GB/core HDD: 3.84TB Samsung PM9A3 M.2 (2280) OS: CentOS 7.9
ARM80c: Single socket Ampere Altra Q80-30 80-Core Processor (GIGABYTE) CPU: ARM Q80-30 80C @ 3GHz (TDP 210W) RAM: 256GB (16 x 16GB) DDR4 3200MT/s  3.2 GB/core HDD: 3.84TB Samsung PM9A3 M.2 (2280) OS: CentOS 7.9
2xAMD32c / 2xAMD64ht: Dual Socket AMD EPYC 7513 32-Core Processor (DELL) CPU: 2 * x86 AMD EPYC 7513, 32C/64HT @ 2.6GHz (TDP 200W) RAM: 512GB (16 x 32GB) DDR4 3200MT/s  4 GB/core HDD: 3.84TB SSD SATA Read Intensive OS: CentOS 7.9
Hardware in-House
2*ARM80c: Dual Socket Ampere Altra Q80-30 80-Core Processor (MegaRAC) CPU: 2 * ARM Q80-30 80C @ 3GHz (TDP 210W) RAM: 512GB (32 x 16GB or 16 x 32GB) DDR4 3200MT/s  3.2 GB/core HDD: 2 * 1Tb NVMe (INTEL + SAMSUNG) OS: Rocky 9.2
~ 100
~ 10
1
1
Notes: MT/s = Mega-Transfers per second (~ twice the MHz frequency)

## Slide 4
Tested Remotely
2*AMD256ht: Dual Socket AMD EPYC 9754 128-Core Processor (SuperMicro) CPU: 2 * x86 AMD EPYC 9754, 128C/256HT @ 3.1GHz (TDP 360W) RAM: 1.536TB (24 x 64GB) DDR4 3200MT/s  3 GB/core HDD: 512GB NVMe + 3.84TB SSD OS: Rocky 9.2
ARM128c: Single Socket Ampere Altra Max Q80-28 128-Core Processor (XMA) CPU: ARM Q128-28 @ 2.8GHz (TDP 250W) RAM: 512GB (64 x 8GB) DDR4 3200MT/s  4 GB/core HDD: 1Tb NVMe Storage OS: Rocky 8.8 Green Obsidian
SuperMicro
XMA
AMD128c: Single Socket AMD EPYC 8534P 64-Core Processor (SuperMicro) CPU: AMD EPYC 8534P @ 3.1GHz (TDP 200W) RAM: 576GB (6 x 96GB) DDR5 3200MT/s  4.5 GB/core HDD: 1Tb NVMe Storage OS: Rocky 8.8 Green Obsidian
New hardware we are currently testing: AMD Siena (at SuperMicro)
Also: we ordered a NVidia Grace (ARM) machine, and we are looking for AmpereOne (not yet available from our vendors).
SuperMicro

## Slide 5
Latest Results
Notes: results

## Slide 6
Latest HEPscore/Watt
I had the chance to test a few more machines, and I added them to my comparative charts.
The last one (AMD EPYC Bergamo) slightly increased the scale …

## Slide 7
Latest Thread-Scan
I also tried to run my “thread-scan” (where I limit the number of copies of each workload). Not all the workload had a clean run on all machine, but I could save a few …
cms-gen-sim-run3-ma-bmk
Here showing one of the few fully successful runs:
I run each workload separately, with the command:
singularity run -B $(pwd):/results oras://${CONTAINER} -c ${nCP} -t ${nTR} -e ${nEvt}

## Slide 8
Latest Frequency Throttling
I re-ran the HEPscore benchmark at different frequencies, with a finer step (where possible). This confirmed our previous observation that mid-frequencies gives the best performance per watt …
Notes:
- only two frequency bins were tested on AltraMax,
- the Bergamo middle point is fleaky* : frequency was not constant during job execution.
*
… but also raised a few more questions:
Why 1*Q80 ≠ 2*Q80 ?

## Slide 9
Other Results …
From the in-house results:
Ampere Altra Q80: DualSocket (2618) = 1.73 * SingleSocket (1513)
From Tommaso (INFN) + in-house results:
Ampere Altra Q128: DualSocket AltraMax (3768) = 1.82 * SingleSocket AltraMax (2064)
We found some study about inter-socket bandwidth as a possible explanation (for ARMs). We don’t know if x86s behave similarly …
- https://www.anandtech.com/show/16979/the-ampere-altra-max-review-pushing-it-to-128-cores-per-socket/3
- https://www.anandtech.com/show/16315/the-ampere-altra-review/3
Taking a closer look at the HEPscore results, it looks like 1+1<2
not 2x

## Slide 10
What Watt
Visually, it is pretty clear what number we want (average plateau or gaussian peak), but I am not sure what statistical tricks I must use to extract it from data …
(Next: looking into K-mean clustering?)
ARM80c
// Idle Power = idleAverage = (idlePower/idleBins) ;
// Max Power = maxPower ;
// (Max+Idle)/2 = halfMaxMin = (maxPower + (idlePower/idleBins))/2. ;
// Average Power = averagePower ;
// Trapezoidal Average = trapzAverage = sumJobPow/sumJobSec ;
// Modal Power (2W) = powMode2 ;
// Modal Power (5W) = powMode5 ;
// Max Average (2min) = maxPow2min ;
// Max Average (5min) = maxPow5min ;
// AverAverage = the average of plateau's averages = averAverage ;
// Power above 75% threshold = powAboveThreshold ;
// Upper Quartile = powQuartile ;
We had some discussions about what is the most representative figure for the average Power (watts)

## Slide 11
ARM80c
AMD96ht
2*ARM80c
2*AMD256ht
2*AMD64ht
ARM128c

## Slide 12
Me vs the Energy Plug-In
Notes: plugin

## Slide 13
Testing Experience
My 1st experience was terrible: Ladislav’s energy plug-in only produced 0s … because the IPMI command did not work on my machine.
When I changed it, I started getting weird error messages:
[ERROR] Plugin "CommandExecutor" failed: IndexError("no such group")
which made me think about user privileges (only root can run IPMI).
So, I tried sudo ipmi and cat ipmi.json (local) … but still got 0s at best!
I tested different versions of HEPscore + Suite, but a few of them did not work with plugins (1.6rc3 & 1.6rc4) and just crashed.
After opening an issue, exchanging a few email, and bothered
my colleagues, I gained a better understanding regex, and
finally fixed the troublesome line in the plug-in configuration …

## Slide 14
activemq:
...
global:
benchmarks:
- hepscore
...
hepscore:
version: $HEPSCORE_VERSION
config: default
options:
userns: True
# clean: True
plugins:
CommandExecutor:
metrics:
cpu-frequency:
...
power-consumption:
command: sudo ipmitool dcmi power reading | grep "Instantaneous power reading:"
regex: '\s+Instantaneous power reading:\s*(?P<value>\d+).*'
# command: cat /tmp/ipminfo.json | grep ipmi_power_watt | tr -d -c 0-9
# regex: '(?P<value>\d+)'
unit: W
interval_mins: $PLUGIN_INTERVAL_MIN
load:
...
used-memory:
...
used-swap-memory:
...
Run Script
hepscore_config.yml
#!/bin/bash
## set environment OUTFILE="run_HEPplugin.csv"
SAMPLING_INTERVAL_SEC="30"
WAIT="10"
EXEDIR=$(pwd)
...
## output the versions & stuff
echo "** User: $(whoami)"
echo "** Architecture: $(uname -i)"
echo "** Singularity Version: $(singularity --version)"
echo "** Python Version: $(python3 --version)"
echo "** Number of Threads: $(nproc)"
echo "** System: $(uname -a)"
echo "** Frequency: $(cpupower frequency-info | grep 'GHz (ass')"
echo "** Date-Time: $(date)"
## start collector & wait N sec.
./jget.sh ${OUTFILE} ${SAMPLING_INTERVAL_SEC} &
sleep ${WAIT}
## ---
while getopts ':c:k:iprs:e:wd:' OPTION; do ...
...
echo "Running script: $0 - version: $SCRIPT_VERSION"
...
## ---
pkill jget.sh
cp ${EXEDIR}/workdir/suite_results/run_*/bmkrun_report.json .
echo "Final HEP-Score:"
jq . ${EXEDIR}/bmkrun_report.json | grep '"score": [0-9]'
exit 0
run_hepscore_plugins.sh
standard run.sh script
Note: this ?<value> thing is crucial !
starts my own IPMI collector

## Slide 15
Latest Test Results
First look (just counting the lines):
- AMD: "start_time": "2023-11-08T12:43:45.844219Z" , "end_time": "2023-11-08T16:42:15.880657Z" ~ 4h
start-line=674 , end-line=1151 , interval=30sec. ; 1151-674 = 477 lines * 1/2min. ~ 240min. = 4h
- ARM: "start_time": "2023-11-08T12:41:16.625898Z", "end_time": "2023-11-08T16:00:46.475620Z", ~ 3h20min.
start-line=596 , end-line=996 , interval=30sec. ; 996-596 = 400 lines * 1/2min. ~ 200min. = 3h20min
All my experience is reported in a Jira issue: https://its.cern.ch/jira/browse/BMK-1374
Line by Line comparison (see excel):
The above comparison was done by setting the same sampling interval (30 seconds) on all plug-ins and in my exporter script. Results match 

## Slide 16
{
"date_yyyymmdd": "$DATE" ,
"time_hhmmss": "$TIME" ,
"cpu_usage_percent": "$CPUSE" ,
"memory_usage_gb": "$MEMUSE" ,
"cpu_frequency_ghz": "$FREQ" ,
"ipmi_power_watt": "$POWER"
}
jdump.sh
IPMI
(root’s crontab)
/tmp/ipmidump.json
jget.sh + Job
(user’s script)
ipmi_runtime.csv
ipmi2root.C
(ROOT script)
Excel
My IPMI collector & analyser

## Slide 17
energy_plugin
IPMI
HEPscore
run.sh
bmkrun_report.json
?
HEPscore Energy Plug-in
{
"host": {
"hostname": "arm-e22",
...
"plugins": {
...
"hepscore": {
"cpu-frequency": {
...
"power-consumption": {
"start_time": "2023-11-03T15:55:11.310751Z",
"end_time": "2023-11-03T19:11:11.293188Z",
"values": [
115.0,
303.0,
...
169.0
],
"statistics": {
"min": 108.0,
"mean": 269.0862944162437,
"max": 344.0
},
"config": {
...
},
...
"score": 1509.9384,
"status": "success"
}
}
}
about 500 lines
I am not sure how / I have not developed the tools to deal with this output …

## Slide 18
OutLook
Notes: outlook

## Slide 19
Things on my List
Improve on the calculation and reach a consensus about What Watt to use in benchmarking and agree on a common HEPscore/Watt metric.
Consolidate my results and streamline the process from benchmarking to a reference table / excel (a.t.m. a lot of copy/paste by hands).
Study the effect of frequency throttling at cluster level: we have an Ansible script to tune the frequency remotely! How to use in production?
Benchmark newly available x86 & ARM chips: AMD Siena (ongoing!), Nvidia Grace (we bought one), AmpereOne (looking for), …
Provide my input and feature request in the plug-in development … and maybe make my hands dirty – we should talk about this.

## Slide 20
Feature Request
To make this plug-in into a fully usable product, there are a few things that we need to fixed / streamline / optimise. My proposal is to open a fresh Jira issue to discuss possible new features. With some guidance, I can then I can take part in the development process …
I believe the following issues / features should be addressed:
- Export plug-in metric as a timeseries in a CSV file with (e.g., time-stamp, CPU, RAM, Frequency, Power, …), either during or at the end of the run.
- What happens if a plugin skips a beat? How often does it happen (never)? We should define an error message and set the metric to NaN (not 0) !
- Tag the time-series with workload name and number (start-end)! Or … we can think about a Utility that does so by reading the json file …
- Add more statistic calculations, including the mean* power, once we agree on it.
- Understand limitations about sampling interval (30 sec. ok, but 15 sec. crashes).
- Any other thoughts?

## Slide 21
End
Notes: when the machinery works on its own, we can think about something else …

## Slide 22
#!/bin/bash
## NEW ipmidump script, renamed "jdump.sh" because it dumps JSON ## v1.0 by Emanuele ##
##
## It dumps a bunch of system metrics to a json-like file (with the proper metric names).
## The sampling frequency can be set as command line argument when starting the script.
## Default frequency is 5 sec (good enough for most purposes), it cannot be less than 1 sec.
## Output:
##
## {
## "date_yyyymmdd": $DATE ,
## "time_hhmmss": $TIME ,
## "cpu_usage_percent": ${CPUSE} ,
## "memory_usage_gb": ${MEMUSE} ,
## "cpu_frequency_ghz": ${FREQ} ,
## "ipmi_power_watt": ${POWER} ,
## }
##
## This script should run as a background process (by root):
## $ sudo ./jdump.sh 5 &
##
## Or started on boot (add an entry to root's crontab):
## $ sudo crontab -e <-- @reboot /opt/jdump.sh 5
##
EXPORT_DIR="/tmp"
EXPORT_JSON="ipminfo.json"
EXPORT_CSV="ipminfo.csv"
SAMPLING="5"
# Regular expression to test for floats
re='^[0-9]+([.][0-9]+)?$'
# Set sampling frequency (minimum is 1 sec)
if [ $# -ge 1 ]; then
if [[ ${SAMPLING} =~ $re ]] ; then
SAMPLING=$1
fi
fi
#echo "Sampling = ${SAMPLING}"
My IPMI script(s)
#!/bin/bash
## jget.sh v1.0 by Peppo
##
## Grabs the IPMI info (and other metrics) from a JSON dump file and appends them to a CSV file, indefinitely.
## It works with the new JSON output from 'jdump.sh' (hardcoded as JFILE), the output file can be given as command line argument.
## Normally, this is run as a sub-process by the script running the actual benchmark.
##
## Usage (to just dump runtime metric to CSV):
## $ ./jget.sh &
##
OUTFILE="ipminfo.csv"
JFILE="/tmp/ipminfo.json"
json_to_csv()
{
local json_file="$1"
local csv_file="$2"
if [ ! -s "$csv_file" ]; then
# Extract keys using grep and format them as CSV line & Remove ":" and the trailing comma & Write the values to CSV file
keys=$(grep -oP '"[^"]+":' "$json_file" | tr -d '":' | tr '\n' ',')
keys=${keys%,}
echo "$keys" > "$csv_file"
fi
# Extract values using grep and format them as CSV line & Remove the trailing comma & Write the values to CSV file
values=$(grep -oP '"[^"]+":\s*"\K[^"]+' "$json_file" | tr '\n' ',')
values=${values%,}
echo "$values" >> "$csv_file"
}
# Check if dump file exists
if [ ! -f "$JFILE" ]; then
echo "No IPMI dump file was found: $JFILE. I quit!"
exit 1
fi
# Check if one command line agrument is given, if so set the output file accordingly
if [ $# -eq 0 ]; then
echo "No output filename supplied. Using default: $OUTFILE ..."
elif [ $# -eq 1 ]; then
OUTFILE=$1
echo "Output filename: $OUTFILE ..."
else
echo "Too many arguments. I quit!"
fi
# Check if old output file exists (just print a warning and overwrite it)
if [ -f "$OUTFILE" ]; then
echo "Previous IPMI file found: $OUTFILE. It will be overwritten!"
rm $OUTFILE
fi
# Read the dump file when it changes (requires 'ifnotify-tools')
while inotifywait -q -e close_write ${JFILE} 1>/dev/null
do
json_to_csv $JFILE $OUTFILE
done
jget.sh
# Main loop: exports metrics every ${SAMPLING} seconds
while true
do
# Trick to keep the exporter synchronised: sleep & ... wait
sleep ${SAMPLING} &
# Set the time-stamp
DATE=$(date +"%F")
TIME=$(date +"%T")
# CPU usage (total %) & Check for floating point number (or NaN)
CPUSE=$(top -bn1 | grep "Cpu(s)" | sed "s/.*, *\([0-9.]*\)%* id.*/\1/" | awk '{print 100 - $1}')
if ! [[ ${CPUSE} =~ $re ]] ; then
CPUSE="NaN"
else
CPUSE="${CPUSE}"
fi
# Memory usage (total GB) & Check for floating point number (or NaN)
MEMUSE=$(free -tm | awk 'FNR == 2 {printf("%.2f"), $3/1024}')
if ! [[ ${MEMUSE} =~ $re ]] ; then
MEMUSE="NaN"
else
MEMUSE="${MEMUSE}"
fi
# CPU Frequency (GHz) & Check for floating point number (or NaN), requires 'kernel-tools'
FREQ=$(cpupower frequency-info -f | grep "current CPU frequency:" | awk '{print $4 / 1000000}')
if ! [[ ${FREQ} =~ $re ]] ; then
FREQ="NaN"
else
FREQ="${FREQ}"
fi
# IPMI Power Consumption output & Check for floating point number (or NaN), requires 'ipmitool'
IPMIQUERY=$(ipmitool dcmi power reading | grep "Instantaneous power reading:")
arr=($IPMIQUERY)
POWER=$(echo ${arr[3]})
POWEX=${POWER}
if ! [[ ${POWER} =~ $re ]] ; then
POWER="NaN"
POWEX="${POWER}"
else
POWER="${POWER}"
fi
## Print to json file (overwrite):
cat > $EXPORT_DIR/$EXPORT_JSON <<EOF
{
"date_yyyymmdd": "$DATE" ,
"time_hhmmss": "$TIME" ,
"cpu_usage_percent": "$CPUSE" ,
"memory_usage_gb": "$MEMUSE" ,
"cpu_frequency_ghz": "$FREQ" ,
"ipmi_power_watt": "$POWER"
}
EOF
#echo "${WHEN} , ${CPUSE} , ${POWER} , ${MEMUSE} , ${FREQ} , ${GPUSMI}"
## For backward compatibility, let's dump values in the old CSV standard as well
if [ ! -z "$EXPORT_CSV" ]; then
echo "${DATE} , ${TIME} , ${CPUSE} , ${POWER} , ${MEMUSE} , ${FREQ} , ${GPUSMI}" > "$EXPORT_DIR/$EXPORT_CSV"
fi
wait
done
jdump.sh
root
user
... and the HEPscore benchmark runs in parallel

## Slide 23
Bugs

## Slide 24
x86 vs ARM