## Slide 1: Applications of optical technology in accelerator instrumentation and diagnostics
John Byrd
Lawrence Berkeley National Laboratory

## Slide 2: Introduction
Accelerator development has a long history of adopting and adapting new technologies to make bigger, better, and cheaper machines.
Revolutions in two fields are being applied towards accelerators:
  Ultrastable mode-locked lasers
  Optical fiber networking technology
Optical technology is approaching a similar level as RF and microwave technology to controlling accelerators.

## Slide 3: Selected topics in optical accelerator instrumentation
Time
  Femtosecond timing distribution for accelerators using stabilized optical fiber links (LC, LPA, XFELs)
  Optical techniques for measuring ultrafast electron bunches (LC, LPA, XFELs)
Intensity
  Laser stripping of high intensity H- beams (PX, ADS)
  Laser diagnostics of H- beams (PX, ADS)

## Slide 4: High precision timing and synchronization
Next generation linacs require unprecedented level of synchronization to achieve high beam quality: Linear colliders, FELs, and LPAs (staging)
  LC needs <50 fsec relative stability in linac systems
  CLIC needs <15 fsec
Master
1 psec=0.5 deg @1.3 GHz
Stabilized link
Stabilized link
Stabilized link
Stabilized link

## Slide 5: X-ray/optical Pump-probe
Ultrafast laser pulse “pumps” a process in the sample
Ultrafast x-ray pulse “probes” the sample after time ∆t
By varying the time ∆t, one can make a “movie” of the dynamics in a sample.
Synchronism is achieved by locking the x-rays and laser to a common clock.
Laser pump pulse
Electron linac/undulator
∆t
Pump laser
Master

## Slide 6: Time and Frequency Domain Stabilized Links
Fiber links can be stabilized based on the revolution in metrology time and wavelength standards over the past decade.
Optical fiber
Measure relative forward/reverse phase
CW Signal
Source
Compensate fiber length
50% reflective mirror
Maintain constant number of optical wavelengths
Optical fiber
Measure repetition rate compared to source
Pulsed Signal
Source
Compensate fiber length
50% reflective mirror
Maintain constant repetition rate of forward/reflected pulses
Correction BW limited to R/T travel time on fiber (e.g. 1 km fiber gives 100 kHz)

## Slide 7: Three Challenges
Provide long-term stable clock over entire accelerator complex: injector, linac, diagnostics, and lasers
  Use stabilized links to maintain stable relative phase
  Laser-laser stability should be <10 fsec (maybe better).
  RF cavity stability should be <50-100 fsec.
Lock remote clients to stable clock
  Advanced digital controllers (RF and mode-locked laser oscillators)
  Direct seeding of remote lasers
Measure resulting electron and photon timing stability
  Femtosecond electron arrival time and bunch length and energy spread monitors
  Femtosecond x-ray arrival time, pulse length, spectrometer

## Slide 8: Single Channel Link
Rb
lock
0.01C
AM
CW
laser
0.01C
FS
RF phase
detect
and
correct
optical
delay
sensing
FRM
FRM
Signal fiber
Beat fiber
d1
d2
fFS
fRF
Transmitter
Receiver
FRM is Faraday rotator mirror (ends of the Michelson interferometer)
FS is optical frequency shifter
CW laser is absolutely stabilized
Transmitted RF frequency is 2856 MHz
Detection of fringes is at receiver
Signal paths not actively stabilized are temperature controlled

## Slide 9: RF Transmission tests
1560nm
Rb
freq.
locker
0.01C
ref.
arm
AM
RF in
RF in
CW
fiber
laser
0.01C
+50MHz
RF phase
detection
and
correction
ref.
arm
RF in
2km
+50MHz
optical
delay
sensing
delay
data
phase
data
Compare relative phase of 2856 MHz transmitted long and short stabilized links.
Shift RF phase to compensate for link variation
Compensate for GVD correction
Actively calibrate RF phase detection front end (mixers, splitters, etc.)

## Slide 10: RF Transmission results
61 hours
Relative delay of 2km and 2 meter fibers

## Slide 11: Detailed results
1kHz bandwidth
For 2.2km, 19fs RMS over 60 hours
For 200m, 8.4fs RMS over 20 hours
2-hour variation is room temperature
time, seconds
Allan deviation
2km data
time, hours
delay error, femtoseconds
2.2km
200m

## Slide 12: All-optical lock schemes
Synchronization of lasers with RF signals limited by resolution in phase(0.01 deg@3GHz=10 fsec)
Go to optical frequencies…
Create a beat wave generated from two mode-locked comb lines (up to a few THz)
Lock the beat wave of one laser with a remote laser

## Slide 13
Electro-Optic Detection of Direct Beam Fields
SLAC DESY
LBNL, ...
FELIX DESY
RAL(CLF) MPQ
Jena, ...
FELIX DESY
LBNL
...
Spectral Decoding
Spatial Encoding
Temporal Decoding
complexity
demonstrated
time resolution
spectral upconversion

## Slide 14: EO Sampling: spectral encoding
Probe laser is optically stretched with time-wavelength correlation
EO effect is imprinted on pulse
Correlation is imaged from an optical spectrometer.

## Slide 15: Spectral upconversion diagnostic
Aim to measure the bunch Fourier spectrum...
... accepting loss of phase information & explicit temporal information
... gaining potential for determining information on even shorter structure
... gaining measurement simplicity
use long pulse, narrow band, probe laser
laser complexity reduced, reliability increased
laser transport becomes trivial (fibre)
problematic artefacts of spectral decoding become solution
NOTE: the long probe is converted to optical replica
same physics as “standard” EO
Courtesy, S. Jamison

## Slide 16: Spectral upconversion diagnostic
difference frequency mixing
sum frequency mixing
Results from experiments at FELIX (Feb 2009)
in FEL’09; (Appl. Phys. Lett.)
Theory / Expt. comparison
FELIX temporal profile
inferred FELIX spectrum
S.P. Jamison, G. Berden, P. J. Phillips, W.A. Gillespie, A.M. MacLeod
APL 2010: 96(23): 231114- 231114-3

## Slide 17: Group-velocity mismatch
Inside the crystal the two different wavelengths have different group velocities.
Define the Group-Velocity Mismatch (GVM):
Crystal
As the pulse
enters the crystal:
As the pulse
leaves the crystal:
Second harmonic created
just as pulse enters crystal
(overlaps the input pulse)
Second harmonic pulse lags
behind input pulse due to GVM

## Slide 18: Alternative method for phase-matching: periodic poling
Recall that the second-harmonic phase alternates every coherence length when phase-matching is not achieved, which is always the case for the same polarizations—whose nonlinearity is much higher.
Periodic poling solves this problem. But such complex crystals are hard to grow and have only recently become available.
Notes: Drawing courtesy of George Stegeman of CREOL.

## Slide 19: Example product
Covesion MgO:PPLN for Second Harmonic Generation

## Slide 20: Example: Beam Arrival Time Monitor using MLL pulses
Florian Loehl, et al., PRL 104, 144801 (2010)

## Slide 21: Sub-fsec arrival monitor
Sensitivity of e-beam arrival monitors proportional to reference frequency.
Use THz beat wave as a reference frequency.
Electro-optically modulate beat wave with e-beam electric field.
fsec e-bunch

## Slide 22: Frequency-Resolved Optical Gating (FROG)
FROG involves gating the pulse with a variably delayed replica of itself in an instantaneous nonlinear-optical medium and then spectrally resolving the gated pulse vs. delay.
Use any ultrafast nonlinearity: Second-harmonic generation, etc.
SHG
crystal
Pulse to be measured
Variable delay, t
Camera
Spec-
trometer
Beam
splitter
E(t)
E(t–t)
Esig(t,t)= E(t)E(t-t)
SHG FROG is simply a spectrally resolved autocorrelation.
Notes: Invented by Rick Trebino and Dan Kane

## Slide 23: SHG FROG Measurements of a Free-Electron Laser
SHG FROG works very well, even in the mid-IR and for difficult sources.
Richman, et al., Opt. Lett., 22, 721 (1997).
Time (ps)
Wavelength (nm)
5076 5112 5148
-4 -2 0 2 4
Intensity
Spectral Intensity
Phase (rad)
Spectral Phase (rad)
0
4
3
2
1
5
0
4
3
2
1
5

## Slide 24: Simulated FROG results for LCLS

## Slide 25: Laser-(assisted) Stripping of high intensity H- beams
Charge exchange injection is used for high intensity accumulation in proton synchrotrons
  Accelerate H- beams
  Remove first electron via Lorentz stripping (magnetic field)
  Remove second electron with carbon foil
Issues
  Foil generates losses in the ring
  Losses activate accelerator components
  Carbon foils cannot survive multi-MW beams
  Machine impedance
Possible Solution: Laser stripping of hydrogen
  Use optical field to promote electron to higher energy level and Lorentz strip
Challenges:
  Laser systems with sufficient average power and quality to achieve 100% stripping.
e
H-
H0
p
e
p

## Slide 26
reflected
power and
alignment
sensor
transmitted
power
transport
optics
waist, 40um
evacuated
tube
motor/piezo
controller
from
laser
Four-mirror cavity:
Round-trip time relatively independent of focal spot size
Cavity length is actively tuned to stay on optical resonance
Pulse length is long enough to not require stabilization of laser offset frequency
H- beam
active
align
~20cm
coarse
tune
info
fine tune info
Laser Stripping: transport and cavity system
active
align

## Slide 27: Laser Neutralization of H-
Radius ~ 4”
laser
detector
H-
Photodissociation for H- ions is 0.75eV
Photons with λ<1500 nm can separate H- ion into free electron and neutral H
Deflect and detect low energy electrons
Used at Los Alamos for transverse and longitudinal emittance measurements
Routinely used in SNS for measurement of transverse beam profiles
Challenge: reproduce this setup at multiple stations along the linac.
Solution: fiber distribution of laser signal.
Photodissociation x-section

## Slide 28: Overall layout
MLL
lock
box
mod
control, analysis
1MHz
lockin
amp
transimpedance
preamp
Faraday cup
H-
e-
integrating
sphere
power monitor
galvo
fiber
coax
amplitude
modulator
laser
timing
control
Narrow band lockin amp detects 1MHz modulated signal
Laser reprate is locked to 325MHz from machine
Galvo scan is triggered by macropulse event signal
Upper components are in tunnel, lower are in a laser hutch

## Slide 29: Commercial 10ps, 10W, 325MHz laser
Modelocked laser with internal amplifier
Sealed laser head, turn key
Pulse widths can be longer than 10ps, fixed at factory
Sync to RF option
Our laser is basically the same, without amplifier

## Slide 30: Distribution to multiple stations
Loss will be 10dB or less through 100m fibers
Alternative is more lasers of lower power, but it’s $99k for 10W, $84k for 0.8W
No problem with solid fiber, <1dB
400m (approximate size of facility)
100m
laser
laser
laser
precision rotation stage directs beam to any of 8 outputs by “go to position” command
pre-aligned collimators on X-Y and tilt stages
hollow fiber
solid fiber
100m
100m
100m

## Slide 31: Summary
Time
  Present:Femtosecond timing distribution has demonstrated <10 fsec over few km. Future: Demonstrate <1 fsec and 20 km.
  Present: EO sampling techniques can measure electron signals with 10 THz bandwidths. Arrival times w.r.t clock at <10 fsec. Internet communication technology quite relevant.
  Future: Demonstrate <1 fsec.
Intensity
  Present: Laser stripping principle demonstrated. IR laser systems capable of ~100% stripping to be demonstrated in the next year.
  Future: UV laser systems under development
  Present: Concepts for fiber delivery of laser wires are developed.
  Future: Demonstrate concept on prototype H- beam.