## Slide 1: Cosmic Ray in the Northern Hemisphere: Results from the Telescope Array Experiment
Charlie Jui
University of Utah
DPF, Brown University
Aug. 11, 2011

## Slide 2: Telescope Array Collaboration
T Abu-Zayyad1, R Aida2, M Allen1, R Azuma3, E Barcikowski1, JW Belz1, T Benno4, DR Bergman1,
SA Blake1, O Brusova1, R Cady1, BG Cheon6, J Chiba7, M Chikawa4, EJ Cho6, LS Cho8, WR Cho8,
F Cohen9, K Doura4, C Ebeling1, H Fujii10, T Fujii11, T Fukuda3, M Fukushima9,22, D Gorbunov12,
W Hanlon1, K Hayashi3, Y Hayashi11, N Hayashida9, K Hibino13, K Hiyama9, K Honda2, G Hughes5,
T Iguchi3, D Ikeda9, K Ikuta2, SJJ Innemee5, N Inoue14, T Ishii2, R Ishimori3, D Ivanov5, S Iwamoto2,
CCH Jui1, K Kadota15, F Kakimoto3, O Kalashev12, T Kanbe2, H Kang16, K Kasahara17, H Kawai18,
S Kawakami11, S Kawana14, E Kido9, BG Kim19, HB Kim6, JH Kim6, JH Kim20, A Kitsugi9, K Kobayashi7,
H Koers21, Y Kondo9, V Kuzmin12, YJ Kwon8, JH Lim16, SI Lim19, S Machida3, K Martens22, J Martineau1,
T Matsuda10, T Matsuyama11, JN Matthews1, M Minamino11, K Miyata7, H Miyauchi11, Y Murano3,
T Nakamura23, SW Nam19, T Nonaka9, S Ogio11, M Ohnishi9, H Ohoka9, T Okuda11, A Oshima11, S Ozawa17, IH Park19, D Rodriguez1, SY Roh20, G Rubtsov12, D Ryu20, H Sagawa9, N Sakurai9, LM Scott5,
PD Shah1, T Shibata9, H Shimodaira9, BK Shin6, JD Smith1, P Sokolsky1, TJ Sonley1, RW Springer1,
BT Stokes1, TA Stroman1, SR Stratton5, S Suzuki10, Y Takahashi9, M Takeda9, A Taketa9, M Takita9,
Y Tameda3, H Tanaka11, K Tanaka24, M Tanaka10, JR Thomas1, SB Thomas1, GB Thomson1, P Tinyakov12,21, I Tkachev12, H Tokuno9, T Tomida2, R Torii9, S Troitsky12, Y Tsunesada3, Y Tsuyuguchi2, Y Uchihori25,
S Udo13, H Ukai2, B Van Klaveren1, Y Wada14, M Wood1, T Yamakawa9, Y Yamakawa9, H Yamaoka10,
J Yang19, S Yoshida18, H Yoshii26, Z Zundel1
1University of Utah, 2University of Yamanashi, 3Tokyo Institute of Technology, 4Kinki University,
5Rutgers University, 6Hanyang University, 7Tokyo University of Science, 8Yonsei University,
9Institute for Cosmic Ray Research, University of Tokyo, 10Institute of Particle and Nuclear Studies, KEK,
11Osaka City University, 12Institute for Nuclear Research of the Russian Academy of Sciences,
13Kanagawa University, 14Saitama University, 15Tokyo City University, 16Pusan National University,
17Waseda University, 18Chiba University 19Ewha Womans University, 20Chungnam National University,
21University Libre de Bruxelles, 22University of Tokyo, 23Kochi University, 24Hiroshima City University,
25National Institute of Radiological Science, Japan, 26Ehime University

## Slide 3
Telescope Array Experiment
TA is a ultrahigh energy (>1017 eV) cosmic ray observatory located in the West Desert of Utah: largest in the northern hemisphere

## Slide 4: Outline
Introduction to Telescope Array
TA Data Analysis
Energy Spectrum Results
Composition Results
Anisotropy Results

## Slide 5: TA Detectors
TA is a hybrid experiment
507 scintillation counters surface detector (SD)
  Covers 730 km2.
3 fluorescence detector (FD) stations
  Located at the corners of the SD array
Middle Drum FD
Black
Rock
FD
Long Ridge FD
Part 1

## Slide 6: Scintillation Counters
Pre-assembled in Japan, Final Assby/testing in Delta: 2 layers, 1.25 cm scintillator, 3m2 area

## Slide 7
Scintillator Detectors on a 1.2 km square grid
Power: Solar/Battery
Readout: Radio
Self-calibrated: m background
Operational: 3/2008

## Slide 8: TA Fluorescence Detectors
Long Ridge
Black Rock Mesa
Middle Drum
Refurbished
from HiRes-I
~30km
New FDs
6.8 m2
~1 m2
14 telescopes@station
256 PMTs/camera
5.2 m2
Observations since ~10/2007
Observation since ~11/2007
Observation since ~6/2007
12 telescopes/station
256 PMTs/camera
Hamamatsu R9508
FOV~15x18deg
Notes: 8

## Slide 9: Example Event from 2008-10-26
MD
LR
BR
SD
 | q [o] | f [o] | x[km] | y[km]
MD mono | 51.43 | 73.76 | 7.83 | -3.10
BR mono | 51.50 | 77.09 | 7.67 | -4.14
Stereo BR&LR | 50.21 | 71.30 | 8.55 | -4.88

## Slide 10: Analyzing SD Event
r = 800m
Lateral Density Distribution Fit
Geometry Fit (modified Linsley)
Fit with AGASA LDF
  S(800): Primary Energy
  Zenith attenuation by MC
2008/Jun/25 - 19:45:52.588670 UTC
Part 2

## Slide 11: Surface Array Energy Measurement
Energy table is constructed using the MC (CORSIKA)
Determination of event energy by interpolating between S800 vs. sec(θ) lines
Uses novel “de-thinning” of CORSIKA (paper draft in internal review)

## Slide 12: FD Geometrical Reconstruction
The trajectory of the EAS can be determined in one of two ways:
  Monocular reconstruction using the arrival time of light signal at the detector.
  By intersecting the shower-detector planes (SDP) seen from the two detector sites.
2.
1.

## Slide 13: Measurement of a fluorescence Event
Event Display Black Rock Mesa
Monocular timing fit
Reconstructed Shower Profile
Fluorescence
Direct (Cerenkov)
Rayleigh scatt.
Aerosol scatt.

## Slide 14: Hybrid Reconstruction
Primary Cosmic Ray
UV Fluorescence Photons
Isotropic Emission
Charged Particles
Electromagnetic Shower
3. Hybrid reconstruction:
Incorporating timing information of SD into FD geometry fit
BLACK: Fluorescence
Telescope PMT
RED: Surface Detector
“Virtual” PMT
FD mono has ~5° ang. resolution
Adding SD  ~0.5° resolution.
( Stereo FD resolution ~0.5° )

## Slide 15: Energy Spectrum of UHE CR
The TA Collaboration was in part a merger of the High Resolution Fly’s Eye (HiRes) and the Akeno Giant Air Shower Array (AGASA)
AGASA and HiRes disagreed over the observation of the GZK Suppression @ ~1019.8 eV: proton+ CMBR g  D  ...
Part 3
Differential flux multiplied by E3
To highlight the subtle features in a steeply falling spectrum
AGASA: continuing spectrum seen
HiRes: GZK suppression
At 5s significance

## Slide 16: TA Middle Drum FD
HiRes : 1 layer of telescopes: < 17  in elevation, all azimuths
MD: two layers : <31, 110 azimuth
Same MC and reconstruction code for aperture calculation and spectrum as HiRes.
3 yrs = 1/3 exposure of HiRes
Same spectrum! (paper draft in internal review)
TA Middle Drum (northern) FD site is instrumented with 14 refurbished telescopes from HiRes
TA MD 3 yrs

## Slide 17: Transfer of HiRes energy scale
Agreement between the TA MD and HiRes spectra (taken with the same telescopes)  Common fluorescence energy scale for TA
Hybrid events > 1018.5 eV: SD energy scale (CORSIKA) 27% higher than the FD: adopt single (linear) scaling factor of 1.27
SD energy divided by 1.27
SD energy divided by 1.27

## Slide 18: SD spectrum
3 yrs of data represents about 2 AGASA exposure
Resulting SD spectrum is in excellent agreement with the MD FD result
SD consistent with GZK Cut-off
Using SD data from 2008/05/11-2011/04/25
Only the energy is rescaled down by a factor of 1.27 (determined from hybrid events)
TA SD aperture

## Slide 19: GZK significance
Broken power law fits show breaks consistent with ankle and GZK cut-off as observed by HiRes (GZK at 19.70.1)
Assuming continuing power law beyond cut-off: Expect events; observe 28 events
(Paper draft in internal review)

## Slide 20: Hybrid Results: MD
Using hybrid events from MD site : energy spectrum in good agreement with SD spectrum
Same FD MC and reconstruction code as HiRes but with hybrid geometry
=0.54
=0.38%
=0.52
=32g/cm2
Y angle
Rp
Zenith
Xmax
PRELIMINARY
AUG 2011

## Slide 21: Hybrid Results: BR+LR
BR+LR have large overlap:
Combined hybrid spectrum consistent with the others
  Overlaid with MD FD here
1018.2eV
Hybrid Exposure
Arrival direction
resolution
(68%): 0.9deg
Rp resolution
(68%): 1.5%
PRELIMINARY
AUG 2011

## Slide 22: Composition Study: Xmax
Controversy?
Collider Blog
Mar 3, 2010
http://muon.wordpress.com/2010/03/03/highest-energy-cosmics-rays-are-iron-nuclei/
The composition of the highest energy cosmic rays, those with energies on the order of tens of EeV (= 106 TeV), appears to include a significant number of iron nuclei – a result that I find truly astonishing. I learned about this from a nice post at Diax’s Rake…
Part 4
AUGER: Phys.Rev.Lett.104:091101,2010
Suggests shift to heavier composition at higher energies:
But the <Xmax> and RMS(Xmax) are inconsistent w.r.t a simple two-component model
HiRes: Phys.Rev.Lett.104:161101,2010 (with Xmax data suppl.)
Completely consistent with predominately light (protons) composition

## Slide 23: TA preliminary result from BR+LR stereo events
First <Xmax> results consistent with predominately proton composition
Over all distribution and shape also matches proton better than iron.
QGSJET-II
protons
Iron nuclei
PRELIMINARY
AUG 2011

## Slide 24
In 0.2 logE bins data distribution also agrees better with protons
K-S test favors protons (line at p=0.05) up to 1019.3 eV
  Low statistics at 1019.4 eV and above (~2.5 years of data)
Log (E/eV)=
19.2-19.4
Log (E/eV)=
18.8-19.0
K-S p values
QGS-JET II protons
QGS-JET II iron
Coming soon
  Xmax width analysis
  Hybrid Xmax analysis
Future
  Pushing analysis up to the GZK cut-off with more events
QGS-JET II iron
QGS-JET II protons
PRELIMINARY
AUG 2011

## Slide 25: Anisotropy?
3 yrs of SD Events :
  856 events > 1019 eV;
  49 events > 4.01019 eV
Part 5
Angular resolution ~1.5 at > 1019 eV
20 events
> 5.7 1019 eV
Dec and RA distribution consistent with isotropy
AGN
TA SD event with 3.1 circle
PRELIMINARY
AUG 2011

## Slide 26: AGN correlation?
Using AUGER hypothesis (2007): 3.1, E>5.7 1019 eV correlated with AGN z<0.018 (8/13 correlated)
Expect: ~15/20, observe 8/20,
vs. isotropic background: 5/20  pISO=0.25
Updated AUGER (2010): 21/55 consistent with current TA result
TA excess is however only 3 of 5 expected
More TA data to come!
AUGER 2010
AUGER 2007
TA surface array
PRELIMINARY
AUG 2011

## Slide 27: Conclusions
Telescope Array has been observing UHE cosmic rays in the Northern Hemisphere for ~3 years
Energy spectrum consistent with HiRes results (GZK cut-off + ankle structure)
  ***TA surface scintillator array consistent with GZK cut-off
Preliminary <Xmax> composition result from stereo data consistent with light (proton) composition
  Xmax width and hybrid results to follow soon
TA SD data consistent with isotropy
  But AUGER 2010 AGN correlation consistent with TA
More data and results to come in the next few years
Low Energy Extension (TALE) to begin construction in 2011
RADAR detection of UHE cosmic rays at TA (a la MARIACHI) funded and underway (generating lots of RF interference!)