## Slide 1: 2011 LHC Energy/2012 Operation
Energy greater than 3.5TeV:
Only minor impact on radiation levels, thus not an issue from the R2E point-of-view
Impact of 2012 operation
Will lead to a delay of R2E mitigation measures (shielding/relocation)
Impact on operation not to be excluded
Risk of destructive failures
Failure rate expected to be (just) acceptable

## Slide 2: What We Promised To Do…
Preparation of shielding & relocation measures (ready to go as from 2012 onwards)
2011 experience together with detailed monitoring & scheduled radiation tests (e.g., full power-converters) will allow us a further optimization step
Monitoring and preparation of patch solutions
Our Strategy:
Anticipate problems whenever possible (WIC relocation during technical stop)
Aim to be ready for 2012 shutdown in any case
Optimize the long-term solution (H4IRRAD crucial)

## Slide 3: To be kept in mind…
Tests with (LHC) beam
Field-calibration (for detectors) measurements:
  quench-test location would be ideal for additional loss/radiation-field studies
  TCDI near UJ87 would be an additional good spot
Scrubbing & Beam-Gas
(So far) very low radiation levels in most of the ARC/DS locations (only specific loss locations [including some surprises] are concerned already ~1Gy in some cases!)
Minor effect on shielded areas
Tunnel equipment will be exposed
Ion-Operation
One month of ions is in some locations worse than one year of nominal! -> change of B2 settings (Ralph)

## Slide 4: Follow-Ups of Chamonix…
Prepare as much improvement as possible for 2011/12 shutdown.
This requires a frozen layout for all points and the input from radiation tests/operation (to select what equipment) -> work will be anticipated as much as possible (one example: the WIC crate in P8 will most likely be moved during the next technical stop), not much more can be said during the coming months

## Slide 5: Follow-Ups of Chamonix…
2) Change B2 dispersion (IR7L): shorten region with cleaning losses into DS (ions).
No news from Ralph [last statement in Chamonix was that it’s rather easy to be done], not urgent as for ion run

## Slide 6: Follow-Ups of Chamonix…
3) Continue efforts to reduce uncertainty in equipment sensitivity.
H4IRRAD tests in preparation (Power-Converters, EN/EL equipment, GTOs) -> IMPORTANT: risk of getting the facility not ready in time, needs high priority support! (I’m worried!); CNRAD: tests will start soon (installation of first round of equipment next week) -> on the list: PCs, Cryo, QPS, DerivFIP, FipDiag, LED (BLM: new chambers)

## Slide 7: Follow-Ups of Chamonix…
4) Perform beam tests (quench test location + injection region) to improve radiation field calibration.
on the list for OP, will be re-discussed this Thursday with Mirko (should happen during beam setup period), shouldn’t be a big problem!