## Slide 1: Data Acquisition, Trigger and Control (for large Physics Experiments)
Concepts & Principles
Acknowledgements:
This presentation is based on the work of many people throughout many years, Thanks!

## Slide 2: The LHC Experiments

## Slide 3: Data Acquisition at the LHC
Data Acquisition enables physics analyses to be performed on the data produced by the detector. Definitions:
  Trigger System
    Selects in Real Time “interesting” events from the bulk of collisions. - Decides if YES or NO the event should be read out of the detector and stored
  Data Acquisition System
    Gathers the data produced by the detector and stores it (for positive trigger decisions)
  Control System
    Provides the overall Operation, Configuration and Monitoring

## Slide 4: Trigger, DAQ & Control
Detector Channels/Front-End Electronics
Readout Units
Event Building
High Level Trigger
Storage
HwTrigger
Monitoring, Control & Operations
DAQ

## Slide 5: LHC in Numbers

## Slide 6
 | Event Size (MByte) | L1 Rate (KHz) | Bandwidth (GByte/s) | Storage Rate (KHz) | Storage (GBytes/s)
ALICE | 25 | 1 | 25 | 0.050 | 1.250
ATLAS | 1 | 100 | 100 | 0.200 | 0.200
CMS | 1 | 100 | 100 | 0.200 | 0.200
LHCb | 0.05 | 1000 | 50 | 5 | 0.250
LHC Exp DAQ (until 2020)

## Slide 7
LHC DAQ Phase-space

## Slide 8: Basic Concepts

## Slide 9: Trivial DAQ
External View
sensor
ADC Card
sensor
CPU
disk
Physical View
ADC
storage
Trigger (periodic)
Logical View
Proces-
sing

## Slide 10: Trivial DAQ with a real trigger
ADC
Sensor
Delay
Proces-
sing
Interrupt
Discriminator
Trigger
Start
storage
What if a trigger is produced when the ADC or Processing is busy ?

## Slide 11: Trivial DAQ with a real trigger (2)
ADC
Sensor
Delay
Proces-
sing
Interrupt
Discriminator
Trigger
Start
Set
Q
Clear
and
not
Busy Logic
Ready
storage
Deadtime (%) - the ratio between the time the DAQ is busy and the total time

## Slide 12: Trivial DAQ with a real trigger (3)
ADC
Sensor
Delay
Proces-
sing
Discriminator
Trigger
Start
Busy Logic
FIFO
Full
DataReady
and
storage
Buffers: De-randomize data -> decouple data production from data consumption -> Better performance

## Slide 13: Trivial DAQ in collider mode
ADC
Sensor
Proces-
sing
Discriminator
Trigger
Start
storage
Busy Logic
FIFO
DataReady
Timing
BX
Abort
Beam crossing
Full
We know when a collision happens the TRIGGER is used to “reject” the data

## Slide 14: LHC timing
» ms
p p crossing rate 40 MHz (L=1033- 4×1034cm-2 s-1)
25 ns
Level 1
40 MHz
» ms
Level 2
100 kHz
Level n
1 kHz
Level 1 trigger time exceeds bunch interval
Event overlap & signal pileup (multiple crossings since the detector cell memory greater than 25 ns)
Very high number of channels

## Slide 15: Trivial DAQ in LHC
ADC
Sensor
Proces-
sing
Pipelined
Trigger
Clock
storage
Busy Logic
FIFO
DataReady
Timing
BX
Accept/Reject
Beam crossing
Full
Analog
Pipeline
Front-end Pipelines: To wait for the trigger decision + transmission delays are longer than beam crossing period

## Slide 16: Less trivial DAQ
ADC
N channels
Proces-
sing
storage
ADC
Proces-
sing
N channels
ADC
Proces-
sing
N channels
Trigger
Some processing
can proceed in parallel
Proces-
sing
Event
Building

## Slide 17: The Real Thing
?
15 million detector channels -> ~ 1 MByte
@ 40 MHz
= ~1,000,000 * 40,000,000 bytes
= ~ 40 TB/sec

## Slide 18: Trigger

## Slide 19: Trigger System
Typical ATLAS and CMS* event
20 collisions may overlap
This repeats every 25 ns
A Higgs event
The Trigger system detects whether an event is interesting or not
*)LHCb isn’t much nicer and in Alice (PbPb) it can be even worse

## Slide 20: Trigger Levels
Since the detector data is not promptly available and the trigger function is highly complex, it is evaluated by successive approximations:
  Hardware trigger(s):
    Fast trigger, uses data only from few detectors
    has a limited time budget
    Normally implemented using custom electronics
    Level 1, Sometimes Level 2
  Software trigger(s):
    Refines the decisions of the hardware trigger by using more detailed data and more complex algorithms.
    It is usually implemented using processors running a program.
    High Level Triggers (HLT)

## Slide 21: Hardware Trigger

## Slide 22: Example: LHCb Calorimeter Trigger
Detect a high energy in a small surface
Don’t forget the neighbors
Aggregate information
Evaluate decision(s)

## Slide 23: LHC: Trigger communication loop
Trigger
Primitive
Generator
Font-End
Local level-1
Global Trigger
accept/reject
pipeline delay
 3ms
 3 s
latency
loop
Timing and trigger has to be distributed to ALL front-ends
40 MHz synchronous digital system
Synchronization at the exit of the pipeline non trivial.  Timing calibration

## Slide 24: Trigger Levels in LHCb
Trigger
level 0
Event
building
High level
Trigger
Processor
Farms
Storage
Detectors
Readout
buffers
40 MHz
1 MHz
Level-0 (4 ms) (custom processors)
  High pT for electrons, muons, hadrons
HLT (»ms) (commercial processors)
  Refinement of the Level-1. Background rejection.
  Event reconstruction. Select physics channels.
  Needs the full event
5 KHz
(up to 2020)

## Slide 25: Trigger Levels in ATLAS
Trigger
level 1
Trigger
level 2
Front-end
Pipelines
Event
building
Trigger
level 3
Processor
Farms
Storage
Detectors
RoI
Readout
buffers
Region of
interest
Level-1 (3 ms) (custom processors)
  Energy clusters in calorimeters
  Muon trigger: tracking coincidence matrix.
Level-2 (»ms) (~commercial processors)
  Few Regions Of Interest relevant to trigger decisions
  Selected information (ROI) by routers and switches
  More sophisticated algorithms on full-granularity data
Level-3 (»s) (commercial processors)
  Reconstructs the event using all data
  Selection of interesting physics channels
40 MHz
100 KHz
3 KHz
200 Hz

## Slide 26: Data Acquisition

## Slide 27: Front-end electronics
Readout Units (~500)
Event Building Network
HLT Compute Units (~2000)
Storage
DAQ
Front-End Electronics
Amplifier
Filter
Shaper
Range compression
clock
Sampling
Digital filter
Zero suppression
Pipeline
Format & Readout
Buffer
Feature extraction
Detector
Custom point-to-point radiation-hard links

## Slide 28: Front-End Electronics
Detector dependent (Home made)
  On Detector
    Pre-amplification, Discrimination, Shaping amplification and Multiplexing of a few channels
    Problems: Radiation levels, power consumption
  Transmission
    Long Cables (50-100 m), electrical or fiber-optics
  In Counting Rooms
    Hundreds of FE crates : Reception, A/D conversion and Buffering

## Slide 29: Data Acquisition proper
Readout Units (~500)
Event Building Network
HLT Compute Units (~2000)
Storage
DAQ
Every Readout Unit has a piece of the collision data tagged with a unique id
All pieces must be brought together into a single Compute unit
The Compute Unit runs the software filtering (High Level Trigger)
Front-End Electronics

## Slide 30: Event Building to a CPU farm
Data sources
Event Fragments
Event Building
Data storage
Full Events
Event filter CPUs

## Slide 31: Network Technology
Need to use what is popular -> best price
Myrinet very popular when LHC experiments started being designed Used by CMS until 2014
Others could postpone the decision and used Ethernet

## Slide 32: Event Filters
Event
building
Trigger
level 3,4
Event filter
Storage
LHC experiments can not afford to write all acquired data into mass-storage. -> Only useful events should be written to the storage
The event filter function selects events that will be used in the data analysis. Selected physics channels.
Uses commercially available processors (common PCs) But needs thousands of them running in parallel.
Higher level triggers (3, 4, …)

## Slide 33: High Level Trigger
Full Event “Reconstruction”
  Reconstruct all charged particle trajectories
    Find segments, connect them, re-fit to physical trajectory
  Associate the particles with the correct p-p collision
    Multiple interactions in each crossing
  Measure all the energy depositions in the calorimeters
    with fine granularity
  Associate tracks and energy depositions
Decide whether it’s interesting

## Slide 34: ATLAS HLT Farm

## Slide 35: LHC Readout Architecture
Detector Front Ends
Event Builder (Network)
Storage
Readout Units
Event Filter Units
Event Manager
Trigger Level 1/2
...
...
With or Without Event Manager
Push or Pull Protocols

## Slide 36
HLT farm
Detector
TFC
System
L0 trigger
LHC clock
MEP Request
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
Readout
Board
Experiment Control System
VELO
ST
OT
RICH
ECal
HCal
Muon
L0
Trigger
SWITCH
MON farm
C
P
U
C
P
U
C
P
U
C
P
U
Readout
Board
Readout
Board
Readout
Board
Readout
Board
Readout
Board
Readout
Board
FE
Electronics
FE
Electronics
FE
Electronics
FE
Electronics
FE
Electronics
FE
Electronics
FE
Electronics
Front - End
Event Building
SWITCH
SWITCH
SWITCH
SWITCH
SWITCH
SWITCH
SWITCH
READOUT NETWORK
Average event size 50 kB
Average rate into farm 1 MHz
Average rate to tape 5 kHz
Event data
Timing and Fast Control Signals
Control and Monitoring data
50 GB/s
250 MB/s
LHCb DAQ (up to 2020)

## Slide 37: Operations

## Slide 38: Operations
Experiments run 24/24 7/7
In LHCb Only 2 (non-expert) operators
Monitoring
  Detect any problems as soon as possible
Configuration
  Prepare for a particular running mode
Automation
  Avoid human mistakes
  Speed up standard procedures

## Slide 39: Monitoring Dataflow
The other DAQ
UI
Archive
Alarm UI
UIs (Run Control)
Status Counters Rates Alarms
Histos Alarms
Control System
UI
RO/EB Units
UI
Timing & Trigger
Counters Rates
Counters Rates
Infrastr
Dataflow
DQHisto
HLT
Infrastr
Dataflow
DQHisto
Monitoring
Infrastr
Dataflow
DQHisto
Reconstr.
Histos
Histos
Histos
HLT SubFarms
D I M
Infrastr
Dataflow
DQHisto
Infrastr
Dataflow
DQHisto
HLT Nodes
D I M
D I M
HLT SF Ctrl
Histo Savesets
Infrastr
Dataflow
Storage
Event Data
Status, Counters
Counters, Rates
Event Data
Histos
Histos Alarms
Automatic Actions
(aggregation)
(aggregation)
History Counters Rates Alarms
Automatic Analyses
UI
Data Quality UI
History Histos
Operators

## Slide 40: LHCb Data Quality (old)
  Monitor the quality of the data being acquired
  Compare with reference
  Automatic analyses

## Slide 41: LHCb Data Quality: Monet

## Slide 42: LHCb Alarm Screen

## Slide 43: LHCb Online Event Display

## Slide 44: Operator Interfaces
Types of User Interfaces
  Alarm Screens and/or Message Displays
  Monitoring Displays
  Run Control & DCS Control

## Slide 45: DAQ Upgrades

## Slide 46
 | Up to Yesterday |  |  | Upgrade (2022-2026) |  | 
 | L1 Rate (KHz) | Event Size (MByte) | Bandwidth (GByte/s) | L1 Rate (KHz) | Event Size (MByte) | Bandwidth (GByte/s)
ALICE | 1 | 25 | 25 | 50 | 20 | 1000
ATLAS | 100 | 1 | 100 | 200 | 4 | 800
CMS | 100 | 1 | 100 | 1000 | 4 | 4000
LHCb | 1000 | 0.05 | 50 | 40000 | 0.1 | 4000
LHC DAQ Upgrades

## Slide 47: The Upgrades
2022
up to 2022
2022

## Slide 48: LHC Exp. Upgrades
Reasons:
  More Physics/Faster Physics/Better Physics
  (Improved Detectors)
  Reduce impact of Hw Triggers:
    Working with partial information and with drastic simplifications has a price:
      Potentially interesting and valuable events are lost
    Directions:
      Eliminate / reduce hardware Level-1 (ALICE, LHCb)
      Substantially upgrade Level-1 (ATLAS, CMS)
  Emphasize Real-Time Alignment and Calibration

## Slide 49: LHCb Upgrade
Detector Channels
R/O Electronics
To be kept
DAQ
40 MHz Trigger-less Readout
  < 10% detector channels kept
  100% or R/O electronics replaced
  New DAQ system
  New Data Center

## Slide 50: The LHCb Example
Storage
HwTrigger
Monitoring & Control
DAQ
Detector Channels/Front-Ends
Readout Units
Event Building
High Level Trigger
40 MHz
1 MHz
Storage
Monitoring & Control
DAQ
Detector Channels/Front-Ends
Readout Units
Event Building
High Level Trigger
40 MHz
x
1st Large Physics Experiment to completely abolish the Hardware Trigger -> Probably the largest Data Acquisition System in the world today
Spoiler: Commissioned last year -> And it works!!

## Slide 51: The New LHCb DAQ
Detector Channels
Front End Electronics
Readout Boards/Event Builder/HLT1
Experiment Control System
DAQ
TFC
Monitoring
HLT1 Store
HLT2 Store
Alignment
To Offline
HLT2 Farm
Collapsed Layers (price/perf)
Real-Time Align & Calib
Offline Quality Output data
40 MHz
Split HLT

## Slide 52: LHCb Dataflow Evolution
In 2012: More CPU needed for better Trigger
  Since: unused interfill CPU + free disk space

## Slide 53: HLT Farm Usage Evolution
Farm Node
Farm Node
Resource Optimization in 2012 -> Deferred HLT
  Idea: Buffer data to disk when HLT busy / Process in inter-fill gap
  More time for more complex algorithms
Standard HLT
Deferred HLT
Farm Node
Farm Node during Physics
Farm Node Inter-fill
1 MHz
5 KHz
70 KHz
HLT
HLT
HLT
EvtBuilder
EvtBuilder
~20%
1 MHz

## Slide 54: LHCb Dataflow Evolution
In 2015: Better Trigger and Trigger output data
  Since: HLT anyway composed of two steps

## Slide 55: HLT Farm Usage Evolution
Even better Resource Optimization in 2015 -> Split HLT
  Idea: Buffer ALL data to disk after HLT1 / Perform Calibration & Alignment / Run HLT2 permanently in background
  Calibration and Alignment previously done Offine -> Better data!
Farm Node
100%
For DQ only
Conditions DB
Calib&Align
Selected Events
Local disk Buffer
1 MHz
12.5 KHz
HLT1
HLT2
EvtBuilder
100 KHz

## Slide 56: Farm Usage in 2018
  Keeping farm busy
  Simulation when less physics
  Disk Usage < 25%

## Slide 57: LHCb Dataflow Evolution
In 2022: Even better -> No HW Trigger
  Since: Better readout and network technology available
x

## Slide 58: New DAQ Design Principles
Selected Concepts:
  Simplicity (whenever possible)
  Integration & Homogeneity
  Promote HW Standardization
    Same hardware components for all sub-systems
  Promote SW Uniformity
    Guidelines, Framework Components, Templates
  Separate Data/Control paths
    From the Front Ends to the High Level Trigger

## Slide 59: Online System Upgrade
New Data Acquisition Hardware and Dataflow Software
New Infrastructure & Sub-Detector Equipment

## Slide 60: FE Electronics
Front-end electronics
  Use CERN GBT chip (Gigabit Transceiver)
  A radiation hard ASIC (Application Specific Integrated Circuit)
  But unlike the drawing: separately for DAQ and for Timing & Control
DAQ
TFC+ECS

## Slide 61: Readout Units
PCIe40 cards in EB PCs
  PCIexpress card
  Large FPGA
  48 GBT links, 10 Gb/s each
  Versatile via the firmware
Located on surface
  Distance from FE: ~350m
In total:
  ~ 10000 optical links
  ~ 500 readout boards
  ~ 100 TFC/ECS cards (separated from data path)
Used also by ALICE (and others)

## Slide 62: Networking
Again, use what is popular -> best price
Basically the choice was Infiniband and/or Ethernet

## Slide 63: Event Builder
Two options tested
  Only one worked well within our time and budget (traffic pattern: All to One/flow control /switch buffering very expensive)
Technology: Infiniband + Ethernet for Distribution
Technology: Ethernet (Would have been simpler and known)
Dedicated EB (TDR baseline)
Distributed EB
Complete events here
Complete events here
x

## Slide 64: High Level Trigger
Processing Options (HLT1)
  Several R&D Projects in all these areas
Notes: Task parallelism is the simultaneous execution on multiple cores of many different functions across the same or different datasets. Data parallelism (aka SIMD) is the simultaneous execution on multiple cores of the same function across the elements of a dataset

## Slide 65: HLT1
Two options: CPU vs GPU
  Both worked: Cost (and politics/sociology) made the difference
HLT1 here
x
HLT1 here

## Slide 66: LHCb Current DAQ Core
EB Servers
  ~160
  Hosting PCIe cards
Readout Units:
  ~500
  Powerful FPGA
  48 FE links (1Gb)
GPUs:
  ~160 -> ~320
  Fast HLT1 Pass
CPUs
  ~4000 (donated)
  Thorough HLT2

## Slide 67: Data Processing
Improvements all the way to analysis strategy: Turbo stream
  Since we can automatically perform final alignment and calibration online
  So we can achieve offline quality alignment and calibration in the trigger
  Store only part of the event → allows for higher output bandwidth

## Slide 68: Alignment and Calibration
Why do we need alignment & Calibration?
  Physical movements, magnetic field, temperature, pressure effects
  Better mass resolution
  Better particle identification (PID)
  Store less background → More bandwidth for physics!
What and when do we align?

## Slide 69: HLT2
A large CPU Farm
  Around 4000 PCs (many inherited for free)
  Also runs Calibration and Alignment tasks
A brand new Computer Center

## Slide 70: Configuration, Control and Monitoring

## Slide 71: Control System Tasks
Configuration
  Selecting which components take part in a certain “Activity”
  Loading several millions of parameters (according to the “Activity”)
Control core
  Sequencing and Synchronization of operations across the various components
Monitoring, Error Reporting & Recovery
  Detect and recover problems as fast as possible
  Automate Standard Operations
User Interfacing
  Allow the operator to visualize and interact with the system

## Slide 72: Control Framework
Can be based on Commercial SCADA Systems (Supervisory Control and Data Acquisition)
  Commonly used for:
    Industrial Automation
    Control of Power Plants, etc.
  Providing:
    Run-time Database and Tools
    Archiving of Monitoring Data including display and trending Tools.
    Alarm definition and reporting tools
    User Interface design tools
  Used in LHC experiments DCS and LHCb for everything
Or can be home made

## Slide 73: The Control System
Detector Channels
Front End Electronics
Readout Boards/Event Builder/HLT1
Experiment Control System
DAQ
Detector & General Infrastructure (Power, Gas, Cooling, etc.)
External Systems (LHC, Technical Services, Safety, etc.)
TFC
Monitoring
HLT1 Store
HLT2 Store
Alignment
To Offline
HLT2 Farm

## Slide 74: Experiment Control System
LV Dev1
LV Dev2
LV DevN
DCS
SubDetN DCS
SubDet2 DCS
SubDet1 DCS
SubDet1 LV
SubDet1 TEMP
SubDet1 GAS
…
…
Commands
DAQ
SubDetN DAQ
SubDet2 DAQ
SubDet1 DAQ
SubDet1 FEE
SubDet1 RO
FEE Dev1
FEE Dev2
FEE DevN
Control Unit
Device Unit
…
…
Legend:
INFR.
TFC
LHC
ECS
HLT
Status & Alarms
Control Units are logical entities:
  Behave as a Finite State Machine / Rule Based system:
    Capable of Partitioning: Exclude/Include children
    Can take local decisions: Sequence & Automate Operations or Recover Errors
Device Units
  Provide the interface to the device (hardware or software)
Implementation: (JCOP project)
  Framework
Deployment:
  Runs distributed over >100 PCs (Virtual Machines)

## Slide 75: Control System Behaviour
LV Dev1
LV Dev2
LV DevN
DCS
SubDetN DCS
SubDet2 DCS
SubDet1 DCS
SubDet1 LV
SubDet1 TEMP
SubDet1 GAS
…
…
Commands
DAQ
SubDetN DAQ
SubDet2 DAQ
SubDet1 DAQ
SubDet1 FE
SubDet1 RU
FE Dev1
FE Dev2
FE DevN
Control Unit
Device Unit
…
…
Legend:
INFR.
TFC
LHC
ECS
HLT
Status & Alarms
Distributed “Intelligent” Hierarchical System
RUNNING
READY
NOT_READY
Start
Stop
ERROR
UNKNOWN
Configure
Reset
Recover
CONFIGURING

## Slide 76: Operations
  RunControl
    Handles the DAQ & Dataflow
    Allows to:
      Configure the system
      Start & Stop runs
  AutoPilot
    Knows how to start and keep a run going from any state.
  BigBrother
    Based on the LHC state:
      Controls SD Voltages
      VELO Closure
      RunControl
Main Tools:

## Slide 77: Run Control
  Run Control & The Autopilot:
    Configures, Starts and Keeps the RUN going.
    Configuration Driven by an “Activity”

## Slide 78: Run Control
ALICE: Tcl/Tk
ATLAS: Java (modular)
CMS: Web Tools (JavaScript+HTML)
LHCb: JCOP FW (UI builder)

## Slide 79: Big Brother
Based on LHC state, controls:
  Voltages
  VELO Closure
  Run Control
Can sequence activities, ex.:
  End-of-fill Calibration
Confirmation requests and Information
  Voice Messages

## Slide 80: Detector Control System
JCOP FW
ALICE
ATLAS
CMS
LHCb

## Slide 81: LHCb Control System
Courtesy of CMS DCS Team (by analyzing our FSM tree)

## Slide 82: Concluding Remarks
Trigger and Data Acquisition systems have become increasingly complex.
Luckily the requirements of telecommunications and computing in general have strongly contributed to the development of standard technologies:
  Hardware: Fast ADCs, Field-Programmable Gate Arrays, Analog memories, multi-core PCs, Networks, Helical scan recording, Data compression, Image processing (GPUs), ...
  Software: Distributed computing, Software development environments, Supervisory systems, Artificial Intelligence tools...
We can now build a large fraction of our systems using commercial components (customization will still be needed in the front-end).
It is essential that we keep up-to-date with the progress being made by industry.

## Slide 83: LHC/LHCb Fill Sequence
NO_BEAM
INJECTION
RAMP
PHYS_ADJUST
PHYSICS
(ADJUST)
DUMP/EOF
Handshake for Injection(TI8_Setup)
Handshake for Adjust
Act: Lower Voltages, VELO Out
Injection Permit = FALSE, Internal Clock, Any state of LHCb
Injection Permit = TRUE
Injection Permit = FALSE Act: Start Raising Voltages At FLAT_TOP: Act: External Clock, Reset DAQ
Act: Raise Voltages, VELO In
Act: VELO Out, Internal Clock Act: EOF Calibrations
(Act: Lower Voltages, VELO Out)
Handshake: Confirm Handshake -> Prepare detector -> Confirm Ready
Simple Confirmation

## Slide 84: Other Tools & Components
Main Framework Components:
  Communications
    Device Access and Message Exchange between processes
  Intelligence: Finite State Machines/Expert System Functionality
    System Description, Synchronization and Sequencing
    Error Recovery, Assistance and Automation
  Databases
    Configuration, Archive, Conditions, etc.
  User Interfaces
    Visualization and Operation
  Other Services:
    Process Management (start/stop processes across machines)
    Resource Management (allocate/de-allocate common resources)
    Logging, etc.

## Slide 85: Communications (example)
DIM – Distributed Information Management System
  Efficient and light weight data exchange across processes (and machines)
  Available for:
    C, C++, Java, Python
    Linux, Windows, etc.
  Client/Server (Publish/Subscribe)
  Services
    Set of data, any type or size
      Single items, arrays or structures
    Free name space
      But better use a naming convention
    Servers publish Services.
    Clients subscribe to Services.
      Once, at regular intervals or on change
    Clients can also send Commands to Servers
  Name Server
    Keeps the coordinates of available Services

## Slide 86: Automation (example)
SMI++ - State Management Interface
  A Tool for the Automation of large distributed control systems
  Method:
    Classes and Objects
      Allow the decomposition of a complex system into smaller manageable entities
    Finite State Machines
      Allow the modeling of the behavior of each entity and of the interaction between entities in terms of STATES and ACTIONS
    Rule-based reasoning
      React to asynchronous events (allow Automation and Error Recovery)
Proxy
Proxy
Proxy
Hardware Devices
Obj
Obj
Obj
SMI Domain
Obj
Obj
Obj
Obj
Obj
SMI Domain
READY
NOT_READY
StartRun
StopRun
ERROR
Configure
Reset
RUNNING
Recover

## Slide 87: SMI++ - The Language: SML
  Finite State Logic
    Objects are described as FSMs their main attribute is a STATE
  Parallelism
    Actions can be sent in parallel to several objects.
  Synchronization and Sequencing
    The user can also wait until actions finish before sending the next one.
  Asynchronous Rules
    Actions can be triggered by logical conditions on the state of other objects.

## Slide 88: Online Databases
Three main logical Database concepts in the Online System
But naming, grouping and technology can be different in the different experiments…
Experiment’s HW & SW
PVSS
To Offline
Cond.
DB
Config.
DB
To Offline
Configuration settings for a running mode
Monitoring data (at regular intervals)
if History needed
if needed by Offline
if needed for next run settings (Pedestal Followers)
Control System
Archive
DB