## Slide 1: Update on the status of the 205Tl(n,γ) cross section measurement
A. Casanovas1, A.Tarifeño-Saldivia1, F. Calviño1, C. Domingo-Pardo2, E. Maugeri3, V. Alcayne, V. Babiano, J. Lerendegui, C. Guerrero and the n_TOF Collaboration
¹ Universitat Politècnica de Catalunya (UPC), Barcelona, Spain
² Instituto de Fisica Corpuscular (CSIC-Universitat de Valencia), Valencia, Spain
3Paul Scherrer Institute, Switzerland

## Slide 2: Outline of the presentation
Reminder of the motivations for the measurement
Report of the signal analysis work (still ongoing)
Calibrations with simulations
Notes: I will start with an Introduction part, where I will describe the astrophysical motivations for this measurement and I will also give a brief description of the neutron capture process.
In the second part I will explain the measurement tech. and describe the facility where the experiments were performed and the experimental setup
Then I will describe some of the important aspects of the measurement and the analysis procedure of the 203Tl measurement, including the most relevant results obtained
I will do the same for the 204Tl measurement
And finally I will summarize the results, with

## Slide 3: The 205Pb-205Tl decay system
205Tl is the most abundant (71%) stable (at earth) thallium isotope (Z=81)
 | 204Pb | 205Pb | 206Pb | 
 | 203Tl | 204Tl | 205Tl | 206Tl
Already measured at n_TOF(C. Domingo-Pardo et al.,
Phys. Rev. C 75, 015806 (2007))
(n,g)
(n,g)
(n,g)
EC
b-
C-13 pocket s-process
After s-process
b-
s-process flow
(n,g)
Already measured at n_TOF (A. Casanovas Ph.D. thesis (2020), submitted to PRL)
TP s-process
s-only
1. K. Yokoi et al., The production and survival of Pb-205 in stars, and the 205Pb/205Tl s-process chronometry, Astronomy and Astrophysics 145, 339-346 (1985)
2. R.G.A. Baker et al. , The thallium isotope composition of carbonaceous chondrites — New evidence for live 205Pb in the early solar system, Earth and Plan. Sc. Lett (2010)
3. Mowlavi, N., Goriely, S., Arnould, M., The survival of 205Pb in intermediate-mass AGB stars, Astron. Astrophys. 330, 206–214 (1998)
(n,g)
Stellar effects on 205Pb: at s-process sites temperature, EC decay is so strongly enhanced that its survival is compromised
The 205Pb/204Pb ratio could be used as a “chronometer” of the s-process1,2,3
  Time elapsed since the last injection of main s-process products into the pre-solar nebula
AGB (red giant) time evolution
Activation of the bound state β decay of 205Tl
Recently measured! Final results in the near future
EPJ Web of Conferences 279, 06010 (2023)
Notes: One of the main points of interest of this región is that 204Pb and 205Pb are s-only […] , and on top of that, Pb5 is radiaoctive blablá
But there is a problem… during the first stage of s-process nucleosynthesis, where neutrons are released through the reaction c13na
However, during the second stage, during the recurrent TP, T rises due to flash He burning, and neutrons are released… The high T activates the decay…
A part from that, it is worth mentioning that most reactions affecting the Pb5 abundance have already been measured

## Slide 4: Main ideas
205Tl is the most abundant (71%) stable (at earth) thallium isotope (Z=81)
 | 204Pb | 205Pb | 206Pb | 
 | 203Tl | 204Tl | 205Tl | 206Tl
Already measured at n_TOF(C. Domingo-Pardo et al.,
Phys. Rev. C 75, 015806 (2007))
(n,g)
(n,g)
(n,g)
EC
b-
C-13 pocket s-process
After s-process
b-
s-process flow
(n,g)
Already measured at n_TOF (A. Casanovas Ph.D. thesis, 2018)
TP s-process
s-only
1. K. Yokoi et al., The production and survival of Pb-205 in stars, and the 205Pb/205Tl s-process chronometry, Astronomy and Astrophysics 145, 339-346 (1985)
2. R.G.A. Baker et al. , The thallium isotope composition of carbonaceous chondrites — New evidence for live 205Pb in the early solar system, Earth and Plan. Sc. Lett (2010)
3. Mowlavi, N., Goriely, S., Arnould, M., The survival of 205Pb in intermediate-mass AGB stars, Astron. Astrophys. 330, 206–214 (1998)
(n,g)
Stellar effects on 205Pb: at s-process sites temperature, EC decay is so strongly enhanced that its survival is compromised
The 205Pb/204Pb ratio could be used as a “chronometer” of the s-process1,2,3
  Time elapsed since the last injection of main s-process products into the pre-solar nebula
AGB (red giant) time evolution
Activation of the bound state β decay of 205Tl
The 205Tl(n,γ) capture reaction, by affecting the abundance of 205Tl, could play a relevant role in the final abundance (and survival) of 205Pb
The 205Pb/204Pb ratio has the potential to be used as a “chronometer” of the s-process
A precise knowledge of this cross section is also important to complete the analysis of the 204Tl branching point
Notes: Now I’ll will focus on the tl and pb isotopes, and describe the nucleosynthesis process over time in this region. […] During h-Shell burning in AGB stars, neutrons are produced by the reaction c13 blablá
This decay process bounds the 205Pb abundance to the 205Tl abundance

## Slide 5: Status of the data for 205Tl(n,γ) : cross section
Only one previous measurement: R. L. Macklin and R. R. Winters, Stellar neutron capture in the thallium isotopes, Astrophys. J. 208, 812 (1976)
  Experimental capture cross section or resonance parameters never published
  Related EXFOR data: only resonance kernels, no uncertainties, up to 102 keV
  Explicit correction factor for systematic error at ORNL: not known (0.95 for 203Tl)
Most recent evaluations show important discrepancies:
Notes: Issues , not problems

## Slide 6: Status of the data for 205Tl(n,γ): MACS
MACS at 30 keV comparison:
  Kadonis reference value: 52.6 ± 3.9 mb (ENDF evaluation)
  Examination of ENDF data suggests it is based on 1976 ORNL measurement
  No direct uncertainty assessment in the whole energy range (8 keV to 50 keV)
ENDF/B-VII.1
JEFF 3.2 (!)
Macklin&Winters (1976)
Activation measurements
205Tl(n,γ)
Estimation of the uncertainty in the accuracy of the MACS
MACS range variation over reference (+10% to -60%)
+10%
-60%
Notes: We selected this range as rapresentative of the uncertainty in the accuracy of the macs

## Slide 7: Main points
From the current status of the data a +10% to -40% uncertainty in the value of the 205Tl(n,γ) is assumed
This leads to an approx. 40% global uncertainty in the 205Pb/204Pb ratio only due to this reaction
Goal: increase precision and accuracy of 205Tl(n,γ) to reduce the uncertainty in the 205Pb/204Pb ratio

## Slide 8: 205Tl(n,γ) measurement: sample issue
Acquired “pure” sample was heavily contaminated with bromine
A new, on-the-go sample of natural thallium was produced in a few days thanks to our PSI colleagues (E. Maugeri’s team)
  3.7 g of natural thallium, of which 2.6 g is 205Tl
  Same diameter, similar thickness
This sample luckily had no bromine
  (or an undetectable amount)
As nat. Tl, sample contains also 29% of 203Tl
Resonance spacing of Tl isotopes resonances is high “easier” to separate them
203Tl was measured in 2015, resonance information up to 25 keV
Higher energy results could be used to complete 203Tl(n,γ) analysis of 2015 measurement (to be carefully studied)
Meas. Setup: standard C6D6 Legnaro detectors, “old” PMT

## Slide 9: Measurement summary
TOTAL | 2.508E+18
Assigned | 2.60E+18
Sum on good targets: | 1.853E+18
Sum backgrounds: | 4.315E+17
Sum useful data: | 2.284E+18
Sum Tl-nat 99%: | 1.613E+18
Sum Tl-nat 99% filters: | 1.09E+17
Sum dummy: | 2.322E+17
Sum dummy filters: | 6.743E+16
Total dummy: | 2.996E+17
Sum Gold: | 1,314E+17
Sum Pb-nat: | 4.753E+16
Sum Pb-nat filters: | 4.403E+16
Total Pb-nat | 9.156E+16
Sum empty: | 4.036E+16
Sum Br cont. thick: | 1.822E+17
Sum Br cont. thin: | 4.165E+16
Sum contaminated: | 2.238E+17
2·1018 protons approved
1.7·1018 allocated

## Slide 10: First steps: signal analysis
EAR1 Legnaro C6D6 detectors equipped with old PMT have always suffered from strong “rebound” signals, appearing around 600 ns after the primary signal and with much les amplitude (for example, see multiple talks by V. Babiano on 80Se(n,g), or more recently by F. García on 176Yb(n,g), etc.)
  Issue much worse in some detectors tan others
Since Legnaro became the standard C6D6 setup, this issue has been circumvented by using high E. dep. thresholds (250 - 300 keV)
“Official” PSA routine parameters not changed in years: parabolic fit to the amplitude, no PSF, no fit of the baseline
As a first step in the analysis, we have been working in new sets parameters:
  Same old parameters, but with PSF and adaptative baseline (“oldParPSF”)
  PSF + baseline + new more agressive parameters to try to eliminate 600 ns rebounds during PSA (“newPar” parameters)

## Slide 11: ΔT between consecutive signals (E.dep. th = 120 keV)

## Slide 12: Rebounds in data (E. dep. = 120 keV)
Rebound is artificial contribution to resonance integrals
Can lead even to false double structures

## Slide 13: Old PSA parameters and rebounds

## Slide 14: Old PSA parameters and rebounds

## Slide 15: Old vs new parameters
Derivative step
Threshold in derivative

## Slide 16: New PSA parameters (first version)
New parameters: increase in step size and derivative threshold
Goal: eliminate rebounds while keeping signals of similar amplitude

## Slide 17: New PSA parameters (first version)
New parameters: increase in step size and derivative threshold
Goal: eliminate rebounds while keeping signals of similar amplitude

## Slide 18: New PSA parameters (first version)
New parameters: increase in step size and derivative threshold
Goal: eliminate rebounds while keeping signals of similar amplitude

## Slide 19: New PSA parameters (first version)
New parameters: increase in step size and derivative threshold
Goal: eliminate rebounds while keeping signals of similar amplitude

## Slide 20: New PSA parameters (first version)
New parameters: increase in step size and derivative threshold
Goal: eliminate rebounds while keeping signals of similar amplitude

## Slide 21: New PSA parameters (first version)
New parameters: increase in step size and derivative threshold
Goal: eliminate rebounds while keeping signals of similar amplitude

## Slide 22: ΔT between consecutive signals: th=120 keV
Flat distribution also for low threshold
Increase in step size increases “dead time” (i.e. time under which two signals can’t be distinguished) from 30 to 40 ns 25% additional pile up correction
Due to wider stepsize, not reliable for TOF 25-30 us (200 keV)

## Slide 23: ΔT between consecutive signals: th=250 keV
Flat distribution also for low threshold
Increase in step size increases “dead time” (i.e. time under which two signals can’t be distinguished) from 30 to 40 ns 25% additional pile up correction
Due to wider stepsize, not reliable for TOF 25-30 us (200 keV)

## Slide 24: ΔT between consecutive signals: th=600 keV
Flat distribution also for low threshold
Increase in step size increases “dead time” (i.e. time under which two signals can’t be distinguished) from 30 to 40 ns 25% additional pile up correction
Due to wider stepsize, not reliable for TOF 25-30 us (200 keV)

## Slide 25: ΔT between consecutive signals: th=1000 keV
Flat distribution also for low threshold
Increase in step size increases “dead time” (i.e. time under which two signals can’t be distinguished) from 30 to 40 ns 25% additional pile up correction
Due to wider stepsize, not reliable for TOF 25-30 us (200 keV)

## Slide 26: ΔT between consecutive signals: same detector
L6D6-2-C

## Slide 27: Calibrations with simulations
Linear or double linear calibrations provide a satisfactory agreement with sources for all detectors
Overall very good gain stability (±1-2%) along the measurement

## Slide 28: Calibrations with simulations
Linear or double linear calibrations provide a satisfactory agreement with sources for all detectors
Overall very good gain stability (±1-2%) along the measurement

## Slide 29: Calibrations with simulations
Linear or double linear calibrations provide a satisfactory agreement with sources for all detectors
Overall very good gain stability (±1-2%) along the measurement
Example L6D6 1-G: Good agreement with a single linear calib for Cs-137 (0.662 MeV)

## Slide 30: Calibrations with simulations
Linear or double linear calibrations provide a satisfactory agreement with sources for all detectors
Overall very good gain stability (±1-2%) along the measurement
Example L6D6 1-G: Good agreement with a single linear calib for Y-88 (0.898 MeV)

## Slide 31: Calibrations with simulations
Linear or double linear calibrations provide a satisfactory agreement with sources for all detectors
Overall very good gain stability (±1-2%) along the measurement
Example L6D6 1-G: Good agreement with a single linear calib for Y-88 (1.8 MeV)

## Slide 32: Calibrations with simulations
Linear or double linear calibrations provide a satisfactory agreement with sources for all detectors
Overall very good gain stability (±1-2%) along the measurement
Example L6D6 1-G: Good agreement with a single linear calib for AmBe (4.43 MeV)

## Slide 33: Calibrations with simulations
Linear or double linear calibrations provide a satisfactory agreement with sources for all detectors
Overall very good gain stability (±1-2%) along the measurement
Example L6D6 1-G: Good agreement with a single linear calib for CmC source (6.12 MeV)

## Slide 34: Calibrations with simulations
Linear or double linear calibrations provide a satisfactory agreement with sources for all detectors
Overall very good gain stability (±1-2%) along the measurement
But… agreement with Ba-133 source bad second double linear needed for low energy

## Slide 35: Calibrations with simulations
Linear or double linear calibrations provide a satisfactory agreement with sources for all detectors
Overall very good gain stability (±1-2%) along the measurement
Second linear at low E. dep. (<400 keV) for det. 1 and 3 Ba-133 source calibration very important (few gamma rays below 300 keV)

## Slide 36: Ratios between resonance integrals
Ratios obtained for four Au resonances (4.9 eV, 60 eV, 79 eV, 110 eV) for each threshold and detector
L6D6-1-G

## Slide 37: Ratios between resonance integrals
Ratios obtained for four Au resonances (4.9 eV, 60 eV, 79 eV, 110 eV) for each threshold and detector
L6D6-3-D

## Slide 38: Ratios between resonance integrals
Ratios obtained for four Au resonances (4.9 eV, 60 eV, 79 eV, 110 eV) for each threshold and detector
L6D6-4-D

## Slide 39: Summary and outlook
A fine tuning of the PSA values should allow for a “clean” elimination of the rebounds, while allowing to keep the threshold in deposited energy as low as possible
Work still in progress
  Check comparison signal Area-amplitude ratio, C6D6 low amplitude signal high dispersion in shape
I warmly encourage everyone working on C6D6 data analysis to play with the PSA and provide new (and possible) better parameters
Detector calibrations with simulations confirm very stable and linear behaviour of the four detector
Next meeting: analysis should be in advanced stage