## Slide 1: BNL/CERN discussion Accelerator aspects (energy and intensity control) 19 July 2023
E. P. Johnson, M. Fraser, R. Garcia, K. Bilko, A. Waets, N. Emriskova, M. Delrieux, D. Cotte, I. Ruiz

## Slide 2: How the PS delivered Pb beam for CHIMERA ?
Energy
Intensity
Spill time profile

## Slide 3: Energy
Energy control, stripping and energies used in 2022

## Slide 5: Ion beam
Accelerate partially stripped Pb54+ (28e-) in PS
  Isotope A=208=82p+126n
Fully stripped lead ion Pb82+ beam
  In transfer line: lower rigidity  requires less B-field
Charge
q = 54
q = 82

## Slide 6: Energies
For 2022 run three energies selected
Large spacing in LET
  Trade-off between lower energies and intensities (transmission/instrumentation vis.)
  Partially stopped by degraders
Kinetic energies at target are lower
  interaction with vacuum windows, instruments and air molecules

## Slide 7: Energy control
Energy controlled via PS B-field
  Single knob
  Rigidity propagated to transfer line (dipole, quadrupole)
B-field
Notes: Mention: hand-scaling, non-linear transfer function, non-PPM
LEQ = Low Energy Quadrupoles
QSE = Quadrupole for Slow Extraction

## Slide 8: PFW
Ion cycle improvement
  Switching off PFW for low energy beams (<2GeV/n)
    Strong non-linear component
    Allowed scaling of the PS
    Tune reached and controlled with LEQ + QSE
Closed block
Open block
Notes: Mention: hand-scaling, non-linear transfer function, non-PPM
LEQ = Low Energy Quadrupoles
QSE = Quadrupole for Slow Extraction

## Slide 9: Active change of the primary beam energy
Dedicated energy scan on the CHARM diode with 775, 800, 825, 850, 900 MeV/u
  < 30 sec to change energy
Will be focus of 2023 (instead of 3 discrete energies)
  Removes need for several users
Lowest energy ?
  Matter interaction ?
  Vacuum pipe installation in T8 ?
  Degrader system before target ?

## Slide 10: Energy scan to East Dump

## Slide 11: Intensity
RFKO, intensity measurement and gain setting
Energy
Intensity
Spill profile

## Slide 12: Slow extraction (SX)
Uses magnetic septum SMH57 and SMH61
Amplitude growth done with third order integer resonance and SX

## Slide 13: Iteration on SX
Change tune Q with PFW, QSE, LEQ
  OK for high energy beams (5.3 GeV/u)
  ≤ 2 GeV/u no PFW
  Bunch rotation (large dp/p)
  Flat QSE under resonance
  Ramp tune with LEQ
RF Knock Out
  Constant extracted beam optics
  RF Excitation with transverse damper
  No bunch rotation (small dp/p)
  More stable at different energy (no PFW and chirp on damper excitation freq)
  Easier control of the beam intensity (single knob)
Bare machine tune
Extraction

## Slide 14: RFKO
Emittance increase through RF excitation
Transverse Damper (exciter)
T. Bass
Notes: Chromaticity: tune dependence on momentum

## Slide 15: Intensity vs gain
Calibration with diode allows to convert from XSEC amplitude to ions/cm^2/spill
Flux ∝ to 1/momentum at certain gain
  650 MeV transmission (air interaction)?
Saturation at high gain
  Exponential + 2nd order
  Constant power TFB
XSEC70 intensity
Notes: Mention: Reproducible intensity per gain

## Slide 16: Intensity vs gain
Intensity in the PS as a function of RFKO gain
Low gain
High gain
Notes: Mention: Reproducible intensity per gain

## Slide 17: Challenge: Supercycle composition
Machine reproducibility is a challenge
Spike in intensity when different cycle is played
Degauss cycle not possible in PS
Careful programming of SC to minimise perturbation
B-train measurement system to help

## Slide 18: Spill time profile
Time structure, frequencies in the beam, spill-by-spill variability
Energy
Intensity
Spill profile

## Slide 19: Spill time profile
> 7 instruments to measure spill time profile
Gas scintillator (BCGAA/BXSCINT)
XSEC 23/70/94
XION 71/94
Diode
(BLM, SRAM, …)
BCGAA023
XSEC023

## Slide 20
Instrument location

## Slide 24: Spill profile
Time resolution:
  20 ms for XION, XSEC
  2-3 ms for Diode
  0.5 ms for BXSCINT
  Finer sampling possible with BXSCAL (0.3-0.04 ms) and white rabbit (not logged) in F61 and Diode up to 0.5 µs
Notes: Mention that this is for a single gain and energy

## Slide 25: Spill time profile
Average time 360 ms
Longer spill time (~1000 ms) could be tested if needed
  Long flat top
  No bunch rotation
  Only GRPOS tune shift

## Slide 26: Comparison between gain
Intensity gain
Reproducible shape per gain
Peak shifts with gain
  Dynamic effect
  True for range of gains
  Amplitude Modulation with feedback

## Slide 27: Spill structure
Slow and fast frequencies time structure
Slow because of RFKO technique
  Software limitation to max chirp rep rate of 1 ms intervals
  1 kHz

## Slide 28: Spill structure
Fast spill structure at the fractional tune of third integer
  Frev/3
  ~ 130 kHz
  (beam still bunched and debunching during extraction)
Diode fast sampling rate
  0.5 µs
650 MeV/n

## Slide 29: R&D
Signal generator
Exploit low-pass filter effect of beam (transit time) by exciting at higher freq
Variable gain during spill
Transit time (10-100 turns)
Remote app
  Send python commands
  Continuous chirp

## Slide 30: Spill-by-spill variability
Flux variation during Nov. 2022 run
  Instrumentation gain (not logged)
  Supercycle composition

## Slide 31: Spill-by-spill variability

## Slide 32: Conclusion
Energy:
  Upgraded control system for energy scaling of PS and TL
Intensity:
  SX technique changed to RFKO
  Simple control with TFB voltage
Spill time profile:
  R&D for 2023
    Damping of the slow frequency by chirping faster
    Longer spill
    (Uniform spill with AM)

## Slide 33: Questions
or comments

## Slide 35: Extra slides

## Slide 36: Instrument comparison
Good time profile agreement
XION saturates at > 0.1 gain

## Slide 37: Spill-by-spill variability