## Slide 1: QFib Test Beam
S. OZKORUCUKLU
27 July 2023

## Slide 2
Beam defining counters
Beam defıned as 5mm diameter or 10x10mm2 according to combination of coincidence of beam counters
DUT: Detector Under Test
1.5m long HF-PPP fibers + MCP-PMT/PMT
TRS: Time Reference System
SB1-2: MCP-PMT + Qbar doublets (two 5x5x100mm3), 45o to the beam
TRC: MCP-PMT + Qblock (12x12x25mm3)/UVT Plexi (12x12x20mm3), Head on
Qfib Test Beam Setup

## Slide 3
180 GeV pion beam with high intensity
Almost all the beam time(180GeV pion) was used with the runs and scans.
The team used almost all the beam time with a 180GeV pion beam. It was not possible to get data with the main user's beam request, which is a 20GeV positron beam.
24 Runs and 4 Scans were taken.
More than 14 Million events were taken.
TRS calibrated with the scans.
Attenuation and time resolution in the long fiber is investigated with the DUT study.
Data Taking Conditions

## Slide 4
TRS Amplitudes
Blue – SB2 – Ch3
Red – SB1 – Ch2
TRC
Beam
SB2
SB1
180 GeV Pions
TRC – With 12x12x25mm3 QBlock

## Slide 5
TRS Timing
Sigma_1-2  20.71 0.084 ps
Sigma_1-3  22.8 ps
Sigma_2-3  29.1 ps
Intrinsic time resolutions
  Sigma1(TRC) 7.14 2.19 ps
  Sigma2(SB1) 19.44 0.80 ps
  Sigma3(SB2)  0.72 ps
SB1  5 cm
SB2  5 cm
SBs are 45 deg

## Slide 6
Beam
SB2
SB1
180 GeV Pions
TRC – With 12x12x25mm3 QBlock
1.5 m long
HF-PPP Fibers
MCP-PMT
R7525 PMT
Different kind of photodetectors (PMT/MCP-PMT) were used.
Timing measurement was performed using long fibers for different distances to the photodetector.
DUT Setup

## Slide 7
Beam
SB2
SB1
180 GeV Pions
TRC – With 12x12x25mm3 QBlock
1.5 m long
HF-PPP Fibers
MCP-PMT
R7525 PMT
Different kind of photodetectors (PMT/MCP-PMT) were used.
Timing measurement was performed using long fibers for different distances to the photodetector.
Time Resolution
Time resolution of HF-PPP fiber 20 cm away from the photodetector
HF-PPP + R7525
HF-PPP + MCP-PMT
31.48 ps
135.8 ps