## Slide 1: Update on the power loss computations (III)
SPS BWS Task Force
Carlo, Christine, Thomas and Patrick (in 2017), Leo, Elena, Chiara, Niky, Alice, Rama, Michael, Giulia, Giovanni, Benoit
Many thanks to our colleagues from BI for the teamwork (William, Federico, Jonathan, Manfred) and to the IWG members for the help and advice

## Slide 2: Outlook
Analysis of power deposed on the wire and on the ferrites with the two mitigation solutions:
  5 ferrite tiles + coupler* (V-BWS)
  6 ferrite tiles (H-BWS)
*coupler has an approximated geometry

## Slide 3: Impedance curves
5 ferrite tiles vs 6 ferrite tiles (CST Studio® Wakefield Solver)
Very subtle changes, 5 ferrite case slightly higher impedance for the two main modes (160 MHz and 800 MHz) – as expected

## Slide 4: Impedance curves (II)
5 ferrite tiles vs 5 ferrite tiles + coupler (CST Studio® Wakefield Solver)
Coupler has a big impact in the total impedance of the BWS
Frequency shift + reduction of the 160 MHz mode
Reduction + broadening of 800 MHz mode

## Slide 5: Impedances + beam spectrum
160 MHz mode shifted away from the spectral line and with lower amplitude → less power loss expected
Measured spectrum, bunch length = 1.6 ns

## Slide 6: Power deposed on the wire (comparison)
H-BWS: 6 Tiles
V-BWS: 5 Tiles + coupler
Power ~3 W less on V-BWS due to lower amplitude of 160 MHz
Min/Max curves closer due to broader peaks

## Slide 7: Power deposed on the ferrites (comparison)
H-BWS: 6 Tiles
V-BWS: 5 Tiles + coupler
Power ~10 W less on the V-BWS due to lower amplitude of 160 MHz
Min/Max curves closer due to broader peaks

## Slide 8: Power extracted by the coupler
V-BWS: 5 Tiles + coupler
Significant impact of power extracted by the coupler, especially for the 160MHz mode

## Slide 9: Summary
Coupler has a big but overall positive impact in the total impedance curve and on dissipated power.
Better behavior of V-BWS consistent with simulations:
  Max. calculated power on the wire expected around 3 W lower for the V-BWS (5 ferrites + coupler)
  Avg. calculated power on the ferrite expected around 10 W lower for the V-BWS

## Slide 10
Elena de la Fuente García (BE–ABP–CEI)
Update on the power loss computations (III)
Thank you 
Leonardo Sito (BE–ABP–CEI)

## Slide 11: Agreement with observations
22/04 (Breakage): 1.8e11 p/b,
bunch length 1.55 ns
20/07 Measured during past high intensity MD: 2.1e11 p/b, bunch length 1.7 ns
V-BWS’s wire heats less thanks to coupler, H-BWS shows thermionic emission (?) but still far from scrubbing run’s measurements 
Thermionic?

## Slide 12: Backup: Power Loss calculation
Measurements of beam spectrum in time domain along the cycle
Beam spectrum in frequency domain along the cycle
Post-processing*
CST Wakefield and Eigenmode simulations to get the longitudinal Impedance
Spectrum
Impedance
Beam Intensity
* Correct baseline, do FFT, normalize, apply transfer function
Implemented in BIHC python package